## Slide 1: Real Options: Valuation of Storage
P. V. Krishnarao
Enron Research Group
Houston, January 27, 1999
© 1999 PK-9010292-<number>

## Slide 2: Valuation of Storage: Outline
Why Value Storage?
Types of Natural Gas Storage
  Reservoir
  Salt-dome Storage
  Aquifer
Storage Valuation Issues
  Physical: Injection & Withdrawal capacities, Pipeline Capacities
  Contractual: firm/interruptible contracts, storage contracts
  Market: Multiple prices, Market movement, Counter parties
  Regulation, Taxes, System Reliability etc.

## Slide 3: Valuation of Storage: Outline (Cont’d)
Storage Valuation Using Simulation
  Reservoir : Seasonal Spreads & Options
  Salt-dome: Short-term Arbitrage
Storage Valuation Using Real Options
  Dynamic Programming

## Slide 4: Why Value Storage?
Long-term Strategic Decisions
  Long-term (10+ years) strategy and planning
  Asset acquisitions, sales, construction
Medium-term Purchase/Sale decisions
  5-year Storage participation
Short-term Storage Contracts
  6-month storage contract

## Slide 5: Types of Storage
Reservoir Storage
Salt Cavern Storage
Aquifer Storage

## Slide 6: Types of Storage: Reservoirs
Reservoir Storage
  Depleted oil and gas fields
  Most common type
  Large capacities, take months to fill
  Cushion gas-50% of total gas volume

## Slide 7: Types of Storage: Reservoirs (Cont’d)
Reservoir Storage Example: Bammel
  Total Working Gas = 58 BCF
  Injection rate = 360,000 MMBtu/day
  Withdrawal rate = 1,250,000 MMBtu/day
  Injection months = April-October
  Withdrawal months = October-February

## Slide 8: Types of Storage: Salt Caverns
Salt Cavern Storage
  Mined hollow spaces underground
  Salt in bedded salt formation or salt domes
  High deliverability and injectability
  Low cushion gas (33% of total), Low cycling costs
  Development time is 1-2 years

## Slide 9: Types of Storage: Salt Caverns (Cont’d)
Salt Cavern Example: Napoleonville
  Total working gas = 4 BCF
  Injection rate = 400,000 MMBtu/Day
  Withdrawal rate = 200,000 MMBtu/Day
  Annual turnover = 3 to 4

## Slide 10: Types of Storage: Aquifers
Aquifer Storage
  Porous/permeable water-bearing rock formations
  Second most common type of storage
  High cushion gas requirement (up to 80% of total gas)
  Long development times (5 years)

## Slide 11: Types of Storage: Aquifers (Cont’d)
Aquifer Storage Examples
Anoca
    Northern Illinois Gas, La Salle (Illinois)
    Total gas: 169 BCF
    Working gas: 60 BCF
Redfield
  Northern natural gas, Iowa
  Total gas: 118 BCF
  Working gas: 26 BCF

## Slide 12: Storage Valuation Issues
Physical:
  Someone else’s storage: Play by their rules
  Own storage: Play by laws of physics
  Injection & withdrawal capacities (compressors, pressures)
  Target volume limits, pipeline capacities
Contractual:
  Storage contracts, pipeline contracts
Market:
  Price movement, demand (weather!), Counter parties
Other: Regulation, taxes, system reliability

## Slide 13: Storage Valuation Using Simulation
Price Simulation
Operating
Strategy
Storage
Optimization
Storage Value
Inputs
Price Process
Real Options

## Slide 14: Storage Valuation Using Simulation (Cont’d)
Valuation Procedure
  Simulate the price curve for each day of valuation period
  Price data + user-specified strategy decide storage usage & buy/sell volumes
  Volume constraints satisfied: Injection/ withdrawal, buy/sell (market), storage capacity

## Slide 15: Storage Valuation Using Simulation (cont’d)
Prices & volume decisions over all days determine the storage value.
Several thousand simulations give a probability distribution for storage value.
Difficult issue: daily decisions.

## Slide 16: Storage Valuation Using Simulation (cont’d)
Advantages
  Simulation method is very flexible: can incorporate many constraints
  Relatively easy to understand and implement
  Can incorporate any price process
  User can try different operating strategies and measure the impact
Disadvantages
  Does not capture all the optionality available
  Storage value dependent on the operating strategy

## Slide 17: Reservoir Storage Valuation
Main value of reservoir storage is from seasonality - spread between winter and summer prices
Many inter-related options
Value computed subject to volume constraints:
  Injection/Withdrawal limits as a function of volume in storage
  Pipeline/Market volume limits
  Limits due to market movements
In practice: third party lease payments important

## Slide 18: Reservoir Valuation Procedure
Generate Price curves for each day of the hedging period
    HJM model that captures the historical relationships between futures prices of different months is used for this.
Each day, volumes are hedged up to the market limit.
Pairs of summer and winter months are chosen in the decreasing order of their spreads. Only positive spreads are considered.
Hedge volumes are chosen subject to monthly volume limits for summer and winter months.

## Slide 19: Salt Cavern Storage Valuation
Main value of salt-dome storage is from short-term cycling, price spikes, and high deliverability
Value computed subject to volume constraints:
  Injection/Withdrawal limits as a function of volume in storage
  Pipeline/Market volume limits
  Limits due to market movements
Again, in practice, third party lease payments important

## Slide 20: Salt-Dome Storage Valuation: Price Simulation
Heath-Jarrow-Morton (HJM) technology to simulate the entire price curve
Spot price correlated with the prompt-month price
Spot price can be based on Jump Diffusion process to simulate spikes

## Slide 21: Salt Cavern Storage Valuation: Price Simulation (Cont’d)
Forward Price
Simulation
HJM Method
Current
Spot
Spot Price
Simulation
Jump Diffusion
Current Fwd.Curve
Storage
Optimi-
zation

## Slide 22: Salt Cavern Storage Valuation
Daily decisions regarding buy/sell and inject/withdraw made according to some criteria
For example, to capture value of price spikes
  Spot price > Next month price ==> Sell today
  Spot price < Next month price ==> Buy today
Any strategy chosen will not capture all the optionality

## Slide 23: Storage Valuation Using Real Options Method
Recognize that today’s decision changes the future value of the storage asset
Choose the alternative that maximizes the expected present value of the asset

## Slide 24: Storage Valuation Using Real Options (Cont’d)
Solution Technique: Dynamic Programming
  Starting at the last time step and working backwards in time to find the value
  Solve for the optimal decision at each time step that maximizes the expected present value
  Similar to valuing an American option using binomial trees

## Slide 25: Storage Valuation Using Real Options (Cont’d)
Price Process
  Different processes can be used
    Geometric Brownian motion
    Processes with mean reversion
    Jump diffusion
  Heath-Jarrow-Morton to simulate the whole price curve
    Simulation works forward in time whereas Dynamic Programming works backwards
    Simulate prices using HJM and construct a probability tree of prices by grouping the prices generated into different bins

## Slide 26: Conclusions
For valuation, it is important to recognize all the optionality in an asset.
Deterministic (discounted cash flow) or perturbation methods are useful tools, but they can not capture all the embedded real options.
To correctly value assets and related projects, option pricing techniques have to be used.