## Slide 1: The California Power Crisis: What Happened, Why, and Key Lessons Learned
09/27/25 01:19
CONFIDENTIAL
Sebastian Barth, Tim Bleakley,
Peter Glynn, Tommy Inglesby, Adrian Reed, Thomas Seitz
February 21, 2001
EPNG PRACTICE DOCUMENT
This report contains information that is confidential and proprietary to McKinsey & Company and is solely for the use of McKinsey & Company personnel. No part of it may be used, circulated, quoted, or reproduced for distribution outside McKinsey & Company. If you are not the intended recipient of this report, you are hereby notified that the use, circulation, quoting, or reproducing of this report is strictly prohibited and may be unlawful.

## Slide 2: TODAY’S DISCUSSION
  Background – from deregulation to default
  The current crisis
    Why power prices rose dramatically
    Why the electric utilities are poised on the edge of bankruptcy
  Lessons learned and key takeaways
  Appendices
    A: California deregulation basics
    B: The impact of natural gas costs on the California market
    C: Estimating the impact of demand elasticity
    D: Supply and demand estimates and drivers
    E: Market behavior observations
    F: NOx credits in California
    G: Back-up
    H: Glossary
Notes: <number>
txho/10209 zxd414.ppt

## Slide 3: CALIFORNIA’S DEREGULATION PROCESS BEGAN IN 1994
1994
1995
1996
1997
1998
  Blue book proposal
    Proposes direct access in 1996 for industrial customers with full access by 2002
  CPUC policy decision
    Adopts hybrid pool/bilateral market structure and 5-year (1998-2002) phase-in of full access
  AB 1890 legislation
    Authors CPUC policy decision
    Suggests 4-year phase-in to full access (1998-2001)
  CPUC order
    Requires full access implementation in 1998
  SCE and PG&E auction of substantial portions of generation portfolio
  FERC authorizes operation of CalSO and CalPx
  AB 1890 implemented
    Customers free to choose alternative providers
    CalPx begins operations
    CalSO begins operations
    Stranded cost recovery begins
Notes: <number>
txho/10209 zxd414.ppt

## Slide 4: MANY CONSTITUENCIES WITH DISPARATE AGENDAS FORCED A PROTRACTED NEGOTIATION PROCESS . . .
Small customers (e.g., TURN)
  Reliable electricity supply
  Lower rates
  No full recovery of stranded costs
  No advantages of large customers over small ones
Governors (e.g., Pete Wilson)
  Economic growth through lower energy prices
Labor unions
  Assurance that existing labor agreements will be maintained
  Assurance that retraining and severance will be included in stranded costs
Environmentalists (e.g., Sierra)
  Subsidy for renewable energy sources in the competitive market
  No relaxation of emission limits
Utilities (e.g., Southern California Edison, PG&E)
  No retail wheeling
  No vertical deintegration
  Full recovery of “stranded” costs
  Regulation-intensive alternative to direct access
Independent power producers and marketers (e.g., AES)
  Assurance that existing contracts will be respected
  Some certainty as to the calculation of avoided costs
  Retail head room
Large customers/industrial organizations (e.g., California Large Consumer Association, Agricultural Energy Consumer Association)
  Lower rates
  Direct access
  Vertical deintegration
  No full recovery of “stranded” costs
FERC (Federal Energy Regulatory Commission)
  Replace ROR regulations with competitive market structure
  Full recovery of utilities’ stranded cost
“Utilities want their CTC, small customers want to be sure they don’t get shafted, IPP producers want access to customers, and renewable power producers want subsidies . . .”
– Utility negotiator
Deregulation legislation
(a negotiated
settlement)
Notes: <number>
txho/10209 zxd414.ppt

## Slide 5: IN THE END, AB I890 SEEMED TO PROVIDE SOMETHING FOR EVERYONE, INCLUDING A RELATIVELY QUICK TRANSITION TO COMPETITION Key features of AB 1890 (passed August 31, 1996)
* Wholesale commodity price as determined by PX plus T&D charges
Source: Regulatory Research Associates; Team analysis
Intention
Provide an efficient market-based wholesale price-setting mechanism and ensure grid reliability
Prescribe quick transition to customer choice
Accelerate recovery of stranded costs and speed market to full competition
Ensure consumers would realize rate reductions immediately
Major provision
  Established the creation of non-profit ISO and PX entities to enable orderly wholesale market and dispatching operations
  Directs the CPUC to establish customer-direct access schedule to reach 100% access by 1/1/02
  Stranded investment recovery
    To be completed prior to 12/31/01
    Beyond 2001, IOUs at risk for recovery of any remaining stranded costs
    Competitive transition charge (CTC) calculated as the difference between frozen retail rates and cost to supply electricity*
  Retail prices
    Frozen for large C&I and industrial customers
    10% automatic rate reduction for small commercial and residential customers
Intended primary beneficiary
  All participants
  Retail customers
  PG&E, SDG&E, SoCal Edison
  Retail customers
Notes: <number>
txho/10209 zxd414.ppt

## Slide 6: CLEARLY, MOST PARTIES TO THE NEGOTIATIONS ANTICIPATED A SMOOTH TRANSITION TO LOWER PRICES
Source: Press releases
“A powerful new stimulant for any new business looking to grow or move to California.”
– Pete Wilson
California Governor
September 24, 1996
“It is the best way to move to a desirable competitive market that will benefit all customers, large and small.”
– John Bryson, CEO
Southern California Edison
December 21, 1995
“We think the aggregation of our power purchases . . . will bring us substantial savings.”
– Bob Largent,
Director of Energy Management
McDonald’s Corp.
September 30, 1996
“This [legislation] is designed to reduce costs to all customers of all classes and simultaneously bring stability to the system.”
– Senator Steve Peace
California Legislature
August 27, 1996
“Consumer groups . . . can combine to negotiate for a lower basic contract rate supplemented by less expensive power from the spot market.”
– C. Edward Wolf, President
Sr. Utility Ratepayers of California
September 15, 1996
Notes: <number>
txho/10209 zxd414.ppt

## Slide 7: HOWEVER, DEREGULATION PROVED TO BE MORE COMPLEX THAN ANTICIPATED Key market issues emerging after ISO/PX start-up in 1998
Issue/challenge
No retail competition
System
implementation
Grid expansion
Gaming behavior
Ancillary service market design
Observations
  The mechanism for CTC recovery did not allow for retail headroom, effectively pushing back retail competition to 2002
  Problem with key system software threatened to delay operations and complicate system management
  Bottlenecks on the south to north transmission system impacted ability to receive inputs of power and ancillary services
  Inconsistencies in rules surrounding bid process and settlement methodology at times may have allowed participants to realize higher prices
  The local nature of service requirements may have effectively reduced competition to only a few players in each market, driving up prices
Source: CaISO Annual report on Market Performance, June 1999
Notes: <number>
txho/10209 zxd414.ppt

## Slide 8: . . . SUCH THAT THE DEREGULATORY PROCESS NEVER TRULY ENDED REVISIONS TO RULES AFTER PASSING AB 1890
Principal issues
  Refine rules to address issues surfaced during implementation
  Coordinate participants and expand procedural detail
  Provide transparency and environmental safety
  Skyrocketing wholesale prices
  Capacity shortages
  Transmission constraints
  Inadequate pricing regulations
  Permitting/environmental impediments
Key legislation
  AB 360
  SB 1305
  AB 1775
  CPUC Order 166
  SB 110
  SB 90
  AB 1154
  AB 265
  AB 1970
  AB 1156
  SB 1388
  SB 1194
  AB 995
  AB 918
  AB 94
  SB 552
  SB 1771
  AB 2705
  SB 38
  AB 58
  SB 36
  SB 47
  AB 1
AB 1890
1996
San Diego price run-up 2000
2001
Plus over 35 additional legislative amendments
Deregulation was a “moving target” as, on average market rules were changed or amended many times per month
Source: California State Assembly Web site
EXAMPLES
Notes: <number>
txho/10209 zxd414.ppt

## Slide 9: DESPITE FREQUENT RULE REVISIONS, SPOT PRICING BECAME MORE VOLATILE AND AVERAGE PRICES INCREASED
Dollar per megawatt-hour peak price
Source: California Power Exchange; California Independent System Operator
12-month average
Daily peak price
Investigations into ancillary services market power 7/00
San Diego customers scream for price relief 7/26/00
Independent generators threaten to stop selling power to California fearing credit risk 12/00
SCE and PG&E warn of impending bankruptcy
12/1/00
CalPx suspends day-ahead and day-of market operations 1/30/01
CA Attorney General to investigate San Diego price spikes 7/28/00
CalPx and CaISO begin operations 3/31/98
FERC grants ISO authority to cap ancillary and balance prices 7/17/98
SDG&E recovers stranded costs and increase rates for customers 7/1/99
CaISO orders PG&E to begin rolling blackouts in Bay Area 6/15/00
CaISO authorized to invest $750 million over 3 years in new power plants to battle capacity shortages 11/1/00
1998
1999
2000
Notes: <number>
txho/10209 zxd414.ppt

## Slide 10: TODAY’S DISCUSSION
  Background – from deregulation to default
  The current crisis
    Why power prices rose dramatically
    Why the electric utilities are poised on the edge of bankruptcy
  Lessons learned and key takeaways
  Appendices
    A: California deregulation basics
    B: The impact of natural gas costs on the California market
    C: Estimating the impact of demand elasticity
    D: Supply and demand estimates and drivers
    E: Market behavior observations
    F: NOx credits in California
    G: Back-up
    H: Glossary
Notes: <number>
txho/10209 zxd414.ppt

## Slide 11: THE CURRENT CRISIS
Why power prices rose dramatically
Why the electric utilities are poised on the edge of bankruptcy
  What were the key drivers of high prices and price volatility?
  Why, specifically, did the IOUs bear much of the financial burden?
Two related, but very much separate, issues
Notes: <number>
txho/10209 zxd414.ppt

## Slide 12: THERE WERE 3 PRIMARY DRIVERS OF HIGHER POWER PRICES
Higher variable production costs
CONCEPTUAL
Higher value of generation capacity (up to full reinvestment economics)
Higher prices due to power market inefficiencies (beyond full reinvestment economics)
Total increase in power prices
Notes: <number>
txho/10209 zxd414.ppt

## Slide 13: NATURAL GAS-FIRED UNITS ARE GENERALLY ON THE MARGIN IN CALIFORNIA CaISO power and load duration cost curves, 2000
Marginal generation costs*
$/MWh
CaISO generation capacity
MW
Actual load
Hours**
* Based on capacity weighted average of generator reported monthly fuel costs for May-September 2000 variable operating costs; estimated unit by unit; does not include NOx credit costs
** Total hours at given level of demand for Winter 10/99 through 2/00, Summer demand hours between 5/00 through 9/00
Source: RDI base case; RDI PowerDat; CaISO; Team analysis
900
Gas-fired capacity
Gas-fired capacity was virtually always on the margin setting price in California during 2000
Load duration
ESTIMATE
Winter Loads
Summer Loads
Notes: <number>
txho/10209 zxd414.ppt

## Slide 14: VARIABLE PRODUCTION COSTS INCREASED OVER 650% YEAR ON YEAR FOR A TYPICAL MARGINAL GAS UNIT The variable cost structure of a 12,000 heat rate simple cycle gas unit
Dollars per megawatt hour
* For more on the impact of higher natural gas costs on the California power crisis, see Appendix A
** Represents typical values for 2000 vintage NOx RTC credits during December 1999 and 2000 respectively
*** California gas turbines with heat rates from 11,000 to 13,000 MMBtu/kWh running January to June 2000 emitted an average 0.93 lbs/MWh of NOx. Range of gas fined power plant NOx emissions in 2000 was 0.06 to 5 lbs/MWh
Source: DRI; Western Natural Gas Market Review; CaISO; EPA; Team analysis
December 2000
December 1999
Natural gas at
$2.56/MMBtu*
NOx credits at
$1.0/lb.**
Other variable costs
Total variable cost of production
Natural gas at
$16.56/MMBtu
NOx credits at
$46.0/lb.**
Other variable costs
Total variable cost of production
ESTIMATE
Dramatically higher delivered natural gas costs and NOx credits are largely responsible for the increase
Notes: <number>
txho/10209 zxd414.ppt

## Slide 15: THE HIGHER NATURAL GAS PRICES ARE, IN TURN DRIVEN BY 4 KEY FACTORS *
Permian basin basis
differential with Henry Hub
increased
$/MMBtu **
* For more in the impact of higher natural gas costs on the California power crisis, see Appendix A
** Natural gas prices are volume weighed monthly average index prices based from Natural Gas Week
Source: DRI; Western Natural Gas Market Review; Natural Gas Week
Higher Henry Hub Pricing
Greater interstate basis
differential CA border
(Topock) – Supply Basin
Greater intrastate transport
costs – CA border to PG&E
Citygate
Total PG&E Citygate
December 1999
December 2000
(0.01)
While natural gas prices across the nation were much higher, much of the increase in delivered gas costs can be attributed to higher interstate and intra-California transport/basis costs
Notes: <number>
txho/10209 zxd414.ppt

## Slide 16: NATURAL GAS TRANSPORT CAPACITY INTO CALIFORNIA WAS CONTROLLED BY ONLY A FEW PLAYERS
* Assumes that Enron capacity reverted to El Paso when contract was canceled by Enron 1/31/00. Release volumes were aggregated to parcel number rather than delivery point to avoid double counting on contracts with option for multiple delivery points
** Represents maximum value assuming all release volumes flow. Calculations: Total monthly volume x [(basis differential – (reservation + commodity + fuel)], where basis differential is Permian to California border (El Paso Topock) using average monthly prices, and average monthly commodity charges (4¢/MMBtu), fuel costs (4.85% of Permian price ~$4.00/MMBtu), and reservation charges(20¢/MMBtu).
*** Other include 21 participants during Q4 including BP, KN Energy, Duke, Williams and other marketers
Source: RDI/Gas Dat for release capacity data; Topock prices – Natural Gas Week; Permian prices – Gas Daily; Team analysis
Purchased Release Capacity at California Border 2000
MMcf/day - released volume*
El Paso merchant services
Other***
Potential total gross profit generation of
El Paso release capacity holders during Q4 2000**
100 = $1.148 billion
It is not just the
merchant generators that fared well in
California
El Paso
merchant
services
EL PASO PIPELINE EXAMPLE
Other
Enron
Reliant
Enron
Reliant
Basis differential – Permian to California border (Topock)
$/MMBtu
Notes: <number>
txho/10209 zxd414.ppt

## Slide 17: HIGHER VARIABLE PRODUCTION COSTS ACCOUNTED FOR ROUGHLY 35% TO 45% OF THE TOTAL INCREASE IN CALIFORNIA POWER PRICES
Variable costs*
Capacity value up to FRE
Market inefficiencies beyond FRE
Total**
* $8.2 billion (40% of the wholesale revenue increase) in incremental variable costs estimated as the difference between the 2000 and 1999 sums of variable cost x total CalSO load for all hours when CalSO price exceeds variable cost for a 10,000 heat rate gas plant (= 10,000 x California volume weighted average border daily gas price + 0.93 lb. NOx/MWh x monthly average NOx RTC price $/lb. + $1.03/MWh variable O&M)
** The difference in 2000 vs. 1999 CalSO total energy + ancillary services costs of $20.6 billion as reported in CalSO 1/16/01 market analysis report
FRE = Full reinvestment economics
Source: Platt’s Gas Daily; Cantor Fitzgerald; CalSO; RDI PowerDat; Team analysis
ESTIMATE
2000 over 1999 annual CaISO generation revenues
Percent
?
?
The
California crisis
is not a power
crisis, it is an integrated gas,
gas delivery,
and power
generation
crisis
Notes: <number>
txho/10209 zxd414.ppt

## Slide 18: BY 1999, AVERAGE WHOLESALE PRICES IN CALIFORNIA EXCEEDED THE FULL REINVESTMENT ECONOMICS OF A CCGT
California 1999 power and gas prices
1 Power price calculated as day-ahead volume weighted market clearing price; CalPX
2 PG&E city gate daily average price; Gas Daily
3 Includes PX, bilateral, ISO real-time and ancillary service costs; CalSO Market Analysis Report 1/16/01
4 Assumes 6,800 heat rate; 10% return, 90% utilization; $500/kW capex; 20-year life, 38% tax rate; $8/kW/year fixed O&M; $1.03/MWh variable O&M
5 Fuel cost at volume weighted PG&E daily city gate average price of $2.62/MMBtu for 1999; Gas Daily
6 Includes $0.16/MWh NOx omission cost at 0.4 lbs/MWh on $0.4/lb. RTC credit/ CEMS and Cantor Fitzgerald
30.1
1999 average CalSO power price3
Full reinvest-ment costs4
$/MWh
Return on reinvestment
Fixed O&M
Variable O&M6
Fuel cost5
1999 CalPX price
$/MWh1
1999 gas price
$/MMBtu2
ESTIMATE
Notes: <number>
txho/10209 zxd414.ppt

## Slide 19: A FEW OBSERVATIONS
  Despite recent trade press reports to the contrary, the market was receiving clear indication by 1999 via price signals from the PX that new capacity was necessary
  In fact, full reinvestment economics for new CCGT construction had been fully met in 1999
  The increase in power price between 1999 and 2000 therefore cannot be attributed to the higher value of generation capacity (up to fuel reinvestment economics) but must instead be attributed to a number of market inefficiencies that led to the price fly-ups* beyond full investment costs
* The (arguably) slow response by generators to the market price signals in 1999 is a form of market inefficiency

## Slide 20: WE THEREFORE ESTIMATE THAT WHILE 35-45% OF THE PROBLEM WAS DUE TO VARIABLE COSTS, THE REMAINDER CAN BE ATTRIBUTED TO A VARIETY OF MARKET INEFFICIENCIES
* $8.2 billion incremental variable cost (40% of revenue increase) estimated as the difference between the 2000 and 1999 sums of variable cost x total CalSO load for all hours when CalSO price exceeds variable cost for a 10,000 heat rate gas plant (= 10,000 x California volume weighted average border daily gas price + 0.93 lb. NOx/MWh x monthly average NOx RTC price $/lb. + $1.03/MWh
** Full reinvestment economics
*** The difference in 2000 vs. 1999 CalSO total energy + ancillary services costs of $20.6 billion as reported in CalSO 1/16/01 market analysis report
Source: Platt’s Gas Daily; Cantor Fitzgerald; CalSO; RDI PowerDat; Team analysis
ESTIMATE
Variable cost*
Capacity value up to FRE**
Market
Inefficiencies beyond FRE**
Total***
2000 over 1999 annual CaISO generation revenues
Percent
We now turn
our attention to
the drivers and sources of market inefficiency
Notes: <number>
txho/10209 zxd414.ppt

## Slide 21: WHEN THE CALIFORNIA DEREGULATION DEBATE BEGAN IN 1994, THERE WAS CONSIDERABLY MORE SUPPLY (CAPACITY) THAN DEMAND
Gigawatts
* Firm transmission capacity contracted (net of export) forecast in 1993 for 1994: ES&D database; this compares to 9.5 GW and 15.2 GW available capacity for import in 1994 assuming minimum reserve margins in the WSCC ex-California of 15% and 7% respectively and assuming a coincident peak demand in California and the WSCC ex-California
** Actual summer peak capacity for CANV subregion (Nevada has no generation capacity within the CANV subregion); ES&D database
*** Actual peak day demand for California (includes: PG&E, SCE, SDG&E, LADWP, SMUD, Pasadena, IID): CaISO – “Historical Coincident Peak Demand and Operating Reserve Peak Demand . . .”, FERC form 861
Source: FERC; NERC ES&D database; CaISO; Team analysis
Nameplate summer capacity and net imports
Peak
demand***
Reserve
margin
Import capacity*
100% =
65
Internal capacity**
ESTIMATE
California reserve
margins were roughly
26% at the time the deregulation debate
began
Notes: <number>
txho/10209 zxd414.ppt

## Slide 22: . . . AND, OVER THE NEXT 6 YEARS, CAPACITY APPEARED TO BE MORE THAN SUFFICIENT
1994
Gigawatts
1 Firm transmission capacity contracted (net of export) forecast in 1993 for 1994 and 1999 for 2000 respectively: ES&D database
2 Actual summer peak capacity for CANV subregion (Nevada has no generation capacity within the CANV subregion); ES&D database
3 Actual peak day demand for California (includes: PG&E, SCE, SDG&E, LADWP, SMUD, Pasadena, IID): CaISO – “Historical Coincident Peak Demand and Operating Reserve Peak Demand . . .”, FERC form 861
4 Includes 1.7 GW of voluntary curtailments
5 Reserve margin = (capacity – peak demand)/capacity
Source: EIA; RDI PowerDat; CaISO; NERC; Team analysis
2000
1994
2000
1994
2000
Peak demand3
Peak day reserve margin5
Percent
2.0%
CAGR
. . . leaving California with significantly lower but still somewhat comfortable reserve margins
Capacity actually dropped . . .
. . . while peak-day demand grew . . .
Import capacity1
Internal capacity2
65
-1.1%
CAGR
61
Capacity
ESTIMATE
4
-12.1%
CAGR
Notes: <number>
txho/10209 zxd414.ppt

## Slide 23: HOWEVER, SEVERAL FACTORS LED TO THE COLLAPSE OF THIS RESERVE MARGIN 5 key reasons
  Lack of coordination among nuclear plant operators led to large scale coincidence planned outages in the September-October 2000 time frame
  At the same time, old gas fired generators began breaking down as a result of higher than average utilization during the summer of 2000
  California, indeed the entire WSCC, is highly sensitive to rainfall. As a result of low precipitation, hydro power output was down roughly 43% from 5,639 MW in August 1999 to 3,215 MW in August 2000
  Increased overall energy demand forced more rapid depletion of reservoirs leading to lower availability during off-peak hours
  Price differentials between California and neighboring states disincented generators, marketers and utilities from selling into the state
  Historically, generators could not produce past their allowed NOx credit limits. Almost 4 GW were taken offline in December 2000 despite very high prices because no credits were available to generators
  The CEC and other regulatory groups expected strong growth in demand as a result of strong economic growth on the west coast, yet nothing was done to bring on new supply
  The summer of 2000 proved to be extremely hot with June being the fourth-hottest month in 69 years; this drove air conditioning load and peak demand up significantly
Increased outages
Poor hydro year
Price caps
Inflexible NOx credit availability and pricing
Increased demand
Source: NERC; ISO
Notes: <number>
txho/10209 zxd414.ppt

## Slide 24: AS A RESULT, THE SUMMER OF 2000 SAW DANGEROUSLY LOW NET RESERVE MARGINS August 2000 California reserve margin
Gigawatts
* Estimated as sum of actual summer peak capacity for CANV subregion and firm transmission capacity contracted (net of export) forecast in 1999 for 2000; this compares to 5.7 GW and 12.4 GW available capacity for import in 2000 assuming minimum reserve margins in the WSCC ex-California of 15% and 7% respectively and assuming a coincident peak demand in California and the WSCC ex-California; assumes no planned or unplanned downtime; ES&D database
** Actual hourly average capacity out during August 2000 (3.4 GW unplanned, 0.7 GW planned); FERC
*** Average 2000 August total imports were 3.4 GW below 1999 levels; hydro/thermal split estimated assuming imports into NP15 are hydro, imports into SP15 are thermal; 2.7 total import reduction estimated as plug between supply, actual outages and actual available capacity
Source: CaISO; WSCC Summer 2000 Assessment; RDI PowerDat; FERC; Bonneville Power; Team analysis
Supply (capacity)*
Actual
outages**
Reduced thermal imports***
Actual available capacity
8/16/00 peak demand
Net
reserve margin
3.5%
Reduced hydro imports***
ESTIMATE
Voluntary curtailments
Notes: <number>
txho/10209 zxd414.ppt

## Slide 25: . . . AND, AS SUMMER TRANSITIONED TO WINTER, NEW ISSUES EMERGED December 2000 CaISO reserve margins
Gigawatts
1 NERC Winter 2000 Assessment of California available generation capacity including estimated net firm capacity sales and purchases.
2 Includes LADWP (5.8 MW, SMUD (0.2 GW), Pasadena Water (1.1 GW) & Imperial Irrigation (0.6 MW).
3 Roughly 11 GW total capacity offline at peak on 12/8/00 (FERC Staff Report on November & December 2000); 3,956 GW due to insufficient emissions credits according to AES, Duke and Reliant press releases during the week of 12/15/000.
4 Actual (12/8/00) peak imports below forecasted net imports from October 2000 WSCC Forecast for Winter Assessment in California.
5 Peak demand includes 1,704 MW interrupted load.
Source: Company press releases; CaISO; WSCC; NERC; FERC; RDI PowerDat; Team analysis
Supply (Capacity)1
Non CalSO capacity2
Outages3
Reduced imports4
Available capacity
Peak demand 12/8/005
Net
reserve margin
6.8%
ESTIMATE
Notes: <number>
txho/10209 zxd414.ppt

## Slide 26: A NUMBER OF OTHER POWER MARKET INEFFICIENCIES* FURTHER EXACERBATED THE SITUATION
* Either through price caps or long-term fixed price negotiated contracts
1. Limited supply response to higher prices
2. No demand response to higher prices
  California state and local regulations make it difficult and time consuming to permit and construct new plants. It takes at least 20 months to permit a new plant in California vs. 7 months for Texas on average
  The utilities were forced to purchase essentially all their power needs on an hourly basis through the PX. As a result, no forward market emerged, and potential generators who might have built plants had they been able to manage their risks by selling forward were unable to do so
  Frequent rule changes, an intrusive regulatory (and reregulatory) process, and a number of activist stakeholders made it difficult for potential investors in new generation plants to feel comfortable that they would receive a compensatory return on their investments.
  AB 1890 mandated fixed prices for most residential, commercial, and even industrial consumers. Despite skyrocketing wholesale energy prices, over 84% of residential and industrial/commercial customers continued to pay fixed prices.* As a result, there was very little demand response to the higher prices
EXAMPLES
Notes: <number>
txho/10209 zxd414.ppt

## Slide 27: A NUMBER OF OTHER POWER MARKET INEFFICIENCIES * FURTHER EXACERBATED THE SITUATION (CONTINUED)
* E.g., poor market design, regulation
3. Market design flaws*
Bidding optimization
Price cap distortions
  California officials and noted economists have pointed to market design flaws that they believe lead to the exercise of market power by marketers, generators and utilities
  Regulators made pricing data readily available, so bidding behavior and strategies of most players could be interpreted easily. Over time, and especially under tight supply/demand conditions, game-theoretic “optimal” solutions could be obtained through trial and error
  Government imposed price caps exacerbated market distortions in several ways
    IOUs, believing that they could capture lower prices in the CalPX day-ahead markets, began shifting the demand curve to the right until the MCP matched the $750 price cap
    Dropping the price cap from $750 to $500 actually increased generator margins
    Finally, the $250 price cap had the unintended consequence of driving sorely needed imports out of California
EXAMPLES
Notes: <number>
txho/10209 zxd414.ppt

## Slide 28: 1. LIMITED SUPPLY RESPONSE Anticipated new capacity never got built
Actual*
1995
forecast
* Beginning year actual capacity for entire State of California
** Estimates based on capacity growth rate forecasts for California/Mexico system (1992,1998) and California/Nevada/ Arizona system (1995) as defined by the WSCC and applied to California actual nameplate capacity
Source: ERA; RDI PowerData; NERC ES&D database; Team analysis
ESTIMATES
1992 forecast
1998 forecast
  Arduous permitting process with numerous stake holders takes twice as long as other U.S. locations
  High regulatory uncertainty
  No forward market to allow project sponsors to hedge price risks
“… projected reserve capacity is expected to be adequate throughout the WSCC region for the 2000 through 2009 10-year period. The assessment assumes that approximately 30,200 MW of new generation will be built when and where needed.”
– WSCC 10-year coordinated
plan summary 2000-09
October 2000
Gigawatts
California nameplate capacity
Notes: <number>
txho/10209 zxd414.ppt

## Slide 29: 2. NO DEMAND RESPONSE San Diego experience indicates that demand elasticity could have made a significant impact on reserve margins
* Beginning of stage 3 emergency due to 12 GW offline
** San Diego observed demand elasticity applied to all of California assuming retail prices like those seen in San Diego
*** Consumer response came 2 months after price increase
Source: The Sacramento Bee; CaISO; Team analysis
ILLUSTRATIVE
1999 Summer
2000 Summer
San Diego monthly residential bill (including wires)
$/month
San Diego electric usage***
Index
Reserve margin 12/08/00*
Demand response**
Estimated reserve margin with demand response
Hypothetical impact on reserve margins
Percent
-5%
1999 Summer
2000 Summer

## Slide 30: 3. MARKET DESIGN FLAWS Many academics and officials believe price increases were exacerbated by design flaws leading to an increase of market power*
Dollars per megawatt hour (peak)
* Market power is defined as the ability of companies to price above marginal cost without sales dropping to zero. Outside theoretical condition of perfect competition, all companies maintain some degree of market power
Source: CaISO Market Surveillance Committee Report June 2000; Joskow Report on Wholesale Electricity Markets Summer 2000; Platt’s Electric Power Daily, March 12, 1999
Electricity prices in real time energy market
Summer 2000
“Market design flaws have enhanced the ability of market participants to exercise market power in the real-time and ancillary service markets.”
– Frank Wolak, Professor of Economics, Stanford University
“Limits on formal contracting enhanced the ability of generation owners to exercise market power during high demand conditions”
– CaISO, Market Surveillance Report 2000
“After considering variable components there remains a resulting “price gap attributable to market power and related market power imperfections”
– Paul Joskow, Professor of Economics, MIT
“California’s new generation owners have exercised significant market power over the states ancillary services markets but have drawn only scant profits from their dominant position.”
–CalPx, March 1999
Summer 2000 price spikes drive CalSO board to request investigation into potential market abuses
May
June
July
August
September
Notes: <number>
txho/10209 zxd414.ppt

## Slide 31: 4. BIDDING OPTIMIZATION Generators and marketers moved capacity out of the CalPX day ahead market
* Bids plotted for 7/15/98 hour 17 (day ahead forecasted load 41,083 MW), 6/30/99 hour 17 (40,796 MW), 6/29/00 hour 14 (41,360 MW), and adjusted for monthly average outages. 7/98 – 1,804 MW, 6/30/99 – 2,398 MW, 6/29/00 – 4,037 MW; 6/29/00 also adjusted for 3,400 MW reduced hydro and thermal imports over 1999 levels. Outages and imports added back into total capacity bid at a price of 0 (shifting entire curve to right)
** Delayed 90 days starting October 2000
*** Registered CalSO participants only
Source: Electric Power Daily; CalSO; WSCC; CalPX; FERC, RDI PowerDat; Team analysis
CalPX supply bids adjusted for outages and import reductions*
$/MWh CaISO bid
MW capacity CalPX bid
June 29, 2000
Hour 14
June 30, 1999
Hour 17
July 15, 1998
Hour 17
EXAMPLE
  The generators learned to optimize bidding strategy as the market clearing price settlement process was repeated several times each day, 365 days per year
  Suppliers moved capacity out of the CalPX day-ahead market into real time energy and export markets where higher prices were achieved
Notes: <number>
txho/10209 zxd414.ppt

## Slide 32: MULTIPLE MARKETS IN OPERATION SIMULTANEOUSLY CREATED MANY ARBITRAGE OPPORTUNITIES FOR GENERATORS Markets trading in advance of delivery in Hour H in California
Source: California Power Exchange
Before H-18 to H-40 (day-ahead window)
Day-ahead energy market
D
S
Bilateral energy market
D
S
Long-term
D
S
Standard (7x24, 6x18)
D
S
Custom or APX
Bilateral services market
D
S
Black start
D
S
Reactive power
Day-ahead adjustment and congestion pricing market
D
S
Zone 1
D
S
Zone 2
D
S
Transmission
H-2
H-1
Hour H
Interscheduling coordinator adjustment energy market
D
S
Day-ahead ancillary services market
D
S
Spinning
D
S
Non-
spinning
D
S
Regulation
D
S
Replace-ment
Day-of energy market
D
S
Day-of adjustment and congestion pricing market
D
S
D
S
D
S
Real-time imbalance energy market
D
S
Day-of ancillary services market
D
S
D
S
D
S
D
S
Each megawatt-hour delivered in Hour H has been sold in 1 and only 1 of these markets
Day-ahead ancillary services market
D
S
Spinning
D
S
Non-
spinning
D
S
Regulation
D
S
Replace-ment
. . . but it may have made multiple trips “in and out” before physical delivery
Notes: <number>
txho/10209 zxd414.ppt

## Slide 33: 5. PRICE CAP DISTORTIONS Price caps further distorted market price signals June through December 2000 CalPX prices
* Maximum hourly price for daily peak (7 a.m.-10 p.m.) and off peak (11 p.m.-6 a.m.) time periods
Source: Cantor Fitzgerald; RDI Basecase; California Power Exchange; Team Analysis
Maximum peak*
Maximum off peak*
$750 price cap through 7/1
$500 price cap 7/1-8/7
$250 price cap 8/7-12/15
Price cap lifted 12/9
Dollars per megawatt
Price cap
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Notes: <number>
txho/10209 zxd414.ppt

## Slide 34: IOUs ALTERED DEMAND BIDDING STRATEGIES TO FORCE VOLUMES INTO LOWER PRICED CalPX DAY-AHEAD MARKETS
Dollars per megawatt-hour
Note: CalSO forecast loads were 44.8, 46.8, and 42.3 GW for June 13, 14, and 28, 2000 respectively
Source: CaISO; CalPX
June 13
June 14
June 28
Aggregate CalPX Summer 2000 day-ahead market demand and supply curves
15
20
25
30
35
40
45
50
Capacity bid, gigawatts
Aggregate demand bids for Hour 16 on given date
Aggregate supply bids for Hour 16 on given date
    The $750 price cap in the CalSO real-time market during June 2000 did not exist in the CalPX day ahead market
    IOUs sought to purchase more of their load in the CalPX day-ahead market in order to avoid higher prices in the day-of and real time markets and potential under-scheduling penalties from the ISO
    A dramatic demand curve shift up and to the right resulted
Notes: <number>
txho/10209 zxd414.ppt

## Slide 35: MOREOVER, THE $500 PRICE CAP ACTUALLY INCREASED AVERAGE MARGINS TO GENERATORS
* Generator margin calculated for a 10,000 Btu/kWh gas turbine using daily spot CA border gas prices, monthly NOx emission credit charges and average variable O&M charges and averaged for all hours when a given capacity utilization occurred over the $750 (6/1/00-7/1/00) and $500 (7/1/00-8/7/00) price cap periods respectively
** Capacity utilization calculated using CaISO load / (max supply bid during week in PX + max real time imports into CaISO during week.); capacity utilization over 100% spill over into CalSO real-time markets from CalPX day-ahead market
Source: CaISO; California Power Exchange; Cantor Fitzgerald; Team analysis
Generators see
improved margins
Average peak generator margin during Summer 2000 periods of $750 and $500 price caps *
$/MWh
  Average peak hour margins increased by 11% under the $500 cap vs. those under the $750 cap
  At loads of 37 GW to 42 GW, average generator margins rose 36%
$500 cap
$750 cap
Capacity utilization
Percent**
(July 1 to August 7, 2000)
(June 1 to July 1, 2000)
Notes: <number>
txho/10209 zxd414.ppt

## Slide 36: ON THE OTHER HAND, THE $250 PRICE CAP REDUCED PEAK PRICES AND MARGINS BUT ALSO DROVE IMPORTS AWAY
$750
cap
Source: RDI Basecase; California Power Exchange; California ISO; Megawatt Daily; Team Analysis
$500
cap
$250
cap
$750
cap
$500
cap
$250
cap
Total
@ >85% capacity
utilization
Average peak margin
$/MWh
California border to CalPX differential
$/MWh Peak-hour Differential 8/7/00 to 8/31/00
Palo
Verde
Mead
Nevada
Four
Corners
Average peak hour net imports to California
MW
$750 cap
$500 cap
$250 cap
4,744 MW average imports
3,736 MW average
imports
2,340 MW average imports
Notes: <number>
txho/10209 zxd414.ppt

## Slide 37: IN SUMMARY, THE CALIFORNIA “CRISIS” IS REALLY COMPRISED OF 2 MAIN PROBLEMS 2000 over 1999 annual CaISO generation revenues Percent
1 $8.2 billion incremental variable cost (40% of revenue increase) estimated as the difference between the 2000 and 1999 sums of variable cost x total CalSO load for all hours when CalSO price exceeds variable cost for a 10,000 heat rate gas plant (= 10,000 x California volume weighted average border daily gas price + 0.93 lb. NOx/MWh x monthly average NOx RTC price $/lb. + $1.03/MWh
2 Full reinvestment economics
3 Estimated as difference between total increases in wholesale revenue and the sum of available cost and capacity value increases
4 The difference in 2000 vs. 1999 CalSO total energy + ancillary services costs of $20.6 billion as reported in CalSO 1/16/01 market analysis report
ESTIMATE
Variable cost1
Capacity value up to FRE2
Market
Inefficiencies3 beyond FRE2
Total4
Many “solutions” currently under
debate fail to
address the full
range of problems – from gas to the
market
inefficiencies
that exist
Notes: <number>
txho/10209 zxd414.ppt

## Slide 38: THE CURRENT CRISIS
Why power prices rose dramatically
Why the electric utilities are posed on the edge of bankruptcy
  What are the key drivers of high prices and price volatility?
  Why, specifically, did the IOUs bear much of the financial burden?
Two related, but very much separate, issues
Notes: <number>
txho/10209 zxd414.ppt

## Slide 39: WHY THE ELECTRIC UTILITIES WERE FORCED CLOSE TO THE EDGE OF BANKRUPTCY 3 key reasons
  The IOUs struck a regulatory deal that allowed them to recover their stranded costs at the risk that unregulated wholesale prices might rise above the fixed prices they had agreed to provide their customers
  As early as August 2000, SoCal Edison sought to exercise its option to forgo additional collection of CTC monies in order to escape the fixed retail price regime. The CPUC compelled Edison to continue the price freeze
  The utilities remained optimistic that they could come to a solution in early 2001 by the means they know best: legal and regulatory, while neglecting forward contracting solutions
  The senior management of the California IOUs came predominately from legal/regulatory backgrounds. The “solution” they negotiated solved a problem they understood (the stranded investment) at a cost/risk they did not understand
  Until December 2000, the IOUs were prohibited from participating in bilaterals or using certain price risk management tools to help hedge their risk exposure. Some utilities were able to mitigate a limited portion of their fuel-related risks but, overall, the design of the pool left the utilities completely exposed
  When forced to sell some of their generation plant, the utilities chose to sell those assets (i.e., gas fired) that were essentially setting price much, if not all, of the time. Furthermore, these assets were sold in blocks to relatively few players, leaving the IOUs painfully exposed to potential market manipulations. Rather than sell the (mandated) 50% of gas assets, the utilities chose to sell them all
Overly focused on regulatory solution – miscalculated regulatory exposure
Poor understanding/ appreciation of market risks
Lack of micro-economic foundation for asset decisions
Notes: <number>
txho/10209 zxd414.ppt

## Slide 40: THE KEY CHALLENGE FACING MANY UTILITY MANAGEMENT TEAMS The (de)regulatory trade-off
Many utility management teams may be more willing to trade off what they know and understand – stranded costs – for risks they cannot or do not fully understand and value
Stranded costs/
CTC recovery, other potential benefits
Potential
settlement
risks

## Slide 41: TODAY’S DISCUSSION
  Background – from deregulation to default
  The current crisis
    Why power prices rose dramatically
    Why the electric utilities are poised on the edge of bankruptcy
  Lessons learned and key takeaways
  Appendices
    A: California deregulation basics
    B: The impact of natural gas costs on the California market
    C: Estimating the impact of demand elasticity
    D: Supply and demand estimates and drivers
    E: Market behavior observations
    F: NOx credits in California
    G: Back-up
    H: Glossary
Notes: <number>
txho/10209 zxd414.ppt

## Slide 42: OUR KEY LESSONS LEARNED FALL INTO 3 MAJOR CATEGORIES
High-level observations
Broad observations on what appears to work – and not work – in electric power deregulation
Wholesale market rules and structure
First thoughts on wholesales rules and structure improvements
“Do’s” and “Don’ts” for IOUs
Deregulation from the point of view of the IOUs
Notes: <number>
txho/10209 zxd414.ppt

## Slide 43: DON’T ANALYZE USING AVERAGES
While on average these
2 market participants are doing fine, neither is particularly comfortable

## Slide 44: A NUMBER OF STOCHASTIC VARIABLES MAKE AVERAGES MEANINGLESS
ILLUSTRATIVE
Uncertainties
  Plant availability
  Hydro availability
  Weather (demand)
Description
  Planned downtime (such as nuclear unit turnaround and refueling) can take significant capacity offline for an uncertain length of time
  Forced outages such as plant breakdowns vary by plant type, utilization and age
    Number of occurrences
    Duration of occurrences
    Timing of occurrences
  Precipitation fluctuations have significant impact on available hydro capacity in the Pacific Northwest and California
  Uncertain temperature variation directly drives peak loads
Each variable alone is not likely to create a crisis situation, but simultaneous occurrences of extreme conditions in two or more variables can be catastrophic

## Slide 45: AS A RESULT, THE RESERVE MARGIN NEEDS TO BE VIEWED AS A DYNAMIC VARIABLE Modeled 2000 WSCC reserve margin and range of uncertainty*
Percent
Mean, +1/-1sd
+95%, -5%
ESTIMATE
* Based on Monte Carlo simulation of the following stochastic inputs: planned and forced outages, and hydro peak capacity on the supply side and peak demand as a function of HDD and CDD; hydro capacity assumed to be 80% peaking with a peak to average monthly capacity ratio of 2:1
Source: NERC (WSCC summer and winter plant capacity by GADS type); GADS database (1991-98 annual planned outage hours and forced outage hours and number of occurrences by GADS type); RDS PowerDat (1970-2000 monthly WSCC hydro energy output); National Oceanic and Atmospheric Administration National Weather Service Climate Analysis Center (1931-99 population-weighted monthly HDD and CDD data for the WSCC); RDI PowerDat (1988-99 monthly WSCC peak demand); Team analysis
Notes: <number>
txho/10209 zxd414.ppt

## Slide 46: FOR ANY GIVEN AUGUST, ONE WOULD EXPECT ABOUT A 5% CHANCE FOR A PEAK RESERVE MARGIN OF LESS THAN 2.5% IN THE WSCC Distribution for reserve margin*, August
90%
5%
Reserve margin, percent
-15
-5
5
15
25
Frequency
Mean = 13%
5%
* Based on Monte Carlo simulation of the following stochastic inputs: planned and forced outages, and hydro peak capacity on the supply side and peak demand as a function of HDD and CDD; hydro capacity assumed to be 80% peaking with a peak to average monthly capacity ratio of 2:1
Source: NERC (WSCC summer and winter plant capacity by GADS type); GADS database (1991-98 annual planned outage hours and forced outage hours and number of occurrences by GADS type); RDI PowerDat (1970-2000 monthly WSCC hydro energy output); National Oceanic and Atmospheric Administration National Weather Service Climate Analysis Center (1931-99 population-weighted monthly HDD and CDD data for the WSCC); RDI PowerDat (1988-99 monthly WSCC peak demand); Team analysis
ESTIMATE
Notes: <number>
txho/10209 zxd414.ppt

## Slide 47: FOR CALIFORNIA, THE LIKELIHOOD OF DANGEROUSLY LOW RESERVE MARGINS ARE EVEN HIGHER
We have changed from a regulatory process of setting reserve margin targets to a stochastic process of trying to dynamically measure the margin
Issue
  Current analysis is done at the WSCC level
  Conservative estimates of plant outages based on U.S. averages
  Hydro Peaking capacity assumptions are optimistic
  Correlation among variables
Impact to California
  Transmission constraints between sub-regions likely increase volatility of reserve margins
  Power price basis differentials driven by regional weather variation, transmission constraints and regulatory based wholesale pricing (price caps) magnify the volatility observed at the WSCC level
  California gas fired steam turbines are old and subject to failure more often than U.S. averages suggest
  Nuclear plant availability should be modeled using specific plant refueling schedules and historical unplanned outages
  Better data on run of river vs. peaking capacity and the ratio of peak to average will likely result in a deterioration of reserve margins
  Positively correlated variables lead to increased variance: higher loads lead to longer running times and more plant outages, for example

## Slide 48: THIS LEADS TO AN INTERESTING QUESTION: WHO GUARANTEES – AND PAYS FOR – RELIABILITY IN A DEREGULATED WORLD?
In one in every 10 or 20 years, a confluence of events will lead to very tight supply/demand conditions and resulting price spikes. Who will guarantee that sufficient capacity exists at each stage of the value chain for potentially anomalous events?
Gas deliverability
Gas transportation
Power plants

## Slide 49: GUARANTEEING – AND PAYING FOR – RELIABILITY The 2 competing schools of thought
Quasi deregulation:
Indirectly mandate reserve margins
  Force 2-part pricing mechanisms (e.g., separate capacity and energy markets like PJM)
  Force retail aggregators to contract for more supply than they have demand
  Provide the ISO the ability to contract for sufficient supplies to maintain system security and pass costs on average to all market players
Deregulation:
Allow the market to price and value, reliability
  Establish both bilateral as well as forward markets
  Allow industry to develop – and price – product/service suites with different levels of price and reliability certainty
  Use insurance industry to price risks (e.g., business interruption) related to weather, unit-contingent operations, etc.
There is considerable debate in the market as to which method is more efficient/effective. The demand for market-based offerings that price reliability will grow dramatically
Notes: <number>
txho/10209 zxd414.ppt

## Slide 50: KEY LESSONS LEARNED: SOME OTHER HIGH-LEVEL OBSERVATIONS
Partial deregulation is an economic oxymoron
Deregulation works better when (surprise!) supply is much greater than demand
“Too many cooks spoil the broth”
Regulators should get real jobs
  The California market never truly deregulated. The need to satisfy numerous stakeholders led to a hybrid model that failed to provide true economic price signals to either end users or generators. Partial deregulation yields significant risk and fails to provide for the traditional advantages deregulation typically brings
  One could argue that California had many of the right ideas, but that the process took much too long. The settlement took too long to negotiate, too long to implement, and required too long a period of time for recovery of stranded costs. During those years the S/D gap narrowed quickly to unsustainable levels
  The “deregulation” process in California directly involved too many stakeholders and the emerging rules were so complex that smart generators could find a way to arbitrage market inefficiencies. One PhD economist, left alone in a room for a week, could have designed a better system than California settled on
  Regulators regulate. After “deregulation” in California – even after the IOUs sold much of their generation – CPUC and other regulators continued to modify the process and rules. The regulators slowly reregulated the industry with a set of increasingly convoluted and confusing rules. The resulting regulatory uncertainty made it difficult for generators to understand the potential attractiveness of investing in California. The regulatory and political risk in California was – and still is – higher than the regulatory and political risk in Indonesia
Notes: <number>
txho/10209 zxd414.ppt

## Slide 51: KEY LESSONS LEARNED: SOME OTHER HIGH-LEVEL OBSERVATIONS (CONTINUED)
Economists are often better on theory than they are in real markets
Caveat emptor, or “there is no such thing as a free lunch”
Suppliers and buyers need to see real price signals
  The broad intent of California deregulation was clear: establish a system in which excess supply competed for state load in such a way that market prices fell to the variable operating cost of the marginal producer. P = MC and the California resident benefits. But, in the real world, P  MC – one does not, after all, typically buy houses, cars, or refrigerators based on marginal costs. And, when supply and demand converge, price fly-ups occur (see ethylene, methanol, etc.)
  It was always disingenuous to believe that prices would fall to the variable operating cost of the marginal producers yet be high enough to incent investment in generation plants. The market design was not inherently flawed as much as it was designed to be inherently volatile. More astute market players saw the volatility play early and invested in then “out of favor” gas-fired peaking units in 1997-98
  Most of the end-use market in California was insulated from real market prices and, as a result, demand was broadly unaffected by skyrocketing wholesale prices. Similarly, generators saw high and volatile spot prices but no clear long-term price signal to help end-use investment
    End-users need to see (and pay) real market prices
    Bilateral and forward markets are needed to help all parties better manage risk and provide for more stable investment price signals
Notes: <number>
txho/10209 zxd414.ppt

## Slide 52: KEY LESSONS LEARNED: FIRST THOUGHTS ON WHOLESALE MARKET RULES AND STRUCTURE
Allow forward contracting
Price caps often create more problems than benefits
Allow retail rates to “float” as CTC is recovered
Pay attention to fuel mix of supply
Market concentration can occur even in “fragmented” markets
  Forward contracts allow prospective generators to lock in prices on new construction
  In the short term, price caps may exacerbate market distortions; in the long term, they dis-incent the construction of new capacity
  Without retail competition, fixed retail prices were employed to limit market power of local distributors.
  Fixed retail prices eliminated demand elasticity and facilitated profit maximizing supply bidding strategies
  Retail prices that float with fuel costs would have partially mitigated this issue
  Over-dependence on uncertain hydro capacity and gas capacity subject to potential fuel supply tightness can lead to market instability
  Concentration of supply at the margin is what matters, not the overall market fragmentation. As a result, traditional measures of market concentration such as the HH index are ineffective
  Separate micro markets further the potential for concentration
  Ability of marketers to aggregate supply can even further concentrate the market
Notes: <number>
txho/10209 zxd414.ppt

## Slide 53: KEY LESSONS LEARNED: FIRST THOUGHTS ON WHOLESALE MARKET RULES AND STRUCTURE (CONTINUED)
Ensure that interconnected grid has common rules
Imports and exports of electricity of a large sub region should be balanced
Market participants must be credit worthy
There is no need for separate ancillary services markets
It is not just power, but gas too
  Rules applied in one sub region can be easily avoided by shipping power to another nearby sub region
  Rules should allow for full and open access to transmission across the entire grid (FERC Order 2000: RTO should be enforced)
  Transporting fuel is cheaper than electricity (hydro and lignite only exceptions)
  The transport of large bulks of electricity can create instabilities and requires significant transmission investment
  The transmission grid requires long planning cycles
  Bank style capital regulation is required to avoid negative short term effects on reliability of supply
  Too many markets in California allowed generators to game and otherwise arbitrage real-time differences among them
  Natural gas supply is the truly pervasive problem in California . . . and it is getting too little attention
Notes: <number>
txho/10209 zxd414.ppt

## Slide 54: KEY LESSONS LEARNED: “DO’S AND DON’TS” FOR IOUs
“Deregulation” is just the origination of a complex risk position
As such, the key parameters around deregulation are best developed not by in-house legal or regulatory groups, but by the origination/ trading/ commercial engine within the company
For most utilities, deregulation poses as much downside risk as upside potential
Yet most utilities are poorly positioned to develop a winning deregulation strategy
  It is interesting how much time, money, and attention IOUs around the world will spend on measuring and managing the risks around their trading positions. Yet very large risk positions can be developed via deregulation, M&A, or origination that are rarely fully evaluated, quantified, or even understood. The California utilities did not understand the risks associated with their positions
  What deal is best for the IOU should be the purview of a commercial group. How the deal can be best achieved should be the purview of legal/regulatory groups. Regulators should execute, not transact
  Despite the California debacle, well-structured “deregulation” can be highly value creating. The key is to know the potential value and risk associated with each potential outcome
  Legal, regulatory, and other corporate center functions drive too much of the typical deregulation negotiation strategy, and process
Notes: <number>
txho/10209 zxd414.ppt

## Slide 55: TODAY’S DISCUSSION
  Background – from deregulation to default
  The current crisis
    Why power prices rose dramatically
    Why the electric utilities are poised on the edge of bankruptcy
  Lessons learned and key takeaways
  Appendices
    A: California deregulation basics
    B: The impact of natural gas costs on the California market
    C: Estimating the impact of demand elasticity
    D: Supply and demand estimates and drivers
    E: Market behavior observations
    F: NOx credits in California
    G: Back-up
    H: Glossary
Notes: <number>
txho/10209 zxd414.ppt