## Slide 1: General Trends and Summary
New gas generation is presently increasing faster than supply.
However a slowing economy and less rapid demand in the industrial and commercial sectors will allow gas storage to return to normal levels by the fall.
Greater than 50,000MW new gas gen in 2001- coal approx 500MW.
Greater than 70,000 MW new gas gen in 2001- coal greater than 500MW.
Interest in Coal is increasing due to economics, this will require gas to stay above >$3.50 to be economical.
Interest in LNG is increasing due to economics, this will require gas to stay above >$4.50 to be economical.
New coal plants will require base load to be economical.
New coal plant issues are sitting, larger capital and longer lead time to build.
Gas transportation bottlenecks will make LNG viable were transportation problems are encountered (coastal areas).
Electricity transportation problems will make coal plants at existing sites marginal due transmission loading relief due to bottlenecks.

## Slide 2: Eastern Interconnect Grid Overview
Consists of the following NERC regions:
  NEPOOL
  NYPP
  PJM
  ECAR
  MAIN
Approximately 600,000 MW of installed capacity
  44% coal
  29% gas
  14% nuclear
Distinct summer and winter daily load profile
  Graphical description to come for each NERC region
The majority of maintenance outages occur in the spring and fall
Capacity margin for 2001 is approximately 13%
  Capacity margin is defined as the excess installed capacity over peak load (considered reserve)
    MAPP
    SPP
    FRCC
    SERC

## Slide 3: Eastern Interconnect Fuel Consumption and New Generation

## Slide 4
New Gas Generation

## Slide 5: Eastern Interconnect & Ercot New Gas Generation vs Installed Coal Gen
2001
2002
Total Capacity
Coal
% Coal
NORTHEAST
NE ISO
5,713
8,654
26,169
2,633
10%
NYPP
440
5,639
34,663
3,812
11%
PJM
2,925
7,339
59,863
20,813
35%
TOTAL
9,078
21,632
120,695
27,258
23%
MIDWEST
ECAR
7,441
11,330
110,798
83,118
75%
MAIN
7,468
3,728
55,167
26,946
49%
MAPP
944
1,271
33,116
20,124
61%
TOTAL
15,853
16,329
199,081
130,188
65%
SOUTHEAST
FRCC
1,570
5,597
39,028
10,408
27%
SERC
7,024
6,958
SOCO
4,518
3,358
43,842
25,044
57%
TVA
680
1,460
31,222
15,390
49%
VACAR
1,826
2,140
56,758
13,208
23%
SPP
4,907
10,518
71,243
26,600
37%
TOTAL
13,501
23,073
242,093
90,650
37%
EIC Total
48,590
66,264
561,869
263,542
46%
ERCOT
10,158
5,230
65,875
15,446
23%
NEW GAS GEN
Installed Through 2000

## Slide 6: Fuel Consumption

## Slide 7: Forward Power Production
Note Decreasing Heat Rates Over Time

## Slide 8: Hub Specific Trading Information

## Slide 9: Forward Power Prices (5X16)

## Slide 10: Cinergy Monthly Price (Megawatt Daily)
Note absence of price spikes in summer 2000 and increasing Q4 2000 prices

## Slide 11: Coal Information

## Slide 12: Background Information
The production cost difference between two different generation sources is $13/Mw-hr
VOM = variable operation and maintenance costs

## Slide 13: CCPP-Coal Generation Cost Spread
Current long-term curves show greatest generation cost spread in recent history
FRCC is particularly gas overpriced
WSCC is gas overpriced due to delivery constraints
CCPP = Combine Cycle Power Plant

## Slide 14: Background – New Generation
As new capacity enters service, supply constraints will diminish
Power “peaks” will flatten
Price of power will now be driven more by underlying commodity
Result: Except in WSCC, dampened “spikes” with highly coupled power and fuel prices

## Slide 15: Coal Background
Generation Production Costs
(Fuel + VOM)
Eastern Interconnect Generation Mix
If gas price drops below $2.50/MMBtu delivered, the coal and CCPP stacks begin to “flip”
Announced or newly completed plants
  NatGas = 300,000 Mw
  Coal = Negligible
The gas portion of the power stack is increasing, while the coal portion is shrinking
Result: Higher “floor” prices for power

## Slide 16: Coal Emissions Background
Emissions of New Coal Plants
Coal is getting cleaner
Clean-up techniques are getting better and more cost effective
New technologies (IGCC) are reducing emissions even further

## Slide 17: Opportunity - - Asset Play Economics
Assumptions
$1200/Kw Coal construction costs
$650/Kw CCPP (gas) construction costs
30% Equity @15%
70% Debt @9%
90% Capacity Factor
1000 Mw plant
Heat Rates
  IGCC = 8200 Btu/Kw-hr
  CFB = 9500 Btu/Kw-hr
  CCPP = 6800 Btu/Kw-hr
Power Curves
  FRCC (ICF)
  FRCC (Desk)
  ERCOT (Desk)
  WSCC (Desk)
Results

## Slide 18: Technology Comparison - IGCC
Pros
Integrated Gasification Combined Cycle Basically a coal gasifier connected to a regular combined cycle plant
Uses well known power island technology gas turbines
Has very low emissions easier to permit in “difficult” states
Provides fuel optionality can easily shift between NatGas and Coal gas
Overall higher capacity factor potential
Potential shorter construction schedule
Improved heat rate (~8200)
Potential staggered approach (SS/CC/IG)
Potential bi-product revenue streams (Argon, CO2, etc)
Can be modularized would provide a staggered COD schedule (250Mw year 1, 500 Mw year 2, etc)
Potential “clean coal” money
Cons
Potential first year low coal capacity factor
Newer, less-proven technology
Potential higher capital costs
Potential higher VOM costs

## Slide 19: Technology Comparison - CFB
Pros
Potential lower capital costs than IGCC
Circulating Fluidized Bed
Potential lower VOM costs
Can use a variety of coals including very low quality “waste coal” - - allows significant coal delivery cost reductions
Less complicated technology than IGCC
Lower emissions than older technology “pulverized coal”
Can be modularized - - installed in blocks of 100Mw - 250Mw
Potential “clean coal” money
Cons
No fuel optionality - - designed for coal only
Higher capacity factor while on coal
No byproduct revenue streams
Potential longer construction schedule

## Slide 20: NERC Region Profiles Eastern Interconnect and Ercot

## Slide 21
EASTERN INTERCONNECT

## Slide 22
NEPOOL

## Slide 23
PJM

## Slide 24
NYPP

## Slide 25
ECAR

## Slide 26
MAIN

## Slide 27
MAPP

## Slide 28
SERC-TVA

## Slide 29
SERC-VACAR

## Slide 30
SERC- SOCO

## Slide 31
SERC

## Slide 32
SPP

## Slide 33
FRCC

## Slide 34
ERCOT