## Slide 1: AAA POWER INC.
NEAR ZERO EMISSIONS
GREEN POWER
Notes: jjj

## Slide 2: Technology
Breakthrough for Sulfur Recovery
Patented Technology
Zero Emission Technology
World Wide Market
Significant capital and operating costs savings

## Slide 3: Description
Process for Zero Emission Recovery of Sulfur from Acid Gases.
A new chemical process for converting hydrogen sulfide (H2S) to elemental sulfur.
The atmospheric emissions of sulfur-containing compounds are effectively zero for this new recovery process.
“The University of California Sulfur Recovery Process: A New Approach”, for presentation at Sulfur 2001, 5 November – 8 November 2001, Amsterdam, The Netherlands (with Michael Quinlan & Daniel Velasquez, Kellogg Brown & Root, Inc. and Dennis Leppin, gas Research Institute).

## Slide 4: Market Trend – Business Drivers
Sulfur/H2S levels in natural gas and other fossil fuels have been steadily rising as shallow/sweet reservoirs are depleted and newer/deeper reserves are developed;
Energy demand for natural gas and other fossil fuels is rising to unprecedented levels; most of the 350 proposed power plants being built in the U.S. are fueled by natural gas;
There is a world wide trend, led by the U.S. Environmental Protection Agency’s Tier II automotive regulations, to reduce the sulfur levels in gasoline and diesel fuels.

## Slide 5: Sulfur in Alberta –Western Canada
Over 25,000 metrics tones per year of sulfur dioxide (SO2) is released into the atmosphere annually from flare gas derived from gas plants and gas wells.
Over 16,000 new wells will be drilled in Alberta in 2001 of which 70% will be natural gas wells.
All gas wells have H2S is some degree of concentration.
Reportedly over 1,000 new wells will have H2S concentrations between 100 ppm and 300,000 ppm.
By 2005 15% to 20% of all gas wells, ( + 4,000 wells ) should fall in the range between 15% or 150,000 ppm to 20% or 200,000 ppm.
All gas has to meet pipeline grade of below 30 ppm of H2S.
H2S over 100 ppm causes death.

## Slide 6: Sulfur in Alberta –Western Canada
Alberta’s 35 Grand-fathered Gas Plants which are in a 2 - 3 year grace period must now conform to the new regulations for sulfur emissions.

## Slide 7: Technology - Advantages
The process is a net exporter of energy in the form of steam at 150 to 200 psia or higher.
SO2 reacts to extinction in the presence of excess H2S; under the stipulated processing conditions there is no equilibrium limitation. The resulting sulfur forms a second liquid phase.
Molten sulfur, of marketable quality, is produced directly from the reaction. In contrast to aqueous redox systems (such as LoCat, Stretford or Sulferox), make-up chemicals are required only to offset mechanical losses such as evaporation or entrainment.
The process will produce a tail gas that meets air-quality standards < 4 ppm. In addition the process can be designed to tolerate a large amount of CO2 as well as COS, mercaptans, hydrocarbons, etc. Only ammonia would require prior removal.
The process is economical for sulfur duties as low as one tones per day; there is no upper limit to the capacity.
The process configuration can be varied depending on the gas to be treated. For example, to treat sour natural gas at pipeline pressure, one would only add a high-pressure absorber to the list of equipment above; the gas would be dried as well as sweetened.
Carbon steel can be used for most of the equipment; the possible exceptions are the re-boilers for the primary stripper and the sour-water stripper.

## Slide 8: Development Team
Developed by Scientists at the University of California, Berkeley
Pre-engineered by Kellogg Brown & Root, Inc.
Collaborated on by the Gas Technology Institute, USA.
Alberta Research Council

## Slide 9: Market
Any high or low pressure gas stream containing from 1 ton of sulfur per day (LTPD) with no upper limit
Large size Market ( greater than ~ 25 LTPD), amine/Claus or amine/Claus/TGT, well proven
Medium size (~0.2 to 25 LTPD), aqueous-iron ‘liquid redox’ appears least expensive on paper ( reputation of unreliability, high costs have limited applications.)
Small Size ( less than ~0.2 LTPD) H2S scavengers least expensive option well proven.


## Slide 10: Market
Direct Treat ­ - (1.0 – 25 LTPD, 25 > LTPD) applications where H2S is removed from sour gas streams (e.g. high-pressure sour natural gas, miscellaneous oil and gas industry sour gas streams, geothermal vent gas streams, other streams that fall in the traditional liquid redox market, other streams that fall in the traditional amine process plant with acid-gas injection).
HDS Recycle – (1.0 – 25 LTPD, 25 > LTPD) applications where H2S is removed from the hydrogen recycle stream of a hydrotreater (hydrodesulfurization units). This segment is treated separately from the direct treat segment listed above for several reasons. The sizes of the applications are generally larger (the average HDS recycle application 2-3 times than the average direct treat application) and the applications have other unique differences such as the desire to selectively remove hydrocarbons and ammonia from the recycle stream.
Clause Tail Gas – large-sized (greater than 25 LTPD) applications where the modified Claus process is used as the primary sulfur recovery unit and where a separate tail gas treating process is required. The tail gas exiting the Claus plant contains 2,000 to 6,000 ppm of untreated H2S and SO2 and must be treated in a tail gas unit. The tail gas unit is about expensive as the Claus plant, uses a substantial amount of energy and does not completely eliminate sulfur emissions. The UCSRP replaces the Claus plant and the associated tail-gas unit. Capital costs are estimated to be about 60.0% and operating costs about 68.0% of those for a three-stage Claus plant plus a Shell Claus Off-gas Treatment (SCOT) unit. The atmospheric emissions of sulfur-containing compounds are effectively zero for the UCSRP.

## Slide 11: Market – Power Generation
California is in short supply of power.
AAA has the environmental solution for cleaning sour gas to generate green power.
A strategic alliance with a power company to secure either direct gas or tail gas by third party financing offers major potential for the company.

## Slide 12: Schedule
<number>
<footer>
09/27/25
Milestones
Jul
01
Aug
Sep
Oct
Nov
Dec
Jan
Feb
Mar
Apr
May
02
Phase 1
Phase 2
Phase 3

## Slide 13
Sales Projections – Over Ten Years
 Direct Treat ­ 80 Sales
HDS Recycle – 29 Sales
Claus Plant /TGT - 100 Sales
Total Plants 209 Sales
Five Years Analysis
Annual Revenue $163,000,000 USD
Pre-tax Earnings $40,000,000
Share Price $ 40.00

## Slide 14: Current Status
Phase I – Go Public CDNX
Secure Equity Financing Commitment for $3million
  Plant hard costs - $ 1 million
  Soft costs engineering design - $ 1 million
  Working capital, marketing - $ 1 million
Start plant engineering & design - $ 500 k
Phase II
Working capital required. $500 k
Phase III
Start- plant construction $ 2 million
Phase IV – April 2002 to Oct 2002
Structure IPO for NASDAQ $10 Million to $30 Million.

## Slide 15: Other Sources of Financing Available
Potential 50% funding capital costs from Canadian Environmental Technical Advancement Corporation (CETACT)
Contribution from a major gas producer and or an energy company.
Alberta Research Council for Commercializing transfer technology.
Major IPO through A.G. Edwards in the U.S.

## Slide 16: Related Documents
Business Plan
Presented by:
Jeremy P. White
President / CEO
1-403-241-1756

## Slide 17: Vision Statement
AAA POWER’s mission statement is as follows:
AAA POWER INC. will acquire, develop, and commercialize environmental technology to reduce costs, enhance operating reliability, and generate zero emissions from sour gas in the energy sector worldwide.
The vision for the company in the year 2010 is given below:
AAA POWER INC. is the largest provider worldwide of green power, which is generated from sour gas using its patented UCSRP technology. AAA POWER INC. is a leading provider of emissions control technology for the energy sector worldwide.
Jointly, these two statements clearly define the core concepts behind AAA POWER INC.: A FOCUS ON GENERATING GREEN POWER that strengthens the bottom lines in the global energy sector, a commitment to creating shareholder value, and an emphasis on Near Zero Emissions.