## Slide 1: ANGTS Commercial Proposal
Alaska North Slope Shippers
Anchorage - January 8, 2002

## Slide 2: Goal
Collaborate with ANS shippers to create the most commercially viable project possible
  Minimize project costs and risks
  Maximize value of existing assets
  Unmatched political and local community support
  Earliest in-service date
1

## Slide 3: System Design
1750 mile pipeline system from Prudhoe Bay to Boundary Lake/Gordondale
48 inch diameter X80 pipe
2050 PSIG
1076 BTU gas
Class IV estimate
ANGTS has analyzed multiple cases for initial and build-up volumes
3

## Slide 4: Base Case
4.334 Bcfd delivered (4.5 Bcfd receipt)
  28 compressor stations - 1.25 million HP
  3.7% fuel (165 MMcfd)
  Capex $US 11.2B (2002 $)
    Includes 10% contingency
  Efficient expandability
4

## Slide 5: Expansion Case
Increase to 5.122 Bcfd delivered in year 3 (5.4 Bcfd receipt)
Additional 18 compressor units
5.1% total fuel (277 MMcfd)
Total Capex $US 12.3B (2002 $)
  includes 10% contingency
5

## Slide 6: ANGTS Advantages
Legislative and regulatory certainty
  ANGTS framework in place in U.S. and Canada
    ANGTA, President’s Decision, Northern Pipeline Act, U.S. and Canada Agreement on Principles
  Go/No Go hurdle has been cleared
  Valid regulatory certificates and environmental permits
    Moving to mitigation/compliance phase
6

## Slide 7: ANGTS Advantages….cont’d
Expedited project schedule
  30-month timing advantage
Flexibility
  ANGTS framework gives FERC and other agencies broad authority to amend certificates, permits and other authorization
  Single window regulatory agencies - OFI and NPA
7

## Slide 8: ANGTS Advantages….cont’d
Rights-of-Way
  Alaska » 434 miles of federal grants
        200 miles of state lands are under active application
  Yukon » grant of easement for entire route through Yukon recognized in Umbrella Final Agreement ratified by all Yukon First Nations
  B.C » valid map reserve and established consultation program with communities and First Nations
  Alberta » consultative notation for rights-of-way
8

## Slide 9: ANGTS Advantages….cont’d
Environmental
  EIS approvals for pipeline
  Clean Water Act, Section 404 permits
  CEAA does not apply
  Specific detailed set of standards and procedures for further review by federal agencies
  Experience with multiple expansions of prebuild under NPA process
  Gas conditioning plant approvals expedited under ANGTA
9

## Slide 10: ANGTS Advantages….cont’d
Engineering, field data and technical information
  Extensive bore-hole data along pipeline route
  Frost heave and thaw settlement research
  Burst test information and analysis
Aboriginal relationships
  Longstanding productive relationships with Alaska Native groups and Yukon and B.C. First Nations
10

## Slide 11: ANGTS Advantages….cont’d
Integrated cross-border transportation system
Strong sponsor group - leading North American pipeline companies
Negotiated tolls and risk-sharing mechanisms
Flexible approach to gas conditioning plant
11

## Slide 12: ANGTS Advantages….cont’d
Collaborative approach
  Co-operation between ANS Shippers and ANGTS will be a catalyst with other key stakeholders
    U.S. and Canadian governments
    State of Alaska
    Yukon, B.C., Alberta
    Alaskan Natives and Canada’s First Nations
    Local communities
12

## Slide 13: Market Delivery Capability
Options at Boundary Lake/Gordondale :
  Continue along ANGTS route
    to Midwest markets via Foothills/Northern Border
    to California or Pacific Northwest markets via Foothills/PG&E
    to Alberta, Eastern Canada or U.S. Northeast markets via Foothills/NOVA/TransCanada
  As well, ANS could target:
    Midwest markets via Alliance
    B.C. and Pacific Northwest markets via Westcoast/Northwest Pipeline
  Multiple options for natural gas liquids
14

## Slide 14: Tolling Assumptions
In-service July 1, 2008 - Full Volumes
70/30 Debt/equity ratio
9.45% WACC
O & M - 1% of Capex
Property taxes - 2% in U.S., 1% in Canada
Capex and O & M escalation rate 2.5%
Shipper contracts
  25 years, renewable
  Basket depreciation (last 5 years) in event of non-renewal
Exchange rate $1.00 US = $1.50 CAD
15

## Slide 15: Tolls
Base Case
$US 1.17*/MMBTU
*Illustrative 25 year levelized tolls in nominal dollars from 2008,
subject to acceptable financing and accounting.
Tolls based on straight-line depreciation would be $1.43 in 2008,
reducing to $ 0.71 by 2033 for the Base Case.
16
Expansion Case
$US 1.10*/MMBTU

## Slide 16: Possible Toll Enhancements
$0.12 Property tax holiday of 5 years
$0.01 Alaska income tax concessions
$0.11 Government loan support (6.0% interest rate)
$0.01 Tax depreciation at 7 years
17

## Slide 17: Next Steps
Joint producer and pipeline technical meeting to discuss details of ANGTS Commercial Proposal.
Brainstorm required action to ensure commercial progress
18

## Slide 18
Thank You
19