## Slide 1: ET&S Operations Staff Meeting August 1, 2000
UAF Fundamentals and Issues
Steven Klimesh
GPG Business Consultant
713-853-7885
sklimesh@enron.com
EB 4198
Notes: The following presentation is essentially the same presentation that I made at the GCO measurement roundtable in Orlando on June 28, 2000
It was focused on discussing some basic and fundamental concepts relative to UAF - providing some history on where we have come from and hopefully some insight on why UAF is important to us and our customers.
I have updated some of the numbers to be more in line with today’s business; for example, when this was first developed, $2.00 to $2.50 per MMBtu was a realistic price for gas. Today $4.00 to $4.50 is where the price stands.
Additionally, this will be presented to Regional UAF teams as part of the continuous improvement effort recommendation of 4/11/2000. There are a couple of lead in slides at the end to transition to a Regional UAF working meeting on the “Matrix Review” for Regional UAF team.

## Slide 2: GCO Measurement Conference June 28, 2000
UAF Fundamentals and Issues
Steven Klimesh
GPG Business Consultant
713-853-7885
sklimesh@enron.com
EB 4198
Notes: Good afternoon, and thank you for inviting me here today to discuss UAF fundamentals and issues.
For those of you who do not know me, my name is Steven Klimesh. I have been an Enron, Internorth, Northern Natural Gas Company employee for 25 years; the last five being spent as an Internal Business Consultant.
Several recent projects that I have been lead, co-lead or participant on include:
Gas Measurement Reengineering (GPG)
GPG Continuous Improvement - Measurement / Invoicing
FGT / LRC UAF review
Director of ETS Y2K Efforts
I am located in Houston. Various methods for contacting me are noted on the screen.
Please call me if you have any questions on this topic at any time.

## Slide 3: GCO Measurement Conference June 28, 2000
UnAccounted For Gas
The difference between all the gas received into, or
entering, the pipeline, and all the gas delivered
from, or leaving, the pipeline.
Notes: Fundamental to any UAF effort is defining and knowing your terms.
This is critical so everyone is working from the same baseline and the same level of understanding.
Be sure you are speaking the same language!!!!!! In just a minute I am going to give you an example of how critical this really is. (NNG 1996-97)
  What is unaccounted for gas - UAF?
Simplistically speaking, UAF is the difference between the amount of gas volume and heating value entering the pipe and the amount of gas volume and heating value leaving the pipe.
  Is UAF the same as Lost and unaccounted for gas?
If that is comfortable for you - yes! Stating LOST is possibly incorrect.
  Is UAF the same as unmetered gas?
NO! Unmetered is just that - gas entering or leaving the pipe which is not metered. Therefore, we need to estimate it and report it on an unmetered report
You can call UAF what you want, and it has many names, BUT the final equation is always the same.
Next slide!

## Slide 4: GCO Measurement Conference June 28, 2000
UnAccounted For Gas
Difference between Receipts and Deliveries = UAF
Statement 1: +100 - 90 = 10 (a loss)
Statement 2: -100 + 90 = (10) a loss
Notes: Lets talk about this equation for a few seconds.
Usually when you think about a receipt into something you envision a positive number. You are filling something up.
Similarly when you think about delivery of something you visualize a negative number or action; You are emptying something.
Under these perceptions, statement one is how you would show the equation. BUT, that gives you a positive number indicating a loss.
Why a loss? Well, EVERYTHING else equal, you took in 100 and delivered 90. Therefore, you lost 10.
SO, to make the equation fit our logic and the commonly accepted accounted practice of having negative numbers equal losses, the computer is programmed to equate to statement two. This then gives us a negative number for the loss.
Don’t let this confuse you - the concept is still the difference between gas in and out.

## Slide 5: GCO Measurement Conference June 28, 2000
A wild goose chase!
Chasing your tail!
Looking for a ghost that isn’t there!
Destined to fail!
Notes: Here is that quick example of what happens when your have confusion about what you are trying to accomplish!
Every one is familiar with Legalese

## Slide 6
LEGAL - ESE
THE SPECIALIZED VOCABULARY OF THE LEGAL PROFESSION
HOUSTON - ESE
THE SPECIALIZED VOCABULARY OF THE HOUSTON OFFICE
OTHER KNOWN “ESE’S” include….
Bushton - ese :where “Shrinkage” means extraction losses and fuel; OR not! - depending on who’s talking
Beatrice - ese :where UAF means the same as unmetered gas
Nebraska - ese :where “guys” equates to “y'all” in Texasese
GMS - ese :well, who knows!
GCO Measurement Conference June 28, 2000
Notes: <number>
<footer>
<header>
<date/time>
3
3
3
Legalese is the lawyers way of confusing us - so we don’t have a clue as to what is going on.
There are additional ESE’s
Houstonese - very similar to legalese with the same intended result - confuse them - make them as ignorant of the topic as I am - clueless!!!
A few more that I have encountered over the years include:
These were not meant to confuse, they just did and do.

## Slide 7
Houston - ese circa 1996
NNG’s UAF is:
14.4 BCF
$35,000,000
GCO Measurement Conference June 28, 2000
Notes: <number>
<footer>
<header>
<date/time>
6
6
6
Anyone - what does this mean to any self respecting and knowledgeable field employee?
Anyone!!!!
Right, we have a BIG UAF problem. We are losing physical volumes at a very significant rate.
SOOOOOO - what do we do???? Anyone!
Right - fire drill and try to find out where the gas losses are occurring.
BUT OOPPS! That ain’t the case once we dig into it.

## Slide 8
Misnomer !!!!!!!!!
NNG’s UAF was NOT $35,000,000
$35,000,000 was the value of the combined OVER / (UNDER) RETAINAGE of NNG’s fuel/company used gas and UAF.
GCO Measurement Conference June 28, 2000
Notes: <number>
<footer>
<header>
<date/time>
7
7
7
I am not here to give a lesson in Regulatory, Rates and Retention. Suffice it to say….
The next slide

## Slide 9
FUEL and COMPANY USED
Minus FUEL RETAINED
Equals OVER(UNDER) RETAINED FUEL
and
Physical UAF
Minus UAF RETAINED
Equals OVER (UNDER) RETAINED UAF
Resultant Being
Over(under) retained fuel + Over (under) Retained UAF = UAF
GCO Measurement Conference June 28, 2000
Notes: <number>
<footer>
<header>
<date/time>
9
9
9
This is how the folks in Houston were defining UAF

## Slide 10
NET
Fuel Fuel Over Phys UAF Over Over
used retnd (under) UAF retnd (under) (under)
11/93
-10/94 32.2 28.1 (4.1) 7.3 13.7 6.4 2.3
11/94
-10/95 30.6 26.1 (4.5) 12.8 14.3 1.5 (3.0)
11/95
-10/96 36.0 27.1 (9.0) 14.0 14.8 .8 (8.2)
11/96
-03/97 19.0 12.5 (6.5) 5.6 6.6 1.0 (5.5)
Total 117.8 93.8 (24.1) 39.7 49.4 9.7 (14.4)
GCO Measurement Conference June 28, 2000
Data in BCF
Notes: <number>
<footer>
<header>
<date/time>
10
10
10
Here are the real numbers
Where was the real problem?
Right - Fuel rates - having nothing to do with physical UAF.

## Slide 11: GCO Measurement Conference June 28, 2000
Difference between Receipts and Deliveries = UAF
Receipts
Wellhead
Interconnect
Storage withdrawal
Line pack
LNG withdrawal -(Vaporization)
Coal gas manufacture
Deliveries
City Gate or LDC
Fertilizer plant - Other end user
Electric generation plant
Line pack
Storage injection - LNG liquification
Fuel
Blow down, Purge, Leaks, and Condensate
Company used e.g. actuators
Interconnects
Notes: Back to UAF
Remember the basic formula - difference between Receipts and Deliveries
What are receipt and what are delivery examples
This slide lists numerous types of Receipts and Deliveries - it is not all inclusive.
Note, Many types can be both a receipt or delivery; The determining factor is whether the gas is entering or leaving the pipeline.
Examples - storage. Line pack
Another Horror Story - NNG LNG set up as plants and a receipt for gas being liquefied - a receipt to the storage tank yes, BUT we are addressing PIPELINE UAF - Think of yourself as a pipeline when determining if the point is a Receipt or Delivery.
Case in point KOCH Escambia - a delivery, not receipt - I have been picking on NNG long enough - time to spread the wealth - I have stories on everyone. I use them as learning experience however, not vailed threats.

## Slide 12: GCO Measurement Conference June 28, 2000
Metered
or
Unmetered (estimated)
Notes: Does it matter if the gas is metered or unmetered relative to the impact on UAF?
No! Metered items are just easier - MAYBE - However, we have to be sure the meter is operating correctly, calibrated and getting the correct BTU values, Specific Gravity data etc. Part of your UAF can be, and no doubt is, measurement error due to calibration, dirt, liquids, swirl, jetting etc. The UAF impact is there since the metering at the receipt and at the delivery will be “off” in unequal amounts.
So, even though a point is metered, there are opportunities to “create UAF.
A tougher situation is getting a good estimate on the items that are not metered.
  For example - leaks - either at a compressor as a consequence of compression or as fugitive gas via a hole in the pipe.
  Actuator use and vent is another item - how do you estimate and report the total gas loss resulting form all this equipment on the pipeline
  And do not forget, YOU NEED THE CORRECT QUALITY input here.

## Slide 13: GCO Measurement Conference June 28, 2000
29
Financial Implications - Why it is important to minimize UAF
Bottom line or Competitive Advantage
  Impacts vary by pipeline
    NNG tracker, annual true up
    NBPL tracker, monthly true up
    FGT tracker, seasonal true up
    TW no tracker, earnings implications
A .10% change in UAF equals .25 cents per MMBtu throughput impact at $2.50 per MMBtu gas
A .10% change in UAF equals .40 cents per MMBtu throughput impact at $4.00 per MMBtu gas (.25% = 1 cent)
Notes: <number>
<footer>
<header>
<date/time>
Volumetric tracker carries price risk
Surcharge tracker directly affect transportation rates
Marketing opportunities may be available
Earning potential with no tracker
Although the financial impact that UAF can have on NNG, NBPL, and FGT are definitely not the same as TW, a reduction in UAF could:
Reduce transportation rates which could improve our position in a competitive market
  Improve customer satisfaction
UAF Changes Quantified
.1% Annual
UAF Change Valued @
(dth) $2.50
NNG 1,400,000 $3,500,000 Volumetric Tracker, Annual True Up
NBPL 880,000 $ 2,200,000 Volumetric Tracker, Monthly True Up
FGT 570,000 $ 1,425,000 Surcharge Tracker, Seasonal True Up
TW 570,000 $ 1,425,000 No Tracker; Earnings Implications
Sum 3,420,000 $ 8,550,000 IMPACT to GPG or the Customer
One last point - Knowing the true level of UAF eliminates looking for something that is not missing!!!! Next slide - NNG $35,000,000 UAF issue!

## Slide 14: GCO Measurement Conference June 28, 2000
30
TW Example of past performance
UAF reduction
  1998 UAF LOSS 3,280,260 MMBTU (.53%)
  1999 UAF LOSS 851,822 MMBTU (.15%)
  2,428,438 MMBTU improvement equals $6,071,095* ($9.7 MM @ $4)
  $2,000,000* still on the table (reducing the .15% to 0%) ($3.4 MM @ $4)
At what cost?
  Various projects totaling $3,418,152
  Recurring costs of $280,000 annually
Projects resulted from the regional UAF teams
*(at $2.50/MMBTU)
Notes: <number>
<footer>
<header>
<date/time>
30
Maintaining this level of UAF for TW would result in $30,000,000 of increased earnings over 5 years. When valuing the gas at $2.50 MMBtu.
This is $48.5 million at $4.00 and $55 million at $4.50. I have always shyed away from the impacts over 2:00 to 2:50 since gas was stable there for so long. Now the numbers are real at 4 to 4.50
With $2,000,000 per/year (or $3.4 Million) still on the table, continuing our efforts to improve could result in greater earnings potential in the future.
Another 10 ot 15 Million or up to $75,000,000 is available to us.
On the other hand, if we become lax in our efforts, we could revert back to where we were and have a negative impact on earnings.

## Slide 15: GCO Measurement Conference June 28, 2000
Projects that Benefited TW
  West Texas Pigging Facilities $757,000
  Oasis/TW interconnect filter separator $493,000
  West Texas Lateral segmentation meter $420,000
  Meter Tube flow conditioners $324,000
  EFM flow computer upgrades $251,000
  Positive value shut in’s $241,000
  Chromatograph upgrades $237,000
  Installation of ultra sonic measurement $100,000
  SRE testing $100,000
  Data review $200,000
Notes: Additionally, TW began a program to visually inspect and clean meter tubes
and they increased their measurement audits and audit follow-up and resolution activities.
SOOOOOO
What does our UAF look like over the past two years?
Next slide

## Slide 16: GCO Measurement Conference June 28, 2000
  UAF LOSS
  %(‘99) %(‘98)
NNG .14 . 27
TW .16 . 53
FGT .18 . 25
NBPL .06 . 63
LRC .49 . 64
GRI ‘98 Avg. .47
1998 and 1999 Dth UAF Loss
Notes: <number>
<footer>
<header>
<date/time>
Pretty damn impressive!
We already discussed the TW activities to reduce UAF. In addition,
TW, FGT, and part of NNG had formed Regional UAF Teams .
NBPL, NNG, completed Ultrasonic measurement projects on some major delivery points as well as segmentation measurement..
GPG implemented the Stars program.
All of these efforts have had a positive impact on reducing UAF
The year 2000 is also shaping up to be a great year.

## Slide 17: GCO Measurement Conference June 28, 2000
What Does 2000 Look Like
‘98 ‘99 Through June Through May
NNG (.27%) (.14%) (1,765,894) (.25%) (1,382,685) (.23%)
TW (.53%) (.16%) ( 73,865) (.02%) 26,930 .01% GAIN
FGT (.25%) (.18%) 9,300 GAIN .00% ( 122,000) (.04%)
NBPL (.63%) (.06%) (1,095,000) (.25%) (1,045,000) (.28%)
LRC (.64%) (.49%) ( 500,382) (.46%) ( 426,000) (.27%)
HPL (.31%) (.31%) N/A 91,000 .02% GAIN
All data in MMBtu

## Slide 18: GCO Measurement Conference June 28, 2000
Recent UAF Initiatives
FGT / LRC UAF Team
Continuous Improvement - Measurement / Invoicing
Notes: I want to spend a few minutes on these topics before I close.
The FGT LRC UAF Team did a review / overview of the areas where FGT / LRC might be susceptable to UAF impact. This effort was very similar to the on-going ETS efforts we have dealt with over the past several years.
The CI effort has already been presented but I will give you and update on the current status.

## Slide 19: GCO Measurement Conference June 28, 2000
FGT / LRC UAF Team
Quarterly UAF meeting
  * Leaking valves * Low-end unmetered flow
  * Leaking plates * Square root error
  * Flow conditioners * Pilot gas
  * Dirty plates
Completed Items
  * Unmetered gas reporting * EPA STAR program
  * Reporting blow downs * Condensate conversion factors
  * OMV testing and witnessing * Line pack calculation
  * Calibration gas * MIPS data base validation
Notes: The last quarter of 1999 and the first of 2000 saw a UAF task force review FGT and LRC UAF implications. This is something that has been ongoing at ETS for over three years
A number of items were identified that needed a longer time line to complete. In order to efficiently monitor these items , AND establish a UAF focused communication channel, a quarterly UAF meeting with Dan Pribble, his directors and others was established.
We will be getting updates on the items noted . Doug Mosley was initially identified as the champion for this effort. I believe Mike Campo is now the go to man.
Additionally, a great number of items were completed by this task force. They include:
Read them and comment on a couple.

## Slide 20: GCO Measurement Conference June 28, 2000
Continuous Improvement - Measurement / Invoicing
  Reduce PPA’s
  UAF Improvements and Maintenance
  New Technology
  Organization
Notes: Another recent effort that focused on UAF was the CI measurement task force.
We have recently begun implementation on a number of recommendations coming out of that study.

## Slide 21: GCO Measurement Conference June 28, 2000
Continuous Improvement - Measurement / Invoicing
  UAF Improvements and Maintenance
    Form Regional UAF teams (see the matrix)
    Define UAF expectations and accountabilities for GPG
    Initiate a GPG UAF conference
    Enhance facility reviews and evaluation (audits)
    Provide data analysis as deemed necessary ( NNG, NBPL )
Notes: Relative to the UAF Improvement initiatives I have provided the five focus areas.
With regard to bullet three - it is meetings like this were the message will be spread.
You will be hearing more on each of these in the upcoming weeks.
I have included a matrix in your handout - these are the items applicable to bullet one.
NOTE TO ME: Be sure to take the folders to Omaha for this update.)

## Slide 22: GCO Measurement Conference June 28, 2000
Key Points from today
  Understand the definition of UAF
  Be sure everyone is talking about the same thing
  When addressing UAF - think of yourself as a pipeline
  It is real money to someone
  There is more to come on UAF
Notes: This is what I hope you take away from this session.

## Slide 23: GCO Measurement Conference June 28, 2000
QUESTIONS?
QUESTIONS?
??????????
Quaestios?
Notes: <number>
<footer>
<header>
<date/time>
Answer questions
Thank you for inviting me
Call if I can help.

## Slide 24: Regional UAF Team Meetings Aug. - Sept. 2000
Continuous Improvement
UAF Maintenance
Form Regional UAF Teams
Define UAF Expectations and Accountabilities for GPG

## Slide 25: Continuous Improvement Measurement / Invoicing Processes 4/11/00 - UAF Maintenance Team Report
Recommendation:
Form Regional UAF teams
  Point person from each operational team
  Technical Services representatives
    To review and prioritize “Improvement Opportunities” (matrix)
    To implement “Improvement Opportunities” (matrix)
    To coordinate UAF efforts throughout region
    To raise the awareness of the importance of controlling UAF
Notes: <number>
<footer>
<header>
<date/time>
This is where the detective work begins
Cost: Time (any travel costs would be absorbed within existing budgets)
STEVE/ALLAN - address the overlap of the ORG team on this topic

## Slide 26: Continuous Improvement Measurement / Invoicing Processes 4/11/00 - UAF Maintenance Team Report
33
Recommendation:
Define UAF expectations and accountabilities for GPG
  Initiate Operating Company UAF Roundtable Meeting
    Representatives from regional UAF teams, GMS, Gas Control, Marketing, Facility Planning/Engineering, Tech. Services, Measurement Technology, Accounting, & Exec. Sponsor
      Identify each groups impact on UAF
      Define expectations and accountabilities
      Coordinate company-wide UAF efforts
Notes: <number>
<footer>
<header>
<date/time>
33
Cost: Time (travel costs would be absorbed within existing budgets)
This group and the Regional teams must work concurrently to define accountabilities / responsibilities, roles and duties
ARE WE clear on the difference between:
Regional UAF team
Monthly/Quarterly UAF meeting
Operating Co UAF team (Roundtable)?