## Slide 1
Balancing Energy Market
Fundamental Concepts
November 13,2001
Austin, TX

## Slide 2
OK, let’s look at the different categories of Balancing Energy Service (BES) deployments.
There are five current types of BES deployment. Category 1, 2, 3, 4 and OOME. Lets take a look at how they work
Deployment Category
ERCOT Operator

## Slide 3
Load@
800MW
Texas_1
@200MW
Texas_3
@200MW
Texas_4
@200MW
Texas_2
@200MW
Zone I
Zone II
Scheduled flow on the zonal constraint 600MW
Adjusted flow from the BES awards on the zonal constraint
needs to be 200MW
Deployment Category
Flow limit 400MW

## Slide 4
Zone I
Zone II
Deployment Category
Load
800
MW
600
MW
Flow limit 400MW
200
MW
Portfolio obligation is 400 MW
600 – 200 = 400
Portfolio obligation is 400 MW
200 + 200 = 400
DBES 200 MW
UBES 200 MW
QSE Texas Zone I
QSE Texas Zone II

## Slide 5
Zone I
Zone II
Deployment Category
Load
800
MW
400
MW
Flow limit 400MW
400
MW
DBES 200 MW
UBES 200 MW
Category I deployment: By portfolio
Units to be moved are at the discretion of the QSE

## Slide 6
Line limit 200MW
Texas 1 is @ 230MW
ERCOT EMS system
Unit Texas 1
go to or below 200MW
Deployment Category
Category 2 - If the shift factors of a resource are positive for
all the binding operational constraints, the resource is instructed
to operate below the MW LEVEL value.

## Slide 7
Deployment Category
Category 3 - If the shift factors of a resource are negative for
all the binding operational constraints, the resource is instructed
to operate above the MW LEVEL value.
Line limit 200MW
Actual flow 270MW
Texas 1 is @230MW
Load: 500MW
Line Limit 600MW
Actual Flow 500MW
ERCOT EMS system
Unit Texas 1 go to or above 300MW

## Slide 8
Line limit 300MW
Actual flow 370MW
Texas1is @ 230MW
Load: 600MW
Line Limit 700MW
Actual Flow 600MW
ERCOT EMS system
Unit Texas 1 Operate exactly at 300MW
Deployment Category
Category 4 (Security Issue) - If the shift factors of a resource are positive for some of the binding operational constraints, but negative for others, the resource is instructed to operate at the MWLEVEL value.
Line limit 300MW
Actual flow 230MW

## Slide 9
Line limit 200MW
Actual Flow 170MW
Texas 1 is @ 230MW
Load: 400MW
Line Limit 600MW
Actual Flow 400MW
ERCOT EMS system
Unit Texas 1 Operate exactly at 300MW
Deployment Category
Category 4 (Commercially) - If the shift factors of a resource are 0 for all the binding constraints, but the resource is instructed to operate at the MW LEVEL value for settlement purpose .
A New category will be assigned for the commercial category 4.

## Slide 10
Texas 1 is @ 230MW
ERCOT Operator
Deployment Category
Why is my transmission line still overloaded after market clearing?
The Unit Texas 1 needs to go to 300MW.
OOME is an out-of-merit request for energy, specifying a resource. The direction is initiated by ERCOT using a manual or verbal instruction.

## Slide 11
No Instruction
Texas_1
Texas_3
Texas_2
QSE Texas is free to move the three units in the portfolio, in any way to meet the portfolio obligation of 600MW.
Base Power Schedule 600MW
T I M E
Texas 3 is @ 200MW
Texas 2 is @ 200MW
Texas 1 is @ 200MW

## Slide 12
QSE Texas will get paid by ERCOT 0*MCPE ($10/MW)=$0
This bilateral market works perfect.
No Instruction

## Slide 13
QSE Texas is free to move the three unit portfolio to meet the base power and the UBES award obligation,
600MW + 100MW = 700MW.
Base Power Schedule 600MW
UBES awards 100MW
T I M E
UBES Cat I instruction
Texas 3 is @ 200MW
Texas 2 is @ 200MW
Texas 1 is @ 200MW
Texas 3 is @ MW
Texas 2 is @ MW
Texas 1 is @ MW

## Slide 14
QSE Texas is paid by ERCOT 100*10=$1000
My bid price is $8/MWH, $1000 will cover my cost ($800) for the additional 100MW.
MCPE = $10/MWH
UBES Cat I instruction

## Slide 15
QSE Texas is free to move the three unit portfolio to meet the base power and the DBES award obligation 600MW - 100MW = 500MW.
Base Power Schedule 600MW
DBES awards 100MW
DBES Cat I instruction
Texas 3 is @ 200MW
Texas 2 is @ 200MW
Texas 1 is @ 200MW
Texas 3 is @ MW
Texas 2 is @ MW
Texas 1 is @ MW
T I M E

## Slide 16
Hey you! QSE Texas. Pay ERCOT 100*MCPE ($10/MW)=$1000
Let’s see? Marginal bid price is $10/MWH, My fuel & op cost savings is $11/MWH. 100*11=$1100.
$1100 - $1000
My net benefit is =$100.
DBES Cat I instruction
MCPE = $10/MWH

## Slide 17
T I M E
QSE Texas moves Texas1 to 150MW or below. The three unit portfolio maintains
(600 – 50) = 550MW.
Base Power Schedule 600MW
DBES awards 50MW to QSE Texas. Unit Texas 1 to go at or below 150MW
DBES & Cat 2 instruction
Texas 3 is @ 200MW
Texas 2 is @ 200MW
Texas 1 is @ 200MW
Texas 3 is @ MW
Texas 2 is @ MW
Texas 1 is @ 150MW

## Slide 18
Portfolio level, QSE Texas pays ERCOT 50MW*10=$500;
For unit Texas 1, QSE Texas gets paid
net change*MCPE
(200-150)*$10 = $500.
Net payout $500-$500=$0.
I reduced my total generation 50MW and ERCOT arranged service to that portion of the load for me. I pay ERCOT $0 and I can also save some fuel/op cost. This is a mutually beneficial instruction.
MCPE = $10/MWH
Texas 1 resource plan level 200MW
DBES & Cat 2 instruction

## Slide 19
T I M E
QSE Texas must move Texas1 to 250MW or above.
The three unit portfolio must then maintain (600+50) 650MW.
Base Power Schedule 600MW
UBES awards 50MW.
Unit Texas 1.
Go to or above 250MW
Texas 3 is @ 200MW
Texas 2 is @ 200MW
Texas 1 is @ 200MW
Texas 3 is @ MW
Texas 2 is @ MW
Texas 1 is @ 270MW
UBES & Cat 3 instruction

## Slide 20
Portfolio level, ERCOT pays QSE Texas 50MW*10=$500;
For unit Texas 1, QSE Texas gets paid Unit net change*Unit Specific Premium
(250-200)*$20/MW=$1000.
Total: ERCOT to pay QSE Texas 1500$.
1500 bucks!! It’s a good deal.
UBES & Cat 3 instruction
Premium less than
Heat rate
MCPE = $10/MWH
Texas 1 Up Premium $20 and
resource plan level 200MW

## Slide 21
Portfolio level, ERCOT pays QSE Texas 50MW*10=$500;
For unit Texas 1, QSE Texas gets paid Unit net change*(Fuel Index*Heat Rate- MCPE)
(250-200)*$44/MW=$2200.
Total: ERCOT to pay QSE Texas 2700$.
2700 bucks!! Is a good deal.
MCPE = $10/MWH
Texas 1 Up Premium $100 and
resource plan level 200MW
UBES & Cat 3 instruction
Premium more than
Heat rate

## Slide 22
T I M E
QSE Texas moves Texas 1 to 250MW. The total of Texas 2 and Texas 3 needs to be 600 - 250=350MW.
Base Power Schedule 600MW
To unload the overloaded transmission line, the unit Texas 1 needs to go to 250MW.
Texas 3 is @ 200MW
Texas 2 is @ 200MW
Texas 1 is @ 200MW
Texas 3 is @ MW
Texas 2 is @ MW
Texas 1 is @ 250MW
Only OOME Inst.

## Slide 23
ERCOT pays QSE for Texas 1
Unit net change*unit specific premium. That’s (250 - 200)*($20/MW)= $1000
Great! By realigning the generation pattern of my units. I get paid $1000
Only OOME Inst.
MCPE = $10/MWH
Texas 1 Up Premium $20 and
resource plan level 200MW

## Slide 24
Deployment Summary
It seems the instruction is easy to follow. Can you summarize how I respond to the deployment instructions?
The unit specific instruction (i.e., Cat 2, 3, 4, or OOME) tells you the specific level for that resource.
The UBES/DBES instruction (i.e., Cat 1) tells you how much you need to move from your base power schedule at the portfolio level.
Deployment Summary

## Slide 25
Payment/Charge Summary
Corresponding to each unit specific deployment, you will receive a unit specific payment;
At the portfolio level, you will be paid/charged by (Resource Schedule-Meter Reading)*MCPE.
Can you also summarize what is the settlement implication for these instructions?
Payments /Charges ?

## Slide 26
How to prioritize instruction?
1st, meet the specific Resource deployment
Then provide the Balancing Energy Service deployment .
If unable to provide the BES, follow the notification procedures established in Section 5, Dispatch.
For some special conditions, I have difficulty following both the unit specific instructions and portfolio instructions, what I am supposed to do?
Prioritizing Instructions

## Slide 27
Advanced Course is Available
When it gets posted, sign up for - “Balancing Energy Market - Principles and Examples”. This will provide, in technical detail, how the ERCOT protocols direct this balancing market.
We also recognize there’s room for improvement. Currently, the ERCOT Phase 2 project is in progress to improve market system performance.
I understand the expectation, but how do I find out the basis for some of these instructions I’m getting and get a more through understanding of the ERCOT market?
Advanced Course ?

## Slide 28
Questions and Answers
Questions ?????