## Slide 1
Gas Accord II Workshop
Balancing

## Slide 2: Agenda
Gas Accord I Balancing
Most Promising Options OII
OFO and OII Settlements
Balancing Storage Report Dated March 7, 2000
OFO Report Dated July 31, 2000
OFO Forum on August 29, 2000
Concerns for Gas Accord II
Options for Discussion

## Slide 3: Gas Accord I Balancing

## Slide 4: Gas Accord I Balancing
Bundled balancing with the cost included in on-system backbone transportation rates
Balancing resources include:
  Pipeline inventory with an operating range from 400 to 600 MMcf/d
  Storage assigned to balancing resources of 50 MMcf/d injection, 70 MMcf/d withdrawal, and 2.2 Bcf inventory
Monthly balancing requirements with best efforts daily balancing
  Within 5% at end-of-month
  If not within 5%, can trade imbalance
  Amount outside 5% not traded is cashed out

## Slide 5: Gas Accord I Balancing (continued)
OFOs may be called if pipeline inventory
  exceeds or is forecast to exceed desired pipeline inventory by 200 MMcf/d, or
  is below or is forecast to be below desired pipeline inventory by 150 MMcf/d
Multi-stage tolerance band and non-compliance penalty provisions
Ordered at least 12 hours prior to the beginning of the gas day
Also call EFOs or Divert Supply from noncore to core customers in extreme under-supply situations

## Slide 6: Types of Balancing Entities
Core Procurement Group (CPG), which includes PG&E’s Core Procurement Department and all Core Transport Agents (CTAs)
Noncore Balancing Aggregation Agreement (NBAA), which aggregates a group of noncore end-use customers into one entity for balancing purposes.
Individual noncore end-use customer maintains an imbalance account under their Natural Gas Service Agreement (NGSA)

## Slide 7: Most Promising Options OII

## Slide 8: Most Promising Options D.99-07-015
Shippers not only concerned with the frequency of OFOs, but with the difficulty of predicting when they will be called (pg. 32)
  Improve the real-time, detailed information about PG&E’s balancing practices (pg. 35)
Short of requiring daily balancing for all customers, however, the provision of a daily balancing option may be necessary in order to implement other reforms … (pg. 39)
  … customers could elect to commit to daily balancing in exchange for avoiding some or all of the balancing charges … (pg. 40)

## Slide 9: Most Promising Options D.99-07-015 (continued)
Targeted OFOs could also improve the system balance (pg. 41)
  While a targeted OFO alone may not be enough to keep the system in balance, it may be a constructive starting point in some situations (pg. 41)
We find the concept of imbalance trading to hold sufficient promise to merit further inquiry (pg. 44)

## Slide 10: OFO and OII Settlements

## Slide 11: OFO Settlement (D.00-02-050)
Established OFO Forum and Required OFO Report be provided quarterly
More daily operational information posted on Pipe Ranger (www.pge.com/pipeline)
  Forecast operating plan five times per day
  Customer class demand data after 3-days
Required report on cost and effect of adding more storage to support balancing
Modified certain OFO features:
  Improved OFO notification, e.g paging, FAX, Pipe Ranger
  Reduced OFO noncompliance charge for 1st stage
  Added noncompliance charge exemption below $1,000

## Slide 12: OFO Settlement: Calling OFOs
Improved predictability of OFOs by setting specific pipeline inventory limits for calling OFOs
Inventory Limits vary depending on system demand
A tolerance band and noncompliance charge are set depending on the relief needed
OFOs may be system-wide or customer-specific

## Slide 13: OFO Settlement: Customer-Specific OFOs
Added more definitive criteria for calling customer-specific OFOs
There must be ten or less balancing entities whose forecast imbalance exceeds:
  the OFO Tolerance Band percentage, and
  5,000 Dth
The total forecast relief for these entities, multiplied by the Performance Factor, must exceed the Required Relief needed for the pipeline
  Performance factor is ratio of forecast relief to actual system relief provided
  Performance factor can be modified based on average performance to-date

## Slide 14: OFO Settlement: OFO Stages
Noncompliance
Tolerance Band Charge
As a % of Usage Dollars per Therm
Stage 1 up to ±25% $0.025
Stage 2 up to ±20% $0.10
Stage 3 up to ±15% $0.50
Stage 4 up to ±5% $2.50

## Slide 15: Gas OII Settlement (D.00-05-049)
Adds a self-balancing option, with annual election
  Balance daily within ±10%, and accumulative daily imbalance cannot exceed ±1% of the Pre-Determined Monthly Usage
  Compliance measured after the fact, with typical noncompliance charges of $1.00 per dth per day
  Credit of $0.005 per dth times actual monthly usage
Provides for imbalance trading
  Adds electronic trading of monthly imbalances
  Creates OFO day imbalance rights and allows these to be traded

## Slide 16: Balancing Storage Report Dated March 7, 2000

## Slide 17: Storage Balancing Report
Adding storage should help reduce OFOs, if customers do not increase imbalances
Notes: Period: 4/98 - 8/7/99
Number of High OFOs 30
Actual Number of High OFOs 56
OFO Reduction 26
% OFO Reduction 46%
Period: 4/98 - 8/7/99
Number of Low OFOs 9
Actual Number of Low OFOs 21
OFO Reduction 12
% OFO Reduction 57%

## Slide 18: Storage Balancing Report (continued)
Table 4: Estimated Average Backbone Transmission Rate Increase
Increasing the storage resources for balancing to 100 MMcf/d injection, 100 MMcf/d withdrawal, and 4.4 Bcf inventory would increase balancing costs
Added Storage Source
$ per dth
PG&E McDonald Island
$0.0085
Lodi Storage (Western Hub)
$0.0063
Wild Goose Storage
$0.0065 - $0.0072

## Slide 19: OFO Report Dated July 31, 2000

## Slide 20: OFO Report
The OFO Settlement measures have reduced system-wide OFOs

## Slide 21: OFO Report (continued)
Drivers of OFO Events
  The pipeline inventory at the beginning of the three-day period was already at or near the upper pipeline inventory limit
  Large customer imbalances occurred sometime during these three days
Market Center Imbalances did not contribute to OFOs during the quarter
  Market Center activity is managed on a daily basis utilizing available storage assets, and does not rely on either pipeline inventory or storage allocated to pipeline balancing

## Slide 22: OFO Report (continued)
Significant Contributors Leading Up To OFO Days
  Within the total customer imbalance, certain entities are contributing more to packing (or drafting) the pipeline inventory than others.
Table 7: Significant Contributors per OFO Settlement Definition
Number of OFOs
Entity ID
Entity Type
Meeting Criteria
Targeted
1117
NBAA
8
3
1126
NBAA
7
3
1157
NBAA
7
5
2771
NBAA
7
5
51
NGSA
11
0
7604
NGSA
8
1
Notes: Contributed to more than ½ of the OFOs

## Slide 23: OFO Report (continued)
There was a substantially better response to system-wide OFOs compared to customer-specific OFOs (all OFOs were high inventory OFOs)
Table 6: Net OFO Day Total Customer Imbalances
Notes: These were all the high inventory OFOs and all were effective

## Slide 24: OFO Report (continued)
Significant Contributors On OFO Days
  PG&E continues to be concerned that gas is being traded or sold to entities not targeted by the customer-specific OFO
Table 8: Non-Targeted Entities Increasing OFO-Day Imbalances

## Slide 25: First OFO Forum August 29, 2000

## Slide 26: OFO Forum Response to Issues
Goal of a 25% reduction in system-wide OFOs set in OFO Settlement
  Goal met by over 60% reduction
  Continue to monitor performance
Concern for the effectiveness of customer-specific OFOs
  Monitor effectiveness of customer-specific OFOs
  Use Settlement procedures to modify Performance Factor, if necessary
  Evaluate options, as necessary, to improve performance in the next OFO Report

## Slide 27: OFO Forum Response to Issues (continued)
Should parties who significantly contribute to system-wide OFOs be specifically identified? Is there a way to more accurately target entities for customer-specific OFOs?
  Monitor
  Evaluate options to improve targeting customers during customer-specific OFOs.
  Explore options with concerned parties – notify all parties if changes are proposed
Should the exemption for OFO noncompliance charges be increased?
  No change at this time

## Slide 28: OFO Forum Response to Issues (continued)
Should additional storage resources be allocated to balancing?
  Consider this issue as part of the Gas Accord II discussions
Should the Cash-Out procedures be changed?
  No action at this time
  Monitor the level of cash-outs

## Slide 29: OFO Forum – California Gas Production
Some California gas producers (CPBAs) are significantly out of balance on many days. OFO days are of particular concern.

## Slide 30: OFO Forum – California Gas Production
When California gas producers (CPBAs) are significantly out of balance on OFO days, there is potential to jeopardize operational integrity

## Slide 31: OFO Forum Response to Issues (continued)
How can California gas production imbalances on OFO days be reduced?
  Talk to affected parties about the options and the possible regulatory process needed to change
  The OFO Forum expressed a preference for the “freeze nominations” option
Is the 2.2 Bcf storage inventory allocated to balancing adequate?
  Discuss as a part of Gas Accord II

## Slide 32: Balancing Concerns for Gas Accord II

## Slide 33: Concerns Expressed By Parties
Consider adding more balancing storage to reduce OFO frequency
Only assign storage to balancing as needed to meet daily operating requirements, and not to support customer imbalances
Core customers should have the option to use AMR for:
  Daily (self) balancing calculations if they choose this option
  Determining OFO and EFO compliance.
Customers should balance daily within a narrow window

## Slide 34: PG&E Concerns
Increasing electric generation loads may cause imbalances that cannot be managed with current balancing resources and rules
Customers who only receive a portion of their gas supply from the PG&E system may be balancing their full load on PG&E, and not paying for this level of service
Customer-specific OFOs are not always effective
California gas production is adding to imbalances during OFOs

## Slide 35: PG&E Concerns (continued)
Pipeline balancing occasionally exceeds the allocated 50 MMcf/d injection and 70 MMcf/d withdrawal
Notes: Note that Injection is (-) and withdrawal is (+)

## Slide 36: PG&E Concerns (continued)
And they correlate with OFOs

## Slide 37: PG&E Concerns (continued)
Some customers have high and frequent imbalances and others have lower imbalances relative to demand.
Notes: This is more interesting than it is a concern for PG&E. It shows there is a wide range of utilization of balancing by the customers.

## Slide 38: Balancing Options for Discussion

## Slide 39: Options: Retain Status Quo
Status Quo
  Unlimited daily imbalances with occasional OFO/EFO
  Monthly balancing
  Self-balancing option
  Cost bundled in the Backbone Transmission rate
  50 MMcf/d injection, 70 withdrawal, 2.2 Bcf of inventory
Considerations
  Shippers and balancing entities understand rules
  Balancing part of backbone service
  Users of this service do not always pay for the service
  Concern over imbalances created by increasing electric generation gas usage
  California Gas imbalances can aggravate OFO situations

## Slide 40: Options: Remove Balancing Charge From Backbone Rate
Unbundle balancing cost from Backbone rate
  Choose either monthly balancing or self-balancing
  Balancing charge billed to customer based on metered usage
  If customer assigns balancing to an NBAA, then balancing charge follows
Considerations
  Aligns charges with balancing responsibility, which is at the customer’s meter (or for CPGs, at their “forecast”)
  Provides a lower charge for self-balancing rather than a credit
  Does not change the balancing provisions, so other operational and effectiveness concerns remain
  Meets a Gas OII concern about having separate charges for balancing
Notes: This is a variation on the Status Quo

## Slide 41: Options: Add a Daily Limit to Monthly Balancing
Limit or cap the amount of daily and/or accumulated imbalance for monthly balancing
  Noncompliance charges based on metered usage
Considerations
  Addresses some of the concern over imbalances created by increasing electric generation gas usage
  Likely to reduce OFOs caused by a few entities with large accumulative or daily imbalances
  Limits some of the flexibility currently available in monthly balancing
  May reduce need to add storage resources to reduce OFOs, which would increase cost to all customers
Notes: This is another variation on the Status Quo

## Slide 42: Options: Add More Storage to PG&E’s Pipeline Balancing
Increase storage used to support PG&E’s monthly balancing option
  Balancing Storage Report provides analysis
Considerations
  May reduce OFOs, and customer related costs, provided added flexibility is not used by customers to increase imbalances via arbitrage opportunities
  Could reduce those times when PG&E exceeds current assigned storage limits in order to maintain pipeline operational integrity
  Increases the cost of providing current balancing service
  Benefits of added storage may not accrue uniformly to those paying the added costs
  May allow other storage providers to participate in providing balancing service
Notes: This is another variation on the Status Quo

## Slide 43: Options: Daily Auction for Balancing Resources
Use ISO Model to acquire daily balancing resources when needed
  PG&E forecasts daily imbalances and inventory position
  PG&E solicits daily, or as needed, market bids for balancing to control pipeline inventory
  Customers out of balance pay their share of the daily cost
Considerations
  Costly, complex bidding and settlement process required
  Use market to provide and price services
  Customers pay for what they use
  Price volatility likely when demand exceeds supply
  May create severe pipeline operational problems if market fails to provide needed physical relief

## Slide 44: Options: Require Daily Balancing for All Customers
Daily Balancing for All Customers
  Define daily balancing requirements, e.g. similar to self-balancing with tight daily and accumulative limits
  Storage providers, including PG&E, or others can provide services to meet customer balancing needs
Considerations
  Fully unbundled balancing service
    Customers pay for balancing services based on their decisions.
  High pipeline noncompliance charges likely to ensure protection of pipeline operational integrity and safety
  Reduces concern for future effectiveness of pipeline balancing services, e.g., increasing power plant usage
  Cost of balancing likely to be increase for some
  Rewards those who stay in daily balance
Notes: PG&E would develop an unbundled balancing service defined by the Gas Accord II