## Slide 1
Market Analysis Report
Anjali Sheffrin, Ph.D.
Director, Market Analysis
July 25, 2001

## Slide 2: I. Review of Energy, Ancillary, and Congestion Market Performance for June 2001 II. Special Issues Under Investigation and Analysis

## Slide 3: Market Overview
Average energy cost in CA markets was reduced by about 50% from May 2001
Two FERC order became effective for June 2001
  April 26 Order: effective May 29 – June 19: Price mitigation during emergency hours for CA spot markets
  June 19 Order: effective after June 20: Price mitigation expanded to all hours and entire WSCC spot markets
Lower load than June 2000 and increased supply helped moderate costs
  Conservation helped to keep load down
  New power plants brought on-line
  Generation outages reduced significantly (continue the trend from May 2001)
  Reduced natural gas price

## Slide 4
System Load and Average Unit Cost of Energy
Average energy costs since January 2001 based on weighted average of production cost of utility owned generation, and purchase prices of wholesale energy to meet “net short” load of California utility distribution companies (UDCs), and other non-UDC loads

## Slide 5
Significantly Reduced Load Compared With Last Year
(Growth Rates from same month prior year)

## Slide 6
Comparison of Loads - June 2001

## Slide 7
Significant Reduction in Generation Outages

## Slide 8
Reduced imports and hydro would have put pressure on higher cost, but reduced load more than covered those shortfall.
Avg. Hourly Energy by Source

## Slide 9
Average Hourly Energy by source
June 2000 vs. 2001
Reduced imports and hydro would have put pressure on higher cost, but reduced load more than covered those shortfall. As a result total gas fired generation is slightly less than June 2000.

## Slide 10
Net Imports
Peak Hours for (January through June) 2000 and 2001

## Slide 11
Net Imports
Off-peak Hours for (January through June) 2000 and 2001

## Slide 12
Natural Gas Spot Prices for Aug 2000 Through Present
So. Cal. Border and Henry Hub (No Transportation Costs)

## Slide 13
Comparison of Calif Border and National Natural Gas Spot Prices for Aug 2000 Through Present
PG&E Citygate and Henry Hub (No Transportation Costs)

## Slide 14: Significant Reduction in Wholesale Energy Cost and Competitive Baseline Price in June
Market power cost estimates are for the ‘net short’ energy requirement of California UDCs. Part of the net short energy is covered by long term contract which is not affected by the FERC price mitigation for the spot markets.
Price cost mark-up in both real time and spot markets have been reduced in June while the long term contract price kept the overall market power index high.

## Slide 15
Real Time Prices and Net Volumes - June 2001
Loads +
MCP
As-bid
BEEP
OOM
Effective Real Time
Unsch.
Peak
$72
$137
$76
$127
$117
29,966 GWh
37 GWh
0 GWh
37 GWh
504 GWh
541 GWh
2.6%
Off-peak
$49
$124
$53
$85
$78
22,472 GWh
27
1
28
116
144
-1.0%
All Hrs
$64
$136
$68
$113
$104
27,468 GWh
64
1
65
620
685
1.6%
Note: Effective real-time price is weighted average of MCP, As Bid, and OOM.
Dollar figures are $/MWh, Quantities are presented in GWh, and % represents percent
underscheduling. The above dollar values are the average of prices transacted in real-time
and do not represent the average cost of electricity.

## Slide 16: Significant Reduction in Price-Cost Mark-Up in ISO Real-Time Market in June 1 to 19 and further in June 20 to 30

## Slide 17: Regional Spot Market Prices (on-peak) Converge to Competitive Baseline Cost

## Slide 18
Out-of-market Purchases and Average Cost
December 2000 - June 2001

## Slide 19: Ancillary Services Markets and Congestion Management

## Slide 20
Summary for A/S Markets
June 2001

## Slide 21
Average Daily Regulation Up Prices
June 2001

## Slide 22
Average Daily Regulation Down Prices
June 2001

## Slide 23
Average Daily Spin Prices
June 2001

## Slide 24
Average Daily Non-Spin Prices
June 2001

## Slide 25
Average Daily Replacement Reserve Prices
June 2001

## Slide 26
Day Ahead Congestion - June 2000
Day Ahead Congestion - June 2001

## Slide 27
Total Congestion Costs
Day Ahead & Hour Ahead Markets
June 2001 vs. June 2000

## Slide 28
Path 15 Congestion Cost Summary Mar 2002

## Slide 29: Issues Under Investigation
DMA analysis for FERC settlement conference and refund proceeding
Monitoring and reporting to FERC regarding anti-competitive bidding practices
Bid insufficiency in regulation market
Implementation of must-offer procedure for units with long start-up time

## Slide 30: Insufficient Bids in Regulation Market
Insufficient Supply
  IOU participation has been limited due to insolvency issues.
    IOUs prefer to schedule their generation against their own load.
    IOUs concerned about creditworthiness in providing downward regulation.
  The method by which suppliers are paid for regulation energy may be reducing incentives to supply regulation.
    Current pricing approach settles regulation energy at the ISO Real-time Uninstructed Energy Price, which can be very volatile and risky.
High Demand for Regulation being driven in part by sub-optimal forward energy procurement.
  16 hour block forward energy purchases can create excessive energy imbalances across the shoulder hours of the day that must be offset by regulation energy given the absence of an efficient Imbalance Energy market.

## Slide 31: Regulation Market Performance Issue
High Demand and Insufficient Supply have reduced the competitiveness of the regulation market.
  Regulation market has been generally dominated by 2-3 Scheduling Coordinators.
  Market concentration is very high.
  In June 2001, a single SC set the day-ahead downward regulation price in over 50% of the total hours.

## Slide 32: ISO Efforts to Improve Regulation Market Performance
Efforts to increase regulation supply
  ISO is encouraging CERS to pursue long-term bilateral contracts for regulation capacity to reduce dependence on spot market.
  ISO is examining several alternative regulation energy payment methods that would provide greater energy price certainty and reduce risk.
Efforts to decrease regulation demand
  ISO is working with CERS to improve forward energy procurement practices to better match demand during the shoulder hours of the day.