## Slide 1: Transwestern Pipeline Company
Operations and Market Services Presentation to
Citizens Communications & Joint Owners (PP&L and Duke) of Griffith Power Plant
May 30, 2001

## Slide 2
Transwestern Pipeline Company System Map
San Juan
Basin
Panhandle
Permian
Basin
West Flow
Capacity to
California
1,090,000 MMBtu/d
San Juan
Lateral Capacity
850,000 MMBtu/d
Total System
Deliverability
2,000,0000 MMBtu/d

## Slide 3
Transwestern Pipeline Company West End Delivery Capacities
SoCal
Topock
(0)
Calpine
South Point
(90)
Mojave
(300)
PG&E
(400)
SoCal
Needles
(750/800)
Citizens
Griffith
Power
(120)
North
Star Steel
(3.5)
Southwest
Gas Corp.
(100)
Citizens
Kingman
(25)
California Deliveries
East of California

## Slide 4
Transwestern Pipeline Company

## Slide 5: Transwestern’s Recent Expansions
  Gallup Expansion (140,000 MMBtu/d)
    Placed into service May 2000
    Raised mainline west capacity to 1,090,000 MMBtu/d
  Red Rock Expansion (150,000 MMBtu/d)
    Filed for FERC certificate on March 30, 2001
    Expected in-service date of June 2001
    Will raise mainline west capacity to 1,240,000 MMBtu/d

## Slide 6: Transwestern’s Scheduling Process
Shippers nominate the volumes they want to flow
Operators confirm the amount of gas they want to Receive/Deliver
Transwestern evaluates capacities and current flows, then allocates accordingly
Scheduled numbers are available

## Slide 7: Nomination Services
Firm- Transportation from primary receipt points to primary delivery points under a rate schedule that is performed on a firm basis
  Alternate Firm Deliveries- Transportation from primary receipt points to alternate firm delivery points
Interruptible- Gas transported under this rate schedule is on an interruptible or as available basis when capacity exists on Transwestern’s system
Pooling- This service allows for the aggregation of receipts to logical point(s) or the disaggregation of a logical point(s) to multiple delivery points
Park-N-Ride (PNR) Service- An as available service that allows shippers to either borrow gas (Ride) or leave gas (Park) on Transwestern

## Slide 8: Nomination Deadlines
Transwestern has 6 cycles
11:30 a.m. Timely
6:00 p.m. Evening
7:30 a.m. Non-Grid AM*
10:00 a.m Intraday I
5:00 p.m. Intraday II
8:00 a.m. Final AM*
*Non GISB deadlines specific to Transwestern
(All times Central Clock Time)

## Slide 9: Non-GISB Cycles
These cycles are not recognized by all interconnecting operators
Non-Grid AM: This cycle is used by the shippers and operators to make any necessary changes before gas flow begins (9 AM current day).

## Slide 10: .
Final 8 AM: This cycle is used for after hours transactions approved by Gas Control which have been agreed upon by the shipper, the Receipt and Delivery point operator and Transwestern and have already started to physically flow
The scheduling paperwork to approve the transaction is completed before 8 AM the following day
Transwestern reserves the right to reject any transaction which occurs after the Intraday 2 process

## Slide 11: Nominations
Must be received by the stated deadline
Cannot be taken below Elapsed Pro-rata Scheduled Quantities once the gas day has begun
Screen used in the Hottap System is the Nomination Maintenance Screen
If system problems should occur while you are trying to input nominations, you can reach the Hottap Helpdesk at 1-800-421-6221

## Slide 12: Confirmation Deadlines
3:30 p.m. Timely
9:00 p.m. Evening
8:00 a.m. Non-Grid AM*
1:00 p.m. Intraday I
8:00 p.m. Intraday II
8:00 a.m. Final AM*
*Non-GISB deadlines specific to Transwestern
(All times Central Clock Time)

## Slide 13: Confirmations
This process gives Operators the opportunity to determine which shippers’ gas will flow
Confirmations must be completed before the stated deadline for each cycle
Confirmations are done in the Confirmation Maintenance Screen in Hottap
Operators can choose the method of confirmation which best suits their day to day business

## Slide 14: Operator Choice for Confirmations
Active Confirmation: The Operator must confirm all nominations on every cycle
Passive Confirmation: The Operator’s confirmation in Timely process will roll throughout the rest of the gas day and into the next gas day for the date range specified

## Slide 15
Confirmation by Exception: TW will automatically confirm ALL NOMINATIONS at a location. All confirmed quantities will equal nominated quantities for all cycles. Operators will be able to change any confirmation that is automatically confirmed by TW during any cycle. Any manual change will remain in place for the entire gas day or date range.

## Slide 16: Allocation Process
This process is run right after the confirmation process
The Hottap system identifies points, laterals and groups where transportation nominations exceed Transwestern capacity
Allocations are also administered to ensure pipeline integrity at interconnecting points

## Slide 17: Scheduled Quantities
Available after each process
Finalized at the end of the gas day (9:00 a.m. the following day)
Can be viewed by Operators in the Confirmation Maintenance Screen in Hotttap
Can be viewed by Shippers in the Scheduled Quantities Screen

## Slide 18: Measured Quantities
Finalized after the Measurement Close at the beginning of the following month
Measurement Estimates may be viewed, where available, throughout the current month in the Confirmations Summary Screen in Hottap
Scheduled Quantities v. Actual Quantities will be verified after the measurement close.
Volumetric differences shall be applied to the Operator Balancing Agreement (OBA)
Transwestern will send Operator a report of Scheduled Volumes, Actual Volumes.
Transwestern and Operator will work together to resolve any OBA imbalances pursuant to the Transwestern FERC Gas Tariff

## Slide 19: Exhibit “B” (Delivery Point Minimum Pressure Operating Parameters) Delivery Point Construction and Operations Agreement
Sets forth several Operating Scenarios for the plant with concomitant gas consumption rates (hourly, daily)
Transwestern will provide hourly take flexibility to the plant according to the scenarios described in Exhibit “B”
If plant requires additional flexibility, Transwestern shall use commercially reasonable efforts to provide, subject to availability of Transwestern system resources and competitive uses of resource (ex. Park-N-Ride or as available transport)