## Slide 1
Gas Accord II Workshop
Demand - Supply
Projections

## Slide 2: Today’s Agenda
Purpose of Presentation
Background
Forecast End-Use Demands
Analysis Process
Uncertainty Variables
Combined Uncertainty Analysis
Observations and Options

## Slide 3: Purpose of Presentation
Begin to identify the need and timing for new backbone pipeline capacity
Explain the major variables that drive the demand for backbone capacity, and their associated uncertainty

## Slide 4: Background

## Slide 5: Background
Historical storage capacity additions based primarily on meeting core winter season peaking supply needs, both peak day and over the winter season
  McDonald Island -- 1970’s
  Los Medanos -- 1980’s
New storage capacity has been market-based
  Wild Goose -- 1999
  Lodi -- 2001?
Backbone capacity additions have been infrequent and have been large
  Line 300 -- 1950’s
  Line 400 -- 1960’s
  Line 401 -- 1993

## Slide 6: Background (continued)
CPUC policy on backbone capacity additions driven by market considerations:
  No specific criteria for utilities
  Need based on slack capacity to promote gas-on-gas competition, e.g. 10 and 20% of cold year demand
  Timing based on “let the market decide” projects
Backbone supply delivery system should be sized to at least support local transmission capacity design to serve core under APD and all end-use demand under CWD

## Slide 7: Forecast End-Use Demands

## Slide 8: PG&E on-system demand will continue to increase
Recorded
Projected

## Slide 9: Gas demand for power generation is highly variable
Recorded
Forecast
190 MMcf/d

## Slide 10: Analysis Process

## Slide 11: Analysis Process
Identify variables that have greatest impact on demand for backbone gas supplies
  Short-term: Temperature, hydro, storage, off-system
  Long-term: Gas-fired electric generation forecasts
For each short-term variable, develop 3-5 potential scenarios with an associated probability of occurrence
For each long-term demand forecast, estimate the impact on demand for backbone supply for all possible combinations for all the short-term variables
Summarize the results into a probability distribution of demand for backbone supplies by month

## Slide 12: Uncertainty Variables

## Slide 13: Uncertainty Variables
(1) Temperature effect on Core demand
(2) Electric generation resource mix (e.g., hydro) effect on gas-fired electric generation demand
(3) Gas market (e.g., Malin-Topock price spread) effect on off-system throughput
(4) Underground storage market effect on injections into and withdrawals from storage
(5) Long-term outlook for gas demand
  Electric generation uncertainty
  Economic factors, e.g., economic growth, interest rates, energy prices, etc.

## Slide 14: Demand Variable #1: Temperature
Primarily correlated to space heating demand
Greatest impact during winter season
A 1-in-10 cold or warm winter would change core demands by an average of about 150-175 MMcf/day from November through February; about a 12% increase in the seasonal core demand
Analysis based on five historical weather patterns
  Probability
  1-in-10 Cold 10%
  1-in-5 Cold 20%
  Normal 50%
  1-in-5 Warm 20%
  1-in-10 Warm 10%

## Slide 15: Demand Variable #1: Temperature

## Slide 16: Demand Variable #2: EG Resource Mix

## Slide 17: Demand Variable #2: EG Resource Mix
Gas-fired EG tends to be marginal generation source
Year-to-year and month-to-month variation in resource mix drives gas-fired generation demand
Historical variability is about 400 MMcf/day on an annual average basis (500-900 MMcf/day)
Evolving electric generation market increases future variability
Three EG scenarios:
  Probability
  Normal 33%
  Wet 33%
  Dry 33%

## Slide 18: Demand Variable #2: EG Resource Mix

## Slide 19: Demand Variable #3: Off-System Demand
Affected by several factors:
  On-system demands
  Malin-Topock price differential
  Supplies coming in from SoCalGas, e.g., SoCal storage
Tends to vary seasonally
On-system load growth may reduce off-system flows over time
Three throughput scenarios used for analysis:
  Probability
  High 33%
  Medium 33%
  Low 33%

## Slide 20: Demand Variable #3: Off-System Demand

## Slide 21: Demand Variable #3: Off-System Demand

## Slide 22: Variable #4: Storage Injection/Withdrawal
Storage used for price arbitrage, reliability, and balancing
Traditional seasonal cycling may not persist, especially in the competitive noncore market
Increasing use of storage for price arbitrage and to meet summer demand peaks
New storage providers increase injection/withdrawal capacity, and thereby increase uncertainty of backbone throughput
  Analysis reflects assumed annual storage utilization profiles that includes Wild Goose and Lodi

## Slide 23: Variable #4: Storage Injection/Withdrawal
Little ability to predict how storage will be used in any given year
  Decisions made by the buyers of storage services
  Storage utilization increasingly driven by prices
Developed five potential profiles for analysis:
  Probability
  Status quo: seasonal cycle, about 60 Bcf 30%
  Double Peak: winter and summer 30%
  Expansion: seasonal cycle, about 80 Bcf 20%
  Double Peak + Expansion 10%
  Suppressed Cycle, about 35 Bcf 10%

## Slide 24: Variable #4: Storage Profile Scenarios
Injection
Withdrawal

## Slide 25: Variable #5: Long-term Growth Trends
Drivers include:
  Economic factors
  Development of electric generation market
  Regulatory framework/rules
Gas-fired electric generation currently seen as most uncertain over the next 5-10 years
Used two EG growth scenarios for analysis
  California Gas Report (CGR) forecast adjusted for BCAP settlement
  “High growth” scenario, about 2 to 2.5% growth/year

## Slide 26: Variable #5: Long-term Growth Trends
190 MMcf/d

## Slide 27: Combined Uncertainty Analysis

## Slide 28: Backbone Throughput versus Capacity

## Slide 29: Backbone Throughput versus Capacity: Higher Electric Generation Growth

## Slide 30: Higher EG Growth Case: Slack Capacity

## Slide 31: Higher EG Growth: Average Demand Related to Slack Capacity

## Slide 32: Observations and Options

## Slide 33: Observations
Growth in the gas-fired electric generation market will be the major factor in determining the size and timing of new gas system infrastructure
New backbone capacity and supply may well be needed within the next five years, or so
Lead time for adding new capacity is significant, probably 3 to 5 years, at a minimum
Requires coordination with upstream capacity additions
Will need to consider how new backbone capacity additions will be addressed in Gas Accord II

## Slide 34: Option: Build Backbone Capacity Additions Into Settlement
Agree on amount of slack capacity and added backbone capital costs which are reflected in the rates
Considerations:
  Considerable uncertainty in growth of EG gas demand
  Level of slack capacity needed
    Promotes gas-on-gas competition
    Moderates gas and electric commodity prices
  Improves supply reliability to meet uncertain future demands
  New capacity will need matching upstream capacity
  Cost impact of new capacity
  May still need a mechanism to address further capacity needs

## Slide 35: Option: Let Market Decide
Include mechanism to address backbone transmission capacity additions and rate increases
Considerations:
  Market tends to wait until constraints occur, which:
    Decreases reliability
    Increases commodity costs
    Reduces gas-on-gas competition
  What is PG&E’s obligation?
  Allows for uncertainty in need and timing of projects
  New capacity will need matching upstream capacity