## Slide 1: Draft 1/17/01 Commercial and Business Development

## Slide 2
System Map
16,500 Miles
4.3 Bcf/d Market Area Peak
2.0 Bcf/d Field Area Deliveries
59 Bcf Storage
Michigan
Texas
Oklahoma
Kansas
Missouri
Nebraska
South
Dakota
Wisconsin
Iowa
Illinois
North
Dakota
Montana
Wyoming
New Mexico
Minnesota
Market Area
Supply Area
Hugoton
Basin
Anadarko
Basin
Permian
Basin
Western
Canadian Basin
Rocky Mountain Basins
.
Gulf
Coast
Storage Locations
Notes: In addition to our growth opportunities, NNG continues to be a prominent player throughout the Midwest. Our Northern system serves as a key connection between Midwest utility customers and critical gas supplies to the north and south, providing our customers with supply optionality.
Northern Natural, with over 16,000 miles of pipe, is the largest single pipeline system in the U.S. and serves a market area in the upper Midwest, principally, Minneapolis, Wisconsin, Nebraska, Iowa and Illinois.
Northern is directly connected to the Permian, Anadarko and Hugoton supply basins in Texas, Oklahoma and Kansas. Through the Trailblazer pipeline system, which we have a 1/3 equity interest, we connect to supplies in the Rocky Mountains. And our NBPL system delivers up to 1.3 Bcf/D of Canadian supplies. This provides our customers with great supply options.
Northern also operates 56 Bcf of storage, providing shippers both physical and financial flexibility in managing their gas supply portfolios.
We are 95% contracted through 2003 in the market area. 85% revenues are fixed demand charges, and we have no rate case requirement through 2003.
We recently completed an open season for our market area to understand our customers needs for the future. We had non-bidding requests for over 300 MMcf/d of new capacity. We are working with customers to finalize deals.

## Slide 3
Gas
-
Fired
Generation
Other
219
New England
694
547
South Atlantic
292
Mid Atlantic
California/
Pacific Northwest
548
Total U.S.
2,665
146
South Central
North Central
Southwest
219
Gas Demand Growth
2000 - 2005 Increase (Bcf)
Source:
WEFA, Cambridge Energy, Enron Corp., Industry and Analyst Publications
Gas
-
Fired
Generation
Other
Gas
-
Fired
Generation
Other
Other
219
New England
694
547
South Atlantic
292
Mid Atlantic
California/
Pacific Northwest
548
Total U.S.
2,665
146
South Central
North Central
Southwest
219
North Central Region:
ND, MN, MI, WI, SD, IA, IL, IN, OH, NE, KS, MO
Northern Natural Gas Pipeline

## Slide 4: Market Area
NNG’s pipeline in the Market Area was built primarily as a delivery system integrated with the facilities of Local Distribution Companies with over 2,000 delivery points. This grid system is expensive to duplicate by competing parties.
Growth of natural gas usage by LDC’s in the Market Area is 1-2% per year.
Additional growth is expected with new construction of power and ethanol plants.

## Slide 5: Market Area Competitors
Major competitors in the Market Area:
Alliance
ANR Great Lakes
Natural Gas Pipeline
Northern Border
Trailblazer
Viking

## Slide 6: Traditional Market Area - Competitive Threats
Minnesota – Stable earnings through 2007.
Iowa – Lower value due to competing pipelines, but stable through 2005.
Wisconsin /Chicago – At risk in 2003. Market prices are below max tariff rates due to high concentration of competing pipelines.
Great Lakes
Northern Border
Alliance
ANR
Competitive Threat Areas
Notes: North end of NNG Pipeline
  Minnesota –(EF)
    Captive markets historically
    Physical assets go to town boarder – different than TW or FGT – more complex but helps keep out competition
    Contracted through 2007
  Iowa/Wisconsin – (ABC, D)
    Des Moines, East of Dubuque, Milwaukee
    Greater degree of competition
    Chicago pricing
South end
  Grid, multiple interconnects, supply oriented
  Depletion – declining reserves
  Selling non productive assets
  Cost allocation from South to North – becoming more of an issue – 2003 Rate Case issue
  Had success on pricing desk building business. - e.g.CMS/Reliant/Dominion Deal

## Slide 7: South End System
Built to connect traditional market area with MidContinent and Permian supply regions.
NNG is a transporter in the national pipeline grid with connections to multiple supply basins and interconnecting pipelines.
Short term contracts.
Wider Customer Base
Bi-directional flows
Notes: Used to own all of the gathering. When sold, dynamics of pipeline was changed.
History of Revenues:
$Millions | 1999 | 2000 | 2001 | 2002
Demarcation | 5.0 | 7.8 | 10.3 | 10.5
Total Pricing&St.r | 20.9 | 25.8 | 33.6 | 33.8

## Slide 8: Market Growth Strategies
Michigan
Project MAX: Market Area Expansion (See detail page 20)
Capture growth with minimal capital requirements
New gas fired power plants
Interconnect expansions for Market and Supply areas
Estimated demand growth is 1-2%
Viking
Storage
Northern Natural Pipeline
NNG Assets
Great Lakes
Trailblazer
Northern Border
Major Pipeline Interconnects
Texas
Oklahoma
Kansas
Missouri
Nebraska
South
Dakota
Wisconsin
Iowa
Illinois
North
Dakota
Montana
Wyoming
New Mexico
Minnesota
Market Area
Supply Area
Hugoton
Basin
Anadarko
Basin
Permian
Basin
Western
Canadian Basin
Rocky Mountain Basins
.
Notes: In addition to our growth opportunities, NNG continues to be a prominent player throughout the Midwest. Our Northern system serves as a key connection between Midwest utility customers and critical gas supplies to the north and south, providing our customers with supply optionality.
Northern Natural, with over 16,000 miles of pipe, is the largest single pipeline system in the U.S. and serves a market area in the upper Midwest, principally, Minneapolis, Wisconsin, Nebraska, Iowa and Illinois.
Northern is directly connected to the Permian, Anadarko and Hugoton supply basins in Texas, Oklahoma and Kansas. Through the Trailblazer pipeline system, which we have a 1/3 equity interest, we connect to supplies in the Rocky Mountains. And our NBPL system delivers up to 1.3 Bcf/D of Canadian supplies. This provides our customers with great supply options.
Northern also operates 56 Bcf of storage, providing shippers both physical and financial flexibility in managing their gas supply portfolios.
We are 95% contracted through 2003 in the market area. 85% revenues are fixed demand charges, and we have no rate case requirement through 2003.
We recently completed an open season for our market area to understand our customers needs for the future. We had non-bidding requests for over 300 MMcf/d of new capacity. We are working with customers to finalize deals.

## Slide 9: Supply Sources
Ample supply access to serve Major Utilities
and Industrials in the Upper Midwest

## Slide 10: Supply Area Trends
Michigan
Texas
Oklahoma
Kansas
Missouri
Nebraska
South
Dakota
Wisconsin
Iowa
Illinois
North
Dakota
Montana
Wyoming
New Mexico
Minnesota
Hugoton
Basin
Anadarko
Basin
Permian
Basin
Western
Canadian Basin
Rocky Mountain Basins
Source WEFA, INC Natural Gas Outlook 2001
Market Area
Supply Area

## Slide 11: Number of Customers by Type
Based on 12/2000-11/2001 Production Months

## Slide 12: Percent of Total Revenue by Customer Type
Based on 12/2000-11/2001 Production Months

## Slide 13: Contract Structure
Long Term contracts (TF) are typically held by LDC customers to serve residential, commercial and industrial customers behind the city gate. These contracts are primarily made up of annual and winter-month service periods. Long term contracts are typically executed in groups during rate case cycles. Customers holding long term contracts are predominately captive to the NNG system and pay maximum rates.
Short Term contracts are typically for daily and monthly periods (TF, TFX, TI). These contracts usually fill the need for marketing and producer groups to move gas on a short term basis. The customers are predominately non-captive and purchase transportation based on price spread opportunities over one or two seasons.

## Slide 14: Contract Structure
Rate Schedule
Description
Typical Use
TF
Firm Throughput Service
Used primarily by LDC markets made up of residential, commercial
and industrial users.
TFF is a service available for receipt in the Field Area and delivery
to the field/market demarcation point.
TFX
Firm Throughput Service
Available for Field and Market Areas with flexibility in term length
and monthly/seasonal quantities. Used primarily for short term firm
transportation.
TI
Interruptible Throughput Service
Available for Field and Market Areas on an interruptible basis.
GS-T
Firm Throughput Service -
Small Customer
Available for Market Area Small Customers with daily firm
entitlement of 5,500 mcf or less.
SMS
System Management Service -
No Notice Service
Available as a companion service to Firm Throughput Service and
provides no-notice firm delivery.
FDD
Firm Deferred Delivery -
Storage Service
Available for firm storage services. Provides shipper the ability to
have natural gas transported to or received from Northern on a
deferred basis.
IDD
Interruptible Deferred Delivery -
Storage Service
Available year-round for interruptible storage services. Provides
shipper the ability to have natural gas transported to or received
from Northern on a deferred basis.

## Slide 15: Revenue Sources
Firm Transport - Market
80%
Firm Transport - Field
7%
Interruptible Transport – Market
1%
Interruptible Transport - Field
1%
Storage
11%
Demand
84%
Commodity
16%

## Slide 16
Currently Under Contract
Contract Year Basis
2003 FDD: 22 Customers; 28 BCF
Transport: 72 Customers; 1.6 BCF/D
Expiration Dates for Reservation Revenues
Currently Under Contract
Contract Year Basis
$30.4
$141.5
$10.9
$20.4
$130.5
0
20
40
60
80
100
120
140
160
2003-4
2004-5
2005-6
2006-7
2007-8
millions
$
Market
Field
Storage
$ 95.0 Million Market Value
Notes: Above graph shows the $ value per contract year of contracts expiring in the respective years.
For example, the value of a full contract year for contracts expiring in 2003 = $141.5 million (coincident with rate case).
Of the $141.5 million, $12.4 million is from TFF of 287/d
Market Value is estimated at $95.0 million
Market $xx.x
Field $xx.x
Storage $xx.x
Lock in contract extensions b4 Rate Case

## Slide 17
Top 10 Shippers – Transportation Revenue
Contract Year
% of Revenue
2002-2005
45%
2006-2010
51%
2010-2013
3%
Rollover/Evergreen
1%
Top 10 - Expiration Data
Note:
For the Accounting Months of December 2000 through November 2001
Top 10 Customers represent 69% of total revenue for this time period.

## Slide 18: Historical Breakdown of Transport Revenue Firm/Interruptible
Notes:
Source: Commodity/Demand Margin Reports
2000 had increase in So Onshore due to volatility.
1999 had a one-time increase due to Seasonal Rates.
1998 was 16% warmer than previous year.

## Slide 19: Seasonality – Revenue/Volume
Source: MFE

## Slide 20: Project MAX Market Area eXpansion
Volume requests received during Open Season = 368,500 MMBtu/d
  Traditional growth = 176,500
  Electric generation = 192,000 (96,000 is uneconomical and will not be pursued)
Traditional growth is approximately a 4% increase in NNG’s current peak day market.
Requested volumes are staggered over a six-year period beginning in 2002 with the largest percent to begin in 2003.
Customer meetings are currently in progress
Precedent Agreements to be completed in February 2002
FERC filing scheduled to be filed prior to August 2002
Construction to begin Spring 2003

## Slide 21
Power Plant Expansions
•
•
•
•
Salt Valley
Lincoln Electric
159 MW
24,000 MMBtu/d-F
(2003)
Cass County
OPPD
330 MW
67,000 MMBtu/d-I
(2003)
Black Dog
NSP Generation
225 MW
35,000 MMBtu/d-I
(2003)
Inver Hills
NSP Generation
343 MW
70,000 MMBtu/d-I
(1999)
Cottage Grove
Cogentrix
240 MW
34,000 MMBtu/d-F
(1997)
Whitewater
Cogentrix
240 MW
30,000 MMBtu/d-F
(1997)
•
Pleasant Hill
MidAmerican
770 MW
180,000 MMbtu/d-F/I
(2003-5)
NPPD
250 MW
36,000 MMBtu/d-F
(2005)
Wisdom
Corn Belt
85 MW
16,000 MMBtu/d-I
(2004)
•
Alliant
800 MW
110,000 MMBtu/d-F/I
(2003-4)
•
•
Xcel
1035 MW
135,000 MMbtu/d-F/I
(2003-9)
Recent Plants
Proposed Plants
•
Potential additions of 737,000 Mmbtu/d
Additions represent about 200% of current connected gas fired generation.
Source: NewGEN and PowerDAT, 2002
Pleasant Valley
Great River Energy
445 MW
82,000 MMBtu/d-I
(2001)

## Slide 22
Ethanol Plant Expansions
-
•
•
•
Sioux Center IA
1,600 MMBtu/d
(9/01)
•
Denison, IA
2,400-
3,250 MMBtu/d
Earlville, IA
2,000 MMBtu/d
Columbia County, WI
3,000 MMBtu/d
Monroe, WI
4,000 MMBtu/d
Big Stone
Millbank, SD
1,500 MMBtu/d
Wentworth, SD
5,300 MMBtu/d
Rosholt
1,800 MMBtu/d
Heartland Corn
Winthrop MN
1,500 MMBtu/d
Minnesota Corn
13,000 MMBtu/d
Little Sioux, IA
4,500 MMBtu/d
(2002)
Galva, IA
2,400 MMBtu/d
(12/01)
Al Corn Clean Fuels
Austin, MN
1,500 MMBtu/d
Pro Corn LLC
Preston, MN
1,500 MMBtu/d
Agri Energy
Luverne, MN
1,200 MMBtu/d
•
Plants Being Built
Proposed Plants
Existing Direct Connects
Coon Rapids, IA
4,750 MMBtu/d
(2002)
Granite Falls, MN
3,000 MMBtu/d
Hardin County, IA
3,000 MMBtu/d
Potential additions of 58,000 Mmbtu/d
Seven additional plants at confidential locations are being considered. (40,000 MMBtu/d Total.)
Estimated 75% increase in ethanol production over the next two years. (California Energy Commission)