## Slide 1: Ensuring Generation Adequacy

## Slide 2: Ensuring Generation Adequacy
Replacing old regulatory assurances
ICAP in the Northeast before deregulation
ICAP after deregulation
Can generators survive without ICAP?
Promoting reliability through surplus capacity

## Slide 3: Reliability Assurances in Regulated Markets
Integrated Resource Plans
  Difficult to maintain in competitive environment
  Suppliers can’t project market share with enough certainty to make capacity projections meaningful

## Slide 4: New Reliability Assurances
Supply will respond to price signals
  But, will the response be quick enough to avoid California-type disasters?
Northeast power pools attempted to transform Reserve Sharing Arrangements into Reliability Assurance and implemented Installed Capacity (“ICAP”) obligations (ICAP after deregulation)

## Slide 5: Is ICAP Effective?
Two of ten NERC regions are using ICAP, and one (NY) faces potential blackouts in Summer 2001
Before California, MAAC and NPCC have had the most blackouts
Seven of eight regions without ICAP have adequate supply

## Slide 6: How Much Does ICAP Cost Retail Customers?
PJM last year
  1.1 cents/kWh on average
New York City
  1.8 cents/kWh
New England
  1.1 cents/kWh

## Slide 7: What Do We Get For ICAP $?
4,600 MW to maintain 15% Reserve

## Slide 8: Who Receives ICAP Payments?

## Slide 9: How Much Does ICAP Cost Retail Customers?
PJM
Less than 0.1¢/kWh of 1.1¢/kWh ICAP payment goes to new generators

## Slide 10: Do Existing Generators Need ICAP?
Can generators cover fixed and variable expenses through firm energy sales?
Are subsidies necessary to keep generators from going away when spot energy prices are low?
ICAP proponents warn of a “revenue gap”.

## Slide 11
How do generators make money?
Maximum Possible Contribution to Fixed Cost from Energy Market
(Example Unit w/ $40/MWH Variable Cost)
0
50
100
150
200
250
300
Energy Market Price ($/MWH)
Maximum Total Possible
Contribution Toward Fixed Cost
Total Variable Cost
Hours Resource Not Operating
(Energy Market Price < Bid)
40
Energy Bid
(Set Equal to Variable Cost)
Hours Resource Operating
(Energy Market Price > Bid)
Revenue gap from energy market revenues? Not really. Option value compensates more than enough.

## Slide 12
Generators create revenue by:
Commonly Understood Methods
  Selling into the spot market
  Uplift charges
  Ancillary Services
Little-Known Methods
  Selling into the forward market
  Optimizing sales through portfolio management techniques
  Extracting the option value of the generator by “range trading” around the variable cost of production, among other methods. Let’s review this method.

## Slide 13: Option Value
Generators have an option, in real-time, to generate or not to generate
  This flexibility is extremely valuable both in the forward markets and in the hourly markets
  The following two slides illustrate a very simple approach to extract this value

## Slide 14
30
32
34
36
38
40
42
44
46
48
9/16/98
9/30/98
10/14/98
10/28/98
11/11/98
11/25/98
12/9/98
12/23/98
1/6/99
1/20/99
2/3/99
2/17/99
3/3/99
3/17/99
3/31/99
4/14/99
4/28/99
5/12/99
5/26/99
6/9/99
6/23/99
30
32
34
36
38
40
42
44
46
48
Explaining Option Value:
Cinergy Sep ’99 Contract
Selling at The Peak Yields $8/MWh
Variable Cost
Timing the market perfectly to extract this
$8/MWh is nearly impossible
Notes: Many people believe that the generator will lose money if the spot price for energy in September is below the generator’s variable cost of generation because the generator will incur fixed costs without generating any revenues.
This chart shows that, for much of the year before September ’99, the forward price was above this generator’s variable cost. If the generator timed it right, it could have sold power for September ’99 in October ’98 for almost $46/MWh, locking in a contribution margin of nearly $8/MWh.
Of course, it is difficult to time the market perfectly, but this is only part of the story.

## Slide 15
Explaining Option Value:
Cinergy Sep ’99 Contract
Selling around bandwidth yields $17
This approach is simple and yields much greater value.
Notes: By setting up a trading range around the unit’s cost, the generator can sell at $38 and buy back at $35 locking in $3 margin without even running. This way, the generator maintains its option to run in the daily market if prices exceed the cost to run in September ’99.
Of course, there is plenty of time and volatility in the market to continue “flipping” positions. If the generator sells a second time at $38, it still has the option to run the plant to satisfy the sale, but it could decide to purchase in the market if prices in September are lower than its cost to generate. Importantly, the generator has this option on an hourly basis, creating a great deal of opportunity to increase contributions to margin.
In this example using real price data, the generator could lock in $17/MWh, or $1.7 cents/kWh before September even arrives, and September has opportunity to contribute much more to the generator’s bottom line. And this is using a fairly narrow trading bandwidth.
This is how generators and marketers extract value from the options that are embedded in generation by the nature of their function. An hourly option is extremely valuable. In fact, hourly options are so valuable that, if you could buy one, its price could exceed the price of power.

## Slide 16: Generators Extracting Value
This approach to extracting value to help pay the fixed costs of a generator is a simple method showing how generators can create value
  Even in a low-volatility month like September
  Using narrow, conservative trading ranges
  No risk
$17/MWh for one month translates to $70/kW-year from this tool alone

## Slide 17: Examples We’ve Seen
The next two slides show examples used by proponents of ICAP to explain why they need ICAP subsidies
  Example 1: base-load, gas-fired plant
  Example 2: peaking plant

## Slide 18
Incomplete Example 1
Excludes Option Value
Fixed cost requirement (levelized)
Expected net revenues:
  energy market
  uplift
  ancillary services
  total
revenue gap
$95 - $140 per kw-yr
$50 - $70 per kw-yr1
$1 - $1.5 per kw-yr2
$2 - $2.5 per kw-yr3
$53 - $74 kw-yr
$21 - $87 kw-yr
500 MW gas-fired combined cycle
less
equals
However, our example showed September returning $17/MWh which translates to $5.78/kW-month. The same return over 12 months is $69.36, and that doesn’t even count off-peak hours and Saturdays! Obviously, this covers the “revenue gap”.

## Slide 19
Fixed cost requirement (levelized)
Expected net revenues:
  energy market
  uplift
  ancillary services
  total
revenue gap
$60 - $90 per kw-yr
$25 - $40 per kw-yr1
$0.5 - $1 per kw-yr2
$2.5 - $3 per kw-yr3
$28 - $44 kw-yr
$16 - $62 kw-yr
125 MW gas-fired combustion turbine
Here, the burden is even smaller. Clearly, the $70 contribution of the option value covers the “revenue gap”.
less
equals
Incomplete Example 2
Excludes Option Value

## Slide 20: Will All Generators Turn Profits Without ICAP?
Maybe not
  Some may not be sophisticated enough to employ simple portfolio management techniques
Still, generating equipment will not disappear
  Owners will learn how to manage better, or will sell to someone who can create more value

## Slide 21
ICAP Is Not Needed
Capacity market is not needed to assure adequate entry of new generation capacity for reliability purposes
ICAP is anticompetitive – it artificially sustains weak competitors

## Slide 22: If Policy Makers Must Subsidize
Not convinced that new generation will be built without subsidy?
Not willing to risk that markets will react quickly enough to prevent California-type disaster?
Then limit subsidies to new generators.

## Slide 23: Guarantee Payment Only to New Generators
Pay new generators $50/kW per year for the first five years of operation
Fund through surcharge of $0.002/kWh to all customers through a $1.50/MWh charge to all suppliers that schedule through the ISO for delivery to retail customers
Apply only when reserves drop below 15%

## Slide 24: Benefits of Retail Choice If Not For ICAP

## Slide 25: Current ICAP Steals the Benefits of Retail Choice
Capacity Credit Charges Absorb the
Benefits of Competition
0
1
2
3
4
5
6
7
Year
1
2
3
4
5
6
7
8
9
10
Capacity Credits
Wholesale Energy Price
ICAP prices increase to absorb the benefit as
wholesale prices fall, up to the deficiency rate
Capped Utility Rate

## Slide 26: 1. Customers Benefit When Prices Fall 2. Revenue Continues When Prices Rise

## Slide 27: Summary
Policy makers service reliability & price stability
ICAP currently is too expensive
Existing generators don’t need ICAP
New generation can be encouraged at much lower cost to customers if payments are directed to new generators only