## Slide 1
787
993
935
31.92 mi
15.44 mi
47.36 mi
10.96 mi
30”
30”
BLOOMFIELD C.S.
PIPELINE
PIPELINE PRESSURE IN P.S.I.G.
COMPRESSOR STATION
7
970
LEGEND
4
5
BISTI C.S.
LA PLATA “A” C.S.
750
993
880
977
1192
1200
36.36 mi
60.47 mi
33.4 mi
30”
30”
30”
TRANSWESTERN PIPELINE COMPANY
DOCKET NO. CP01-
EXHIBIT G
FLOW DIAGRAM OF EXISTING FACILITIES
DAILY DESIGN CAPACITY (SUMMER DAY)
GALLUP C.S.
763
950
COMPRESSOR STATION NUMBER
NUMBER OF COMPRESSOR UNITS
CENTRIFUGAL
RECIPROCATING
HORSEPOWER INSTALLED
NAMEPLATE RATED
SITE RATED
HORSEPOWER REQUIRED
FUEL GAS
COMPRESSOR FUEL MCFD
OTHER COMPANY USE MCFD
SUCTION PRESSURE
DISCHARGE PRESSURE
COMPRESSOR RATIO
VOLUME COMPRESSED MCFD
4 La Plata “A” Bloomfield Bisti Gallup
Low High
0 2 1 3 1 1
3 0 0 0 0 0
12,000 12,500 7,000 21,000 10,000 10,000
12,000 8,250 4,400 15,800 10,000 10,000
11,300 8,250 4,400 15,152 9,039 10,000
2,260 1,815 968 1,794 0 0
60 50 0 50 50 50
787 750 650 880 975 763
993 993 880 1192 1200 950
1.26 1.32 1.35 1.36 1.23 1.24
1,106,703 500,000 250,000 850,100 850,050 850,000
Notes: 2

## Slide 2
808
1005
963
31.92 mi
15.44 mi
47.36 mi
10.96 mi
30”
30”
BLOOMFIELD C.S.
PIPELINE
PIPELINE PRESSURE IN P.S.I.G.
COMPRESSOR STATION
7
970
LEGEND
4
5
BISTI C.S.
LA PLATA “A” C.S.
750
993
880
964
1187
1200
36.36 mi
60.47 mi
33.4 mi
30”
30”
30”
TRANSWESTERN PIPELINE COMPANY
DOCKET NO. CP01-
EXHIBIT G
FLOW DIAGRAM OF PROPOSED FACILITIES
DAILY DESIGN CAPACITY (SUMMER DAY)
GALLUP C.S.
748
970
COMPRESSOR STATION NUMBER
NUMBER OF COMPRESSOR UNITS
CENTRIFUGAL
RECIPROCATING
HORSEPOWER INSTALLED
NAMEPLATE RATED
SITE RATED
HORSEPOWER REQUIRED
FUEL GAS
COMPRESSOR FUEL MCFD
OTHER COMPANY USE MCFD
SUCTION PRESSURE
DISCHARGE PRESSURE
COMPRESSOR RATIO
VOLUME COMPRESSED MCFD
4 La Plata “A” Bloomfield Bisti Gallup
Low High
0 2 1 3 1 1
3 0 0 0 0 0
12,000 12,500 7,000 21,000 10,000 12,500
12,000 8,250 4,400 15,800 10,000 12,500
10,925 8,250 4,400 15,152 9,302 11,397
2,185 1,815 968 1,794 0 0
60 50 0 50 50 50
808 750 650 880 964 748
1005 993 880 1187 1200 970
1.24 1.32 1.34 1.35 1.24 1.29
1,137,143 500,000 250,000 860,100 860,050 860,000
Notes: 2