## Slide 1: Enron North America Florida Merchant Power Plant
July 5, 2000

## Slide 2: Project Development Overview Florida Power Plant
  Installation of an approximate 279 MW (91ºF and 65º humidity, natural gas operations) simple cycle peaker at one of three potential locations in SE Florida.
  Estimated project development budget of $3 million.
  Multiple site development to hedge development risk and create generation/origination optionality.
  Targeted commercial operations is June 1, 2001.
  First market mover advantage - no prior merchant IPPs constructed in Florida to date.
  Take advantage of short generation supply and recent market volatility in Florida market through summer 2003.
  Optionality of transmission along entire Eastern U.S.
  Option to expand into combined cycle and increase capacity by roughly 75 MW with installation of STG.
  Exit Strategy: sale to GENCO or 3rd party developer.
  Locations in order of priority: Broward, Medley-Dunn, and Midway. Land option term will allow for continued development optionality through 2002.
  Two additional sites under control for development by summer 2002.
  Sites in other states (i.e. LA and MO) being pursued in part as hedges for Florida development risk.
Project Description
Strategy

## Slide 3
Project Development Critical Path Issues Florida Power Plant
FPL is not likely to cooperate on electrical interconnection and has been historically successful in blocking merchant IPPs in Florida.
Rezoning and land use approvals will take at least 4-6 months at each site. Public comment is likely.
Best case construction schedule as a result of the above is 4-5 months assuming a June 1 start.

## Slide 4
FP&L Interconnect Request Queue Florida Power Plant
Based on the best available information at time of publication.

## Slide 5
Florida Curve Scenarios
Florida Power Plant
* Capex of $161 MM amortized over 30 years with 10% residual value and 7% interest.

## Slide 6
Estimated Construction Budget Florida Power Plant

## Slide 7
Florida Development Budget Florida Power Plant

## Slide 8: Equipment: 6 GE LM6000 turbines with enhanced SPRINT
* Run hours are based on non-PSD emission limits of 250 tons/year which applies to simple cycle plants.

## Slide 9
Project Details - June 2001 Target Sites Florida Power Plant

## Slide 10
Site / Acre
Option Term & Premium
Exercise Price
Air Permit
Gas Interconnect
Power Interconnect
Water Supply
Corbett
1-year lease with option to
extend lease through year
2/$56,250 every 3 months
during year 1
$2.5 - 3.0 MM based on $125,000/acre in yr 1 and $150,000 in yr. 2
Application to
be submitted
7/00, results
expected 10/00
Proposed 12-mile NUI
pipeline<.5 miles from
site, expected
completion in late 2001
230 kV line<1000 feet
from site, study requested
6/9/00
Goundwater from
Surficial aquifer at
200 feet
underground
Homestead
3-twelve month option periods.
Option premium: $40K/year for
each of the first two 12 month
periods, $50K for the last 12
month period
$1.1 - 1.2 MM based on $30,000/acre in yr. 1 and $33,000/acre in yr. 2.
Application to
be submitted
7/00, results
expected 10/00
FGT's 18'' pipeline is
within 2 miles of the
site
230 kV line<1 mile from
site, study requested
6/9/00
Groundwater from
Floridian aquifer.
Capex will be in
excess of .5 MM.
Project Details - June 2002 Target Sites Florida Power Plant

## Slide 11: Florida Supply/Demand Issues Florida Power Plant