## Slide 1: Modeling Markets and Behavior: Oligopoly Market Models Applied to ERCOT
Presentation to IEEE PES
By: Lance B. Cunningham, PE
July 18, 2001
Enron Quantitative Research Group

## Slide 2: Legal Disclaimer
This work originated at The University of Texas at Austin. The views presented here are not necessarily attributable to the author’s current employer, previous employers, or The University of Texas at Austin. Any remaining errors are the sole responsibility of the author. A supporting paper, “An Empirical Study of Applied Game Theory: Transmission Constrained Cournot Behavior” (2000TR761) is currently under review by the IEEE Power Engineering Society, the Power System Analysis, Computing and Economics Committee. The paper is co-authored with Ross Baldick and Martin Baughman.

## Slide 3: Presentation Overview
Introduction
3 bus system
ERCOT study

## Slide 4: Introduction and Background

## Slide 5: Definition of Perfect Competition
Firms produce homogenous products
Divisible
No barriers to entry or exit
Consumers have price information
Suppliers and consumers are price takers

## Slide 6: Monopoly Definition
Only one supplier
Product has no close substitute
Set price above marginal cost

## Slide 7: Oligopoly Definition (Imperfect Competition)
Small number of firms
Act independently
One firm’s actions impact all others

## Slide 8: Oligopoly
  Cournot models the quantity as the strategic variable

## Slide 9: Definition of Market Power
A company has sufficient ability to impact market price and thus is able to charge above marginal cost.

## Slide 10: Market Power and Stranded Cost
California a consideration
Texas, SB 7 limits ownership
Auction off 15% of capacity rights
Texas SB 7 requires a rate freeze until 2002
  10% retail rate reduction
Market price used for stranded cost
Contracts or costs projected above market price
SB 7, PUC ECOM model

## Slide 11: Key Findings
Cournot
  Transmission constraint above unconstrained flow disrupts equilibrium.
ERCOT, new entrants
  Reduce price for competitive and strategic behavior.
  Large capacities may be uneconomical.
Strategic behavior will impact transmission operations and planning.

## Slide 12: Overview of Analysis
Three Bus
    Competitive
    Cournot
ERCOT case study
    Competitive
    Cournot
    Impact of new entrants

## Slide 13: Three Utility Case Study System
Three Utilities
  Three types of units
  Nuclear, coal, gas
  Variable cost defined by fuel and dispatch
Three transmission lines
  Lossless
  Equal impedance

## Slide 14: Perfect Competition Transmission Unconstrained Results

## Slide 15: Perfect Competition Transmission Constrained Results (transmission line T2 constrained to 5 MW bidirectionally)

## Slide 16: Results of the Competitive Market
Transmission unconstrained provides the lowest uniform price compared to following market behaviors.
There is no price mark up above marginal cost.
All utilities have equal marginal cost, transmission unconstrained.
No deadweight loss.

## Slide 17: Cournot Behavior
Each firm chooses its output quantity
Assumption, rival’s outputs are fixed
Considers the effect of its decision on the price

## Slide 18: Typical Cournot best response functions for two players

## Slide 19: Cournot Transmission Unconstrained Best Response Functions
j
k

l

(
)
a
b

c

(
)

d
e

f

(
)

g
h

i

(
)

Unconstrained best responses
  Flat
  No bends or kinks

## Slide 20: Cournot Transmission Unconstrained Results
Strategic behavior has altered both price and line flows

## Slide 21: Cournot Transmission Constrained Results for T1 constrained uni-directionally
Consider line flow constrained in one direction

## Slide 22: Cournot Transmission Constrained Results for T1 constrained uni-directionally to 100 MW
Utility A’s best response, two regions
Region one, identical to the unconstrained best response.
Region two is formed because of the 100 MW constraint.

## Slide 23: Cournot Transmission Constrained Results for T1 constrained bi-directionally to 100 MW
Utilities A and C, complimentary best response shapes, due to the bi-directional constraint.
Cournot equilibrium exists.

## Slide 24: Cournot Transmission Constrained Results for T1 constrained bi-directionally to 66 MW
Utilities B and C best response surfaces pass through the unconstrained Cournot equilibrium point.
Utility A’s best response “jumps” from region three to region four before the unconstrained point.
The existence of a transmission constraint that exceeds the value of the unconstrained line flow has disrupted the pure strategy equilibrium.

## Slide 25: Key Findings of Cournot Behavior in the Presence of Transmission Constraints
Equilibrium can exist with 3 strategic players.
Behavioral change even if the equilibrium flow in the absence of the constraint is significantly less than the transmission limit.

## Slide 26: ERCOT case study
Transmission unconstrained & constrained
  Competitive
  Cournot
  Impact of new entrants

## Slide 27: ERCOT case study
ERCOT summer 2001 summer peak power flow CSC planning case

## Slide 28: ERCOT case study assumptions
Fuel cost $3.15/MBtu
Three different cost curves that correspond to unit commitment to meet load
7.5% outage rate

## Slide 29: ERCOT case study, reduced system equivalent - Pure competition

## Slide 30: ERCOT case study, Cournot transmission unconstrained
BRAEP
BRTXU
BRReliant/CBSP
Cournot Equilibrium

## Slide 31: ERCOT case study, Cournot transmission unconstrained
The Cournot solution results in a mark-up of $67.15/MWh above the fully competitive price, a price markup of 169%.
Gen
Profit
Price
TXU
12,921
1,082,791
106.88
Reliant + CPSB
13,262
1,226,898
106.89
AEP
7,518
565,405
106.89
Others
10,694
798,972
106.89
44,395

## Slide 32: ERCOT case study, Cournot transmission unconstrained load flow

## Slide 33: ERCOT case study, Cournot transmission constrained scenario
TXU
G
G
G
G
Others
AEP
Reliant
1
2
3
4
5
6
Bidirectional
Constraint

## Slide 34: ERCOT case study, Cournot line T4 constrained to 3700 MW bi-directional
TXU
BRTXU
BRReliant/CPSB
AEP

## Slide 35: ERCOT case study, Cournot line T4 constrained bi-directional
Results of transmission constrained case is that a pure strategy Cournot equilibrium is likely not to exist at the actual operating limit of the North to South constraint.
Extrapolating from the previous 3 bus model, a Stackelberg equilibrium could potentially exist given that there are clear market leaders in ERCOT zones.

## Slide 36: ERCOT case study, impact of new market entrants
California, no new capacity added
Will new entrants add discipline to market to reduce potential market power?
18,000 MW of new generation announced.
  Study 10%, 20%, 40%, 60%, 80% and 100%

## Slide 37: ERCOT case study, impact of new market entrants, Cournot and competitive price scenario comparison, transmission unconstrained
Peak load only

## Slide 38: ERCOT case study, impact of new market entrants, non-peak analysis
10% of announced new entrant capacity
20% of announced new entrant capacity
40% of announced new entrant capacity
Solution presents a dichotomy, new entrants reduce prices both competitively and strategically but over 42% announced capacity fail to make profit annually

## Slide 39: Percent of load and hours

## Slide 40: Sample cost curves

## Slide 41: Comparison of Cournot across load ranges
Price Comparison
Annual % Profit Comparison compared to competitive solution as a baseline

## Slide 42: ERCOT case study, impact of new market entrants, Profit Comparison
Single plant profitable
Above  % announced capacity is not profitable

## Slide 43: ERCOT Case Study Summary Remarks
Equivalent model has numerically shown that with no constraints, strategic behavior is possible.
Because of zone definitions in ERCOT, the lack of a pure strategy Cournot equilibrium does not rule out the possibility of a Stackelberg equilibrium.
Stranded cost can potentially create an uneven playing field between incumbents and entrants, perplexing regulators and legislators alike. Competing goals to encourage new entry to reduce cost and strategic behavior but trade off profit.
A large amount of new entry could potentially reduce the difference between the competitive and strategic price.

## Slide 44: Historical ERCOT Prices Compared to Houston Ship Channel

## Slide 45: Key Literature
Borenstein, Bushnell and Stoft (1997)
  Two utility duopoly system using Cournot.
  California electricity market based on a duopoly.
  Conclusion: generator limit output can potentially create congestion
Younes and Ilic (1998)
  Cournot, Bertrand, and supply functions.
  Conclusion: transmission line congestion creates sub-markets that could encourage strategic behavior.

## Slide 46: Key Literature
Stoft (1999)
  Demand curve that is limited by transmission.
  Economic profit function includes transmission congestion contracts (TCCs).
    Transmission congestion contracts are financial instruments that represent tradable transmission rights and pay the owner the difference between two nodal prices.
Berry, Hobbs, Meroney, O’Neill and Stewart (1999)
  Competitive and imperfectly competitive markets.
  Focus: price and profit impacts to holders of TCCs.

## Slide 47: Key Literature
Borenstein, Bushnell and Stoft (1999)
  California electricity market modeled all generators with pipeline model (no loop flows)
  Conclusion: potential exists in California market for strategic behavior