## Slide 1: (How) Can The California Electricity Market Be Saved?
John D. Chandley
Power Crisis in the West
INFOCAST Conference, San Diego
February 13, 2001

## Slide 2: Disclaimer
John Chandley is a Principal at LECG and a member of the LECG electricity market design group, led by Harvard’s William Hogan and LECG’s Scott Harvey, based in Cambridge. The members of this group have been involved in the development of market design and pricing rules for several eastern markets, including those in PJM, New York, New England and Ontario. The group is also engaged in the development of market rules for emerging RTOs in the Midwest and the Southwest Power Pool. The group has advised utilities, regulators, emerging RTOs and other clients throughout the country and in New Zealand, Australia and elsewhere.
The views expressed here are solely those of the author and do not necessarily reflect the positions of any of the clients or LECG.
John D. Chandley
617 761-0118 John_Chandley@lecg.com

## Slide 3: What Did FERC’s December 15, 2000 Order Find?
FERC’s Order sought to address both the structural defects in the California market and the high prices resulting from those defects.
FERC concluded that a combination of poor market structure and design, genuine supply shortages, high operating costs and the possible exercise of market power were leading to prices that were not “just and reasonable.”
Supply shortages resulted from:
  Rapid demand growth from rapid economic expansion in the West
  Failure to build new capacity during the 1990s
  Low hydro availability in California and the Northwest
  High outages resulting from running an aging generation fleet
High operating costs driven by very high prices for natural gas and NOx emission credits (in SCAQMD) inevitably led to extremely high prices.

## Slide 4: What Did FERC’s Order Find?
FERC also found that California’s extremely high prices were partly caused by faulty market structure and design. In particular, FERC found:
  An excessive reliance by all parties on the volatile “spot markets”
  A mandatory state requirement that utilities buy all of their needs from the PX and sell all of their generation into the PX
  An inability to hedge spot market “volatility” through long-run contracts
  Restrictions on the ability to use utility-owned generation to offset reliance on high market prices
  Reliance on a single-price auction and market-clearing prices
Given this diagnosis, the remedy was clear: Destroy the spot market and force everyone into almost exclusive reliance on contracts. But was the diagnosis correct?

## Slide 5: Did FERC Get it Right? -- Limit the spot market?
“Excessive” reliance on spot markets is not a defect; it is a symptom. Imposing restrictions/penalties on its use will just cause problems. Parties rely on spot markets whenever:
  They are forced to do so (mandatory buy/sell), or they are otherwise discouraged from contracting forward
  Inconsistent pricing rules encourage them to do so
    Loads might “underschedule” in the PX to get ISO price cap protection
    Loads might be forced into the ISO real-time market if sellers’ offer prices in the PX and forward markets appear too high
  They need to sell uncontracted supply or cover extra demand, or just cover imbalances -- an essential tool to support trading
Lesson from PJM and NY: There are no restrictions on the use of the spot market and no problems with “underscheduling.” Parties are free to contract forward and/or rely on the spot market to any degree they want, given their commercial needs.

## Slide 6: Did FERC Get it Right? -- Abolish the PX?
FERC threw the baby out with the bath water.
  It abolished the utilities’ mandatory buy/sell requirement
  It suspended the entire PX tariff -- thus killing the PX
  It killed the PX’s bid-based day-ahead and hour-ahead markets
There never was a valid justification for separating the PX from the ISO.
The mandatory buy/sell rule could have been lifted without destroying the day-ahead and hour-ahead markets.
Lessons from the Eastern markets: The NY and PJM ISOs operate bid-based day-ahead markets that are coordinated with the ISO real-time spot (balancing) markets. Pricing, dispatch and congestion management are consistent between the forward and real-time markets. New England is developing the same model, with FERC’s endorsement.

## Slide 7: Did FERC Get it Right? -- Counting IOU energy
FERC mistakenly thought it found a pot of money to reduce rates: Sell power from IOU generators to their loads at cost.
FERC did not understand how California accounts for the value of utility-owned generation. Although the CPUC rules are arcane and still under debate, the ultimate accounting rule was never in doubt:
  The market prices received by IOU generators will be credited against the prices paid to serve IOU loads.
FERC “found” money that California had already counted. Thus, FERC’s order “returning” utility-owned generation to state PUC control accomplished nothing. Yet FERC said this was their major contribution to lowering prices in California!

## Slide 8: Did FERC Get it Right? Pay as bid?
FERC made the classic mistake in forcing the ISO and PX to use a pay-as-bid pricing scheme.
Paying generators the price they bid, rather than a “market-clearing” price will probably not save a dime.
Most economists teach that in a “pay-as-bid” auction format, bidders will change their bids, trying to capture the market-clearing price (or their opportunity cost). In a “pay-as-bid” regime:
  Bidders have no incentive to bid their marginal running costs
  Bidders with lower marginal costs will tend to raise their bids so that they too can receive the prices paid to those with the highest marginal costs. This has already hit the ISO.
Lessons from PJM and NY (and NZ, Aust, Chile, etc): Paying bidders the market-clearing price works fine: They tend to bid at or close to their marginal operating costs. There is substantially less bid “gaming.”

## Slide 9: The Challenge of Market Design
Designing electricity markets that work well is proving to be far more challenging than many thought (or feared). Among many reasons:
  Electricity markets can’t define themselves -- the need for central coordination of short-run operations means that someone (who?) has to write the rules for how this coordination occurs.
  No one (or everyone) is in charge -- FERC, NERC, state regulators, politicians, and many stakeholder working groups want to decide.
  There is limited operating experience, and the lessons are (endlessly) debatable. Is the UK the model? California? PJM?
  In most regions, self-interested stakeholders naturally seek to fashion rules that favor their interests. Even “balanced” stakeholder groups and boards are suspect. What is “balanced”?
  Design and pricing issues can be quite complex. How should congestion be priced? How should market power be mitigated?

## Slide 10: Market Design by Sound Bite
Market design can be driven by simplistic slogans that may turn out to be misleading. My (partial, growing) list for the most misleading sound bites:
  “The RTO should focus exclusively on reliability and stay out of the market.” -- Does this mean that the RTO should not use voluntary market bids to arrange/price the dispatch that keeps the lights on?
  “The RTO should focus on transmission and stay out of energy.” -- Same question. Isn’t arranging and pricing the RT dispatch -- injecting and selling energy here and withdrawing and buying it there -- closely related to defining/pricing transmission use?
  “Limiting access to the RTO’s coordinated trading will lead to more efficient markets.” How do you square that with the need for central coordination of short-run operations?
  “If you simplify the market/pricing, it will work better.” So why is the ISO always intervening in these “simple” markets?

## Slide 11: Defining the Core Principles
Despite real concerns in many regions -- given California experience --electricity markets can be designed to work reasonably well.
Successful markets seem to have been designed around certain core principles and a number of important market design objectives. E.g.:
  The public interest in an efficient market is the overall design objective
  Giving participants open access to the RTO’s short-run coordinated markets is the foundation for well-functioning markets.
  Pricing the short-run markets efficiently is essential.
  Getting the transmission (congestion) prices right is critical.
  Pay attention to the market rules -- the details matter.
What follows is a partial list of key market design lessons gathered from market experience in the US and elsewhere.

## Slide 12: 1. Do a really good job in arranging an economic dispatch.
An efficient balancing/spot market is essential to any well-functioning electricity market. In electricity, the real-time spot market flows from the real-time dispatch, which the RTO uses to maintain reliability.
  The RTO accepts voluntary bids from participants
  The RTO uses the bids to arrange a regional security-constrained economic dispatch that simultaneously
    Balances the system
    Clears the market
    Redispatches the system to relieve all congestion (Note that a real-time balancing market and market-based congestion management flow from the same bid-based dispatch)
    Does so at the lowest cost, given the bids and the constraints
The RTO should apply the same concept in any forward market (day-ahead and/or hour-ahead) that the RTO coordinates.

## Slide 13: Consequences of restricted access to an efficient dispatch
California has always restricted access to an efficient dispatch. Their rules:
  Define the RT spot market as a “limited balancing market”
  Impose penalties on those who use “too much” balancing
  Force parties to submit and maintain balanced schedules
  Limit RTO ISO redispatch to “the minimum shift” needed
And the results are predictable:
  Higher costs for balancing and congestion redispatch
  Fewer options for participants
  Harder for the ISO to relieve congestion and maintain reliability
  Incentives/potential for market concentration

## Slide 14: 2. Use the same process/models to solve all the congestion
Efficient markets use the voluntary participant bids to relieve all congestion in each market: Real-Time, Day-Ahead, Hour-Ahead.
  All congestion is treated the same
    Use the same network model to identify the constraints
    Use the same bids to relieve the congestion
  No distinctions are made between “important” and “unimportant” congestion; it all has to be relieved
  No attempt to limit the market to managing only the congestion that is predicted to be “important” while forcing the RTO to deal with everything else outside the market

## Slide 15: Consequences of treating some congestion differently
It is more complicated to use two processes -- one to solve for “important” congestion and another to solve for “unimportant” congestion.
  You can get inconsistent results (e.g., infeasible schedules)
  You can get inconsistent prices (and invite gaming)
  And it will cost more to relieve congestion
Predictions that there won’t be much congestion are invariably wrong
  Historic congestion patterns are very poor predictors
  Congestion after the market starts is always more pervasive and costly than predicted before the market starts
  Even post-market patterns change from year to year

## Slide 16: 3. Price the dispatch/spot market accurately, using locational marginal pricing (LMP)
Getting the prices right is essential. Accurately pricing the dispatch using LMP will result in prices that reflect:
  The market-clearing price at each location
    So participants have incentives to bid their marginal costs
    And the parties have no incentive to game their bids/schedules
  The marginal cost of redispatch at each location
    So you can offer a market-priced redispatch alternative to curtailments
  The marginal cost of serving an increment of load at each location
    So generators and loads get the right price signals
  Prices that are consistent with the dispatch
    So the market’s response to these prices will be consistent with what the RTO needs the market to do to maintain reliability
    And participants can be free to respond to those prices without RTO intervention

## Slide 17: Consequences of inefficient (non-LMP) pricing
The settlement prices do not clear the market
  Some parties will have submitted bids that should have been taken, but were rejected, and vice versa
Side payments will be necessary
  Generators constrained off to relieve congestion must be paid to get off, because the settlement price is above their bid
  Generators constrained on to relieve congestion must be paid to get on, because the settlement price is below their bid
Generators will probably game their bids to maximize the side payments
The price signals will not induce appropriate short-term operations or long-run investments
The RTO will have to intervene in the market’s decisions, and often.

## Slide 18: 4. Use consistent approaches in the forward and real-time markets
If the RTO coordinates short-run forward markets -- such as day-ahead or hour-ahead -- then the RTO should use the same economic dispatch approach, and the same grid models, as it uses in its real-time spot/balancing market
Supposedly simpler “commercial” models developed for some forward markets are constant sources of market problems:
  Simplified models lead to infeasible schedules in the forward markets -- they ignore real constraints that the RTO must deal with
  This guarantees that the RTO will still have big problems to solve in the real-time market. Forward markets become less useful
  Inconsistent models allow gaming between forward and RT markets.

## Slide 19: 5. Apply consistent pricing between energy and transmission
Transmission pricing and energy pricing are closely related
  Injecting and selling energy at one location and withdrawing and buying energy at another location is the same thing as . . .
  Scheduling/buying transmission between the same two locations
    Transmission pricing is thus a function of the difference in locational energy prices -- that is how/why LMP works
Inconsistent pricing (or allowing an ISO to price congestion, but allowing a separate PX to price energy) will invariably create problems:
  Parties engaging in bilateral schedules are treated differently from parties engaged in equivalent spot sales/purchases
  Parties may be encouraged to overuse congested transmission and/or game schedules and rely on the imbalance/spot market
  The RTO must restrict market choices and/or intervene.

## Slide 20: 6. Provide simultaneous auctions and consistent pricing for reserves and energy
The market value of energy is also linked to the market value of reserves.
  Resources that provide energy can also provide reserves; those that can provide quick-response reserves can also provide slower-response reserves -- substitution allows optimization
RTO energy/reserve markets should be simultaneous, allowing the RTO to select the least-cost mix of resources to meet all needs. This simplifies the market for participants and eliminates the need for them to guess market prices in one market before they bid in another.
Sequential markets can lead to inconsistent and higher prices

## Slide 21: 7. Define and allocate point-to-point financial transmission rights (FTRs)
If the RTO prices congestion and redispatch efficiently, energy prices will differ by location, and point-to-point schedules will face congestion charges based on the locational differences in prices. FTRs provide financial hedges against locational price differences.
Despite concerns about complexity and liquidity, point-to-point FTRs are the best way to define tradable transmission rights that provide hedging.
  An FTR locks in the delivered price of energy, in advance
  FTRs are financial hedges, not physical rights
    Don’t need one to schedule; don’t need to match FTR and schedule
    No use it or lose it rule; you get an FTR’s value no matter what you do
  FTR forward prices provide long-run signals for upgrades
  FTRs are easily decomposed to support hub trading

## Slide 22: Can flowgate rights work?
Rights defined by constraints -- flowgate rights (FGRs) -- are possible, but the more closely they are examined, the less attractive they become.
  There may be a lot more flowgates than the “few” that many assume
  Even if the number of flowgates is “manageable,” the distribution factors differ for each contingency, and there are many of these
  The binding contingency can change frequently, and unexpectedly, depending on market and grid conditions
  For different contingencies, the distribution of flows across each constraint may be different
Traders may not be able to predict which set of FGRs they will need, unless the RTO arbitrarily selects only a “few” flowgates and fixes the distribution factors in advance, while socializing the risks.
Bottom line: No one who understands the commercial risks has been willing to take them.

## Slide 23: 8. Apply market power mitigation up front and selectively
Market power can be a problem in every region, and insufficient attention has caused serious problems in some regions. It has to be addressed.
It may be easier to address generation market power up front by structural solutions -- divestiture and careful attention to market shares.
“Vesting contracts” structured as contracts for differences can be used to hedge the divesting utilities (or their customers) from market price volatility, while discouraging market power.
Once the market starts, some market power, especially in load pockets constrained by limited transmission, is still likely in most markets and may require bid caps (not price caps).
Selective application of mitigation is important. In the long run, you want new entrants and/or demand responses to minimize the exercise.

## Slide 24: 9. Allow prices to rise (fall) to market-clearing levels to encourage appropriate investments
Once market power mitigation is applied, it’s important not to insist on (or expect) lower prices per se. Market clearing prices in regions where supplies are tight can and should be allowed to rise, and will sometimes need to reflect shortage costs.
The expectation that some (very) high market prices may occur during tight supply or shortage conditions is necessary to encourage new entrants and demand response.

## Slide 25: 10. Do everything you can to encourage demand-side participation in setting market prices
Bid-based markets that rely only on supply-side bids are incomplete. True market-clearing prices require some degree of demand-side participation.
Good markets actively encourage the demand side to respond to and help in setting prices, by giving it opportunities to express its willingness to pay.
  Support for interval metering
  Real-time (within five minutes) posting of prices
  Explicit accommodation of demand-side bidding
  Active search for “dispatchable loads”
  RTO-coordinated forward markets, which give “non-dispatchable loads” enough time to respond to forward prices
None of these will work if most loads are not exposed to market-clearing prices. Patience and forbearance by regulators/elected officials is hard but necessary. (Assumes sufficient market power mitigation.)

## Slide 26: Summary: Market design is important, and the details matter
Many of the directions FERC gave California will have to be reversed if California is to have an efficient market.
Careful attention to the lessons from successful markets elsewhere can help California avoid some real headaches. The major lessons:
  Provide an efficient dispatch and price it accurately, using LMP.
  Make access to spot markets and access to contracting a matter of market choice, not regulatory fiat
  If something isn’t working, check the pricing; the incentives/signals are probably wrong.
  Pay attention to market power, then allow market-clearing prices
  Get the demand side engaged