## Slide 1: An “Ideal”Interim Market Model
Frontier Economics, Inc.
Strictly Private and Confidential
www.frontier-economics.com
Boston London Melbourne

## Slide 2: RTO design objectives
The initial paper identified five key objectives for RTO design:
Robust and liquid forwards markets
Robust and liquid spot markets
Resistant to generator market power
Provide information on parameters that will affect supply, demand and delivery costs
Minimize role for system operators and regulators to avoid distortionary interventions

## Slide 3: What conditions hold in an ideal market?
Many buyers and sellers - no concentration
No interactions between trades - no external costs such as loop flows
Low or no transactions costs - participants can interact cheaply and instantaneously
Perfect information on future supply and demand - all information is reflected in market prices
Full forwards markets exist - all risks can be hedged efficiently
No sunk costs - production has no fixed cost components

## Slide 4: Constraints on electricity markets depart from the ideal economic assumptions
Congestion - limited transfer capability on lines creates external costs
Coordination and transaction costs - large number of transaction necessary in a short period of time
Losses - marginal losses are higher than average losses
“Non-convexities” - such as start costs and ramp rates
Public good aspects of reliability - all users receive the same level of reliability on an unswitched network
Imperfect information - traders have considerable uncertainty about key parameters such as the state of the network
Market power - for transmission as well as generation if open access and release rules are inadequate

## Slide 5: Power markets functions are designed around these constraints
Forward
No “sunk” costs or decisions yet
Commitment
Check whether generation and load plans are consistent with constraints
Procure capacity if not consistent
Dispatch
Meet real-time load variation
Operate units consistent with actual transmission constraints
Settlement
What happened and who pays?
-1 to 0 hours
+ hours
-24 to -12 hours
< -24 hours

## Slide 6: Commitment is the key issue in RTO design
Generation schedule must meet locational transmission constraints (e.g. some plants in NYC and not all in Buffalo)
Must also meet temporal constraints such as ramp rates and minimum on and off times for units
Commitment
process
Day ahead
prices by location
Day ahead
schedules by location
Market price and
quantity offers
Transmission constraints
(thermal and voltage)
Dynamic constraints
(ramp rates, on/off times)

## Slide 7: Commitment mechanisms for managing day ahead congestion
Optimizing
software
Nodal DA prices
Nodal DA schedules
Bids
Max A-B = 300
Max A-C = 500
Constraints
Examples: PJM, NYISO
A
B
C
D
Examples: Flow-based RTO proposals
Centralized bid-based commitment
Purely decentralized rights trading

## Slide 8: Flow rights allow decentralized trading that respects interactions on the grid
Individual flow rights created and auctioned
PTDF matrix published by grid operator defines portfolio of rights required to complete a scheduled transaction (e.g. from A to C)
This portfolio of flow rights is equivalent to a single point-to-point right (e.g. an FTR or a traditional “physical” right)
A
B
C
D
A-B
A-C
B-C
B-D
D-C
A-B
A-C
B-C
B-D
D-C
A-D
Transactions
Rights Required

## Slide 9: Problem: the number of flow rights required may be impractically large
On large systems, the number of possible flow rights required to adequately represent the system may be very large
For example, the unit commitment process in PJM considers hundreds of potential constraints in the day ahead market
If a very large number of rights are required this could:
  raise transactions costs and hence lower forward liquidity
  reduce the number of participants willing to trade
The real problem with current flow-based RTO designs is that there is little real knowledge of how many rights must be traded
If the “commercial” flowgate model does not match operational realities then RMR-type gaming will increase need for RTO interventions

## Slide 10: Why not just have financial trading and FTRs in power markets?
Possible flows across constraints are a function not only of the network but also of gen. schedules
For example, prices in a constrained region will depend on whether a large plant in that region will run
Pure financial trading provides less information to market - no “open interest” on a deliverable contract
FTRs and swaps act as a weaker mechanism for price discovery - FTR markets have been highly illiquid in practice
If the counterflow plant in the constrained area is not scheduled the effective constrained flow is reduced and LMPs will be affected
Constrained flow

## Slide 11: Pros and cons of the two commitment mechanisms
Centralized bid-based commitment
Decentralized rights trading
Large role for RTO/ISO in market
Forward price discovery may be weak
Uniform price auctions manipulable
Little information - “black box”
Low transactions costs
Reach feasible schedule quickly
Handle large numbers of constraints
FERC acceptability
High transactions costs
Will flow rights markets be liquid?
Practicality untested in real systems
Unrealistic PTDF assumptions?
Minimal role for RTO/ISO
Opportunities for trading transmission
True forward price certainty
Consistent with longer-term vision

## Slide 12: Trading portfolios of transmission rights through an exchange
Hub
Feasible
transactions
Trader A
Trader B
Feasible
transactions
Flow from Trader B > Hub
Flow from Trader A > Hub
Line flow constraints
Rights to and from various locations can’t be traded on a one-to-one basis, as impacts on congested lines are different (e.g. PTDF elements are different)
Could be traded through an exchange, if done on an unequal quantity basis

## Slide 13: Transmission exchange could lower costs of trading numerous transmission rights
MW of rights offered from Trader A node to hub “converted” to MW of rights from Trader B node to hub - true “point-to-point” rights
Exchange made at ratio of PTDF elements for the transactions (2:1 in example above) - insures that all binding constraints are still met
Exchange need only network parameters and line loadings from system operator - does not need to optimize all bids, etc.
Transmission
portfolio
exchange
Trader A
Trader B
Trader A offers to sell100 MW of his rights
Trader B receives offer to buy 50 MW of her rights
Trader A receives offer to buy 150 MW of his rights
Trader B offers to sell 75 MW of her rights

## Slide 14: Choosing a preferred market structure
If system can be adequately represented by a reasonable number of flow rights this is the preferred solution for forward trading and day ahead commitment
  Minimizes role of system operator in day ahead and forward markets
  Allows for price certainty and continuous price discovery
  Avoids need for uniform price auctions and hence reduces scope for market manipulation
  Maximizes information flow to the market
  Transactions costs can be minimized through transmission exchanges
If the number of rights required is just too large then will need to fall back on a more centralized model
  Simplified PJM-type structure with energy-only bids, no uplift and purely financial trading
  Should support improved information release but it is unlikely to occur

## Slide 15: Overview of the ideal interim market structure
Trading in deliverable energy to and from one or more hubs
Traders submit proposed schedules and portfolios of transmission rights to SO for verification that proposed transactions are feasible
SO continuously updates info on quantities scheduled and projected flows
Energy trading at hub(s) can operate as a continuous bid-ask market
No need for a centralized day ahead commitment optimization - final stage of forward trading in deliverable energy and ancillary services
Time
-
Bid-ask prices
Energy hub
Generator
Generator
Generator
Load
Load
Load
Energy hub
Generator
Load
Load
Load

## Slide 16: Moving from day ahead to real-time market
G
L
Energy schedule for hours 6-18
Trans flow right 1
Trans flow right 2
Trans flow right 3
Trans. rights portfolio
0
6
12
18
24
Megawatts
System operator’s accepted schedules
G
L
Real-time LMP
auction
Inc/dec bids
Real-time LMPs
for settlement
Day ahead
and forward
Real-time
New schedule
Existing schedules

## Slide 17: Forward trading can operate with minimal RTO involvement
System operator will publish and update network data (e.g. expected PTDF and limits) and volumes scheduled (energy and transmission) on a continuous basis
Traders wanting price certainty can acquire flow rights and submit physical schedules to SO that ensure priority - “firm power”
Financial trading is always possible against energy hub prices or real-time LMPs - financial swaps are outside any RTO control
Trading in transmission rights can be conducted independently or through a commercial bid-ask portfolio exchange - an “EnronOnline” for transmission

## Slide 18: Conclusions on an ideal model for RTOs
Need to recognize tradeoffs in selecting an RTO model
  decentralized flow rights models best fit Enron’s strategic objectives for an ‘ideal’ market design in day ahead and forwards trading
  centralized models are much simpler if the number of constraints is unreasonably high - and may actually improve liquidity in these circumstances
  Enron will need to assess system characteristics and the number of likely transmission constraints in developing RTO positions
In real-time there is little scope for avoiding LMP-type markets for dispatch and clearing imbalances