## Slide 1: MEASURING ENERGY RISK
Vince Kaminski
Research Group
New York, February 13, 2001

## Slide 2
The market is as much dependent
on economists, as weather on
meteorologists.
George Herbert Wells

## Slide 3: Outline
Main sources of risk in energy-related transactions
Energy markets vs. financial markets
Definition of volatility
Importance of volatility to option pricing and financial risk analysis
Recent experience of volatility of power prices in the United States
Estimation of volatility from historical data
Volatility derived from a structural model

## Slide 4: Sources of Risk in Energy Transactions
Financial risk models evolve traditionally around measurement of market and credit risks
Recently, the regulators and quants have focused on operational and model risks
Risk estimates are typically based on value-at-risk models
  Exposures are measured over relatively short period of time
  Interactions between market and credit risk (and/or other types of risks) are typically ignored

## Slide 5: Sources of Risk in Energy Transactions (2)
Measuring risks in energy markets
  Extreme levels of price volatility amplify other types of risks
  It is critical to capture impact of price volatility on credit worthiness of the counterparties
Special types of risks
  Volume risk
    Weather exposure
    Exposure to economic growth in long-term transactions
  Complicated contract structures increase model risk
  One cannot ignore the physical infrastructure supporting production and distribution of energy commodities

## Slide 6: Examples
Interaction of market and credit risks
  Electricity price spikes of the summer of 1998 in the Midwest
  Extreme price spikes devastated portfolios of certain power marketers who wrote naked options
  Defaults propagated along the daisy chain of transactions separating generators and end users of electricity
  Credit sleeving practices contributed to the frequency and severity of defaults
  Prices, decoupled from the marginal cost of production, reflected the ability and desire to avoid defaults on contractual obligations

## Slide 7: Examples (2)
Volume risk in swing options (gas or power)
Forward start option: strike set at the beginning of the period (typically month) to the so-called index
Index: a swap (one month tenor) price based on the phone survey of transaction executed during the so called bid-week
Fixed strike price options become more popular
Physical options or financially settled options (so-called Gas Daily options)
The right to purchase natural gas at a strike price, within certain volumetric limits (Vmax, Vmin)
The number of swings is typically less than the number of days in a month

## Slide 8: Swing Options
Bid Week
Index is set
1
31
Calendar Month
Exercise Decisions

## Slide 9: Examples (3)
Volume risk in full requirements deals
A long-term contract to satisfy energy needs of a customer (a local distribution company, an industrial company)
  Typically at a predetermined price
  Over a long time period
The provider assumes volume risk (limited or unlimited)
Exposure to short-term and long-term volume fluctuations
  Short-term fluctuations are typically driven by the weather
  Long-term fluctuations result from the changes in the levels of economic activity, technology and from demographic shifts

## Slide 10: Examples (4)
Price shock typically results from an event in the energy infrastructure (production and/or distribution side)
An outage of a power plant produces a price spike
An outage in one power plant or transmission problem may increase an outage risk in other plants
One has to model the physical side of the industry to capture the underlying risk

## Slide 11: Importance of Volatility
Price volatility is the common risk factor amplifying other types of risks in the energy - related transactions
Critical input to option pricing models
  More accurate volatility forecasts increase the efficiency of hedging strategies
Used as a measure of risk in models applied in
  Risk management (value-at-risk)
  Portfolio selection
  Margining

## Slide 12: Different Types of Volatility
Volatility - a statistical measure of price return variability
Historical volatility: volatility estimated from historical prices
Implied volatility: volatility calculated from option prices observed in the market place
Volatility implied by a fundamental model

## Slide 13: Different Types of Volatility (2)
Different definitions of volatility reflect different modeling philosophies
Reduced form approach
  Historical / implied volatility approach is based on the use of a formal statistical model
  Reduced from approach assumes that a single, general form equation describes price dynamics
Structural model assumes that the balance of supply and demand in the underlying markets can be modeled
  Partial or general equilibrium models

## Slide 14: Option Pricing Technology
Prices evolve in a real economy and are characterized by certain empirical probability distributions
Options are priced in a risk-neutral economy: a theoretical concept. Prices are characterized in terms of risk-neutral (i.e. fake) probability distributions.
If the math is done correctly, option prices in both economies will be identical
Volatility constitutes the bridge between the two economies
The risk-neutral economy can be constructed if a replicating (hedging) portfolio can be created

## Slide 15: Option Pricing Technology (2)
The only controversial input an option trader has to provide in order to price an option is the volatility
The shortcomings of an option pricing model are addressed by adjusting the volatility assumption
The approach developed for financial options has been applied to energy commodities in a fairly mechanical way
The inadequacy of this framework for energy commodities is becoming painfully obvious

## Slide 16: Modeling Energy Prices
Energy prices have split personality (Dragana Pilipovic)
  Traditional modeling tools (Geometric Brownian Motion) may apply to long-term forward prices
  As we get closer to delivery, the price dynamics changes
  Gapping behavior of spot prices and the front of the forward curve
  Prices may be negative or equal to zero

## Slide 17: Modeling Energy Prices
Traditional answers to modeling problems seem not to perform well
  mean reversion
    seasonality of the mean level
    different rate of mean reversion for positive and negative deviations from the mean
  jump-diffusion processes
    asymmetric jumps with a positive bias
    one can speak rather of a floor-reversion

## Slide 18: Limitations of the Arbitrage Argument
In many cases it is impossible or very difficult to create a replicating portfolio
  No intra-month forward markets (or insufficient liquidity)
  It is not feasible to delta hedge with physical gas or electricity
  Balance of-the-month contract: imperfect as a hedge, low liquidity
Risk mitigation strategies are used
  Portfolio approach
  Physical positions in the underlying commodity
  Positions in physical assets (storage facilities, power plants)

## Slide 19: Recent Price History in the US: Examples
History of extreme price shocks in many trading hubs
High volatility results from a combination of a number of factors
  Shortage of generation capacity
  Extreme weather events
  Flaws in the design of the market mechanism

## Slide 22: Supply and Demand in The Power Markets
MWh
Demand
Price
Volume
Supply stack

## Slide 23: Volatility: Estimation Challenges
Limited historical data
Seasonality
  Insufficient number of price observations to properly deseasonalize the data
Non-stationary time series
The presentation below enumerates and exemplifies the difficulties
No easy solutions

## Slide 24: Definition of Volatility
Volatility can be defined only in the context of a stochastic process used to describe the dynamics of prices
Standard assumption in the option pricing theory: Geometric Brownian Motion
Definition of volatility will change if a different stochastic process is assumed
Option pricing models typically assume Geometric Brownian Motion

## Slide 25: Geometric Brownian Motion
dP = Pdt + Pdz
  P - price
   - instantaneous drift
   - volatility
  t - time
  dz - Wiener’s variable (dz =  dt, 

## Slide 26: Estimation of Historical Volatility
Estimation of historical volatility
  Calculate price ratios: Pt / Pt-1
  Take natural logarithms of price ratios
  Calculate standard deviation of log price ratios (= logarithmic price returns)
  Annualize the standard deviation (multiply by the square root of 300 (250), 52, 12, respectively, for daily (Western U.S., Eastern U.S.), weekly and monthly data
Why use 300 or 250 for the daily data? Answer: it’s related to the number of trading days in a year.

## Slide 27: Annualization Factor
M
T
W
T
F
M
4 Daily Returns
Weekend Return

## Slide 28: Annualization Factor
Alternative approaches to annualization
  Ignore the problem: close-to-close basis
  Calendar day basis
  Trading day basis
Trading day approach
  French and Roll (1986): weekend equal to 1.107 trading days (based on close-to-close variance comparison) for U.S. stocks
  Number of days in a year: 52*(4+ 1.107) = 266

## Slide 29: Annualization Factor
Close-to-close variability of returns over weekend in the stock market is lower because the flow of information regarding stocks slows down
Is this true of energy markets?
The answer: Yes, but to a much lower extent
The information regarding weather arrives at the same rate, irrespective of the day of the week

## Slide 30: Seasonality
How does seasonality affect the volatility estimates?
Assume multiplicative seasonality
  Pt = sPa
  Seasonality coefficient s in calculations of price ratios will cancel
The price ratio corresponding to a contract rollover date should be eliminated from the sample

## Slide 32: Mean Reversion Process
Prices of commodities gravitate to the marginal cost of production
Mean reversion models borrowed from financial economics
  Ornstein - Uhlenbeck
  Brennan - Schwartz

## Slide 33: Ornstein-Uhlenbeck Process
dP = (Pa - P)dt + dz
   speed of mean reversion
   volatility
  Pa average price level
The parameters of the equation above can be estimated using a discrete version of the model above (an AR1 model)
  Pt = a + b Pt-1 + t

## Slide 34: Ornstein-Uhlenbeck Process
The coefficients of the original equation can be recovered from the estimated coefficients of the the discrete version
  Pa = -a/b
   =-log(1+b)
In this case,  is measured in monetary units, unlike standard volatility

## Slide 35: Limitations of Mean Reversion Models
The speed of mean reversion may vary above and below the mean level
A realistic price process for electricity must capture the possibility of price gaps
The spikes may be asymmetric
One should rather speak about a “floor reverting process”
  Floor levels are characterized by seasonality

## Slide 36: Modeling Price Jumps
A realistic price process for electricity must capture the possibility of price gaps
Price jumps result from interaction of demand and supply in a market with virtually no storage
The spikes to the upside are more likely
One should rather speak about a “floor reverting process”
  Floor levels are characterized by seasonality

## Slide 37: Jump-Diffusion Model
Standard approach to modeling jumps: jump-diffusion models
Example: GBM
  dP = Pdt + Pdz + (J-1)Pdq
  dq =1 if a jump occurs, 0 otherwise. Probability of a jump is 
  J - the size of the jumps
  J is typically assumed to follow a lognormal distribution, log (J) ~ N(,)

## Slide 38: Ornstein-Uhlenbeck Process (Jumps Included)
Coefficient estimates (Cinergy, Common High, Pasha)
      6/1/99 - 9/30/99
  Pa 19.96
   15.88
   99.44
  495
   19.12
  0.28
  dP = (Pa - P)dt + dz + dq*N(, )
Alternative formulation
  dP = (Pa - P)dt + Pdz

## Slide 39: Stochastic Volatility
Stochastic volatility models have been developed to capture empirically observable facts:
  Volatility tends to cluster: extreme observations tend to be followed by extreme observations
  Volatility in many markets varies with the price level and the general market direction

## Slide 40: GARCH MODEL
GARCH (Generalized Auto Regressive Heteroskedastic model)
Definition
  ln (Pt/Pt-1) = k + tt, t ~ N(0,1)
  2t+1 =  + 2t2t + 2t
  
The term k represents average level of returns, tt - the stochastic innovation to returns

## Slide 41: Model-Implied Volatility
Future spot prices can be predicted using a fundamental model, containing the following components
  Representation of the future generation stack
  Load forecast and load variability
    Load variability is typically related to the weather and economic activity variables
  Assumptions regarding future fuel prices and price volatility

## Slide 42: Model-Implied Volatility
A fundamental model can be used as a simulation tool to translate the assumptions regarding load and fuel price volatility into electricity price volatility
The difficulty: a realistic fundamental model takes a very long time to run
One has to use a more simplistic model and face the consequences

## Slide 43: Correlation
A few comments on correlation
  Comments made about volatility apply generally to correlation
  A poor measure of co-movement of prices
    What is a correlation between X and Y over a symmetric interval (-x,x) if Y= X2?
  Notorious for instability
  There are better alternatives to characterize a co-dependence of prices in returns