## Slide 1
FERC Technical Conference
on
California Natural Gas Transportation Infrastructure
by
Lad Lorenz
Southern California Gas Company May 24, 2001
Washington, D.C.

## Slide 2: I. The SoCalGas Utility
SoCalGas provides bundled procurement, intrastate transportation, storage and balancing service, utilizing interstate transportation, to core customers under volumetric tariff rates -- no contractual commitment.
SoCalGas provides bundled intrastate transportation and liberal balancing services to noncore customers under volumetric tariff rates -- 2-year contract commitment.
SoCalGas’ noncore customers (including electric generators) are responsible for acquiring their own gas supplies, for contracting for interstate transportation, and storage services. SoCalGas redelivers the gas for customer use.
SoCalGas is a matrix, not path based, system - deliveries at any receipt point can be redelivered to customers or storage.

## Slide 3: Current SoCalGas System Capacity
Backbone Transmission:
  3,500 MMcfd Firm
  200 MMcfd Interruptible
Storage:
  105.6 Bcf Storage Inventory Capacity
  1,900 to 3,600 MMcfd Withdrawal Capacity
  800 to 1,000 MMcfd Injection Capacity
System Deliverability:
  Up to 6,000 MMcfd (6 Bcfd) - Peak Day
  (Historical Peak = 5.3 Bcfd in Dec. 1990)

## Slide 4: SoCalGas’ Backbone Transmission System
Southern Trails

## Slide 5: Adequate Infrastructure - Short Term
SoCalGas has adequate transmission capacity to meet the current needs of our customers.
  Transmission capacity is 1,300 Bcf/year vs. demand of 1,257 Bcf/year - 95% load factor.
  No curtailments have occurred for last 10 years.
  No curtailments are projected for this summer or next winter.
  Short-term capacity additions (or insurance) moving forward.

## Slide 6
Historical Use of SoCalGas’
Backbone Transmission Capacity

## Slide 7
SoCalGas’ Historic End-Use Demand

## Slide 8
II. 2001 Outlook
Operationally challenging due to high electrical generation demand.
SoCalGas will be able to avoid curtailments if backbone system is fully utilized to fill storage.
Short-term additions to maximize SoCalGas’ backbone transmission capacity are being undertaken.
Cushion gas options are being pursued.

## Slide 9
SoCalGas’ 2001 Gas Demand Forecast
Forecast assumes best available information, but is subject to variation based on weather, plant outages and completion of new gas peaking units.
(Recorded)

## Slide 10
Maximize existing interruptible capacity.
  Up to 200 MMcfd of existing interruptible capacity is available.
Salvage the Montebello Storage Field.
  Over 50 MMcfd ( >10 Bcf in 2001) of in-basin supply available now.
  Over 23 Bcf of total cushion gas in field.
Proceed with Aliso Canyon and La Goleta cushion gas projects.
  Approximately 14 Bcf of cushion gas is available.
Three Opportunities Currently Available for SoCalGas to Increase Summer Capacity

## Slide 11: SoCalGas’ Summer Injection Profile (Historic, Current and Outlook)

## Slide 12: III. SoCalGas’ Capacity Expansion Policy
Maintain 15-20% annual excess backbone transmission capacity relative to expected, normal weather demand.
  Consistent with CPUC interstate pipeline connection policy.
  Creates operational flexibility & gas-on-gas competition.
Expand in low-cost manner at points where significant, economical upstream supply exists.
Expansion costs rolled-in to all customer rates.
Consider expansions beyond 20% excess with incremental pricing based on shipper commitments.

## Slide 13
Despite 2001 Conditions, No Expansion Warranted Based on Historical or Forecast Utilization of SCG Firm Backbone
Average temperature, normal hydro and 3.5/26 GW EG demand case.
Drop in EG gas demand on SoCalGas due to new plants out-of-area.
  New plants will displace loads from “marginal” generators in LA & SD.
2002-05 forecast is heavily dependent on future EG demand (i.e., timing and location of new generation facilities and other market conditions).
CGR + 400

## Slide 14: IV. SoCalGas’ Near-Term EG Demand Forecast: Key Assumptions
Normal weather
  normal hydro after 2001
  winter/summer temperatures in WSCC
Electricity demand growth of 2.5% per year in the West and 1.4% per year in California
26,000 MW new generation constructed in the West by 2005, representing a reserve margin of 15-20%
  3,500 MW connects to SoCalGas/SDG&E
  22,500 MW assumed built outside SoCalGas’ area
ISO-identified transmission upgrades installed

## Slide 15: Power Plant Development Sites

## Slide 16
SoCalGas is proceeding with expansions and interconnections to add 475 MMcfd (13.5%) of firm backbone transmission capacity to its system.
  200 MMcfd at Kramer Junction using 32 miles of 30 inch pipe for $40 MM.
  50 MMcfd at North Needles using 2,000 HP for $4 MM.
  85 MMcfd at Wheeler Ridge using 5,000 HP for $5 MM.
  40 MMcfd on Line 85 using 3,000 HP for $6 MM.
All projects to be completed by year-end, assuming expedited environmental approvals, then rolled into rates in next cost-of-service proceeding.
Proposed 100 MMcfd interconnection with Questar at Cabazon.
V. Nevertheless, SoCalGas is Proceeding with Least Cost Expansions

## Slide 17: $MM Capital Cost of Expansions Considered
NA = Not Available
Significant O&M costs for all options other than Kramer Junction.

## Slide 18: Inter/Intrastate Pipeline Additions to California
Pipeline proposals announced in press or in open seasons would add:
  8,000 MMcfd of new interstate capacity
  1,600 MMcfd of new intrastate capacity by others
  475 MMcfd of new backbone capacity by SoCalGas
  500 MMcfd new interstate pipeline to Mexico

## Slide 19: VI. Intrastate Capacity Allocation
SoCalGas does not allocate intrastate pipeline capacity.
  Normally - SoCalGas’ full firm plus interruptible intrastate receipt point capacity is available and upstream interstate pipelines determine whose gas flows.
  Occasionally - SoCalGas’ intrastate receipt point capacity is reduced pro-rata if receipts exceed demand plus available injection capacity. Upstream pipes still decide whose gas flows.
  SoCalGas has proposed to the CPUC to provide receipt point specific intrastate transmission rights that would allow SoCalGas to confirm interstate scheduled volumes by downstream contract.

## Slide 20: VII. What is Adequate Infrastructure?
Sufficient Capacity to Meet Expected Needs of Customers?
  No excess during peak years
Sufficient Capacity to Meet All Possible Demand Scenarios?
  Large excess capacity during most years
Based on Long-term Contractual Commitments with Capacity Rights?
  Like interstate pipelines
  Requires unbundling and restructuring in California
Interconnection capacity Vs. Take-away capacity?

## Slide 21: Further Capacity Expansions to SoCalGas System
Should be based on market needs - not interstate pipeline expansions.
Amount of excess intrastate capacity constructed should be determined by CPUC.
All interconnections with SoCalGas system accommodated -- however, downstream take-away based on market.
Local transmission expansions likely, not further backbone expansions.