## Slide 1: Region Wide Load Curtailment Program for the WSCC
Summer 2001

## Slide 2: The Problem
California is forecasted to be from 5000-8000 Mw short for summer peak demand
No way to install sufficient Megawatts of new supply of this magnitude for summer peak
Only solution is Negawatts of demand curtailment
Control areas can typically purchase Negawatts only within their own service territory…no mechanism exists for getting someone else’s customer to interrupt
Insufficient Negawatts within the CAISO control area to cover the expected shortall

## Slide 3: The solution...
Establish a mechanism for allowing negawatts of emergency energy to be easily purchased the same way as megawatts of additional supply…from anywhere within the WSCC

## Slide 4: The Proposal…Bidding
Conduct weekly bid auctions from any load which will interrupt over 10Mw
Loads will bid a price per Mwh for interrupting, and the amount of Mw they would interrupt
The program administrator would use the bids to develop a “bid stack” of available resources

## Slide 5: The Proposal…Dispatch
If a control area needs help, they would call the program administrator
The administrator would work with the WSCC Security Centers to verify the least cost set of bids in the stack that could be exported to the deficit area
Those bids would be selected, the customers notified, and the originating control area would convert the curtailed load amount into an export schedule to the deficit control area
Transmission scheduling handled as for any emergency assistance

## Slide 6: The Proposal…Settlement
The deficit control area pays the market clearing price of the negawatts dispatched
The customer keeps the retail supplier whole for the pre-curtailment level of retail charges
The customer is responsible for imbalance charges (if any) due the originating control area
The curtailing customer nets the negawatt payment minus the retail charges minus any imbalance payment

## Slide 7: Hurdles
Getting all this implemented within the next 60 days
Regulatory restrictions on the resale of retail purchases
Picking the program administrator and setting up the bidding and settlement process
Encouraging customer participation

## Slide 8: Game Plan
Introduce the program to WSCC Board and key policy makers in the west.
Work with the WSCC Market Issues Committee to fully define how to accomplish and who should administer
Work with state and federal policy makers to resolve the retail resale issue
Develop strategy for communicating to potential curtailable customers