## Slide 1
March 2001
Generation Investments
Project Loretta

## Slide 2: Proposal - “Sutton Bridge” Model
As soon as Generation Investments (GI) can assure a completion date in a given region, EPMI puts on a commodity play and places the position in a “hedge book”
EPMI backstops this with a 12 month option on a PPA from the SPV - - also kept in the “hedge book” - - GI limits development costs to a minimum until/if EPMI exercises the option on the PPA
If commodity spread remains constant or increases - - gas and/or power prices relative to coal - - EPMI exercises its option
GI then builds the plant via the SPV using Sr/Jr equity for leverage
GI receives equity in the SPV through development costs (cash) and by meeting milestones (effort)
If commodity spread decreases, EPMI unbundles the deal and monetizes - - plant does not get built
GI
equity
e
--
fixed $
Gas
Power
Other
EPMI
SPV
fixed $
Coal
Seed $ & Effort
EIM

## Slide 3: Economics
Both IGCC and CFB technology were considered
For each, a 20 year PPA is assumed - - values come from the desk for each region (low in “coal country” and higher in “gas” country)
Debt coverages average 1.5 during term with a min of 1.3
Construction bridge financing is assumed with a 75/25 D/E ratio
A residual value of $600/kw is assumed at year 20
A break-even analysis was run on the total equity portion, assuming a 12% hurdle rate - - Sr/Jr equity investors will be used in order to raise Enron’s equity IRR to >15%
Sensitivities were run (attached)
Recommendation:
  Use CFB only in high revenue (PPA) or low fuel cost (minemouth or Pet Coke) regions
  Use IGCC in hard-to-permit regions, assuming technology is fully vetted

## Slide 4: Key Assumptions - - IGCC
Capital Costs
  Plant Cost ($/kw) 1,218 $/kw
  Construction Financing Costs ($/kw) 108 $/kw
  Total 1,326 $/kw
Construction Start Date 7/03
COD 1/06
Capacity Factor 90 %
Heat Rate 8200 Btu/kw-hr
Delivered Coal Cost 1.50 $/Mmbtu
Plant Residual Value in Year 20 600 $/kw
Plant Size 1000 Mw
PPA 38 $/Mw-hr

## Slide 5: Summary Cash Flow - - IGCC
Years 2016 - 2021 are similar

## Slide 6: Sensitivity Analysis - - IGCC

## Slide 7: Key Assumptions - - CFB
Capital Costs
  Plant Cost ($/kw) 1,150 $/kw
  Construction Financing Costs ($/kw) 121 $/kw
  Total 1,271 $/kw
Construction Start Date 1/03
COD 1/06
Capacity Factor 90 %
Heat Rate 9300 Btu/kw-hr
Delivered Coal Cost 1.00 $/Mmbtu
Plant Residual Value in Year 20 600 $/kw
Plant Size 1000 Mw
PPA 34 $/mw-hr

## Slide 8: Summary Cash Flow - - CFB
Years 2016 - 2021 are similar

## Slide 9: Sensitivity Analysis - - CFB

## Slide 10: Draft Timeline
4/15/01 Develop detailed VAR timeline
4/15/01 Pick Probable Sites
4/15/01 Choose technology
        -IGCC
        -CFB
4/15/01 Begin detailed development of sites
4/15/01 Select probable EPC contractor
VAR = $2MM
7/15/01 Land, equipment, etc options - We’ll go back to the Office of the Chairman with
detailed proforma prior to equipment options
VAR = $10MM?
7/15/01 Commit Point - EPMI puts on commodity play
1/1/03 Start Construction
VAR = $300MM?
1/1/06 COD