## Slide 1
Load Profiling

## Slide 2: Objectives
What is load profiling?
Why is load profiling necessary?
What are the load profiling business requirements?
How do the Distribution Companies’ load profiling systems work?

## Slide 3: What is load profiling?
Load profiling is the methodology used to determine customer hourly loads where hourly interval data is not available on a next day basis

## Slide 4: Traditional Model: Vertically Integrated Utility
Delivery Point Meter
Retail distribution area
GENCo
Notes: 4

## Slide 5: Restructured Model: Competitive Electric Supply
Retail distribution area
Delivery point meter
Supplier B
Supplier A
Std Offer Supply
123
XYZ
ABC
NUG
Notes: 3

## Slide 6: Why is Load Profiling Necessary?
Hourly loads are used in ISO Market Settlement
Hourly loads must be reported to ISO-NE by 1300 hours of the second business day.
Therefore,
  Actual hourly interval data are used for customers with telephone access interval recorders
  Load profiling is used for customers without telephone access interval recorders

## Slide 7: Alternative Methods of Developing Supplier Loads
Acceptable
Precision
Maximum
Attainable
Lower
Higher
Cost
100% Estimation
Upstream
Metering
100%
Telemetering
Notes: 5

## Slide 8: ISO-NE Requirements
Participant establishes a Load Asset for each Node where they serve load
Non-Participant supplier must contract with a pool participant
Host Participant reports Participant hourly loads to ISO-NE
Host Participant reports revised monthly values to ISO-NE

## Slide 9: ISO Load Asset Initiation
Market Rule & Procedure #20, Appendix I
Supplier Information Required by Host Distribution Company:
  Copy of Load Asset Registration Form/Letter
  Estimated Maximum Capacity
  Load Asset Effective Date
  Supplier’s Name
  Load Asset Number
  Contact’s Name/Telephone Number
  Other data required by the DisCo contracts

## Slide 10: Daily Estimation Process
Customer Characteristics
Load Profiles
System Data
Telemetered Customer Data
Daily Load Estimation
Report to ISO
Non-PTF Losses

## Slide 11: Daily Estimation Steps
Collect telemetered data
Select appropriate average load shapes
Adjust shapes for customer usage levels
Add non-ptf losses
Reconcile total estimates to delivered loads (allocate residual)

## Slide 12: Load Shape Development
Customer segment load profiles are developed using historic load research samples
Samples have been designed to meet accuracy requirements established by DTE

## Slide 13: Load Shape Development Cont...
Historic Average Day Type
Historic Proxy Day Match
Customer segment average load shapes provided by each Utility on it’s web site

## Slide 14: Loss Adjustments
Non-PTF Losses
  Fixed average factors
  Determined and allocated by Host Participant
PTF Losses
  Determined and allocated by ISO

## Slide 15: Monthly Reconciliation Process
Daily Estimates
Customer Interval Data
Monthly Meter Readings
Monthly Reconciliation
ISO Adjustment to Participant Billing

## Slide 16: Results
Hourly Participant loads are reported to ISO-NE
ISO-NE performs Market Settlement
Revised monthly values are reported to ISO
Monthly adjustments are applied as adjustments to the Energy Market at the average ECP

## Slide 17: Results Comparison: Points to Note
Customer meter usage reflects consumption during billing cycle
Supplier hourly loads reflect non-ptf losses
ISO billing reflects sum of hourly values for calendar month, plus PTF losses

## Slide 18: QUESTIONS?