## Slide 1: MODREG CALIBRATION

## Slide 2: MODREG Fundamentals
MODREG is a linear programming model which is designed to calculate prices and optimize generation in the Argentine Power Market
MODREG works on a weekly basis and in five (5) hourly blocks
MODREG based on hydro generation data previously optimize by another model, optimizes (minimizes) the variable costs of thermal generation, taking into account all the other variables such as demand, transmission lines, imports and exports,
Because of its characteristics, MODREG is a useful tool to approach mid to long term pricing and generation outputs of the Argentine Power market.

## Slide 3: MODREG Inputs
MODREG ’s main inputs:
  Demand
    Total demand is estimated from a reference year and as a result from the aggregation of all regional demands
    Each regional demand is calculated from a reference year and then adjusted by the estimated growth
  Thermal Generation
    Is optimize taking into account: declare cost of generation, Installed Capacity, Heat Rate, Fuel Consumption, Maintenance Schedule, Gas Availability, Specific Fuel Consumption
  Hydro Generation
    Installed Capacity of generation facilities, and historical series of generation (57) 1943-1999
  Exports
    Exports to Brazil determined by each series of hydro situation and aggregate into the total demand
  Transmission Lines
    Regional transmission lines, constraints and losses
  Power Exchange with Uruguay
    Modeled as an integrated region of the Argentine Market

## Slide 4: MODREG Calibration
Calibration Exercise
  Design to test the accuracy of MODREG in predicting prices in the mid term
  Input the actual data from January to July 2001 in regards to:
    Hydro generation
    Exports to Brazil
    Thermal plant availability
    Declare Costs of Generation
  MODREG to calculate:
  Demand Growth Hydro Generation
    Thermal Generation Transmission Losses
    Fuel Consumption Exports and Imports
PRICE is the main output required from MODREG

## Slide 5: MODREG Calibration Local Demand
Total Demand
5,000
5,500
6,000
6,500
7,000
Jan-01
Feb-01
Mar-01
Apr-01
May-01
Jun-01
Jul-01
Actual
Modreg

## Slide 6: MODREG Calibration Hydro Generation

## Slide 7: MODREG Calibration Thermal Generation

## Slide 8: MODREG Calibration Nuclear Production

## Slide 9: MODREG Calibration Imports

## Slide 10: MODREG Calibration Exports

## Slide 11: MODREG Calibration Transmission Losses

## Slide 12: MODREG Calibration Fuel Consumption

## Slide 13: MODREG Calibration Energy Prices

## Slide 14: MODREG Calibration Summary Cumulative

## Slide 15: Conclusions
From MODREG ‘s output using actual data we can draw some conclusion on the accuracy of the model in predicting prices and generation:
  Local Demand
    We can see that MODREG is consistent with actual demand given the estimated demand growth
    Differences in the initial periods may be due to differences in transmission losses, nuclear generation and import requirements
  Hydro Generation
    Consistent with the input given
    Differences in the last two months maybe explained by inconsistency in some hydro plant actual generation data
  Exports
    Consistent with input given
  Transmission Losses
    Significant differences with actuals. Must revise input rates
  Fuel Consumption
    Significant differences in the amounts of Gas Oil and Fuel Oil consumed
  Thermal Generation
    There are some differences. (see price difference slide)

## Slide 16: Conclusions Price Difference
Although we have seen the model generate consistent output regarding Demand and Hydro Production, we have important differences in thermal generation; thus in pricing levels
  Demand Differences
    May account for some of the differences in the first periods of the evaluation
  Fuel Consumption
    Significant differences
      Gas Availability
        Gas curtailment definitely has a significant impact on the Thermal Stack
      Forced Dispatched Units
        Units could be forced on alternate fuels; thus causing price distortion

## Slide 17: Overall MODREG Evaluation
In the mid to long run predictions, MODREG is able to show credible trends of pricing levels
MODREG depends on various inputs that are outputs of models that are run with assumptions we may not agreed with
MODREG has built in too many sets of data that are part of independent research done by the consultant and may not necessary reflect current conditions
MODREG structure does not allowed to run simplified sensitivities

## Slide 18: Improving Accuracy in Price Calculation
There are some considerations that have to be taken into account in order to increase the reliability and accuracy of prices calculated by MOGREG.
  Demand
    Update demand projections according to new social ,economic, and political situation of the market
  Exports
    Work closely with Brazil South Market desk
  Gas Availability
    Forecasting gas availability on a period to period basis
    Find out relationship between temperature and gas curtailment
  Forced Dispatched Units
    Update information on a month to month basis of the machines programmed to be forced dispatched