## Slide 1: Northeast Natural Gas Market Outlook
Ron Denhardt
Vice President, WEFA Energy Services
September 2000
Northeast Natural Gas Market Outlook
Ron Denhardt
Vice President, WEFA Energy Services
October 2000

## Slide 2: Overview
AECO - Henry Hub Basis
Midwest Flows and Basis
Northeast Demand, Pipeline Capacity and Basis

## Slide 3: AECO Basis Formation Before Alliance
Western Canada Price Determination
Before Alliance
-1
-0.8
-0.6
-0.4
-0.2
0
0.2
0.4
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Henry Hub - AECO Basis
($US/Mmbtu)
Available Supply For Export
Firm
Contracts
to NE
Firm
Contracts
to Eastern
Canada
Firm Contracts to
U.S. Midwest
Firm Contracts to
Western U.S.
Decontr
acted:
Short-
Term
Services
Marginal AECO Price
Bcfd

## Slide 4: During the spring and summer of 2000 AECO - Henry Hub basis widened because:
Strong gas demand in Southern California caused the Northern - Southern California basis to widen
Eastern Canadian storage was not filled because of high prices
Maintenance on Nova system
Additional supplies coming on from Fort Liard area in BC

## Slide 5: Alliance addition of 1.6 Bcfd to Midwest will be greater than 1.1 Bcfd de-contracting on TCPL
Bcfd

## Slide 6
Dawn
Joliet
Chicago
NY
Leidy
Eastern Canada
3.4 Bcfd
Vector Supply Link
Independence
Market Link
Millennium
Midwest 14.5 Bcfd
Major projects are to move gas from Midwest (14.5 Bcfd) to Northeast (11.6 Bcfd)
Middle Atlantic
6.5 Bcfd
New England
1.7 Bcfd

## Slide 7: Even with Alliance there will be net flows from the Gulf to the Midwest
Net Flow (Bcfd)
  Annual 11.5
  Summer 9.8
  Winter 12.2
Canada + SW 6.8
Alliance 1.6 Bcfd
Total with Alliance 8.4 Bcfd
Net Gulf 1.4 Bcfd (9.8 - 8.4)
Canada
3.7 Bcfd
3.5 Bcfd
96%
Gulf
7.3 Bcfd
4.7 Bcfd
68%
Southwest
4.7 Bcfd
3.3 Bcfd
70%
Capacity
Flow
Utilization

## Slide 8: Net flows to western Midwest from Gulf could be negative during part of the year
Net Flow (Bcfd)
  Annual 6.3
  Summer 4.9
  Winter 7.5
Canada + SW 5.1
Alliance 1.6
Total with Alliance 6.7 Bcfd
Net Gulf = -1.8 Bcfd in Summer
Canada
3.0 Bcfd
2.8 Bcfd
94%
Gulf
2.8 Bcfd
1.2 Bcfd
42%
Southwest
3.0 Bcfd
2.3 Bcfd
74%
Capacity
Flow
Utilization

## Slide 9: Chicago - Henry Hub basis could go negative part of the year
Positive Henry Hub - Midwest basis could move northeast of Chicago during the non- heating season and Chicago - Henry Hub basis could become negative in the summer
Midwest could reverse flow 600 - 800 MMcfd to Tennessee

## Slide 10: Dawn - Chicago basis will depend a great deal on Alberta - Henry Hub basis

## Slide 11: De-contracting on TCPL and 80% IT floor will widen Chicago - Dawn basis

## Slide 12: The addition of Vector is likely to create excess capacity to Eastern Canada
Vector will add 700 MMcfd from Joliet, Illinois to Dawn, Ontario with near term expansion of 1 Bcfd
Weather normalized Eastern Canadian demand is about 3.4 Bcfd and growing at 1.5% to 2.0% per year (50 to 70 MMcfd).
It would take almost ten years to absorb this capacity on Eastern Canada
Either there must be substantial growth, gas must be exported, or delivered en-route

## Slide 13: Eastern Canadian Capacity is used at a high load factor
Capacity
Flows
Utilization
TCPL/GLGT
5.34
5.16
97%
Others
1.05
0.07
7%
Total
6.39
5.24
82%
Export
Niagara
0.84
0.81
97%
Iroquois
0.81
0.70
87%
Other
0.94
0.31
33%
Total
2.59
1.83
71%
Net Eastern Canada
3.80
3.41
90%
Bcfd

## Slide 14: Power Generation is the big upside for gas demand
Loss of 4375 MW nuclear capacity in Ontario could support gas demand growth 180 - 360 MMcfd
Proposed gas combined cycle plants in Ontario equal 3.2 GW about 720 MMcfd at 90% capacity
Environmental regulations put 9.4 GW of coal at risk in Michigan

## Slide 15: US Northeast market growth is not likely to absorb all the proposed pipeline capacity
PROJECT
CAPACITY
(
MMCFD)
DATE
Distrigas
220
June 1999
M&N
440
Dec 1999
Independence
900
Nov 2001
Millennium
700
Nov 2002
Scotian Shelf
900
2005
Total
3160

## Slide 16: 3.16 Bcfd of additional capacity compare to .8 to 2.4 Bcfd of consumption growth by 2005
Weather normalized Northeast 2000 consumption 8.4 Bcfd
WEFA’s forecast calls for a 2.6% growth rate over the next decade
1000 MW Nuclear Unit is about 250 MMcfd
1% increase in electricity demand 100 MMcfd per year

## Slide 17: Potential Capacity Additions to the New England Market Are Huge Compared to the Market Size
1998 Capacity to New England was 2.7 Bcfd and weather normalized consumption about 1.8 Bcfd (68% capacity utilization)
Capacity additions Distrigas and M&N 640 MMcfd
Another 900 MMcfd from Scotian Shelf
50% increase in pipeline capacity over next five years

## Slide 18: Most likely Northeast can absorb one major project by 2003 (near term - basis will increase substantially with normal winter)

## Slide 19
Atlanta  Boston  Chicago  Los Angeles New York  Philadelphia  Washington, DC
Brussels  Frankfurt  London  Mexico City Milan  Ottawa  Paris  Pretoria  Toronto
Atlanta  Boston  Chicago  Los Angeles New York  Philadelphia  Washington, DC
Brussels  Frankfurt  London  Mexico City Milan  Ottawa  Paris  Pretoria  Toronto