## Slide 1: Federal Agencies 2001 FCRPS Operations Plan Proposal
April 13, 2001

## Slide 2
Introduction
Two Components of the Federal Agencies 2001 Operations Plan Proposal:
Evaluation of FCRPS conditions relative to the emergency criteria included in the “Federal Agencies’ Criteria and Priorities for 2001 FCRPS Operations”
Summary of operations that will be implemented this year, including a decision process for determining spring and summer spill levels

## Slide 3
Emergency Criteria
Criteria 1: Sufficient Resources to Meet Near-Term Demand
  Insufficiency of electrical generation to meet near-term demand
Criteria 2: Sufficient Resources to Meet Long-Term Demand
  No > 5% loss of load probability in the next 12 months
Criteria 3: Sufficient Cash Reserves to Maintain Reliability
  No > 20% probability of $0 cash reserves in the next 12 months

## Slide 4
Emergency Criteria
Criterion 1: Sufficient Resources to Meet Near-Term Power System Demand
NWPPC and BPA analytical results indicate that approximately 54 MAF is required to meet firm load without further jeopardizing 2001-02 power system reliability
The RFC April Final Volume Forecast indicates 40% probability of actual runoff < 54 MAF
A forecast buffer is added to monthly final volume forecasts to provide no > 25% probability of < 54 MAF actual runoff
Final monthly Volume Forecasts to maintain near-term reliability are:
  May 58.5 MAF (54 MAF + 4.5 MAF Buffer)
  June 58.0 MAF (54 MAF + 4.0 MAF Buffer)
  July 57.5 MAF (54 MAF + 3.5 MAF Buffer)

## Slide 5
Emergency Criteria
Criterion 2: Sufficient Resources to Maintain a 5% Loss of Load Probability in Future Months
If Federal U.S. hydro reservoirs begin operating year 2002 at traditional elevations, NWPPC analysis indicate a 26% probability of not meeting PNW power demand this winter
Storing an additional 1,500 MW-Months (approximately 1.5 MAF) into next year can reduce the loss of load probability to 20%
Storage beyond 1,500 MW-Months has little impact on either the loss of load probability or the magnitude of the load loss

## Slide 6
Emergency Criteria
Criterion 3: Sufficient Reserves to Maintain Reliability

## Slide 7
Emergency Criteria
Criterion 3: Sufficient Reserves to Maintain Reliability
Current BPA analysis indicates that with current runoff and market price projections, BPA achieves the goal of avoiding a > 20% probability of negative cash reserves in any of the next 12 months
If runoff and market price estimates remain in their current range, some level of reserves might be available for expenditures this year
Such expenditures might include:
  implementing offset actions
  power purchases from outside the region to reduce storage needed to enhance 2001-02 winter reliability
  power purchases from outside the region to further reduce the 20% loss of load probability

## Slide 8: Meeting All Three Emergency Criteria
SUMMARY RESULTS
1.5 MAF is used as a proxy for the 1500 MW-mo of storage needed for reliability purposes. Depending on the location and shape of the volume, the MAF requirement to provide the MW-mo could change.

## Slide 9
Emergency Criteria
Criterion 1: Sufficient Resources to Meet Near-Term Power System Demand
Proposed Decision Process for 2001 Spill Operations

## Slide 10: Summary of Spring/Summer Operations
Spill start date and spill levels to be determined based on volume forecasts
Transport up to 50% of juvenile migrants in the spring from McNary Dam
Surging operation at Lower Granite to move juveniles through the pool
Priority for Refill of Headwater Projects:
  1. Dworshak
  2. Libby
  3. Hungry Horse
Allow for consideration to reduce minimum flows for bull trout at Libby to aid refill

## Slide 11: Near-Term Operational Issues
Highlights of operations for the next 2 weeks prior to completion of the operational plan include:
Maintain Vernita Bar flows through the end of April
No spill for in-river or hatchery fish in the second half of April
Implement MOP as in-season management recommends
(remove MOP if capacity problems occur)
Begin spring transport at McNary upon completion of Section 10 permit process

## Slide 12: Next Steps
The Federal Agencies are seeking input on this Operations Plan Proposal through Friday, April 20.
Comments may be sent to Suzanne Cooper at sbcooper@bpa.gov or posted on the Federal Caucus bulletin board at www.salmonrecovery.gov

## Slide 13: Meeting All Three Emergency Criteria
STEP 1
Determine amount of water needed to meet Federal load obligations
Any water not needed to meet firm load is stored in the system
In conditions where volume exceeds that needed to meet load, storage may be used to:
  improve ability to meet 5% loss of load probability (Criterion 2)
  generate energy and revenue, building reserves and improving ability to meet < 20% probability of negative cash reserves (Criterion 3)
  spill to improve fish passage and survival

## Slide 14: Meeting All Three Emergency Criteria
STEP 2
Add forecast error buffer to minimize risk associated with volume forecast error
A 4.5 forecast error buffer is added to the May Final Forecast in the following table:
A May Final Volume Forecast of ~ 58.5 MAF is needed to meet load and provide < 25% probability of actual runoff being < 54 MAF

## Slide 15: Meeting All Three Emergency Criteria
STEP 3
Available storage from Step 2 is reduced by the additional 1,500 MW-Months of storage retained in the system to enhance reliability for winter 2001-02
A May Final Volume Forecast of ~ 60 MAF is needed to meet load and store sufficient volume to reach 20% loss of load probability for next winter