## Slide 2: Physical Bilateral Contracts in the IMO Administered Markets
Ontario Standard Physical Bilateral Contract
Drafting Committee
Jack Lubek - IMO November 22, 2000

## Slide 3
What is a Physical Bilateral Contract?
Energy Suppliers
Energy Purchasers
MW
MW
IMO -
Administered
Markets
Energy Market
No Contract
Settlement for all energy is through the IMO
$
$
Contract or no contract
Energy is still supplied and withdrawn from the IMO market via offers to sell and bids to buy

## Slide 4
Physical Bilateral Contract
Settlement for energy quantities specified in the contract is between the supplier and purchaser
What is a Physical Bilateral Contract?
Energy Suppliers
Energy Purchasers
MW
MW
IMO -
Administered
Markets
Energy Market
$
Contract or no contract
Energy is still supplied and withdrawn from the IMO market via offers to sell and bids to buy

## Slide 5: Timing for Settlement Purposes
Dispatch
Day
7
Days
Initial submission and revisions
No earlier than 7 days prior to dispatch day
Within 6 business days after dispatch day
6
Business
Days

## Slide 6: Settlement of Physical Bilateral Contracts
IMO charges Load A for 80 MWh at MCP
Load A pays Gen 1 directly for 45 MWh at bilateral price
IMO pays Gen 1 for 100 - 45 = 55 MWh at MCP
Physical Bilateral Agreement for 45 MW
Generator 1
Load A
Injects
100 MW
Withdraws
80 MW
IMO -
Administered
Markets
Energy Market
IMO pays Load A for 45 MWh at MCP

## Slide 7: Intertie Settlement of Physical Bilateral Contracts - 1
IMO charges Load A for 80 MWh at MCP $20
Load A pays Supplier 1 directly for 45 MWh at bilateral price
IMO pays Supplier 1 for 100 - 45 = 55 MWh at Intertie Zone MCP $18
Physical Bilateral Agreement for 45 MW
Supplier 1
Load A
Imports
100 MW
Withdraws
80 MW
IMO -
Administered
Markets
Energy Market
IMO pays Load A for 45 MWh at Intertie Zone MCP $18
Intertie Zone MCP $18
Ontario MCP $20

## Slide 8: Intertie Settlement of Physical Bilateral Contracts - 2
IMO charges Load A for 80 - 45 = 35 MWh at MCP $20
IMO charges Supplier 1 for 45 MWh at MCP $20
Load A pays Supplier 1 directly for 45 MWh at bilateral price
IMO pays Supplier 1 for 100 MWh at Intertie Zone MCP $18
Physical Bilateral Agreement for 45 MW
Supplier 1
Load A
Imports
100 MW
Withdraws
80 MW
IMO -
Administered
Markets
Energy Market
Intertie Zone MCP $18
Ontario MCP $20

## Slide 9: Another Settlement Example
IMO charges Load A for 80 MWh at MCP
Load A pays Gen 1 directly for 45 MWh at bilateral price
Gen 1 pays IMO for 45 MWh at MCP
IMO Pays Load A for 45 MWh at MCP
Physical Bilateral Agreement for 45 MW
Generator 1
Load A
Not dispatched
Withdraws 80 MW
IMO -
Administered
Markets
Energy Market

## Slide 10: Standard Bilateral Contract Physical or Financial?
Overview
  What is a physical bilateral contract (PBC) in the IMO-administered markets (IAM) ?
  Does a “physical” contract between participants work with the IMO PBC?
  Are “financial” contracts between participants sufficient to deal with all arrangements which may emerge?

## Slide 11: What is the IMO Physical Bilateral Contract
Market rules describe the PBC primarily in terms of the settlement adjustments
    Energy quantities are removed from spot market settlement, at the “purchaser location”, as specified in the PBC data
    Settlement for energy quantities specified in their contract is between the supplier and purchaser
In this light the PBC:
    is “just” a settlement adjustment;
    but one might also describe it as a transaction between the two parties, settled outside the spot market, and requiring adjustments (buying and selling) in the spot market for deviations from contracted amounts.

## Slide 12: What is a “Physical Contract”
If by “physical“ contract we mean
    US style transactions with
    OASIS purchase / reservation of firm or non-firm transmission access
    scheduling of the contracted energy injection and withdrawal quantities as part of the ISO (or other) hour or day-ahead scheduling process
then the IMO PBC is not “physical”
    these actions are not required or even possible in the IMO

## Slide 13: What is a “Physical Contract”
If you view a “physical contract” as the only type which supports delivery guarantees
    delivery is never guaranteed even to a “physical” contract
      if there is a local shortfall of generation and/or transmission supply to an area, there is some form of pro-rata or other sharing (curtailment or rotational load shedding)
IMO PBC mechanism does not affect the priority / access to transmission

## Slide 14: Does a Physical Contract Work?
Current sample contract (EEI) is not compatible with IMO PBC mechanism
    with its references to arranging transmission, scheduling and purchasing of ancillary services
    delivery in contract may not be consistent with notions of delivery in the IMO market
These terms need to be redefined to fit corresponding IMO notions
    e.g. scheduling
      must include submission of PBC data to IMO, and
      may optionally refer to bids / offers into the IMO

## Slide 15: Are Financial Contracts Adequate?
Financial contracts can achieve same results as any physical contract (L. Ruff and others)
But if too simple the standard financial contract may not go far enough to deal with:
    a purchase equivalent to the buyer’s load
    inter-jurisdictional trade where physical contracts are used in the other jurisdiction
    Green power

## Slide 16: Summary
IMO PBC is most commonly viewed as a settlement adjustment
Some common notions in “physical contract” are not compatible with IMO market, and would need to be modified
A financial contract is compatible, but needs to address options / concerns which are “physical”