## Slide 1: Volatility Estimation Techniques for Energy Portfolios
Vince Kaminski
Research Group
Houston, December 19, 2000

## Slide 2: Outline
Definition of volatility
Importance of volatility to option pricing
Recent experience of volatility of power prices in the United States
Estimation of volatility from historical data
Model derived volatility

## Slide 3: Importance of Volatility
Critical input to option pricing models
  More accurate volatility forecasts increase the efficiency of hedging strategies
Used as a measure of risk in models applied in
  Risk management (value-at-risk)
  Portfolio selection
  Margining

## Slide 4: Different Types of Volatility
Volatility - a statistical measure of price return variability
Historical volatility: volatility estimated from historical prices
Implied volatility: volatility calculated from option prices observed in the market place
Volatility implied by a fundamental model

## Slide 5: Option Pricing Technology
Prices evolve in a real economy and are characterized by certain empirical probability distributions
Options are priced in a risk-neutral economy: a theoretical concept. Prices are characterized in terms of risk-neutral (i.e. fake) probability distributions.
If the math is done correctly, option prices in both economies will be identical
Volatility constitutes the bridge between the two economies
The risk-neutral economy can be constructed if a replicating (hedging) portfolio can be created

## Slide 6: Option Pricing Technology (2)
The only controversial input an option trader has to provide in order to price an option is the volatility
The shortcomings of an option pricing model are addressed by adjusting the volatility assumption
The approach developed for financial options has been applied to energy commodities in a fairly mechanical way
The inadequacy of this framework for energy commodities is becoming painfully obvious

## Slide 7: Modeling Energy Prices
Energy prices have split personality (Dragana Pilipovic)
  Traditional modeling tools (Geometric Brownian Motion) may apply to long-term forward prices
  As we get closer to delivery, the price dynamics changes
  Gapping behavior of spot prices and the front of the forward curve
  Prices may be negative or equal to zero

## Slide 8: Modeling Energy Prices
Traditional answers to modeling problems seem not to perform well
  mean reversion
    seasonality of the mean level
    different rate of mean reversion for positive and negative deviations from the mean
  jump-diffusion processes
    asymmetric jumps with a positive bias
    one can speak rather of a floor-reversion

## Slide 9: Limitations of the Arbitrage Argument
In many cases it is impossible or very difficult to create a replicating portfolio
  No intra-month forward markets (or insufficient liquidity)
  It is not feasible to delta hedge with physical gas or electricity
  Balance of-the-month contract: imperfect as a hedge, low liquidity
Risk mitigation strategies are used
  Portfolio approach
  Physical positions in the underlying commodity
  Positions in physical assets (storage facilities, power plants)

## Slide 10: Recent Price History in the US: Examples
History of extreme price shocks in many trading hubs
High volatility results from a combination of a number of factors
  Shortage of generation capacity
  Extreme weather events
  Flaws in the design of the market mechanism

## Slide 13: Supply and Demand in The Power Markets
MWh
Demand
Price
Volume
Supply stack

## Slide 14: Volatility: Estimation Challenges
Limited historical data
Seasonality
  Insufficient number of price observations to properly deseasonalize the data
Non-stationary time series
The presentation below enumerates and exemplifies the difficulties
No easy solutions

## Slide 15: Definition of Volatility
Volatility can be defined only in the context of a stochastic process used to describe the dynamics of prices
Standard assumption in the option pricing theory: Geometric Brownian Motion
Definition of volatility will change if a different stochastic process is assumed
Option pricing models typically assume Geometric Brownian Motion

## Slide 16: Geometric Brownian Motion
dP = Pdt + Pdz
  P - price
   - instantaneous drift
   - volatility
  t - time
  dz - Wiener’s variable (dz =  dt, 

## Slide 17: Geometric Brownian Motion Implications
Price returns follow normal distribution
 denotes normal probability function with mean  and standard deviation 
Prices follow lognormal distribution
Volatility accumulates with time
This statement may be true or not in the case of the prices of financial instruments. It does not hold for the power prices.

## Slide 18: Estimation of Historical Volatility
Estimation of historical volatility
  Calculate price ratios: Pt / Pt-1
  Take natural logarithms of price ratios
  Calculate standard deviation of log price ratios (= logarithmic price returns)
  Annualize the standard deviation (multiply by the square root of 300 (250), 52, 12, respectively, for daily (Western U.S., Eastern U.S.), weekly and monthly data
Why use 300 or 250 for the daily data? Answer: it’s related to the number of trading days in a year.

## Slide 19: Annualization Factor
M
T
W
T
F
M
4 Daily Returns
Weekend Return

## Slide 20: Annualization Factor
Alternative approaches to annualization
  Ignore the problem: close-to-close basis
  Calendar day basis
  Trading day basis
Trading day approach
  French and Roll (1986): weekend equal to 1.107 trading days (based on close-to-close variance comparison) for U.S. stocks
  Number of days in a year: 52*(4+ 1.107) = 266

## Slide 21: Annualization Factor
Close-to-close variability of returns over weekend in the stock market is lower because the flow of information regarding stocks slows down
Is this true of energy markets?
The answer: Yes, but to a much lower extent
The information regarding weather arrives at the same rate, irrespective of the day of the week

## Slide 22: Seasonality
How does seasonality affect the volatility estimates?
Assume multiplicative seasonality
  Pt = sPa
  Seasonality coefficient s in calculations of price ratios will cancel
The price ratio corresponding to a contract rollover date should be eliminated from the sample

## Slide 24: Mean Reversion Process
Prices of commodities gravitate to the marginal cost of production
Mean reversion models borrowed from financial economics
  Ornstein - Uhlenbeck
  Brennan - Schwartz

## Slide 25: Ornstein-Uhlenbeck Process
dP = (Pa - P)dt + dz
   speed of mean reversion
   volatility
  Pa average price level
The parameters of the equation above can be estimated using a discrete version of the model above (an AR1 model)
  Pt = a + b Pt-1 + t

## Slide 26: Ornstein-Uhlenbeck Process
The coefficients of the original equation can be recovered from the estimated coefficients of the the discrete version
  Pa = -a/b
   =-log(1+b)
In this case,  is measured in monetary units, unlike standard volatility

## Slide 27: Limitations of Mean Reversion Models
The speed of mean reversion may vary above and below the mean level
A realistic price process for electricity must capture the possibility of price gaps
The spikes may be asymmetric
One should rather speak about a “floor reverting process”
  Floor levels are characterized by seasonality

## Slide 28: Modeling Price Jumps
A realistic price process for electricity must capture the possibility of price gaps
Price jumps result from interaction of demand and supply in a market with virtually no storage
The spikes to the upside are more likely
One should rather speak about a “floor reverting process”
  Floor levels are characterized by seasonality

## Slide 29: Jump-Diffusion Model
Standard approach to modeling jumps: jump-diffusion models
Example: GBM
  dP = Pdt + Pdz + (J-1)Pdq
  dq =1 if a jump occurs, 0 otherwise. Probability of a jump is 
  J - the size of the jumps
  J is typically assumed to follow a lognormal distribution, log (J) ~ N(,)

## Slide 30: Ornstein-Uhlenbeck Process (Jumps Included)
Coefficient estimates (Cinergy, Common High, Pasha)
      6/1/99 - 9/30/99
  Pa 19.96
   15.88
   99.44
  495
   19.12
  0.28
  dP = (Pa - P)dt + dz + dq*N(, )
Alternative formulation
  dP = (Pa - P)dt + Pdz

## Slide 31: Stochastic Volatility
Stochastic volatility models have been developed to capture empirically observable facts:
  Volatility tends to cluster: extreme observations tend to be followed by extreme observations
  Volatility in many markets varies with the price level and the general market direction

## Slide 32: GARCH MODEL
GARCH (Generalized Auto Regressive Heteroskedastic model)
Definition
  ln (Pt/Pt-1) = k + tt, t ~ N(0,1)
  2t+1 =  + 2t2t + 2t
  
The term k represents average level of returns, tt - the stochastic innovation to returns

## Slide 33: Model-Implied Volatility
Future spot prices can be predicted using a fundamental model, containing the following components
  Representation of the future generation stack
  Load forecast and load variability
  Assumptions regarding future fuel prices and price volatility

## Slide 34: Model-Implied Volatility
A fundamental model can be used as a simulation tool to translate the assumptions regarding load and fuel price volatility into electricity price volatility
The difficulty: a realistic fundamental model takes a very long time to run
One has to use a more simplistic model and face the consequences

## Slide 35: Correlation
A few comments on correlation
  Comments made about volatility apply generally to correlation
  A poor measure of co-movement of prices
    What is a correlation between X and Y over a symmetric interval (-x,x) if Y= X2?
  Notorious for instability
  There are better alternatives to characterize a co-dependence of prices in returns