## Slide 1
Options Pricing and Assets Valuation
Projects Presentation
Zimin Lu
Enron Research
Sept 27, 2001

## Slide 2
Functionality
Options Pricing
Assets Valuation
EOL Trading Analytics
Consulting

## Slide 3
Team

## Slide 4
Presentations
PSIM
Alex Huang and Tom Halliburton
Swing Options Pricing
  Paulo Issler
Options Pricing with Fat Tail Distributions
Alex Huang
American MC, Swing and Storage Valuation
Zimin Lu

## Slide 5
Alex Huang
Tom Halliburton
September 27th 2001
Karapiro
Built 1946
3 units
36 MW each
~120 foot head
PSIM Full Requirements Power Simulator

## Slide 6: Another Session of Electricity Stuff
  Where does this one fit in the maze of electricity models?
  Why do we need it anyway?
  A brief history
  Model details
  Applications

## Slide 7: Hierarchy of Generation Planning Models
Long term planning Henwood, SDDP, PSIM
Operational planning
Unit commitment
Market clearing
Economic dispatch - Optimal Power flow, SCADA
AGC – Automatic Generation Control
Generator governor
1 to 10 years Asset valuation, system expansion Power price trends
One year ahead Fuel requirements, maintenance planning, reservoir management
1 to 7 days ahead Bidding, pre-scheduling
CalPX…………..PJM
Every 20 minutes & on demand, small load adjustments
Every 5 to 10 seconds – Area Control Error
Continuous time – frequency keeping, machine load setting

## Slide 8: Why so many models
Solution time
  governor action within less than one second in a small system
  SDDP requires 24 hours to solve for large system
Real time vs long term planning
  Economic dispatch small adjustments
  Henwood considers long term fuel supply contracts etc.
Unit start up or unit load adjustment? Start up  non-smooth equations / integer variables.
Transmission Planning – Most are static models (no time dimension)
  System expansion, contingency analysis, remedial action strategies, real time power flows (real and reactive)

## Slide 9: A Brief History
Circa 1996 Stinson Gibner, Pavel Zadorozhny
Zimin Lu, Grant Masson
2001 Alex Huang, Tom Halliburton, Chonawee Supatgiat, Karthik Rajan
Many people directly or indirectly contributed to the model: Vince, Vasant, Krishna, Sandeep

## Slide 10: PSIM Interface

## Slide 11: Full Requirements & Asset Management
Full requirements – take over the day to day operations planning of a utility – assets, load, market purchases and sales
Asset management – market the output of a portfolio of merchant generation plants
Leveraging Enron’s marketing and analytical resources Small utilities do not have market intelligence, trading systems, modeling expertise, etc
Target: 40 deals over the next 12 months

## Slide 12: PSIM Structure
Dispatch Module
Bookkeeping (P/L) Module
Simulation Module
Input
Output
Auxiliary Functions: Hedging, Bid-Offer Spread, Fuel Switching, Generation Curtailment, Specific Deal Calculation.

## Slide 13: PSIM Inputs
Up to 10 year horizon, hourly time steps
Inputs:
  Plant physical characteristics
  Forward curves and volatilities for
    Fuel (coal, gas, oil)
    Power
  Native load
  Load profile within each day
  Load change with temperature
  Selling price of power to native load customers
  Daily mean temperatures
  Monthly profile of hourly power prices
  Correlations load/power, power/fuel
  Bid/offer spread

## Slide 14: PSIM Outputs
Intrinsic Value – from current forward curves only
Option Value – evolution of prices modeled, using volatility, random shocks.
Revenue earned by Enron (profit share)
Generation
Native load
Generator starts
Day ahead and spot:
  Sales
  Purchases

## Slide 15: PSIM Algorithm
Monte Carlo Simulation
  Long Term Random shocks:
    Correlated Monthly shock to fuel cost, load, and power price
  Short Term Random shocks:
    Temperature -> power market price, native load
    Native Load -> power market price
    Daily unit forced outage
Each day, schedule unit next day using forecast data
On the day, adjust unit loading only using data with short term shock applied.

## Slide 16: Generation Dispatch – Three Versions
Version I
If unit idle, profit = -startup cost else profit = 0
For each hour of the day, what unit load between min & max gives the most profit for that hour? Increment day’s profit.
At end of day, is total profit positive? Yes – run unit No – shut down unit
Version II
Enhanced algorithm considering ramp rate, min up/down times, stop/start any time of day.
Version III - Chonawee
Stochastic optimization – not yet fully integrated into PSIM.

## Slide 17: Long Term Shock: Forward Prices

## Slide 18: Short Term Shock: Hourly Prices

## Slide 19: Software
Spreadsheet interface
VBA code to extract data
Dll written in C++
Links to Oracle database for fuel costs

## Slide 20: Application: Frontera Deal
450 MW combined cycle unit, at 135 MW base load, merchant plant, owned by TECO.
Located near Rio Grande.
Subject to ISO generation curtailment.
Enron recommends on daily operation issues. Use our marketing systems and intelligence.
Enron shares a certain percentage of profit over a pre-determined threshold.

## Slide 21: Application: MDEA
A small utility company near Yazoo, Mississippi.
Full requirement deal supplying the load for Yazoo area – 5 small units ( 5 to 22 MW)
Too small to negotiate “good” purchases / sales with neighbors.
Enron recommends on operation issues.
Enron shares 40% of peak savings, $1/MWh offpeak profit.