## Slide 1: Newest approaches to Industrial/Commercial Power Quality
Alex McEachern
Power Standards Lab
(510) 658-9600
www.PowerStandards.com
www.Alex.McEachern.com Silicon Valley Manufacturing Group – 8 August 2001

## Slide 2: Power Quality in Silicon Valley
Traditional approaches to power quality at high tech industrial/commercial facilities
  Why they don’t work
One new approach
  Very low cost, or free
One future approach…
www.Alex.McEachern.com Silicon Valley Manufacturing Group – 8 August 2001

## Slide 3: Traditional approaches
Tradition #1: Overkill
  Clean up everything, everywhere
    Big UPS/generator
    Individual UPS / filters
    Why it doesn’t work
      Expensive – unrequired coverage
      Possibly unreliable
      Raises source impedance
      Doesn’t solve the problem
www.Alex.McEachern.com Silicon Valley Manufacturing Group – 8 August 2001

## Slide 4: Traditional approaches
Tradition #2: Passive
  Wait for a problem, then monitor, then solve
    Pray for a repeat of the problem (!)
    Actual problem vs. power quality problem
      Cold beer and hot showers
    Why it doesn’t work
      Management doesn’t see you do anything
      Doctor / softball bat analogy
      Doesn’t solve the problem
www.Alex.McEachern.com Silicon Valley Manufacturing Group – 8 August 2001

## Slide 5: New approach
Power Standards Lab provides
bad quality power.
www.Alex.McEachern.com Silicon Valley Manufacturing Group – 8 August 2001

## Slide 6: What if cars were built like this?
www.Alex.McEachern.com Silicon Valley Manufacturing Group – 8 August 2001
“Requires road that
is +/- 10% smooth.”

## Slide 7: The basic idea:
www.Alex.McEachern.com Silicon Valley Manufacturing Group – 8 August 2001
Power quality is a compatibility issue between
the electric power system and the sensitive load.
To solve the problem, improve either one.

## Slide 8: Solve power quality problems by testing and improving the loads.
www.Alex.McEachern.com Silicon Valley Manufacturing Group – 8 August 2001
Cheap or free improvement
Fundamentally sound
Active, not passive
New standard in semiconductor
business: SEMI F47

## Slide 9: Typical on-site tests when you suspect a power quality problem
www.Alex.McEachern.com Silicon Valley Manufacturing Group – 8 August 2001
Voltage sags – various depths
and durations – 50% 200ms
High frequency impulses:
up to 6kV, up to 5kA
Test equipment: sag generators,
impulse generators, couplers,
data acquisition

## Slide 10: Examples of this approach
www.Alex.McEachern.com Silicon Valley Manufacturing Group – 8 August 2001
Laser manufacturing
Electronic assembly
Automobile plant

## Slide 11: SEMI F47 – a new standard
www.Alex.McEachern.com Silicon Valley Manufacturing Group – 8 August 2001
Requires manufacturing equipment
to tolerate three specific voltage sags
Solves 90%+ of the PQ problems
SEMI F42 is the test standard
Other standards starting to follow
(IEC 61000-4-11, 61000-6-2, NEMA…)

## Slide 12: A future approach to power quality
www.Alex.McEachern.com Silicon Valley Manufacturing Group – 8 August 2001
Doubt is a basic issue in power quality
“Power-quality-aware” loads
Full 3-phase power quality monitoring
built-in – sags, swells, impulses,
frequency, phase rotation, loss,
neutral-ground, waveforms

## Slide 13: Recommendations
www.Alex.McEachern.com Silicon Valley Manufacturing Group – 8 August 2001
Add on-site testing using bad quality power
to your arsenal.
2. Consider specifying SEMI F47 on major
purchases.
3. Watch for power-quality-aware systems
in the future.

## Slide 14: Newest approaches to Industrial/Commercial Power Quality
Alex McEachern
Power Standards Lab
(510) 658-9600
www.PowerStandards.com
www.Alex.McEachern.com Silicon Valley Manufacturing Group – 8 August 2001