## Slide 1
2001 PJM
WEST RESERVE STUDY
Reliability Committee Meeting
Agenda Item # 5B
October 18, 2001

## Slide 2
RAA West Requirements
Available Capacity Obligations
  Obligation is mandatory
    Failure to comply results in CDR charges
  Obligation is equal to 106% of peak load forecast for next day
  Obligation is met with available resources
Installed Capacity Obligations
  Obligation is NOT mandatory
    May serve as an insurance policy to limit the amount of CDR charges
  Is NOT a substitute for satisfying ACAP Obligations
  Obligation is based on Forecasted Period Peak Load (FPPL) and Installed Reserve Margin (IRM) of forecast period
  Obligation is met with installed capacity resources
PJM West Reserve Study

## Slide 3
PJM West Reliability Study
Determination of Installed Reserve Margins (IRM)
  Based on RAA East “R” Study Procedure
  Single IRM calculated for PJM (East + West)
  IRM will vary by forecast period
Verification of 106% Available Reserve Margin
  Demonstrate that 106% day-ahead Available Capacity (ACAP) margin provides reliability level consistent with PJM East standard of a loss of load event, on average, 1 day in 10 years
PJM West Reserve Study

## Slide 4
IRM Study
Based on 2001 R Study Case with AP shifted from “World” into PJM
Study year is 2001/2002
Existing PJM West units modeled with actual rather than GADS class average performance data
PJM East and West capacity models updated with new generation interconnection plans
PJM West load forecast data supplied by AP
New CBM calculated to reflect expanded PJM boundaries
Single IRM determined for expanded PJM
  PJM West IRM converted from an annual 50/50 peak load basis to a forecast period 90/10 peak load basis
PJM West Reserve Study

## Slide 5
CBM Study
Full benefit of 3500 MW CBM to PJM East will be preserved.
Based on PJM East CBM Calculation Procedure.
PJM West merged with PJM East. ATC paths redefined to reflect expanded PJM boundaries.
PJM modeled at 90/10 summer peak load level.
Four generation outage scenarios defined in PJM
  Uniform, High East, High West, High South
PJM imports increased in proportion to external regions’ ICAP reserves.
At transmission limit, emergency import capability is sum of inbound ATC path flows less firm ICAP purchases.
PJM Emergency Import Capability is arithmetic average of four outage scenario import capabilities.
PJM West Reserve Study

## Slide 6
PJM West Reserve Study

## Slide 7
PJM West Reserve Study

## Slide 8
PJM West Reserve Study

## Slide 9
PJM West Reserve Study

## Slide 10
Reserve Study Schedule
September 17, 2001
- Review of Study Scope and Procedure with PJM Planning Comm.
October 9, 2001
- Review of Study Scope and Procedure with RAA West Stakeholders
October 18, 2001
- Review of IRM/CBM Study Results with RAA Reliability Comm.
October 23, 2001
- Release of IRM/CBM Study Report
October 25, 2001
- Review of IRM/CBM Study Report with PJM Planning Comm.
PJM West Reserve Study

## Slide 11
Reserve Study Schedule (cont’d)
October 31, 2001
- PJM Board Approval of Forecast Period IRM to be implemented
January 1, 2002
November 30, 2001
- Completion of ACAP Reserve Study and review of results by
Planning Comm., Reliability Comm. and PJM Board
Spring 2002
- IRM and ACAP Reserve Studies performed for 2002/2003 planning
period
- Current methods subject to modification
    Reliability Re-architecture Project
PJM West Reserve Study