## Slide 1: The Real Flow Model The Solution for Congestion Management
A Presentation For Southwest Power Pool
Congestion Management Subteam Meeting
Dallas/Ft.Worth Airport Hyatt
July 31-August 1, 2000
Notes: Recognize that many of you have seen a number of presentations on flowbased models at previous meetings.
For those who are unclear or are new, a brief review followed by examples, discussion of implementation steps and comparisons with the balance of the time allotted to answering questions.

## Slide 2: Comparing Proposals
What is not in dispute:
  RTO operation of Real-Time Balancing Market covering the entire RTO.
  Existing rights must be converted whether using FTR/PTRs by combination of allocation and auction.
  All use of system must be subject to the same congestion management system including native load.
The key question is how best to organize the Forward Market by:
  A decentralized market in energy and transmission or
  A centralized extension of the dispatch model.

## Slide 3: Model Selection Criteria
Strike a balance that achieves:
  Simplicity of the commercial model (to enhance trading).
  Acceptably small amounts of real-time congestion.
  Consistency between the commercial model ( the Forward Market) and the operations model (the Real-Time Market.
  Controls implementation cost.

## Slide 4: Markets Under Real Flow
Forward Market -- Before-the-Fact Prices (ex-ante):
  Transactions prior to Day-Ahead Scheduling.
  Day-Ahead Scheduling to produce operating plan.
  Adjustments to Schedules prior to real time .
Real-Time -- After-the-fact Prices (ex-post):
  Balancing (Spot) Market operated by RTO.
Settlement:
  After the fact trading of zonal imbalances.

## Slide 5: What is Real Flow?
A flow-based, physical rights model for congestion management.
Key model features:
  Identified Commercially Significant Flowgates (CSF).
  Physical Transmission Rights (PTRs) -- Defined units of physical capacity in the Commercially Significant Flowgates.
  PTRs traded by Market Participants to adjust their needs.
  Trades facilitated by an electronic exchange.
  Ex-ante prices for scheduled energy and transmission.
  Ex-post prices for imbalances from schedule.

## Slide 6: Using PTRs
RTO posts distribution factors.
  Impact on Flowgates for Injection-Withdrawal Pairs.
  Market participants use factor to acquire needed PTRs.
Market Participants submit balanced schedules.
  Generation = Load + Losses.
  Injections and withdrawals specified by Zone.
RTO accepts schedules which are:
  Tests Flowgate rights for consistency with Schedule.
  Ownership status transmitted by Exchange.

## Slide 7: A Real Flow Example
FG 1
100 MW
Limit
100 MW
Limit
FG 2
A
D
B
C
Transmission Distribution Factors
(From Power Flow Analysis)
FG1
FG2
POI to POW
A - D - 0.25 - 0.75
B - D 0.30 - 0.30
C - D 0.10 - 0.10
B-A = (B-D) + (D-A) = (B-D) - (A-D)
B to A Schedule Requirements
FG 1: (B-A) = (0.30) - (-.25) = 0.55
FG 2: (B-A) = (-0.30) - (-.75) = 0.45

## Slide 8: Defining PTRs
Select “commercially significant” flowgates (CSFs) to release into the market
  Perform load flow and market simulation analysis to determine likely congestion patterns and value.
  CSFs determined based on threshold level of significance.
  Selection of Flowgates is re-visited at least annually, and revised as the grid evolves.
  Adding or removing Flowgates does not alter the complexity of market participation.

## Slide 9: How Many Commercially Significant Flowgates?
100%
80%
70%
60%
50%
40%
30%
20%
10%
90%
0%
Number of Flowgates
Congestion Captured
k m n
Congestion Capture By Given Number of Flowgates

## Slide 10: Differences in TDFs (PTDF and OTDF)
SPP Area-Area TDF
  Factors changed for Area to Area transfer depends upon the units included in injection area and the withdrawal area for study.
  Significant Flowgates can be buried inside an area.
  Point-to-Point capacity sold.
Real Flow TDFs
  Commercially Significant Flowgates used to draw the boundaries of the zones.
  A set of seasonal or annual ( a design decision) are produced using a standard set of unit aggregations for zone to zone transfers.
  Segment capacity sold, i.e, build your own Point-to-Point.

## Slide 11: Simultaneous Transfer Capability
Sets of Flowgates fall into “Corridors” between major concentrations of generation and load.
  Some flow gates load affected by one set of conditions, some by another.
  Since “Native Load” served by PTRs as well, all flow included in evaluation of expected flow.
  Determine expected flow pattern(s) for release period.
  When the same conditions affect a set of Flowgates consider simultaneous capability.
Manage by buy-back, redispatch, pro-rata PTR reduction
  PTR holders make economic decisions to adjust their schedules.

## Slide 12: RTO Releases
Initial
  Conversion of existing rights.
Annual
  Evaluation of changes in network, added Flowgates, etc.
Seasonal / Monthly
  When flow pattern provide higher simultaneous limit.
Weekly
  Consider generator status and improved load forecast.
Daily
  Same as weekly plus “Use-It-Or-Lose-It” provisions.

## Slide 13: PTR Owner Releases
Sales (and Purchases)
  Offered in Exchange when aligning transmission portfolio with changes in load and resource plans.
Recallable Offerings
  At anytime, a PTR could be offered in the Exchange subject to conditions, e.g., recall on 8 hours notice.
  Release prior to “Use-It-Or-Lose-It”
    Release for firm resale, right holder gets revenue.
    Release to RTO Recallable Stack:
      RTO sells from highest bid to lowest
      If original holder exercised recall, lowest price offer cut first.

## Slide 14: Real Flow Allows Decentralized Decisions
Each Market Participant acquires the PTRs needed to meets its expected needs:
  Conversion of existing rights (native load & contracts)
  Purchase in auction (annual, monthly, etc.)
Parties adjusts energy and transmission positions based on their own future price expectations:
  Release and purchase to adjust portfolio of PTRs.
  Exchanges facilitates trade with software allowing point-point reconfiguration or Flowgate specific trades.
  Prices are ex-ante, known at the time of the trade.

## Slide 15: Exchanges and Forward markets
The marketplace operates continuously clearing exchanges for energy, transmission rights and ancillary services.
Exchange(s) operate up to the hour-ahead scheduling deadlines.
Market participants use these exchanges (and bilateral trades) to acquire transmission rights, or to make buy-sell arrangements in lieu of transmission rights.
The RTO has no role in forward ancillary services markets, except as “provider of last resort” and for unanticipated real-time conditions.
The RTO posts transmission loss requirements and ancillary services obligations well in advance of the scheduling day.
Notes: <date/time>

## Slide 16: Building and Executing The Operational Plan
Scheduling Coordinators:
  Market Participants or their Agents for Participants who interface with RTO for scheduling, adjustments, etc.
  Scheduling Coordinators certified based on financial and technical qualifications.
Day-Ahead Scheduling used to develop an Operational Plan which will assure secure operation of the system.
Scheduling Coordinators make Adjustment Schedules to adjust market/load/resource changes
RTO accepts adjustments if no new congestion.
RTO Operates a Real-Time Balancing Market.

## Slide 17: Using the Exchange*
SC1 -- Schedules 100 MW B-A
  Releases 5 MW on FG1
  Releases 5 MW on FG2
SC2 -- Schedules 81 MW from A with 49MW to B and 32MW to C
  Releases 2 MW on FG1
  Releases 7 MW on FG2
FG 1
100 MW
Limit
100 MW
Limit
FG 2
A
D
B
C
SC3 -- Goes to Exchange to 50 MW from D to B
  Needs 15 MW on FG2,
  12 MW available from releases offers at price $ xx.xx but would limit schedule to 40 MW.
  3 additional MW available from a counter flow bid at $ yy.yy, which obligates SC 4 to scheduled POI-POW flow.
*Calculation details in attached Example Appendix

## Slide 18: The RTO Function Forward Markets
Prior to Day-Ahead
  With Transmission Exchange: TDF matrix, capacity releases/reductions, PTR purchase status.
  Energy Exchange: receive schedules and adjustments, post PTR purchase requirements.
  Ancillary Exchange: post ancillary and loss requirements for energy transactions, purchase call contracts for day-of deficiencies.
Day-Ahead and Day-Of
  Receive, evaluate and accept schedules and schedule adjustments.
Notes: <date/time>

## Slide 19: The RTO Function Real Time
Active Operations.
  Perform coordinated, hierarchical control of dispatch using signals to existing control areas/centers.
  Perform redispatch and balancing function using ancillary and supplemental energy bids.
  Run balancing market to develop imbalance prices.
Monitoring System Security.

## Slide 20: The RTO Function After-the-Fact
Settlement.
  Imbalance between schedule and actual injections and withdrawals charged at zonal rates.
  Allows market participants to trade imbalances within zones.
  Collect net imbalance payments.
  Calculate and record cost of “intra-zonal” congestion.
  Differences in real-time prices constitute real-time congestion cost.

## Slide 21: Addressing Key Issues: Seams
Real Flow provides a common basis for parallel flow recognition between neighboring RTOs.
  TDFs developed which recognized external flow components.
  Result is explicitly recognition of external effects by Flowgate owners through Exchange(s)
  Possible terms of Inter-RTO reciprocity agreements:
    Fixed cost transfer payments to increase scale of the non-pancaked scheduling area.
    Initial exchange of PTRs to facilitate existing right conversions.
    Inter-Exchange data sharing to foster PTR trade.

## Slide 22: Addressing Key Issues: System Expansion
Forward Sale of Capacity is a pre-requisite to expansions which increase transfer capability.
  Expansion produces transfer capability which translates into Flowgate PTRs.
  The expansion decision is a comparison between :
    The present value of expected future PTR purchases either from the auction or secondary market, versus
    Today’s investment cost for a new line, transformer, etc.
Forward sale of right to collect future congestion rents is problematic.
  Rents zero when line built and grow as system loads up.

## Slide 23: Approximations
Mismatch between commercial model of congestion and dispatch model.
  Zonal aggregation of generators and loads.
  RTO cleans up intra-zonal congestion due to mismatch of Flowgates with actual system.
  Add Flowgates and Zones if necessary at with release reviews made annual allocation/auction.
Linearization of losses.
  Average losses?
  Marginal losses?

## Slide 24: Forward vs Real-Time Market Results
LMP implementations in PJM and New York use a two-settlement system: (1) Day-Ahead and (2) Real-Time
  FTRs (or TCCs) apply only to the Day-Ahead Market
  Variance from Day-Ahead is settled in Real-Time
Strategic Bidding in Day-Ahead Market
  Load underbid to set day-ahead price lower than clearing price would have been with full bid load
  Resulting Day-Ahead dispatch is a poor representation of the Real-Time dispatch

## Slide 25: NY-ISO Major Constraints
Dunwoodie
West
Capital
Central
Hudson Valley
Millwood
N.Y.C.
Long Island
Area of Interest

## Slide 26: NY-ISO Day-Ahead Congestion June 1, 2000
154.34
$
P
8.50
$
L
(17.79)
$
C
157.17
$
P
9.58
$
L
(19.54)
$
C
159.11
$
P
11.17
$
L
(19.89)
$
C
132.99
$
P
13.74
$
L
8.80
$
C
Hudson Valley
Millwood
Dunnwoodie
New York City
159.13
$
P
3.89
$
L
(96.60)
$
C
169.15
$
P
4.39
$
L
(106.12)
$
C
179.79
$
P
5.11
$
L
(108.04)
$
C
173.22
$
P
6.29
$
L
(108.29)
$
C
Hudson Valley
Millwood
Dunnwoodie
New York City
Hour Begin 1100
Hour Begin 1000
$ 0.25
($28.70)
$ 1.92
$ 9.52
$ 0.35
$ 1.75
$ 11.69
 (26.60)

## Slide 27: NY-ISO Day-Ahead Prices June 1, 2000
6/1/00 0:00
6/1/00 3:00
6/1/00 6:00
6/1/00 9:00
6/1/00 12:00
6/1/00 15:00
6/1/00 18:00
6/1/00 21:00
WEST
GENESE
CENTRL
MHK VL
CAPITL
HUD VL
MILLWD
DUNWOD
N.Y.C.
LONGIL
0
50
100
150
200
250
$/MWh
Time
Zone

## Slide 28: NY-ISO Real-Time Prices June 1, 2000
6/1/00 0:00
6/1/00 3:00
6/1/00 6:00
6/1/00 9:00
6/1/00 12:00
6/1/00 15:00
6/1/00 18:00
6/1/00 21:00
WEST
GENESE
CENTRL
MHK VL
CAPITL
HUD VL
MILLWD
DUNWOD
N.Y.C.
LONGIL
-50.0
0.0
50.0
100.0
150.0
200.0
$/MWh
Time
Zone

## Slide 29: Transmission Property Rights
Financial Transmission Rights - FTRs - (LMP)
  Guarantees the holder the price difference between two points (no physical certainty)
  Holder pays if the price difference is negative (obligation)
  Defined for every combination of nodes (complex, illiquid)
  Prices for delivery not known until after the fact (low price certainty)
Physical Transmission Rights - PTRs - (Real Flow)
  Provides the right to inject a certain amount of power at point A and take it out at point B (delivery certainty)
  Holders surrender the right if unused (option)
  Defined for few, commercially significant flowgates (simple, liquid)
  Prices continuously developed in forward market (high price certainty)

## Slide 30: Summary
Real Flow achieves all the objectives of market-based congestion management while preserving the reliability of the grid.
Real Flow allows market participants manage risk up to Real-Time
Forward Market produce realistic operational information for operator.
Ex-post pricing exposure limited to Real-Time Balance Market.