## Slide 1: Regulatory Overview
Andy Rodriquez

## Slide 2: Basic Agenda
Review of NERC activities
Review of FERC activities
Open forum discussion on the needs of West Desk

## Slide 3: NERC Policy 3
NERC Interchange Subcommittee

## Slide 4: Policy 3 Implementation
Charles Yeung (Chair of NERC IS) has been working with WSCC OC and ISAS to get WSCC up to speed on tagging
WSCC is currently non-compliant with Policy 3, and is asking for waivers/ exemptions from requirements

## Slide 5: Policy 3 Implementation
Issues
  No WSCC-wide implementation of real-time tagging
    Several entities seem to be stonewalling on this issue
    WSCC seems to recognize this as a problem, but feels they cannot pursue aggressively
  WSCC does not want to tag all P3-mandated transactions (specifically, they want to be exempt from tagging inadvertent payback and dynamic schedules)
  WSCC has several other P3/tagging rules that conflict with NERC rules

## Slide 6: Policy 3 Implementation
Actions
  IS has sent chastising letter to WSCC OC, telling them their non-compliance is unacceptable
  IS has rejected WSCC variance requests for exemptions for IA, Dynamic
  WSCC will likely appeal to the NERC OC

## Slide 7: Policy 3 Implementation
Discussion
  Should we continue to fight aggressively for WSCC to “get in line” with NERC?
  Or should we work on fighting locally, and get more involved with the WSCC?

## Slide 8: NERC Policy 3
NERC TISWG
And E-Tag 1.7

## Slide 9: E-Tag 1.7 – Why?
Need bridge between E-Tag and OASIS Phase II
  New technology is sorely needed – this will provide incremental step using new technology
  Provides less critical environment to investigate concepts for electronic scheduling

## Slide 10: E-Tag 1.7 – Why?
Several issues brought up to be addressed by several groups:
  Losses
  PSE Adjustments
  Stacking
  POR/POD and Source/Sink
Results
  Major re-write of entire E-tag specification

## Slide 11: Financial and Physical Paths
Paths are more hierarchically arranged to reflect the business model
Identifies Sources, Sinks, PORs, and PODs
Financial
Merchant
Load Server
Source Gen
Sink Load
Import Wheel
Export Wheel
Physical

## Slide 12: Profiles
All profiles are more complex – but also more flexible. Complexity only comes into play when flexibility is used.
PSE issued Adjustments allowed now
All adjustments go through an approval/ confirmation process

## Slide 13: Normal Transaction

## Slide 14: Curtailment, PSE Adjustment and Reload

## Slide 15: Transmission Stacking
Both Vertical and Horizontal stacking is supported
This should allow more diverse use of transmission

## Slide 16: Transmission Stacking

## Slide 17: Transmission Stacking

## Slide 18: Corrections
Allow for changes to tags during the approval process
Cannot completely change tag (i.e., should have same path, etc…)

## Slide 19: Schedule Types
Several different defined schedule types
  NORMAL
  DYNAMIC
  EMERGENCY
  MRD
  LOSS SUPPLY
  CAPACITY

## Slide 20: GPE/LSE Approval
Merchant Generator and LSE approve energy production/consumption is accurate and valid

## Slide 21: Recovery functions
Several new recovery functions to aid during unforeseen computer problems.

## Slide 22: Registration
Developing new Registry with standard POR/POD names, Sources, and Sinks
  PSEs will register their sources and sinks, to be approved by host CAs
  TPs will register PORs and PODs, based on their tariffs

## Slide 23: Technical Landscape
E-Tag 1.7 Impacts to Enron
  Training
    Most “standard” features will look and act the same as they do today, but the more advanced features will need to be taught to our users
  Technology
    OATI will be providing this system – unless we elect to write our own or purchase from a different vendor

## Slide 24: Technical Landscape
Timing
  Current schedule is for November 13 implementation
  May be delayed until March
    Registration system is still being developed
    System testing and training still incomplete
    Some TPs and CAs are arguing that they will not be able to modify their back-end systems in time

## Slide 25: Technical Landscape
Training
  Two training sessions planned
    October 3-4 Phoenix
    October 10-11 Atlanta
  Training will be a four hour session, to be offered at four different times (Wed AM, Wed PM, Thurs AM, Thurs PM)
  Vendors will offer demos and training throughout day

## Slide 26: FERC ESC
Business Practices

## Slide 27: Electronic Scheduling Collaborative
Goal is to eliminate seams through FERC-Approved Business Practices
Facilitate development of standard OASIS, to include the Electronic Scheduling interface
Currently 29 practices described
Guiding the OASIS Standards Collaborative
WSCC feels they have not been represented

## Slide 28: Business Practice 1
Transmission Product Timing granularity
  Transmission must be sold in 15 minute blocks
  This does not preclude larger increments, but at a minimum, the TP must allow someone to reserve a 15-minute piece of transmission

## Slide 29: Business Practice 2
OASIS Timing Requirements
  Basically identical to 638

## Slide 30: Business Practice 3
Transfer of Scheduling Rights to Transmission
  Attempts to facilitate secondary market for TX
  TCs can
    Transfer scheduling rights (PSE to PSE transaction)
    Reassign transmission (PSE to TP to PSE transaction)

## Slide 31: Business Practice 4
Source to Sink Reservation Requirements
  Defines that Transmission Requests should be granted based on analysis of Source-to-sink flows
    If no S/S specified, TP to assume it is POR/POD

## Slide 32: Business Practice 5
Releasing unscheduled Firm as NF Capacity
  TPs can resell unscheduled Firm as NF
  Holders of Firm still have rights, and will displace NF holders if they exercise

## Slide 33: Business Practice 6
Decrementing ATC: Available vs. Committed vs. Scheduled
  Debate centers on what ATC should be based on:
    TTC minus Reservations
    TTC minus Pending Schedules
    TTC minus Approved Schedules

## Slide 34: Business Practice 7
Shifting Transmission Products across time
  Allows for TCs to move reservation forward or back up to one hour

## Slide 35: Business Practice 8
Transmission Stacking
  Allows for TCs to use several different reservations to schedule their transaction

## Slide 36: Business Practice 9
Source to Sink Evaluation
  Allows for use of non-S/S transmission to support S/S transaction
    IF S/S match, approve schedule
    If S/S do not match but no constraint, approve schedule
    If S/S do not match but constraint, deny schedule
    Flow based systems work on FG coverage

## Slide 37: Business Practice 10
Energy Product Timing Granularity
  Energy product must be sold in 15 minute blocks
  This does not preclude larger increments, but at a minimum, the merchant/LSE must allow someone to schedule a 15-minute piece of supply/demand

## Slide 38: Business Practice 11
Transaction Types
  Dynamic
  Emergency
  Loss Supply
  MRD
  Normal
  A few others, but they probably need to be removed

## Slide 39: Business Practice 12
Generator Ramping
  10 minute straddle ramping with block accounting
  Lager ramps must be accomplished through multiple ramps (i.e., multiple inflection points)

## Slide 40: Business Practice 13
Request Submission
  Interday – 20 minutes with passive approval
  Undefined for other scenarios

## Slide 41: Business Practice 14
Interchange Authority Evaluations
  Missing information can “hold” a schedule, with passive denial

## Slide 42: Business Practice 15
Schedule Dissemination
  Schedule must be sent to host BAs, SAs, RTOs, and TSPs, as well as PSEs

## Slide 43: Business Practice 16
Communication Failures
  Defines course of actions when systems fail
  Defines BA operation during loss of system

## Slide 44: Business Practice 17
Approval Rights
  Defines who has rights to approve a transaction at what points in time
  PSEs, TSPs, BAs, SAs, RTOs

## Slide 45: Business Practice 18
Approval Timing
  How quickly approvers must respond
    10 minutes on inter-day
    Undefined for other scenarios

## Slide 46: Business Practice 19
Approval Criteria
  What entities may use to approve/deny a schedule

## Slide 47: Business Practice 20
Proxy Approval rights
  Defines that an entity may transfer their approval rights to another entity (such as an RTO, or other 3rd party)

## Slide 48: Business Practice 21
Approval Overrides
  Defines that Interchange Authority may override approvals/denials to mitigate communications failures

## Slide 49: Business Practice 22
Schedule Status Updating
  Defines who receives schedule status changes (all)

## Slide 50: Business Practice 23
Schedule Status Timing
  Defines when schedule status changes are sent out (ASAP)

## Slide 51: Business Practice 24
Real Time Checkout
  Defines process for checking out schedules prior to start

## Slide 52: Business Practice 25
After the Fact Time Checkout
  Defines process for checking out schedules following completion

## Slide 53: Business Practice 26
Curtailments and Reloads
  Defines terms and rules associated with C & R.

## Slide 54: Business Practice 27
One Stop Shopping Coordination
  Purchase of source to sink path via one request

## Slide 55: Business Practice 28
One Stop Shopping Buy at Market
  Purchase of transmission service at time of scheduling

## Slide 56: Business Practice 29
Loss Accounting
  Will focus on using EI market for losses
  In-Kind within the schedule will not be supported (i.e., 108-106-104-102-100)
  Int and Ext can be implemented, but system will not support directly

## Slide 57: Summary
Several of these BPs conflict with the way business is done today, both in the East and the West
ESC has agreed that to “fix” the industry, we need to greatly change the way things are done today
If we end up with 5 RTOs, these may not really matter (assuming practices will be consistent within the RTO, then seams agreements may solve)

## Slide 58: FERC OSC
Fragmented Scheduling
and OASIS Phase II

## Slide 59: Technical Landscape
Scheduling - OASIS Phase II
  Radical changes to electronic scheduling process
  Goal is to remove seams through technology
  Much more comprehensive process
    Not just “Transmission Service”
    Will likely incorporate postings, market interface portals, scheduling portals, and congestion management portals
    Will likely be several different systems working together, similar to E-Tag

## Slide 60: System Architecture
Market Systems (energy markets, auctions, etc…)
Energy Transaction Manager (trading system)
Transmission and Ancillary Service Transaction Manager (OASIS)
Scheduling System (new tool, position manager)
Schedule Assembler (new tool, Tag Agent)
Interchange Authority (Tag Authority)
BA Approval (Tag Approval)
Reliability Assessment System (IDC, USF, etc…)

## Slide 61
Transmission
and Ancillary
Service Manager
AS
Market
FGR
Auction
Energy
Transaction
System
Scheduling
System
Schedule
Assembler
Book Outs
Physical
Schedule
Fragments
Schedule
Assembler
Schedule
Assembler
Interchange
Authority
BA Approvals
TSP Approvals
RAS
Schedule
Fragmented Scheduling Basic System Interactions

## Slide 62: OASIS Phase II
Traditional functions will still exist
New functionality (AS markets, FGR Auctions, etc…) likely to be handled through “plug in” modules that interface with other components
Scheduling will be accomplished automatically as a function of balancing physical positions across the market (i.e., Frag Scheduling)

## Slide 63: Premises of Frag Scheduling
Traders want a commodity, not a specialized product
  Should be able to aggregate/disaggregate positions
  Should be able to move efficiently between physical and financial

## Slide 64: Premises of Frag Scheduling
Operators want a specialized product, not a commodity
  Should be able to analyze security impacts
  Should be able to unwind efficiently if necessary

## Slide 65: Goal for Frag Scheduling
Develop a system that acts as a commodity trading framework that can derive physical schedules from trades (and vice versa) as necessary
  Speculative positions should be convertible to physical schedules
  Physical schedules should be convertible back to financial positions

## Slide 66: Deal Making
Trades and confirmation of deals results in creation of energy position documents
Internet
Long
Short

## Slide 67: Book-outs and Schedules
Schedulers balance positions through linking position schedules (as book-outs, title transfers, or wheels)
Short
Long
Short
Long
Short
Long
Transmission
Wheel
Book-out
Transmission
Wheel
Title Transfer

## Slide 68: Book-outs and Schedules
LSEs and Merchants balance by linking physical resource schedules to position schedules
Short
Long

## Slide 69: Linkages and Assembly
Linkages are stored on Assemblers, which exchange Linkage Information and watch for potential Source-to-Sink assembly
Short
Long
Short

## Slide 70: Linkages and Assembly
One Assembler builds the Source-to-Sink Assembly
Short
Long
Short
Long
Short
Long
Short
Long
Short
Long

## Slide 71: Source to Sink Scheduling
Once Source-to-Sink Assembly is built, system is treated like an E-Tag and sent to Interchange Authority
Short
Long
Short
Long
Short
Long
Short
Long
Short
Long

## Slide 72: Curtailment
Under Curtailment, curtailed portions are split and returned to Assemblers as unlinked assemblies. PSEs may disassemble and rebalance as they wish.
Long
Short
Short
Long
Short
Long

## Slide 73: Additional Notes
Works with Bilaterals
  Counterparties create transactions
  Transaction modified based on changes
Works with Centralized Markets, Exchanges
  Market Operators broker and create transactions
  Transaction modified based on markets

## Slide 74: Additional Notes
Works with Contract Path (Phys or Fin)
  Linkages contain specific reservations
Works with FIN Flowgates
  Linkages contain RTOs
  Payment handled in settlement process (hedging instrument vs. real-time congestion costs)
  Can work with Phys, but will be unwieldy (same with all other proposals when using Phys FG)

## Slide 75: Technical Landscape
OASIS Phase II – Impacts to Enron
  Training
    Will require significant training. While concepts will be familiar, implementation will be very different from how things are done today
  Technology
    Discussing concepts with NomLogic folks
    Will either want to write our own software, work with vendor(s), or combination of the two

## Slide 76: FERC RTOs
Development and Timing

## Slide 77: Current Status
Business as usual
  Several CAs & TPs
  PTP TX service
  Non-Standard Scheduling (Tags, proprietary systems, etc..)
  Limited Congestion Management (mostly ATC and TLR)

## Slide 78: Order 2000 RTO Development
Prior to recent Orders
  14 North American RTOs
    Eastern Interconnection: ARTO, MISO, SPP, Grid FL, Grid South, SE Trans, PJM, ISO-NE, NY-ISO, Crescent Moon
    ERCOT Interconnection: ERCOT ISO/RTO
    Western Interconnection: CAISO, Desert Star, RTO West

## Slide 79: Order 2000 RTO Development
After recent Orders
  5 North American RTOs?
    Grid FL, Grid South, SE Trans, Entergy
      Mediations complete, ALJ report filed
    PJM, ISO-NE, NY-ISO
      Mediations complete, ALJ report filed
    ARTO, MISO, SPP, Crescent Moon
      States calling for mediation process, SPP and MISO back in negotiations for merger
    CAISO, Desert Star, RTO West
      No definitive action yet
    ERCOT ISO
      No change

## Slide 80: Order 2000 RTO Development
Uncertainty
  Will any RTOs start up on Dec 15?
  If so, what will their lifespan be?
  How can we address seams between RTOs and non-RTOs?

## Slide 81: Order 2000 RTO Development
PJM: Running as ISO
ISO-NE: Running as ISO
NY-ISO: Running as ISO
PJM model is favored by FERC
PJM model is available
PJM model is gaining acceptance

## Slide 82: Order 2000 RTO Development
ARTO: Dec 15 startup uncertain (tools and design seems far along, but mandate from stakeholders very shaky
MISO: Dec 15 startup unlikely (in market trials) – may be only regional tariff operational
SPP: Dec 15 startup unlikely (developing software, but market trials cancelled)
Crescent Moon: Unknown (unlikely)

## Slide 83: Order 2000 RTO Development
Grid South: Dec 15 startup unlikely
Grid Florida: Dec 15 startup unlikely
SE Trans: Dec 15 startup unlikely
Entergy: Dec 15 startup unlikely

## Slide 84: Order 2000 RTO Development
CA ISO: Existing ISO
Desert Star: Unknown (unlikely)
RTO West: Unknown (unlikely)

## Slide 85: Day 1 Issues
What will the markets look like?
  Established ISOs (PJM, ISO-NE, NY-ISO, ERCOT-ISO, IMO, CA-ISO)
    Forward markets, balancing markets, some AS markets
    Web interfaces or API/file transfers
  Forming RTOs
    Balancing markets

## Slide 86: Day 2 Issues
Day 1 operations will be significantly different from Day 2
  Congestion Management?
    Transmission Risk Management instruments?
  Energy Markets?
Some advocates are promoting the concept that day 1 be eliminated and we go directly to day 2

## Slide 87: NAERO
Reliability Legislation,
EISB, and other Questions

## Slide 88: NAERO/EISB
Where is the industry’s leadership?
  NERC wants to take the job and lead strongly, with FERC oversight but not necessarily deference to FERC
  RTOs want to lead regionally and deal with FERC directly through their tariffs, with NERC/Regional Councils playing a minimal role
  FERC wants it to be EISB, with a balanced industry collaboration
  No one knows what’s going to happen to Regional Councils

## Slide 89: Current Situation
Cross-Participation and Loose Collaboration
Regional
Reliability
Councils
Regional
Reliability
Councils
Regional
Reliability
Councils
North American
Electric
Reliability
Council
FERC
Transmission
Providers
Transmission
Providers
Transmission
Providers
Industry
Groups
(OASIS,
ESC, etc…)
Industry
Groups
(OASIS,
ESC, etc…)
Industry
Groups
(OASIS,
ESC, etc…)
Regional
Standards
(mandatory
and/or voluntary)
North
American
Standards
(Voluntary)
United States
Standards
(Mandatory)
Reliability Issues
Reliability Issues
Tariff and Market Issues
Tools and Interfaces
Loose Compliance
Compliance

## Slide 90: Proposed Future
Regional
Reliability
Councils
Regional
Reliability
Councils
Regional
Reliability
Councils/RTOs
North American
Electric
Reliability
Council
FERC
RTOs
RTOs
Regional
Transmission
Organizations
Industry
Groups
(OASIS,
ESC, etc…)
Industry
Groups
(OASIS,
ESC, etc…)
Industry
Groups
(OASIS,
ESC, etc…)
North
American
Standards
(Mandatory
in US, Voluntary in
Canada and Mexico
Unless recognized
by Govt’s)
Tariff and Market Issues
Reliability Issues
Tools and Interfaces
Orders and Approvals
Reliability Issues brought by Regional/RTO Representatives
Note: It is expected that RTOs will eliminate the need for Regional Reliability Councils as we move forward
Compliance

## Slide 91: Discussion – What about the West?
Do we want a single RTO in the West?
Do we want a single set of business practices in the West?
Do we want a single set of business practices across North America?