## Slide 1: Sun Devil Project Update
December 2001

## Slide 2: Agenda
Project scope & capacity
Project costs
Phoenix generation market
Rate Structures
Sonoran proposal to TW
Comparative rate analysis
Alternative financial structures
NPV summary

## Slide 3
Transwestern Pipeline Company System Map
Ignacio
Blanco
Station 9
1090
850
Numbers reflect pipeline capacity in MMBtu/day before Red Rock & Sun Devil
Permian
Anadarko
Thoreau
San Juan
California
Topock/Needles
Phoenix
Existing TW system
Sun Devil Project
1200#
1200#
1008#
1050#
1200#

## Slide 4: Engineering Scope
San Juan lateral – 780,000 MMBtu/d
  97 miles of 36” loop
  Standing Rock compressor station
  Compressor mods at Bloomfield, Bisti, and Gallup
Mainline – 810,000 MMBtu/d
  224 miles of 36” loop
  New compressor at station 4, 1.5, and Kingman
  Compressor mods at stations 2 and 3
New Phoenix lateral - 500,000 MMBtu/d
  168.8 miles of 36” line, no compression
  Delivers to Copper Eagle storage, Panda lateral from El Paso south system

## Slide 5: Project Rationale
Provide a new source of competitive gas supply into a growing marketplace
Diversify Transwestern deliveries into markets other than California and Texas
Provide electric generators with a competitive transportation alternative to the current sole-source provider

## Slide 6: Sun Devil Costs

## Slide 7: Phoenix Power Market
Phoenix
El Paso
Copper Eagle
Duke
Palo Verde
Sempra
APS
Panda
PG&E
TW
Sun Devil

## Slide 8: El Paso Mainline Capacity
Source: Skipping Stone consultant testimony to FERC plus
independent research.
Notes: After All American, EP capacity of north & south mainlines (winter) is 4.5 Bcf/d. Summer capacity is less.
Conservative estimate by consultant shows EP short today by 500 – 700,000/d, not including new gen loads.
New gen load adds to shortfall by 335,000 day in 2002 and another 921,000/day in 2003.

## Slide 9: Sun Devil Power Generators
Notes: 2002 = 1710 Mw 335,000 MMBtu/d
2003 = 5448 Mw 921,080
2004 = 1200 Mw (Gallup) 216,000

## Slide 10: Sun Devil Rate Structure
Assumes:
3% O&M escalation
15% ROE
80/20 Debt / Equity

## Slide 11: Market Update
Panda Energy
  $.5525 for 100,000 MMBtu/d for first 5 years then escalates
  Fuel at 4.75%
  Uplift of 20% daily in 16 hour period, not to exceed MDQ
  All TW receipt / delivery points on alternate basis
APS
  $.5920 for 200,000 MMBtu/d for first 5 years then escalates
  Fuel at 4.75%
  Direct connect into Red Hawk plant, bypass El Paso
  Uplift of 20% daily in 16 hour period, not to exceed MDQ
  All TW receipt / delivery points on alternate basis
Notes:   Panda
  Likes the possibility of using project flexibility as synthetic storage
  Contract shipper on El Paso
  APS
  Largest potential customer
  Equity holder in Copper Eagle storage
  Next meeting week of Jan. 7
  Full requirements customer on El Paso
  Selling points are:
  Pressure commitment
  Swing capability
  San Juan access
  Reliable transportation (no allocation)
  Flexible system with various market access

## Slide 12: KMI Sonoran Proposal
Lease capacity for 20 years, up to 450,000 MMBtu/d
Delivery to:
  Flagstaff - $.28 +/- $.02 (rate = Sun Devil)
  Needles - $.39 +/- $.04
  Blythe - $.447 +/- $.05
Fuel actual via tracker = 1.05%
Ratable delivery, very little swing

## Slide 13: Sonoran vs. Sun Devil
Sonoran
  Lower fuel rate (1% vs 5%)
  Ratable deliveries
  Low swing capability
  Minimizes transport interruption on TW due to construction
  New competition at both main SoCal delivery points
  New delivery point at Blythe
  Can fully integrate with TW
Sun Devil
  Higher swing capability to serve power generators
  New shipper access to proposed salt storage
  Higher Capex due to new compressors
  Equity
  Can fully integrate with TW
Sonoran will conduct a new open season January 2002

## Slide 14: Comparative Rate Analysis

## Slide 15: NPV Summary

## Slide 16: Sun Devil Pipeline LP
Sun Devil provides pipeline capacity to Transwestern on an operating lease basis. Transwestern pledges shippers contracts (2) pending payment default by Transwestern. If Transwestern defaults, capacity is terminated and Sun Devil is assigned shippers contract. Transwestern entitled to cost recovery from rate base.
Shippers contracts- firm periodic payments. Assignable without consent to Sun Devil.
Transwestern provides O & M to Sun Devil. Sun Devil can terminate if TW fails to perform. TW can terminate on payment default by Sun Devil.
Sun Devil uses compression at TW compression stations. Compression contract between TW & Sun Devil cancelable on TW non-performance. TW has to have shippers’ consent to abandon station. FERC operational control issues (?).
97% NBP LP investment earnings target IRR of [ ]%, 3% TW GP investment earns an excess $ over LP target IRR. If GP fails in duties, LP has right to revenues. GP no longer controls, but earns LP target return. LP appoints itself GP and earns GP return.
NBPL
Shippers
Transwestern
Sun Devil
Pipeline L.P.
TW
Capacity
capacity
Pipeline O & M
compression
(1)
(2)
(3)
(4)
(5)
3% GP
97% LP
$
$
$
$

## Slide 17: Process Steps
Finalize negotiations with Market
  Panda, APS, Duke, SWG
Establish financing – NBPL, KMI, others
Meet with FERC to get structure approval
Prepare EIS
File for FERC certificate

## Slide 18
1 yr Avg = $.386
2 yr Avg = $.314
3 yr Avg = $.2326
Permian vs. Non-Bondad

## Slide 19: TW Fuel Parity
TW 2002 Plan
Notes: For every .25% drop in fuel = $4.6mm revenue reduction for TW assuming $2.50 gas price.
If 2002 Plan fuel revenue = $31.2mm, then with Sun Devil in service, tariff fuel could fall to 3.67% at a $2.50 gas price and fuel rev would be on par with 2002 Plan
If Phoenix SD shippers paid 1% less in fuel, the lost revenue only on this piece would be $4.5mm.