## Slide 1
January 20th, 2000
Government Affairs & Telecommunications Policy Strategic Planning Session

## Slide 2: Advanced Fiber Transport Team
Scott Smith, Director
  Joined ECI in September of 1998 from U S WEST Enterprise. Led all of Product Development including AFTS, Media Cast, Media Transport, and Conferencing.
  Currently leading the Product Development, Marketing & Sales for Dark Fiber, AFTS and alternative Carrier Services.
Kim Mayfield, Account Manager
Robb Justice, Account Manager
Bob Cooper, Account Manager
Jennifer Rawlings, Product Manager, AFTS LH
Rebecca Smith-Lynch, Product Manager, AFTS Metro & Colo
Pete Padrigo, Post Sales Support Manger, AFTS
With a lot of help from Kevin K, Steve E, Ted S, Mitch O. and various legal & field personnel, ECI AFTS/DF team generated 12% of Enron’s 1999 Income off 0.5% of Enron’s total Revenues

## Slide 3: Agenda
OSI Reference Model (Telecom 101)
Internetworking Overview
Local Area Networks (Enterprise)
Metropolitan Area Networks (LEC)
Wide Area Networks (IXC)
Carrier Services
Dense Wave Division Multiplexing & AFTS
Protection Schemes
Future of Optical Networking
Intermediation and Blend & Extend
Why are we here?

## Slide 4: OSI Reference Model (USPS)
Layer 7 = Application
Layer 6 = Presentation
Layer 5 = Session
Layer 4 = Transport
Layer 3 = Network
Layer 2 = Link
Layer 1 = Physical
E-Mail, Streams, HTML
Formatting (Look)
Mgmt of multiple windows
TCP or UDP - End-to-End
IP-Convergence
Ethernet, ATM, FR
Copper, Fiber, Air
Letters are converted to binary format, i.e. “A” = 01010110
0101 0110
= Header
= Data or Info

## Slide 5: Internetworking Overview
LAN
Ethernet
(10 Mbps)
Fast Ethernet
(100 Mbps)
Router
Router
MAN
Enterprise
Local Exchange Carrier
(LEC)
T-1/DS-1
(1.5 Mbps)
T-3/DS-3
(45 Mbps)
Internet Service Provider
EIN
Internet
WAN
xyz.com
Router
Server Farm
Router
Interexchage Carrier (IXC)

## Slide 6: Local Area Network (LAN)
The LAN has defined the “ideal” customer experience for applications:
  E-Mail
  Word Processing
  File Transfer & Directory
Protocols associated with the LAN:
  Ethernet (Shared & Switched)
  Fast Ethernet (Switched)
  Gigabit Ethernet (Starting to appear)

## Slide 7: Metropolitan Area Network (MAN)
The MAN and Internet connection is typically the most expensive component for an enterprise
MANs are typically built out and operated by Local Exchange Carriers
  RBOCs ~ U S WEST, SBC
  ILECs ~ GTE, SNET
  CLECs ~ ELI or NextLink

## Slide 8: Wide Area Network (WAN)
The cost of IXC capacity is decreasing rapidly
The WAN is built out and operated by IXCs
  AT&T
  Sprint
  MCI WorldCom
  Level 3
  Qwest
  Williams

## Slide 9: Carrier Services Defined
Carrier Services could include:
  Private Line
  IP Transit
  ATM Transport
  SONET
  Frame Relay
  X.25
  SNA

## Slide 10: Carrier Services Stack
ATM, Ethernet, Frame Relay
SONET and / or Optical Switching
Internet Protocol (IP)
DWDM and / or Optical Switching
VPNs, Apps, Voice, etc
$
$$
$$$
$$$$
$$$$$
$$$$$$
Private Line - DS-1, DS-3
Commoditization - Low Margin
Applications - High Margin

## Slide 11: DWDM Advances
Routers, Switches and SONET gear can tap into and run over a single wavelength
Dense Wave Division Multiplexing - simply using different frequencies of light (i.e. a rainbow) to carry discrete, independent, bits or discernable pieces of information.
Future DWDM advances include:
- SONET-like recovery & muxing
- Higher Power, less regen
- Use of multiple harmonics & sidebands - COOL!

## Slide 12: Advanced Fiber Transport Solutions (AFTS)
ECI offers raw, unprotected point-to-point capacity in:
  OC-12 (622 Mbps) and OC-48 (2.5 Gbps) increments
Ideal applications for AFTS are:
  Closing a SONET ring
  Low cost entry into a new city
  Perfect for IP transport
  Diverse AFTS Windows or Lambdas between city pairs can be terminated into low cost SONET / DACS equipment for emerging carriers (i.e. Cerant)
AFTS is currently provisioned in 15 days or less!!!

## Slide 13: Mesh vs Ring Protection
BLSR vs Mesh - Big capacity savings

## Slide 14: Future of Optical Networking
Carriers such as ECI, Qwest and Williams will deploy the most advanced optronics in the world.
Capacity will be more liquid and more rapidly provisioned.
Prices will drop - The market will expand!

## Slide 15: Intermediation
Intermediation is sophisticated reselling, i.e.
  ECI goes into the market selling traditional private line services
  ECI offers structured financing with “Blend and Extend”
  ECI can either synthetically fill the position or with actual ECI network capacity
  ECI creates, understands and influences the price curve that governs future costs of intercity capacity
  ECI becomes the biggest buyer & seller of BW in the world!!!

## Slide 16: Blend & Extend

## Slide 17: Why we need you?
ECI has Metro fiber in 5+ cities
ECI will have 17,000 Long Haul fiber route miles
For BW Trading, Intermediation and Carrier Services, ECI needs to be able to offer Metro and Long Haul data services