## Slide 1: California ISO - CPUC Electric Settlement Workshop Day 1
Executive Sponsors:
California ISO - Bill Regan - CFO
California Public Utility Commission - Steve Roscow
Notes: Welcome/Thank you
Goals/Overall Objective of the workshop
Importance of accurate reporting of SQMD
What you should go home with

## Slide 2
AGENDA Day One
10:00 - 11:00am
Introduction
ISO/CPUC - Why we are
here
Goals of the Workshop
ISO Statistics - Disputes
Overview - Process
11:00 - 12:00pm
Forecast/Scheduling
Load Profiles
Controls
12:00 - 1:00pm
Lunch will be provided
1:00 - 3:00pm
Metering Aggregation
Overview
Scheduled Read Date + 5
Controls
Estimation
Timing Issues (PST vs. GMT)
Load Profiles
Distribution Loss Factors (DLFs)
Load Profiles Set Up by the Utilities
(Presented by all 3)
SQMD Processing
T + 42/45 Submittals
15 Minute Break
3:15 - 5:15pm
Settlement
ISO Settlement Processes
CalPX Settlement Processes
Enron Settlement Processes
Settlement Issues
Good Practices
*If time and circumstances permit,
a question and answer period
will be at the end of this day.

## Slide 3: Forecasting/Scheduling

## Slide 4: Forward Markets
What are forward markets?
  Day Ahead
  Hour Ahead (Day-of)
Forward market load share
Role of forecasting and scheduling

## Slide 6: Load Forecasting
Starting point for forward market schedule
No one way to forecast load
End Product
  Daily requirement
    By hour
    By zone

## Slide 7: Load Forecasting Options
Top Down
  Forecast whole
  Subtract sub-components
Bottom Up
  Forecast sub-components
  Add then up

## Slide 10: LOAD FORECASTING RESOURCES
UDC
ISO
Other

## Slide 11: UDC Forecasting Resources
12 month billing history
  Secure location
  Specific customer load pattern
Dynamic Load Profile (DLP)
  UDC website
  Relative customer load pattern

## Slide 12: ISO Forecasting Resources
2 Day ahead grid load forecast
1 Day ahead grid load forecast
Actual grid load
Weather
Other information (Non-ISO)
  Weather

## Slide 13: Load Scheduling
Forward market schedule with ISO
Scheduling Coordinator
  Interface with ISO
Balanced schedules (load = supply)

## Slide 14: Scheduling Coordinator
Role of SC
  Aggregate demand with supply
SC relationships
  SC to ISO
  SC to load / supply
Must be certified by ISO
  ISO listing of SCs
  Cal PX: largest SC

## Slide 15: Scheduling Load (DA Market)
Single 24 market
Look ahead - 14 hours
ISO timeline
  Initial schedule to ISO: 10am day before
  Final schedule from ISO: 1pm day before
Bid formats
Adjustment bids

## Slide 16: Scheduling Load (HA Market)
PX: 3 sequential markets (10/6/8 hrs)
ISO: 24 sequential markets
Voluntary market (default=DA sched.)
ISO timeline
  Initial schedule to ISO: 2 hr before
  Final schedule from ISO: 1 hr before
Adjustment bids

## Slide 17: Schedule Adjustments
Congestion Management
Run by ISO
Adjustment bid
  Price willing to adjust schedule for congestion relief
Final Schedule
Zonal prices

## Slide 18: Energy Procurement
Exchanges
  Cal PX (www.calpx.com)
  Automated Power Exchange (www.apx.com)
Bilateral contracts
Futures market
  NYMEX
  Cal PX
ISO real time market

## Slide 19: ISO Charges to Load
Ancillary Services
- Self procurement option
UFE
Neutrality
Grid management

## Slide 20: Questions ?

## Slide 21: Overview
Meter
Data Collection
VEE, DLF, Load Profiles
Aggregation of Data
SC Submitted Data
CA - ISO

## Slide 22: Overview Multiple MDMA Scenario
Meter
Data Collection
VEE, DLF, Load
Profiles
CA - ISO
MDMA 1
SC Submitted
Data
Aggregation
of Data
Meter
Data Collection
VEE, DLF, Load
Profiles
MDMA 2
Meter
Data Collection
VEE, DLF, Load
Profiles
MDMA 3

## Slide 23: Meter Data Exchange File Process (MDEF)
Meter
Data Collection
VEE, DLF, Load Profiles
Aggregation of Data
SC Submitted Data
CA - ISO
Validation
Controls at every Level to create
the Perfect SQMD File

## Slide 24
Aggregation Data
Identifies UDC as well
Acct Codes (ESP, UDC)
Meter Number
Read Type
Cumulative Read Value, Read Period
Load Profile
DLF
Meter Read Value (MWh)
Distribution Loss Value (MWh)
ISO
Load Zone
Customer
&
Meter ID
H1
H2
H3
...
H24
Hourly Data

## Slide 25: The “Perfect SQMD File”
1. Contains all meters for that day.
2. Minimal estimated Data by (MDMA)
Load Profiles applied properly to cumulative meter read
3. The Distribution Loss Factor has been applied correctly
4. The meters are reported in the appropriate load zone
5. Usage is for the correct trade date and time
6. Delivered in time
7. Delivered on the right file format
8. The usage equals the power purchased for that date

## Slide 26: Meter Aggregation
PRE-AGGREGATION
SRD + 5
THE RULE - MDMA TO POST CORRECT, TIMELY DATA
    Timeliness For Validated Meter Reading Data
    (A) Interval Meters:
      (i) 80% of all usage data must be available on the first day after the scheduled read date of the meter.
      (ii)90% of all usage data must be available within two days of the scheduled read date of the meter.
      (iii)99% of all usage data must be available within five days of the scheduled read date of the meter.
* The timeliness standards as defined in the DASMMD, CPUC D.97-12-048, pgs 31-32, modified in D.98-12-
080, pgs. 82-83, and incorporated in Rule 22 (PG&E, SCE) and Rule 25 (SDG&E) (see web addresses)

## Slide 27: PRE-AGGREGATION SRD + 5 THE RULE - MDMA TO POST CORRECT, TIMELY DATA Timeliness For Validated Meter Reading Data
    (B) Non-Interval (Monthly) Data:
      (i) 85 % of all monthly meter readings must be available by 6:00 a.m. on the 1st working day after the scheduled meter read date.
      (ii) 95% must be available by 6:00 a.m. on the 2nd working day after the scheduled meter read date.
      (iii) 99% must be available by 6:00 a.m. on the 5th working day after the scheduled meter read date.
* The timeliness standards as defined in the DASMMD, CPUC D.97-12-048, pgs 31-32, modified in D.98-12-080, pgs. 82-83, and incorporated in Rule 22 (PG&E, SCE) and Rule 25 (SDG&E) (see web addresses)
Meter Aggregation

## Slide 28: Meter Aggregation
PRE-AGGREGATION
SRD + 5
THE REALITY - MADEN PROCESS
METER AND DATA EXCEPTION NOTICE (MADEN)
    Developed by Market Participants in Rule 22 Working Groups
    Standardized communication tool to quickly identify data problems
    Communication among all parties involved to resolve problem
    Whoever notices a problem sends a MADEN to other parties - ESP, MSP, MDMA, and/or UDC
    Missing or incorrect data must be posted to comply with the DASMMD standards or the UDC may estimate the read for billing purposes on SRD + 8*

## Slide 29: THE REALITY- MADEN PROCESS METER AND DATA EXCEPTION NOTICE
* SRD+8 agreed to by BBR participants group, approved by OCC (see glossary and website addreses)
MADEN
SRD
SRD +3
SRD +4
SRD +8*
SRD +5
External MDMA Reads Meter
MADEN Issued by UDC
UDC Expecting data
UDC will estimate usage

## Slide 30
MDMA Estimated Data Process Time Line - SDG&E
Day 4
Day 8
Day 9
Scenario 1: Missing Data (Meter Data Never Posted to Server)
0
Scheduled
Meter is listed
Report.
Day 5
PRE-AGGREGATION
SRD + 5
10/01
10/04
10/05
10/06
10/07
10/08
10/11
10/12
Day 7
10/13
10/14
SRD+1
Day 1
SRD+2
SRD+5
SRD
Day
Read Date
Day 2
on "2 Day Late"
"Missing Data"
MADEN issued.
Day 3
2nd Request
"Missing Data"
MADEN sent
Day 6
Account estimated “Missing Data” MADEN closed without resolution

## Slide 31
MDMA Estimated Data Process Time Line - SDG&E
10/01
10/05
10/06
10/07
10/08
10/11
10/12
Day 4
Day 7
10/13
10/14
Day 8
SRD+1
Day
1
SRD+2
SRD+5
Day 3
SRD
Day 9
Account estimated “Invalid Data” MADEN closed without resolution
Scenario 2: Missing Data with Subsequent Invalid Meter Data Posted to MDMA Server
Day 0
Scheduled Read Date
Day 2
Meter is listed on “2 Day Late” Report. “Missing Data” MADEN issued.
Day 6
SDG&E validation process identifies a “Data Spike”, and issues a MADEN. “Missing Data” MADEN closed.
PRE-AGGREGATION
SRD + 5

## Slide 32
PRE-AGGREGATION
SRD + 5
COMMON DATA PROBLEMS AFFECTING SRD+5
“No Data has been posted for the period from 3/5-4/3/00. Please notify the above analyst within 5 days by phone or e-mail of file name and the date posted. Thank you.”
UDC MADEN # Due Date MeterID UDC Acct No Comment
PGE PGE3333 8/2/00 C12345 16806357 MISSING 100 % OF KWH DATA
UDC Acct Number: 987654321
Billing Cycle: 08
Action Required: We need data for the period 06/12/2000 00:15 to
07/12/2000 24:00(PST).
Comments: Past due.
“Fails high/low check, usage is low compared to history, please verify usage”
WAITING FOR DATA; LAST READ 12/01/1999 24:00. MISSING DATA Please verify that leading zeros are included in GEN ID for CMEMP Record Receiving Sender ID
“The meter ID posted on this account does not match or cannot be found. The MDMA reflects SA#12222222 posting to meter id KZF018-6666666. However our records indicate SA#12222222 posting to meter id KZF018-7777777 Please clarify or forward your MIRN paperwork.”
“File Name: 20804033333 ESP 012345678 MDMA 044444444 SA#0005855555 Start Time: 200006140815 End Time: 200007150800 UDC Meter #: 654321 Please be advised that we have no record of SA# 5855555 nor Meter ID 7654321. Please clarify.”

## Slide 33
PRE-AGGREGATION
SRD + 5
“Action Required: 3rd incorrect file sent. First two files had period of 0’s. 3rd file sent has correct 0’s but incorrect end time of 5/9/00 at 24:00. Please note specific times need below. We need data for the period 04/08/2000 00:15 to 05/10/2000 24:00 (PST).
MDMA File Name: sdge00999.xxx”
“Action Required: File has a spike in data on 3/23/00 04:15. Average demand 224 kw; average consumption 123840. We need data for the period 03/12/2000 00:15 to 04/12/2000 24:00 (PST).
MDMA File Name: sdge00122.xxx”
While not within the MADEN time, we cannot ignore the Schedule Coordinator’s plea…
“Data for meter ABC01111 for cycle 6/26 (install date) to 7/26 is late and past SRD +45.
This data must be posted today!”

## Slide 34
“Action Required: NONE. MADEN has been closed.”
“Sorry about the delay, we were waiting on an HHF from the field. The file for meter ABC01111 has
been posted in file 2000080913333.edi. Thank you for your patience.”

## Slide 35
PRE-AGGREGATION
ESP DATA CONTROLS
IT’S THE DATA, STUPID ! ?
DATA
DATA QUALITY & TIMELINESS ARE CRITICAL
    To Produce Timely, Accurate Bills
    To Deliver Timely, Accurate Settlement Data
    To Optimize Power Supply and Delivery
    To Succeed

## Slide 36: PRE-AGGREGATION SRD + 5
SOURCES OF DATA PROBLEMS...
    New Model
    Systems Communication
    Human Communication
    Lack of Policies & Procedures

## Slide 37: QA / QC PROCESS ELEMENTS
PRE-AGGREGATION
SRD + 5
    Monitor the Meters and Meter Data
    Understand the Systems and Processes
    Understand the Parties
    Manage the Communication
    Determine Problem, Define Corrective
    Action, Implement, Verify

## Slide 38
Sample MADEN - PG&E Format (Handout 1)

## Slide 39
Sample MADEN - SCE Format (Handout 2)
Southern California Edison
Meter And Data Exception Notice
MADEN #: 99999 Date Sent: Monday, July 24, 2000 Due Date: 07/29/2000
MADEN Analyst: Leticia Olmos SDP: 10-1777777777777
E-Mail Address: metering@sce.com Phone #: 1-800-203-4634 Fax #: 1-562-945-9298
Service Account #: 122222 Meter ID: KZF018-66666
Customer Name: WWW Company
Customer Address: Street: 777 N. State St.
City: El Segundo
State: CA
Request:
The meter ID posted on this account does not match or cannot be found. Please see “Comments” for what our records show compared
to what was posted. Please contact the above analyst by phone or e-mail to resolve the problem within 5 days. Thank you.
Comments:
20000721070813 006901995 036679975 3001583791 200006130815 200007130800; The MDMA reflects SA #122222 posting
to meter id KZF018-66666. However, our records indicate SA #122222 posting to meter id KZF018-66667. Please clarify or forward
your MIRN paperwork.
Please return this form to: metering@sce.com
Southern California Edison Meter Operations Support
1-800-203-4634 CONFIDENTIAL

## Slide 40
Sample MADEN - SDG&E Format (Handout 3)
Please correct the following problem with your direct access account:
MDEN INFORMATION
ESP ID: 001234567
MDEN #: 9999
Status: Missing Data
Date Sent: 2000--7-25
Due Date: 2000-07-19
Date Closed:
MDMA ID: 087654321
MSP ID:
Contact Name: Dave Clark
Phone: 858-636-6879
E-mail: dxclark@sdge.com
CUSTOMER INFORMATION
Customer Name: XYZ COMPANY
Address: 12345 DOHENY PARK RD
City: CAPISTRANO BCH
Meter ID: 09009999
UDC Account Number: 9876543210
Date & Time of Event: 200007251321
ESP Account Number: XYZ0001
Old UDC Acct Number: 911111111
Service Delivery Point::
Billing Cycle: 09
Action Required: We need data for the period 06/13/2000 00:15 to 07/13/2000 24:00 (PST)
Comments: Past due.
MDEN RESPONSE
Respondents ID:
Name:
E-mail:
Phone:
Date Responding:
Response:

## Slide 41: Meter Aggregation
Estimation Process

## Slide 42: Meter Aggregation - Estimation
Rules of Estimation
  VEE (Validating, Editing, Estimating)
  Permanent Standards Working Group
  Subcommittee of PSWG: MAVI Working Group (MDMA And VEE Issues)

## Slide 43: Meter Aggregation - Estimation
When is estimation required?
    VEE Rules
      Linear interpolation (less than 2 contiguous hours)
      Like Days (Day of Week, Holidays)
      No Data… use the current month’s usage from the applicable Load Profile (for 15 min data use flat load for each hour)

## Slide 44: Meter Aggregation - Estimation
What are appropriate levels of estimation?
  Tolerance levels with the ISO
  Accessed per Schedule Coordinator

## Slide 45: Meter Aggregation - Estimation
Settlement Quality vs. Timeliness
  Important but conflicting objectives
  Internal Rules must be implemented prior to submittals
  Frequent errors can have adverse consequences

## Slide 46: Meter Aggregation
Time Formats

## Slide 47: Meter Aggregation - Time Formats
Greenwich Mean Time (GMT)
  From the Royal Greenwich Observatory
  Prime Meridian: marks the longitude 0 degrees
  All time zones are indexed to GMT, also referred to as UCT (Universal Coordinated Time)
Pacific Standard Time (PST)
  8 hours behind GMT
  PST does not change, Pacific Daylight Time (PDT) DT adjusts forward one hour to 7 hours behind GMT
  PPT is Pacific Prevailing Time (can be either PDT or PST)

## Slide 48: Meter Aggregation - Time Formats
GMT
  15 Min Interval Data is posted to the GMT
  Line Loss Factors are posted to GMT (SCE posts on hour beginning)
PST
  Load Profiles are posted to PST on hours ending (PGE post in PDT)
  ISO Settlement Data submitted to PST
  Returned from ISO in PPT

## Slide 49: Meter Aggregation - Time Formats
The difference an hour can make: Example: EXPOST Prices are posted hourly, and are very volatile.
  In HE18 the price was $9.40 /MWh and HE 19 the price $245 /MWh
  A deviation +/- 5 MW can be a swing of $1272 /MWh for just one hour

## Slide 50: Meter Aggregation - Time Formats

## Slide 51: Meter Aggregation
Load Profiles

## Slide 52: Meter Aggregation - Load Profiles
What is Load Profiling? Load Profiling is a process where monthly consumptive meters are broken into hourly segments for the settlement process. The ISO must know the hourly usage of each meter to properly assess charges for Ancillary Services, Load Deviation and Congestion Management. In the case of residential and small commercial meters, it is not cost effective to install expensive Interval Data Recorder (IDR) meters. The process of load profiling was developed to address this problem.

## Slide 53: Meter Aggregation - Load Profiles
Two primary types of Load Profiles in California
  Static Load Profiles: Three year averages of load profiles for a certain customer type
  Dynamic Load Profiles: Specific profiles for a particular day

## Slide 54: Meter Aggregation - Load Profiles
Static Load Profiles
  Weather effect is more seasonal
  Can be mapped forward for forecasting purposes
  Shows typical, standard usage patterns
Dynamic Load Profiles
  Specific weather events are visible
  Published after the fact, some 3 to 5 days after the particular day
  Used for settlement process
Useful Applications

## Slide 55: Meter Aggregation - Load Profiles

## Slide 56: Meter Aggregation - Load Profiles
Format for Dynamic Load Profiles Each UDC must post DLP’s for each trade date, but the format and file structures do differ for:
        PGE
        SCE
        SDGE
Notes: PGE Posts one file per day, in half hour increments
SCE Post one file per Profile Type year to date
SDGE

## Slide 57: Meter Aggregation
Distribution Loss Factors

## Slide 58: Meter Aggregation - Distribution Loss Factors
What are Distribution Loss Factors (DLF’s)? DLF’s are used to compensate for distribution system losses through such things as line loss, energy theft, and meter error. The number is derived from the difference between the UDC’s known system load and end use metered load.

## Slide 59: Meter Aggregation - Distribution Loss Factors
In equation form this is shown as,
    Egrid = DLF  Edist (1) where Egrid represents an energy measurement at corresponding ISO/UDC grid interface and Edist represents a distribution level end-use meter measurement.

## Slide 60: Meter Aggregation - Distribution Loss Factors
How is it measured? Distribution Loss Factors are multiples applied to your aggregated load for each hour. The load is first segmented into one of four Voltage Levels:
      Sub Transmission
      Primary
      Secondary
      Transmission

## Slide 61: Meter Aggregation - Distribution Loss Factors
  Example:
  Assume that an ESP has two customers, A and B, whose actual meter data must be reported to the ISO.
  A is served at secondary voltage, and its actual meter read for hour 10 of July 15 was 100 kWh. This consumption would be multiplied by the Secondary DLF for hour 10 of July 15 of 1.0444, to calculate the meter data that must be reported to the ISO for hour 10 of July 15 (100 kWh x 1.0444 = 104.44 kWh)
  B is served at primary voltage, and its actual meter read for hour 10 of July 15 was 100 kWh. This consumption would be multiplied by the Primary DLF for hour 10 of July 15 of 1.0111, to calculate the meter data that must be reported to the ISO for hour 10 of July 15 (100 kWh x 1.0111 = 101.11 kWh)
  The process is repeated for every hour of the day being reported.
  Sample as it appears on SDG&E website (http://www.sdge.com/EIC/html/loss_factors.html)

## Slide 62: Resources
WORKSHOP REPORT ON RETAIL SETTLEMENTS AND INFORMATION FLOWS
    Distribution Loss factors
    Load Profiles
PSWG: Appendix C-VEE Requirements for Validating, Editing and Estimating
ISO Tariff

## Slide 63: Web Sites
Web Addresses
  ORA Web site (http://ora.ca.gov/wk-group/)
  SCE (www.sce-esp.com)
  SDG&E (www.sdge.com)
  PG&E (www.pge.com)

## Slide 64: SCE Load Profiling
Cyrus Sorooshian
Southern California Edison
Notes: 1

## Slide 65: Load Profiling for Direct Access
PX Energy Credit and CTC (Competition Transition Cost) calculation
  Per CPUC Ratesetting Decision 97-08-056
Customer Aggregate Hourly Usage for Settlement with ISO (Independent System Operator)
  Per CPUC Decision 97-10-086
Forecast of Hourly Energy Purchases
  Load profiles are used in forecasting models

## Slide 66: Static Load Profiles
Three years of load profiles are utilized
Averaging historical Annual Rate Group Load Profiles
One profile for each month, day of the week, and holiday (92 profiles were created for each year)
Each day of the year is assigned the appropriate profile

## Slide 67
Static Load Profiles
Static Load Profiles are updated annually
Less than 2 % of SCE customers, 11 rate groups:
  < 20 kW: Domestic Master Metered, PA-1, St Ltng,
  TC-1
  20-500 kW: TOU-GS-2, PA-2, TOU-PA-5, Ag-TOU
  > 500 kW : TOU-8 (sub-transmission, primary,
  secondary)

## Slide 68: Dynamic Load Profiles
SCE implemented dynamic load profiling on 5/18/1998 for Domestic (residential), GS-1 (small commercial), and GS-2 (medium commercial/industrial) Rate Groups.
Rate Groups subject to Dynamic Load Profiling comprise more than 98% of the accounts in SCE service area.

## Slide 69: Dynamic Load Profiles
Dynamic load profiles are available 3 business days (62 hours) after the transaction day.
Dynamic Load Profiles available since 4/1/1998 on the Internet at http://www.sce-esp.com/eca/loadprofiling/lp.htm

## Slide 70: Sampling for Dynamic Load Profiles
Domestic (residential), GS-1 (small commercial, 0-20 kW), GS-2 (medium commercial/industrial, 20-500 kW) Rate Groups
Samples were designed to allow segmentation (large sample size)
Meets PURPA standard for accuracy for each Segment
  A design accuracy of 10% at 90% confidence level at the system and class peak times

## Slide 71
Stratified Random Samples
  Residential (sample size= 3,800): Dwelling type, Climate Zone, Usage
  GS-1 (sample size= 4,000) : Building Type and Annual Average Usage
  GS-2 (sample size= 4,600): Building Type and Annual Peak
  More than 80% of the sampled accounts are currently providing daily data, adequate for dynamic load profiling at the rate group level
Sampling for Dynamic Load Profiles

## Slide 72: Process Flow - Dynamic Load Profiles
Data
Validation
Load Research Samples
NetComm Daily
12PM, Day + 1
PX energy charge factors
2 PM, Day + 1
2 PM, Day + 3
Valid Load Data
DB-2 Table
Internet
Data Collection
Estimation
Energy Cost
Accounting
Billing
PX Settlement
Load Profiles

## Slide 73: Load Profile Format and How to Use It
Monthly Cumulative Meters
Interval values are hour-by-hour class average demand in kW
Time intervals are in Pacific Standard Time
  (1) Compute billing cycle usage
  (2) Extract billing cycle load profile
  (3) Scale load profile to match usage

## Slide 74: SCE Dynamic Load Profiling Normalized Load Profiles System Peak Day, 31AUG1998
DOM--S//M
GS-1
GS-2
50
60
70
80
90
100
110
120
130
140
150
160
170
Hour (PST)
12M
3A
6A
9A
NOON
3P
6P
9P
12M
Percent of Mean KW
Load curtailment per ISO
A/C Cycling for Domestic
customers from 3 P.M.-5 P.M.
147,000 customers, 210 MW

## Slide 75: Resources
Load Profiling Web Site:
http://www.sce-esp.com/eca
  Instruction, format, and protocol on how to use the profiles
  Historical Static and Dynamic Load Profiles
  Rate mapping
  Links to SCE Tariff Website and CPUC Load Profiling websites
  Distribution Loss Factors and PX Average Price Factors
The ESP Direct Access Kit, Chapter 16
  SCE updates this handbook regularly (current Version: 2.9)
  Introduction, methodology, definitions and format, rate mapping, and protocol on how to use the profiles and line loss factors.
  SCE ESP Services
  (888) 371-ESPS (3777)

## Slide 76: SDG&E Load Profiling
Leslie Willoughby

## Slide 77: Dynamic Load Profiles
SDG&E implemented dynamic load profiles on 6/1/1998 for seven of it’s eight class load profiles.
Dynamic Load Profiles are typically posted within four days.
SDG&E uses an integrated approach to Dynamic Load Profiling.
  Developed econometric model based upon historical load research data and weather.
  Developed daily metered estimates from DLP sample.
  Final estimates are derived from a weighted average of the econometric and daily metered estimates.

## Slide 78
Sample Sizes Preliminary Estimate of Sample Sizes

## Slide 81
Http://www.sdge.com/EIC/html/body_loss_factors.htm
Resources

## Slide 82
Website:
http://www.sdge.com/EIC/html/loss_factors.htm
FTP Site: eic.sdge.com
Userid:dadl Password:smc7

## Slide 83: PG&E Load Profiling
Susan McNicoll

## Slide 84: PG&E Load Profiles
PG&E Load Profiles are statistical estimates based on stratified random samples
PG&E Load Profiles are Dynamic (based on daily data retrieval) or Static (based on a 3-year average of historical data.)

## Slide 85: PG&E Load Profiles
Dynamic load profiles used for 16 of 26 classes
Static load profiles used for 10 of 26 classes
Dynamic load profiles are posted within 7 days
Static load profiles are posted the year before

## Slide 86
PG&E Load Profiles

## Slide 87: PG&E Load Profiles
Due to our rate design, PG&E’s Load Profiles:
Consist of 48 half-hour intervals
Are in Daylight-Savings Time

## Slide 88: PG&E’s Static Load Profiles
CSV (comma-separated values). Most computers will open in Excel.
One file per year per class, published the year before.
One row for each day, one column for each of the 48 half-hours.
Values are normalized. They add up to 10,000 for the entire year.

## Slide 89: PG&E’s Static Load Profiles

## Slide 90: Why DLP Example - E20T class - August 01, 2000

## Slide 91: PG&E Dynamic Load Profiling Process
Second Research MV 90
pulse file
retrieve data daily
DATA ACQ
Dynamic data checks
Transfer file
data storage
discard
accept
edit
V E E
Sample Weights
Profile
PG&E web page
PROFILE ESTIMATION
COMMUNICATION & STORAGE within 7 days
data checks

## Slide 92: PG&E’s Dynamic Load Profiles
CSV (comma-separated values). Extension of the file is “DLP”.
One file per day for all classes.
One row for each class, one column for each of the 48 half-hours.
Values are average kW per customer.

## Slide 93: PG&E’s Dynamic Load Profiles
Date and time posted
Size of the posted file, in bytes
File named after the date of the profile. Extension is “DLP.”

## Slide 94: PG&E’s Dynamic Load Profiles
DLP file opened directly from the browser

## Slide 95: PG&E’s Dynamic Load Profiles
DLP file opened in Excel

## Slide 96: Web Site
www.pge.com/profiles

## Slide 97: Web Site
Link to our DLP web page - www.mads.pge.com/profiles
Annual Static Load Profiles for all customer classes for 1998, 1999, and 2000
Description of the Static Load Profiling estimation process
Annual Estimated Consumption by class (kWh per customer)
And more ...

## Slide 98: ISO Settlements Overview
Cathy Young

## Slide 99: ISO Settlements Process Overview
ISO Settlement Charges
  Categories
  Definitions and descriptions of calculations
ISO Dispute Process
Settlements Timeline
Best Practices
Notes: <number>
<footer>
<header>
<date/time>

## Slide 100: ISO Settlement Charge Categories
ISO Market
  Ancillary Services (A/S) Capacity
  Congestion
  Imbalance Energy (IE)
  Neutrality
  Wheeling
ISO Grid Management Charge (GMC)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 101: ISO Market A/S Capacity Settlements
ISO procures A/S capacity in DA and HA on behalf of SCs not self-providing
Market Services
  Regulation
  Spinning Reserve
  Non-Spinning Reserve
  Replacement Reserve
Notes: <number>
<footer>
<header>
<date/time>
ISO procures A/S capacity in DA and HA on behalf of SCs not self-providing
Spinning Reserve
Non-Spinning Reserve
Replacement Reserve
AGC
  -Regulation Up & Regulation Down
  - Procure typically between 5 - 12 % combined (Load Forecast
  and system conditions)
  -% may vary from hour to hour dependent upon system conditions
  -SCs are charged based on Metered Demand
Contracted Services
  Reactive Power and Voltage Control
  Black Start Capability

## Slide 102
ISO Market A/S Capacity Settlements
Payment to Sellers
  Paid MCP for awarded capacity MW for each service
  DA (CT 1-6)
  HA (CT 51-56)
Notes: <number>
<footer>
<header>
<date/time>
AGC
-Regulation Up & Regulation Down -
-on-line, synchronized, gen capacity,
-available to respond to AGC control signals second-by second
-Enables continuous balancing of resources and load
-Allows us to maintain frequency during normal conditions
- Procure typically between 5 - 12 % combined
-Load Forecast and system conditions
  -% may vary from hour to hour dependent upon system conditions
-SCs are charged based on their share of Metered Load
-less self-provisions, and purchases
-plus on demand obligation and sales
SP & NSP -
-Spin on-line and synchronized (available in 10 minutes)
-Not on-line but able to synchronize and be available in 10 min
-Cost allocated to SC’s based on their share of total Metered Demand
(Load + Firm Exports)
Obligation - 100% non-firm import
- 5% of demand served by hydro
- 7% of demand served by thermal generation
RR
-Quantity procured determined by system conditions
-Compare schedules and forecasts
-Cost of Replacement Reserves allocated to SCs deviating from schedule
If dispatched, Energy associated with capacity settled at real-time ex-post interval price
Non-Spinning Reserve
Replacement Reserve

## Slide 103: ISO Market A/S Capacity Settlements
Cost allocation to Buyers
  AGC: pro-rata to Metered Load (CT 115, 116)
  Spin & Non-Spin: to Metered Demand (CT 111, 112)
    Served by hydro resources (5%), non-hydro (7%), and interruptible imports (100%)
  Repl: distributed to deviations (CT 114)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 104: ISO Market A/S Capacity Settlements
Other Charges:
  Rational Buyer (CT 1011)
    Substitutes higher quality for lower quality A/S
    Credit/Charge allocated to A/S buyers
  RMR Preemption
    Units awarded A/S capacity then dispatched RMR
    Capacity payments reversed (CT 61-66, 71-76, 81-86)
    Buyers repaid (CT 1061 - 1066)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 105
ISO Market Inter-zonal Congestion Settlements
Usage Charge- congested transmission paths between 2 zones
  Prices set by marginal adj. bids used
  SCs pay if contributing to congestion
  SCs get paid if relieving congestion
  (DA CT 203 & HA CT 253)
  $ balance refunded to TO & FTR owners by % ownership (CT 254, 255)
Notes: <number>
<footer>
<header>
<date/time>
Adjustment bids contain information on the SC’s value to increment (inc) its generation upward by a specified quantity and the value to move downwards (dec) by a quantity
If ISO DECs SC’s Generator, SC pays ISO
If ISO INCs SC’s Generator, ISO pays SC

## Slide 106
ISO Market Intra-zonal Congestion Settlements
Usage Charge for congested transmission paths within a zone
  Managed in real-time
  Adjustment bids and A/S and SE bids used
  Resources paid/charged as bid (CT 451)
  Cost allocated pro-rata to congested zone (CT 452)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 107
Difference between Schedule vs Metered Energy
Three types of Energy Imbalances:
  Instructed
  Uninstructed
  Unaccounted for Energy (UFE)
ISO Market Imbalance Energy Settlements
Notes: <number>
<footer>
<header>
<date/time>

## Slide 108: ISO Market Imbalance Energy Settlements
Instructed Energy
  Balancing energy dispatched in real-time
  Energy from A/S capacity and Supplemental bids
  Paid/charged at interval ex-post price (CT 301, future CT 401)
  Overpayment for non-delivery collected through CT 502, 503, 504
Notes: <number>
<footer>
<header>
<date/time>

## Slide 109: ISO Market Imbalance Energy Settlements
Uninstructed Energy
  Deviations from Schedules + Instructions
  Attributed to Generation, Load, Imports, Exports (CT 402 - 405, future CT 407)
  Paid/charged at hourly ex-post price
    Weighted average price of instructed dispatches
Notes: <number>
<footer>
<header>
<date/time>

## Slide 110
ISO Market Imbalance Energy Settlements
Unaccounted For Energy (UFE)
  UFE arises from:
    Energy theft
    Distribution loss deviations
    Metering Errors
    Profiling errors
  Calculated hourly by UDC
  Cost allocated pro-rata to UDC metered demand (CT 406)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 111: ISO Market Neutrality Settlements
Imbalance Energy Neutrality Adjustment
  Differences between payments/collections
  Contributors to IE neutrality imbalances
    Imbalance Energy
    Interchange Inadvertent Flow
    Inter-Zonal Congestion
  $ Allocated to Load and Exports (CT 1010)
Notes: <number>
<footer>
<header>
<date/time>
Imbalance Energy Neutrality Adjustment (CT 1010)
  Differences between payments and collections
  Contributors to neutrality imbalances
      Imbalance Energy
      Settlement Statement adjustments
      Interchange Inadvertent Energy
      Periods of Inter-zonal congestion
      Losses
      Out of Market

## Slide 112: ISO Market Neutrality Settlements
ETC Neutrality Adjustment
  ETC deliveries scheduled on non-ISO Grid exempt from UFE and IE Neutrality
    Automatically charged through CT 406 & 1010
  Exemption credited to ETCs (CT 1210)
  Cost allocated to non-ETC Load and Exports (CT 1210)

## Slide 113
Charge for power transported through ISO controlled grid
  Wheel Out, Wheel Through
Charged to scheduled volume (CT 352)
  Non-PTO Load ETC scheduled amount exempt
IOU’s collect payment (CT 354)
ISO Market Wheeling Settlements
Notes: <number>
<footer>
<header>
<date/time>
Charges are refunded to the IOU based upon relative revenue requirement of transmission facilities.????
Rates approved by FERC

## Slide 114: ISO GMC Settlements
ISO Monthly administrative charge
  Recovery of administrative and operating costs
Load & Exports charged at $0.83/MWh
ETC deliveries 50% exempt

## Slide 115
ISO Settlement Dispute Process
SCs can contest charges to Prelim and Final Statements
  Electronically submit ISO Settlement Dispute Form
  Specify trade date, issue, reason, amount claimed
  Attach available evidence to reasonably support claim
Notes: <number>
<footer>
<header>
<date/time>

## Slide 116: ISO Settlement Dispute Process
SC timeline for filing dispute
  8 business days from issue of Prelim Statement
  10 business days from issue of Final Statement
  No dispute indicates agreement
  Late disputes are non-compliant and invalid

## Slide 117: ISO Settlement Dispute Process
ISO timeline for responding (and adjusting)
  14 Business days from Prelim
  25 Business days from Final
    Any adjustment will be retroactive
SCs can pursue Good Faith Negotiations then ADR if continued disagreement

## Slide 118
<footer>
<date/time>
Hourly meters read for Day 0, all data forwarded to ISO meter system for storage
T = 0
T+50C
T+38B
T+45C
B = Business Days
C = Calendar Days
T = Trade Date
Settlements Process Timeline
T+46B
T+51B
T+66B
Last T
of Month
+ 56B
Preliminary Stmt published
All hourly load & gen data to ISO
SCs dispute/validate Prelim Stmts.
Prelim disputes resolved
Final Stmt published
SCs dispute/validate Final Stmts
Final disputes resolved
Prelim Invoice Payment Due
Prelim Invoice Payment Due
Last T
of Month
+ 51B
Late Meter Data Accepted with ISO approval up to T + 45B
* Possible Non-Compliance repercussions *
Notes: <number>
<footer>
<header>
<date/time>

## Slide 119: Best Practices
Learn settlement impacts of your Market activities
Maintain all schedule data and dispatch logs
Submit timely and accurate meter data
Validate settlement charges
Dispute any discrepancies

## Slide 120: Questions
Cathy Young
California Independent System Operator
cyoung@caiso.com

## Slide 121: The Settlement Process The Enron Perspective
George Phillips

## Slide 122: Discussion Topics
  Definition of Settlements
  Market Entities Involved
  Review of Market Entities
  Settlement Timing
  Description of Enron’s Settlement Process
  Market Experience
  Post Settlement Adjustments

## Slide 123: Settlement
SETTLEMENT -- The process of financial settlement for products and services purchased and sold. Each settlement involves a price and quantity. Both the ISO and PX may perform settlement functions.
Notes: Very soon, PG&E will complete the divestiture of its hydroelectric generation facilities… highlight other slide bullets
Let’s take a look at the status of the hydro divestiture … next slide

## Slide 124: Market Entities
Power Generators
Scheduling Coordinators (SC)
Independent System Operator (ISO)
California Power Exchange (PX)
Energy Service Provider (ESP)
Retail Customer

## Slide 125: Review of Market Entities
POWER GENERATORS: Produce electrical energy and supply Ancillary Services (A/S) for grid reliability.
  Sell power directly to customers, marketers, power pools or use the services of brokers.
Notes: At this time, the CPUC is looking at various methods to determine the value of PG&E’s hydro facilities… review slide bullets and time lines
Parties have until June 8th to file alternatives to PG&E’s proposed auction proposal.
The conclusion of the hydro divestiture will bring us close to ending the freeze.
Here’s some background information on the rate freeze… next slide

## Slide 126
Review of Market Entities
SCHEDULING COORDINATORS (SC):
Arrange for transmission capacity with the ISO and ensure that generation and imports always equal load and exports. Must be certified by the ISO.
  Arrange for generation dispatch, transmission reservation, delivery of energy, and provision of capacity for their market participants.
  Responsible for paying ISO charges; submitting annual and weekly forecasts, as well as, day-ahead and hour-ahead schedules for their customers and settling trades with generators, PX, ISO, retailers.

## Slide 127: Review of Market Entities
INDEPENDENT SYSTEM OPERATOR (ISO):
manages around the clock the statewide transmission grid to maintain the reliability of the transmission system. Additionally, the ISO operates the forward A/S markets, real-time energy market and manages transmission congestion based on economic values established by SCs through their adjustment bids.
  A neutral control area operator responsible for maintaining instantaneous balance of the grid system by matching the the net of generation with loads.
Notes: At this time, the CPUC is looking at various methods to determine the value of PG&E’s hydro facilities… review slide bullets and time lines
Parties have until June 8th to file alternatives to PG&E’s proposed auction proposal.
The conclusion of the hydro divestiture will bring us close to ending the freeze.
Here’s some background information on the rate freeze… next slide

## Slide 128: Review of Market Entities
ISO coordinates the dispatch of generation, manages the reliability of the transmission grid, and provides open access to the transmission grid.
ISO requires SCs abide by the industry’s reliability standards

## Slide 129: Review of Market Entities
THE CALIFORNIA POWER EXCHANGE (PX):
a state chartered, non-profit corporation charged with providing Day-Ahead and Hour-Ahead markets for energy and ancillary services, if it chooses to self-provide, in accordance with the PX tariff.
Notes: At this time, the CPUC is looking at various methods to determine the value of PG&E’s hydro facilities… review slide bullets and time lines
Parties have until June 8th to file alternatives to PG&E’s proposed auction proposal.
The conclusion of the hydro divestiture will bring us close to ending the freeze.
Here’s some background information on the rate freeze… next slide

## Slide 130: Review of Market Entities
The PX is a Scheduling Coordinator, and is independent of both the ISO and all other market participants.
  The PX is a marketplace. As bids are accepted, power is being bought and sold. Once a bid is accepted, the power sold is "transferred out" of the PX, since is it no longer available. Power that is available for sale is "transferred in" to the PX. Transfers may also take place directly between the buyer and seller, without PX involvement.

## Slide 131
Review of Market Entities
ENERGY SERVICE PROVIDERS (ESP):
Market energy and energy services to retail customers.
  Power marketers are responsible for matching their load with resources through SCs, who, in turn, must submit balanced transmission schedules to the ISO.
  Can serve as demand aggregators for retail load, bill retail customers for energy and contracted services, schedule load and generation through an SC or the PX and pay SCs and/or generators for energy and ancillary services.

## Slide 132: Review of Market Entities
UTILITY DISTRIBUTION COMPANIES (UDC):
provide local transmission and distribute electricity directly to consumers.
  In general, the UDCs continue to be the entity responsible for the delivery of energy to the customer.
  The UDCs meter energy, process bills for energy, transmission and distribution.
Notes: The rate freeze is a key part of Assembly Bill 1890 -- the State law that defined the restructuring of the electric industry… highlight slide bullets
Now, let’s see how these factors can interact to influence when the freeze will actually end… next slide

## Slide 133: Review of Market Entities
CUSTOMERS:
Residential, Commercial and Industrial customers exercise direct access for purchasing electric power.
  May choose direct access via their UDC, receive power from ESPs or on a contractual basis from a generator.

## Slide 134: Settlement Timing
Trading Day Close + 38 business days:
  a preliminary billing statement from the ISO is made available on the Energy Communications Network (ECN) to each market participant.
Preliminary Billing Statement + 8 business days:
  the time a market participant has to review the preliminary billing statement and forward any billing disputes.

## Slide 135: Settlement Timing
Receipt of Billing Disputes + 4 business days:
  the time the ISO has to respond to the bill disputes submitted by the market participants.
Last Trading Day of the Month + 51 business days:
  ISO issues a final billing statement for the last trade day of the month and issues an invoice for the complete trade month.

## Slide 136: Initial Step in The Enron Process

## Slide 137: Process Flow

## Slide 138: Market Experience
Issue: Lack of Information/Data
  Large Campus Co-Generator Example
  Distribution Loss Factor (DLF)
  Daily Load Profiles (DLP)
Issue: Consistency
  Data Overlaps
  Across all Utilities

## Slide 139: Post-Settlement Adjustment
Question:
Is there a need for a post-settlement adjustment mechanism in the wholesale market to reverse the cost shifting that occurred in the initial settlement due to inaccurate data?
A) Yes B) No
C) Possibly D) Don’t care and can’t wait until this presentation is over

## Slide 140: Post-Settlement Adjustment Background
After final ISO settlement and after the dispute period has passed, data may become available that changes the dollar amount of energy transactions.
Except for ISO’s high dollar adjustments, there is no corresponding adjustment process in the wholesale market.

## Slide 141: Post-Settlement
Answer...….C….….”Possibly”
Suggestions
  Allow UDR process to resolve material discrepancies between the UDC and ESP.
  Extending the time allowed to report settlement data.
  True-up at the ISO level
  Lower current ISO threshold from $100,000.

## Slide 142
Glossary
SRD: Scheduled Read Date for a billing cycle
MADEN: Meter and Data Exception Notice
DASMMD: Direct Access Standards for Meters and Meter Data, California Public Utilities Commission Decision No. 97-12-048, modified by Decision No. 98-912-080

## Slide 143
Websites
DASMMD: http://www.sce-esp.com/ (click on listing in let column)
http://nic.cpuc.ca.gov/electric_restructuring/decisions.shtml
(click on both Decisions)
Rule 22
Working Groups http://www.ora.ca.gov/wk-group/