## Slide 1
Storage assets/contracts are not liquid enough to build intuition for pricing.
In this talk I will present a model that can capture both long term (inter-seasonal) and short term (intra-seasonal) option values embedded in the storage operation.
Time: 4:00-5:00pm, Wednesday, May 19, 1999
Place: EB5C2
Enron Research
Real Options
Storage Facilities Valuation
Zimin Lu
Pricing Issues
Introduction
Our Approach
Results and Implications

## Slide 2
Introduction
Pricing Issues
Our Approach
Results and Implications
Enron Research
Real Options
Storage Facilities Valuation
Zimin Lu
Pricing Issues
Introduction
Our Approach
Results and Implications

## Slide 3
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Why is storage an important asset ?
“In addition, Enron’s North American franchise is benefiting from the increased flexibility at the company’s Bammel storage field north of Houston.”
- 1998 Enron Annual Report
The “flexibility” is our topic today - real options
Introduction
Real Options

## Slide 4
Enron Research
Enron’s Approach
Pricing Issues
Introduction
Our Approach
Why does storage valuation matter?
What is operational value of Bammel storage ?
How much should ECT charge / pay for specific
types of storage contracts ?
What is the sensitivities with respect to contractual
changes and market conditions ?
Introduction
Real Options

## Slide 5
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Real options
Unlike financial options
Its value depends on who owns & operates
Owner’s access to regional pipelines, trading
capability, other gas assets in the region, etc.
Interacting and path-dependent options
An injection creates an option to withdraw
Why Is It Difficult to Price Storage ?
Real Options

## Slide 6
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Interacting & Path-Dependent Options
Real Options
Empty
Half-full
Full
Inject 2
Hold 2
Sell 2
Inject 2
Sell 2
Re-Inject
Sell 2

## Slide 7
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Multiple period options
Option on entire forward curve
the value of one year storage lease depends on 12
forward prices, current spot price, volatilities and
correlations
---> High dimensionality
Why Is It Difficult to Price Storage ?
Real Options

## Slide 8
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Multi-Periods Option
Real Options
Current spot price

## Slide 9
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
American style options
like a financial American option
Inject & withdraw on any day
unlike a financial American option
Multiple exercises - sequential American options
Why Is It Difficult to Price Storage ?
Real Options

## Slide 10
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Physical constraints
Daily injection & withdraw limits
Seasonal injection & withdraw limits
injection/withdraw curve to ensure safe operation
Pipeline capacity
firm / non-firm transportation contracts
Price elasticity
future improvement
Why Is It Difficult to Price Storage ?
Real Options

## Slide 11
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Available approaches
Spread options
choose summer/winter spread options
rank the spreads and allocate gas volume
Advantages
simple function calls to spread option
capture inter-seasonal spread options value
Disadvantages:
does not capture intra-seasonal spread options value;
exercises predetermined;
Pricing Issues
Real Options

## Slide 12
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Available approaches
Binomial forest
Binomial tree for all prices on the curve
to reflect seasonality
Advantages:
capture the American flavor
Disadvantages:
difficult to capture forward curve movements,
especially reshaping.
Pricing Issues
Real Options

## Slide 13
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Available approaches
Simulation of pre-specified operating strategy
Advantages
flexible to satisfy constraints;
easy to evaluate different operating strategies;
Disadvantages:
does not capture American flavor;
does not handle optimal exercise;
Pricing Issues
Real Options

## Slide 14
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Basic idea
Model forward curve as single object
basic curve movements: parallel shifting, slopping,
and twisting;
Use simulation
flexible to satisfy constraints, adopt different price
processes;
Keep American flavor
optimal exercise decisions
Our Approach
Zimin Lu, Stinson Gibner and Vince Kaminski
Real Options

## Slide 15
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Financial modeling technologies
“HJM” to model forward curve moment
curve shift, reshaping, governed by covariance matrix
American Monte-Carlo (AMC)
built tree for the payoff - dimension reduction
Dynamic programming
optimal decisions to inject, hold or withdraw
Our Approach
Real Options

## Slide 16
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
HJM Factor Model
Real Options
1
5
10
15
35
20
25
30
40
45
55
60
Contract Maturity (Months)
Parallel Shift Factor
Slopping Factor
Twisting Factor

## Slide 17
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
American Monte-Carlo
Real Options
Time
Price

## Slide 18
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Real Options
Hold
Withdraw
Injection
Time
Price
Gas in storage
Dynamic Programming
K=0
K=1
K=2

## Slide 19
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Real Options
Financial & Operation Inputs
Curves Inputs: forward price, volatility, historical correlation
Simulation Inputs
“HJM” Simulation of Prices: 3-factors
“AMC”: Tree & Transition Probabilities
Storage Model
Dynamic Programming: Decisions
Unit Storage Price: $/mmBtu
Decision Variables

## Slide 20
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Reservoir
Bammel Storage Field
Total working gas = 58 BCF
Injection rate = 0.365-0.47 BCF/day
Withdraw Rate = 0.89-1.2 BCF/day
Annual turnover = 1
Salt Dome
Napoleonville
Total working gas = 4 BCF
Injection rate = 0.4 BCF/day
Withdraw rate = 0.2 BCF/day
Annual turnover = 3 to 4
Type of NG Storage
Real Options

## Slide 21
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Real Options

## Slide 22
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Real Options
Storage Value vs. Contract Duration

## Slide 23
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Real Options
Storage Value vs. Contract Duration
if forward curve is flat @ $2.3/mmBtu

## Slide 24
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Storage Value vs. Initial Gas Volume
Real Options

## Slide 25
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Eta: Sensitivity to Correlation
Real Options

## Slide 26
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Sensitivity to Transaction Costs
Real Options

## Slide 27
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Rho: Sensitivity to Interest Rate
Real Options

## Slide 28
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Real Options
Vega: Storage Value vs. Volatility

## Slide 29
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Real Options
Optimal Decisions

## Slide 30
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Real Options
Optimal Decisions

## Slide 31
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Real Options
Optimal Decisions

## Slide 32
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Real Options
Optimal Decisions

## Slide 33
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Our Model
Incorporates correlations and forward market
conditions through HJM technology
Handles high dimensionality and different price
processes using American Monte-Carlo techniques
Preserves the American flavor for the options
inherent in storage facilities and provides optimal
exercise strategy through dynamic programming
What Have We Achieved ?
Real Options

## Slide 34
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Our Model
Shed lights on injection-hold-withdraw operating
decisions
Captures the value of both inter- and intra- seasonal
spread options
Same model works for reservoir / salt dome
Warning
The model makes optimal decisions, in reality we
may not exercise optimally due to other constraints
What Have We Achieved ?
Real Options

## Slide 35
Enron Research
Pricing Issues
Introduction
Our Approach
Results and Implications
Power pump storage
pump water during off-peak hours ->injection
generate power during peak-hours ->withdraw
Aquifer storage of water
wet year -> injection
drought year -> withdraw
normal year -> hold
Other Possible Applications
Real Options