## Slide 1: Technology Comparison - IGCC
Pros
Integrated Gasification Combined Cycle - - Basically a coal gasifier connected to a regular combined cycle plant
Uses well known power island technology - - gas turbines
Has very low emissions - - easier to permit in “difficult” states
Provides fuel optionality - - can easily shift between NatGas and Coal gas
Overall higher capacity factor potential
Potential shorter construction schedule
Improved heat rate (~8200)
Potential staggered approach (SS/CC/IG)
Potential bi-product revenue streams (Argon, CO2, etc)
Can be modularized - - would provide a staggered COD schedule (250Mw year 1, 500 Mw year 2, etc)
Potential “clean coal” money
Cons
Potential first year low coal capacity factor
Newer, less-proven technology
Potential higher capital costs
Potential higher VOM costs

## Slide 2: Technology Comparison - CFB
Pros
Potential lower capital costs than IGCC
Circulating Fluidized Bed
Potential lower VOM costs
Can use a variety of coals including very low quality “waste coal” - - allows significant coal delivery cost reductions
Less complicated technology than IGCC
Lower emissions than older technology “pulverized coal”
Can be modularized - - installed in blocks of 100Mw - 250Mw
Potential “clean coal” money
Cons
No fuel optionality - - designed for coal only
Higher capacity factor while on coal
No byproduct revenue streams
Potential longer construction schedule