## Slide 1
WSCC Region-Wide Interruptible Load Auction
Example 1
Customer Interrupts Amount Deployed
Interruptible customer in host control area is deployed (scheduled) by WSCC and interrupts exactly the amount deployed
  100 MW interruption @ $500/MWh
  Retail ESP rate = $50/MWh
  Host control area imbalance cost = $100/MWh
  Meter reading prior to interruption = 100 MW; after interruption = 0 MW
Host Control Area
Deficit Control Area
Deficit CA pays $50,000 Scheduled MW  Market clearing price
Host CA receives $0 Deficit CA payment  Payment to customer
Payment to customer $50,000 (MW interrupted (up to instruction))  Market clearing price
Payment to retail ESP $5,000 (Scheduled MW  Meter usage)  Retail ESP rate
Imbalance payment to host CA $0 (Scheduled MW  Interrupted MW (up to instruction))  Host CA imbalance cost
Customer nets $45,000 Payment to customer  Payment to retail ESP  Imbalance payment to host CA
Customer
100 MW
100 MW
reduced
$0
Retail
ESP
$50,000
$50,000
$5,000

## Slide 2
WSCC Region-Wide Interruptible Load Auction
Example 2
Customer Interrupts Less Than Deployed
Interruptible customer in host control area is deployed (scheduled) by WSCC and customer interrupts only 90 MW out of 100 MW deployed
  100 MW interruption @ $500/MWh
  Retail ESP rate = $50/MWh
  Host control area imbalance cost = $100/MWh
  Meter reading prior to interruption = 100 MW; after interruption =10 MW
Host Control Area
Deficit Control Area
Deficit CA pays $50,000 Scheduled MW  Market clearing price
Host CA receives $5,000 Deficit CA payment  Payment to customer
Payment to customer $45,000 (MW interrupted (up to instruction))  Market clearing price
Payment to retail ESP $5,000 (Scheduled MW  Meter usage)  Retail ESP rate
Imbalance payment to host CA $1,000 (Scheduled MW  Interrupted MW (up to instruction))  Host CA imbalance cost
Customer nets $39,000 Payment to customer  Payment to retail ESP  Imbalance payment to host CA
Customer
100 MW
90 MW
reduced
$1,000
Retail
ESP
$45,000
$50,000
$5,000
$5,000

## Slide 3
WSCC Region-Wide Interruptible Load Auction
Example 3
Customer Interrupts More Than Deployed
Interruptible customer in host control area is deployed (scheduled) by WSCC and interrupts 110 MW out of 100 MW deployed
  100 MW interruption @ $500/MWh
  Retail ESP rate = $50/MWh
  Host control area imbalance cost = $100/MWh
  Meter reading prior to interruption = 110 MW; after interruption = 0 MW
Host Control Area
Deficit Control Area
Deficit CA pays $50,000 Scheduled MW  Market clearing price
Host CA receives $0 Deficit CA payment  Payment to customer
Payment to customer $50,000 (MW interrupted (up to instruction))  Market clearing price
Payment to retail ESP $5,000 (Scheduled MW  Meter usage)  Retail ESP rate
Imbalance payment to host CA $0 (Scheduled MW  Interrupted MW (up to instruction))  Host CA imbalance cost
Customer nets $45,000 Payment to customer  Payment to retail ESP  Imbalance payment to host CA
Customer
100 MW
110 MW
reduced
$0
Retail
ESP
$50,000
$50,000
$5,000