## Slide 1
Winter Supply Reliability
Gas Accord II Workshop

## Slide 2
Agenda
Policy Background
Cold Temperature Hypothetical Event Sequence
Cold Weather Impact on Core
Cold Weather Impact on Noncore and Electric Generation
Cold Weather Impact on Gas Market Costs
Summary of Expected Annual Costs Due to Cold Weather Event
Options for Increasing Supply Reliability

## Slide 3
Policy
Background

## Slide 4
Curtailment Policy Prior to Gas Accord
Curtailment priorities assigned P1 (residential) through P5
P5 customers were first interrupted in a supply shortage followed by P4 and so on
P5 customers were the legacy electric generation plants operated by PG&E and were expected to have fuel oil back-up
PG&E’s Procurement Department was responsible for balancing the system and would buy as much spot gas as possible to support the system during cold weather events

## Slide 5
Curtailment Policy Prior to Gas Accord (Continued)
Because the majority of the electric generation load had alternative fuels, only a very small proportion of noncore customers were expected to be curtailed in a supply shortfall during extreme cold weather events
Noncore customers were also expected to have an alternative fuel source

## Slide 6
Supply Reliability Policy under the Gas Accord
PG&E’s Procurement Department no longer responsible for balancing the system
Non-compliance charges provide the incentive for customers to secure supplies and balance their loads
Core has priority of service. CGT may use diversions of supply to maintain this priority
No priority preference between noncore and electric generation
No requirement for legacy plants or noncore to have alternate fuel source

## Slide 7
Cold Temperature
Hypothetical Event Sequence

## Slide 8
Cold Temperature Hypothetical Event Sequence
On January 10, PG&E forecasts a 33 degree day for January 11 and calls an EFO.
PG&E sends a load forecast to CPGs showing that core load will be 2,900 MMcf/d for January 11.
CPGs schedule 1,200 MMcf/d of firm flowing supply and 1,100 MMcf/d of firm storage withdrawal. Additional spot gas is purchased at Topock and the PG&E citygate.
CPGs call on their additional peak supply arrangements if they have them.

## Slide 9
Cold Temperature Hypothetical Event Sequence (Continued)
CPGs last effort is to buy gas at Stanfield because Redwood capacity is still available. At Stanfield, several utilities with inelastic demands bid up the market price.
  Price escalates rapidly. This price increase has an impact on market prices for several days even after cold weather is gone
Gas is scheduled in the timely cycle at 9:30 a.m. on January 10 for the January 11 gas day.
Once confirmations are completed with the upstream pipelines, CGT determines whether enough supply is scheduled to meet demand.

## Slide 10
Cold Temperature Hypothetical Event Sequence (Continued)
CGT determines that CPGs have only scheduled 2,700 MMcf/d and will be short supply by 200 MMcf/d.
CGT also determines that total market demand will be 4,450 MMcf/d but only 3,890 MMcf/d of supply has been scheduled.
  The system will be short supply by 560 MMcf/d.
  The noncore is short supply by 360 MMcf/d.
At approximately 1:00 p.m., PG&E calls for a diversion of 200 MMcf/d from the noncore to make-up the core supply shortfall.
  PG&E expects that the EFO provides enough incentive for the remaining 360 MMcf/d of noncore load without matching supply to be shut off voluntarily.

## Slide 11
Cold Temperature Hypothetical Event Sequence (Continued)
PG&E diverts gas from as-available transportation first and then firm transportation. PG&E notifies balancing entities that their gas is being diverted.
  PG&E does not distinguish between noncore and EG customers
PG&E freezes the nomination and scheduling process for the next three cycles.
Balancing entities notify their end-users that they do not have supply to burn and must curtail load.
  End-users may ignore order to stop burns
  Marketers may de-schedule the diverted gas into an upstream market with higher prices

## Slide 12
Cold Temperature Hypothetical Event Sequence (Continued)
PG&E expects some non-compliance of the EFO and diversion orders by the noncore and may need to gross up the diversion order by an expected amount (100 – 200 MMcf/d)
  PG&E may not have the manpower to physically shut off all non-compliant customers
As gas-fired electric generators are taken off line by the diversion, the ISO needs to buy more expensive power (e.g. imports) to secure adequate electricity supply
  Electric prices are driven up as various regions compete for available power imports

## Slide 13
Cold Weather
Impact on Core

## Slide 14
Cold Temperature Supply - Demand Projections For the Total Core Market

## Slide 15
Year 2000 Core Demand vs. Supply

## Slide 16
Year 2008 Core Demand vs Supply

## Slide 17
Temperature Probability Curve

## Slide 18
Cost Per Year for Core Diversions
Methodology
  Backcast on 80 years of temperature data
  Assumed $100 per Dth penalty (EFO noncompliance charge plus diversion charge)
  Assumed CPGs will require diversion above 2.7 Bcf
  Calculated diverted load times penalty
Results Expected Maximum
Cost/Year One-Year Cost
Year ($ million) ($ million)
2000 $5 $99 2005 $11 $212
2008 $24 $320

## Slide 19
Cold Weather Impact on Noncore and Electric Generation

## Slide 20
Cold Temperature Demand Projections

## Slide 21
Cold Temperature Supply Projections

## Slide 22
Noncore and EG Supply-Demand Shortfall

## Slide 23
Supply-Demand Picture in 2000
Noncore Diversion and Curtailments
Diversions Needed To Support Core
Core Demand
Total Demand
Available Supply
Core Supply

## Slide 24
Economic Loss to Noncore from Gas Supply Disruption
Diversion of gas from the noncore market has an economic cost. This cost is lost production, damage to equipment (e.g. glass furnaces), and lost profits from industrial customers that must interrupt their business during a gas diversion.
After the December 1998 incident, PG&E was informed by some customers that their disruption costs were as high as $100 per Dth. For this analysis, a disruption cost was assumed to be $50 per Dth.

## Slide 25
Economic Loss to Noncore from Gas Supply Disruption (Continued)
Methodology
  Backcast on 80 years of temperature data
  Assumed a $50 per Dth disruption cost
  Core diversion of noncore not included since customer compensated by core via $50 per Dth diversion charge
  Calculation: Noncore shortfall prior to diversion multiplied by the disruption cost
Results Expected Maximum
Cost/Year One-Year Cost
Year ($ million) ($ million)
2000 $2 $37
2005 $1 $27
2008 $2 $33

## Slide 26
Economic Loss to Electric Generators from Gas Supply Disruption
Without fuel oil back-up, generator must reduce electric output, and therefore, loses revenue
Methodology
  Backcast with same 80 years of temperature data
  Assumed market electric price of $100 per MWh, which is about $10/dth equivalent
  Calculation: EG shortfall prior to diversion multiplied by the gas equivalent price for lost electric sales
Results Expected Maximum
Cost/Year One-Year Cost
Year ($ million) ($ million)
2000 $0.8 $15
2005 $0.5 $10
2008 $0.6 $13

## Slide 27
Cost to Electric Customers from Gas Supply Disruption
Gas diversion to core plus EG gas supply shortfall pulls electric power production off the electric market
The cost of electricity increases for all customers
  Assume 10,000 MWh winter electric demand
  Assume that electric prices rise about $1 per MWh per loss of 100 MW to the electric market
Results Expected Maximum
Cost/Year One-Year Cost
Year ($ million) ($ million)
2000 $1 $22
2005 $1 $24
2008 $2 $34

## Slide 28
Cold Weather Impact on Gas Market Costs

## Slide 29
Gas Cost Increase Due to Cold Event

## Slide 30
Gas Cost Increase for December 1998
Methodology
  Calculated 8 day gas price average prior to event: $2.26 per Dth
  Calculated gas price average for days until price returned to $2.26: $3.10 per Dth average for eleven days
  Assumed an average 1 Bcf of spot purchases daily for eleven days
Results
  Gas price increase for December 98 cold weather event was $9.25 million
  Year 2000 cold weather event could be twice the December 98 cost given that the current price of gas is over $5.00 per Dth
    Cost per future event could be $18.5 million

## Slide 31
Expected Cost of a Price Spike
Assume that price spikes will occur whenever firm assets are fully utilized and the market begins bidding for the last increments of available gas
  This occurs around 3.8 Bcf/d
  Probability of occurrence is once every 3 years in 2000
Results Expected
Cost/Year
Year ($ million)
2000 $6
2005 $12
2008 $19

## Slide 32
Summary of Expected Annual Costs Due to Cold Weather Event

## Slide 33
Summary of Expected Annual Cost to Market Due to a Cold Weather Event

## Slide 34
Messages from Analysis
Growing supply shortage to cover cold weather events
  Increasing need for diversions to serve core
  Even if Core planned to meet total peak demands, the noncore supply shortfall continues to grow
  No indication that customers will hold added supply in storage only for cold weather use
Cost to customers of supply shortfall is very high, even on an annual expected cost basis
  Expected annual costs range from $15 million in Year 2000 to $48 million in Year 2008
  Average total cost for a year that experiences a cold weather event ranges from about $190 million in Year 2000 to about $420 million in Year 2008. A cold weather event is experienced every six to ten years.

## Slide 35
Concerns Expressed by Customers
Noncore market expects and wants more supply reliability even in very cold conditions
Alternate fuels and oil back-up practically gone
  Environmental regulations make it expensive to maintain and use alternative fuels
Interruptible electric customers are frustrated with disruptions and are switching back to firm electric service

## Slide 36
Options for Increasing Supply Reliability

## Slide 37
Options Considered
Status Quo
Require CPGs to Meet Colder Supply Planning Criteria
Increase Diversion Cost
Implement Demand Side Measures
Increase Dedicated Storage Capacity
Add Pipeline Capacity

## Slide 38
Option: Status Quo
Status Quo: Let market decide when facility commitments are needed for additional supply
Considerations:
  Market tends to wait until a crisis occurs
  Even if storage capacity is available, market is not likely to voluntarily hold gas in storage for cold weather events
  Utility has default obligation to assure supply service to core
  Market looks to utility to anticipate reliability needs of the market and propose solutions

## Slide 39
Option: Require CPGs to Meet A Colder Supply Planning Standard
Require Core Procurement Groups (CPGs) to meet a supply standard colder than CWD (perhaps APD)
  Reduce reliance on involuntary noncore and electric generator diversion and/or curtailment
  CPGs would acquire seasonal firm transport and firm storage withdrawal
  Around 700 MMcf/d of additional firm supply needed to meet an APD standard

## Slide 40
Option: Require CPGs to Meet A Colder Supply Planning Standard (continued)
Considerations
  Core customers would incur full cost for increased supply
  Noncore receives significant benefits from not being subject to diversion and/or curtailment
  Current assets inadequate to satisfy this option
  Adequacy of firm contracts and supply need to be verified
  Added supply will moderate cold-weather commodity prices
  Level of penalties for nonperformance
  Lose some diversity benefits if all CPGs acquire assets for individual peak demands

## Slide 41
Option: Increase Diversion Cost
Increase diversion cost by increasing the diversion charge (now $50/dth)
Considerations
  CPGs would add supply based on expected economics compared to penalty
    Core will require more firm assets creating market share concerns
  Penalty may need to be doubled to justify a significant increase in CPG supply commitments
  Noncore receives benefits from reduced diversions and/or curtailments
  Risk of continued shortfalls and resulting use of diversions

## Slide 42
Option: Implement Demand Side Measures
Reduce the demand on the system during peak usage times, either voluntarily or controlled
  Measures could include oil backup, agreements with utility to reduce usage, remote controlled shut-off valves, etc.
Considerations
  Past response to such programs has been weak, even with incentive payments (credits)
  Oil backup is being removed because of expense to maintain and environmental concerns
  Remote controlled gas shut-off equipment is expensive
  Incentives for those willing to reduce load when needed; Other customers less subject to involuntary measures
  Complementary to other options

## Slide 43
Option: Increase Dedicated Storage Capacity
CGT reserves storage for very cold weather service, e.g. colder than CWD
  CPGs plan to provide firm supply for a CWD demand
  CGT reserves an increment of firm storage withdrawal to be used to support core on days colder than a CWD
  When CGT withdraws to support core load above a CWD, CPGs repay gas used along with existing monthly imbalances
  Reserved storage does not support noncore/EG shortfall
  PG&E annual cost to reserve the necessary storage and hold gas in storage is estimated to be $13 to $33 million

## Slide 44
Option: Increase Dedicated Storage Capacity (continued)
Considerations
  Supply guaranteed irrespective of who is short supply
  Entire market pays for added supply “insurance”
  Option is very cost-effective
    Cost to provide storage insurance is $13-33 million per year
    Benefit is avoided cost to customers of $15-48 million per year
  CPGs can continue to acquire supply to CWD standards
  Market may not place same value on cost to customers as this analysis shows
  Need to specify how and when utility will use this “insurance” storage
  Added costs for central backbone upgrade which could reach $24 million per year (may be needed in any case)
  Storage supply will moderate cold-weather market prices

## Slide 45
Option: Add Pipeline Capacity
Add pipeline capacity to increase supply access to basins
Considerations
  Cost not analyzed, but likely very high for just winter “insurance” service
  Pipeline capacity may also be needed on interstate, and perhaps Canadian pipelines
  Even with extra pipeline capacity, supply may not be available unless prices rise very high in California
  Any backbone expansion needed to meet summer peak will possibly add more winter supply