## Slide 1: ELECTRICITY MARKET VISION
FOR RTO IMPLEMENTATION

## Slide 2: Objective
A transmission structure that creates a bilateral forward market.
  Most energy traded in the forward market with ex-ante prices
  Balancing market covers real-time deviations under ex-poste prices
Forward market operates up to real time
  Balance schedules to RTO in day-ahead pre-scheduling
  All parties allowed to submit new schedules (adjustments) up until start of real-time

## Slide 3: Functional Modules for Energy Marketplace
Day Ahead Energy
Market
Marketplace for Secondary
Transmission
Rights
NERC ISN
(FlowBat)
RTO
Reliability Systems
Oasis Phase II
FERC RTO Filings
etag
New FERC Open Access Tariff
Politics
FERC Policy

## Slide 4
Details of Transmission Congestion Management, Reservations, Day Ahead Trading, and Scheduling

## Slide 5: [RTO Module] RTO Auctions Flowgate Rights (PTRs) Year, Month, Week, Daily (Timeframe: Year ahead through Real Time Scheduling Deadline)
RTO Determines “Commercially Significant” Flowgates and amounts of Flowgate Transmissions Rights (Physical Transmission Rights (PTRs))
Customer (or PSE or LSE) Determines What PTRs are Needed via a NERC “ISN”-Type or Similar System by Inputting “Point In” (by Area, Control Area, Hub, Zone, etc.) and “Point Out” (by Area, Control Area, Hub, Zone, etc.)
Acquire PTRs by Bidding in the Initial Auction (could be 2 year, annual, seasonal, on-peak/off-peak, etc.)
  List Flowgate
  MWs Needed
  RTO Does Not Need to Know any “Point In/Source” and “Point Out/Sink” (area, etc. will be necessary at scheduling)

## Slide 6: [RTO Module] RTO Auctions Flowgate Rights (PTRs) (continued)
RTO will Auction Additional PTRs if any become Available Toward Flow Date
Existing Transmission Contract Rights Should be Converted to PTRs
In all probability, existing Load Serving Entities (LSEs) will get some firm transmission right (PTR) allocation
RTO will Permit Counter-Schedules to Resolve Redispatch through the Creation of “Virtual” PTRs

## Slide 7: Day Ahead (or More) Transmission Trading Platform for Secondary Market (Timeframe: Year Ahead through Real Time Scheduling Deadline)
Allows Trading of PTRs up to Close of the Forward Market (such as 1 hour or less before the real time hourly market)
PTRs can be Subdivided through Bilateral Deals into Increments as Small as 1 hour (or less) and 1 MW; Recallable or Non-recallable Strips
PTRs can be Resold as Recallable
No Price Caps in the Secondary Market
Forward Market Not Run by the RTO
Currently allocated Ownership and Amount of PTRs Should be Public (on either the this Platform or RTO)

## Slide 8: Day Ahead Power Mechanism (Timeframe: 10 years Ahead through Real Time Scheduling Deadline)
Provides for Forward Market Settlements
Allows for Multiple Products
-- Into Products
-- Hub Products
-- Portfolio Bids/Unit Contingent
No requirement for a “Balanced” Position in Trading Energy Day Ahead
As much as Possible, State Retail Access Programs Should Obligate Utility Generation to be Offered into Day Ahead Energy PX

## Slide 9: [RTO Module] Day Ahead Scheduling With RTO (Timeframe: Day Ahead Scheduling Deadline)
Scheduling Required “Day Ahead” (Utilities argue “Day Ahead” is Necessary for System Reliability)
Provide “Initial” Balanced Schedule Via Etag (Including “Point In” and “Point Out” by “Control Area” or “Zone”, etc.)
Etag Includes Flowgate Transmission Right (PTR), Which May Still be an “Oasis Phase II” Number

## Slide 10: [RTO Module] Day Ahead Scheduling With RTO (ESCA System) (Timeframe: Day Ahead Scheduling Deadline) (Continued)
“Use it or Lose It”: All Unscheduled/Unnoticed PTRs Can Be Offered for Sale By RTO (Either “Firm” or “Subject to Recall” by Owner); PTRs Can be Subject to Recall as “Firm” in the Hourly Market by Owner (Up to 1 hour (or less) Ahead)(If Customer doesn’t either Schedule or Notify RTO how Customer will Use Its PTRs (subject to recall), then Customer Loses PTR and gets no Compensation -- RTO )
RTO Sells Unscheduled PTRs to Highest Bidder
Ability to put in a Schedule without PTRs, subject to Real Time Locational (Energy Value at the Input Point and Energy Cost at the Output) Balancing Costs -- but can include a Ceiling Price on Congestion Costs that Means the Schedule will get Cut if Congestion Price is Higher

## Slide 11: [RTO Module] Post Day Ahead Scheduling: Adjustment Period Before Real Time (Hourly Market) (Timeframe: Day Ahead Scheduling Deadline through Real Time Scheduling Deadline)
Allows Hour-Ahead Market
Can Submit New Balanced Schedules that Do Not Increase Congestion (Note that Schedules Without PTRs Clear in the Locational Balancing Market)
“Initial” Balanced Schedule Can Be Modified up until the Close of the Forward Market (1 hour (or less) ahead of flow)
Owner can Exercise Recall based on Stack Price (if RTO has sold the Unscheduled PTR)
If Owner has Sold the PTR in the Bilateral Market, Recall Rights can be Structured per your Deal
Allows Market Redispatch Scheduling on “etag” (counterflow) (Becomes “Obligation,” Not “Option”)

## Slide 12: [RTO Module] Post Day Ahead Scheduling: Adjustment Period Before Real Time (Hourly Market) (Timeframe: Day Ahead Scheduling Deadline through Real Time Scheduling Deadline)(Continued)
Hourly Transmission Schedules on “etag” Modified to List “Flowgate Transmission Right” (instead of Current Oasis No.) (PTR Ownership Confirmed Electronically by Secondary Transmission Platform)
Allows Day Ahead “Initial” Balanced Schedule to be Revised Subject to Purchasing Energy from Real Time Balancing Market (If you do not have all Necessary PTRs)
PTRs will flow Because if a Force Majeure Type Event Happens to the FlowGate, then the Cost of the Additional Inc and Dec is Socialized

## Slide 13: [RTO Module] Post Day Ahead Scheduling: Adjustment Period Before Real Time (Hourly Market) (Timeframe: Day Ahead Scheduling Deadline through Real Time Scheduling Deadline)(Continued)
Can Schedule Between Commercially Significant FlowGates without PTRs
Can Schedule to Hourly Shaped Loads (Do you want real time Dynamic Scheduling?)
While Schedules can be Adjusted up until Real Time, there will be Some Penalty for Being Off a “Significant Amount” (>10%? Based on Some Frequency, Scale, etc.) on your Schedule in Real Time

## Slide 14: [RTO Module] Real Time Balancing Mechanism (Timeframe: Within the Hour)
RTO Balances Energy (Provides Frequency Regulation)
RTO uses Voluntary “inc” and “dec” Bids from Both Generation and Loads to Adjust for Incremental Real Time Congestion
Coordination of AGC Operations
Provides Information (On OASIS Phase II) about Real Time Flows and Constraints

## Slide 15: [RTO Module] Real Time Balancing Mechanism (Timing: Within the Hour) (Continued)
(What information would traders Not Want Public?)
Coordinates/Provides Ancillary Services
  Voltage Levels and Var Support (with Some Form of Payment for VARs in Interconnection Agreement)
  RTO is PLR or Self-Provision of regulation, balancing, and reserves if serving load
RTO may Coordinate for or Provide for Losses
RTO is PLR for Ancillary Services

## Slide 16: RTO’S Reliability Model
No Need to Initially Collapse Control Areas
- Can Open Markets Faster and at Lower Costs by Utilizing Existing Infrastructure
RTO Control Areas
Security Authority Balancing
Interchange Authority Local Monitoring and
Redispatch Data Collection Systems

## Slide 17: [RTO Module] Other Functions
Settlements
After the Fact Trading of Imbalances for Settlements (Provided by RTO)

## Slide 18: [RTO Module] Other RTO Issues
Market Power Monitoring Separate (Enforced by FERC or DOJ)
No ICAP requirement
Load-Based Access Fee pays Fixed Costs
Can solve Seams Issues for RTOs that Implement This (Can Possibly be Used in Current Pools at Some Point in the Future)

## Slide 19: [New Tariff Module] Tariff Issues
Non-Pancaking of Rates (current retail customers will pay initial rate similar to what it pays to current utility), plus PTR charge (if separately purchased or allocated)
No Deposit Required (if Customer Creditworthy)
Liquidated Damages Clause for RTO’s Failure to Provide Service

## Slide 20: [Political Module] Political Issues
Advocate at FERC and State PUC Level
Identify Municipal, Industrial, Other Allies
Attempt to Obtain Utility Participation Through the RTO Process