## Slide 1: Gas/Coal Emissions Comparison (lb/MWh)
NOx Emissions
0.13
1.5
0.8
4.9
Existing
Coal Boiler
New Coal
Boiler
Old Gas
Boiler
Gas
Combined-
Cycle
SO2 Emissions
0.004
0.006
14
4
Existing
Coal Boiler
New Coal
Boiler
Old Gas
Boiler
Gas
Combined-
Cycle
CO2 Emissions
1,986
1,112
819
2,090
Existing
Coal Boiler
New Coal
Boiler
Old Gas
Boiler
Gas
Combined-
Cycle
PM-10 Emissions
0.04
0.06
0.8
0.8
Existing
Coal Boiler
New Coal
Boiler
Old Gas
Boiler
Gas
Combined-
Cycle

## Slide 2: There are Multiple Options for Natural Gas Supply
North American gas prices are likely to settle into the $3.50 to $4/MMBtu range.
Gas from Alaska/MacKenzie Delta is expected to be available in the U.S. at less than $3/MMBtu.
LNG can be landed at $3.35 to $4/MMBtu.
Gasification is feasible at $4 to $5/MMBtu.

## Slide 3: Gas Supply Options - Prices

## Slide 4: Power Generation Technology Comparison
Data source: EIA

## Slide 5: Power Plant Water Consumption (gal/MWh)

## Slide 6: Power Generation: Siting Issues
Gas combined cycles have much lower emissions, much smaller footprint, and fewer “fear factors” than other options – but are still very difficult to site.
Siting will be a significant issue for all new energy infrastructure.
  Opposition to construction of new coal & nuclear plants will cause significant delays.
  Nautral Gas and LNG, while more environmentally-friendly, still face NIMBY concerns as well.