## Slide 1
Decision and Information Sciences Division
Argonne National Laboratory
Argonne National Laboratory
Application of Simulation Models to Analyze International Energy and Environmental Issues
Guenter Conzelmann
Energy and Environmental Systems Analysis Group
Argonne National Laboratory (ANL) 9700 South Cass Avenue
Argonne, Illinois 60439, USA phone: 630-252-7173 fax: 630-252-6073 email: guenter@anl.gov

## Slide 2: DIS Develops, Applies, and Transfers Innovative Tools, Models, and Information Systems for Energy and Environmental Systems Analysis
Apply
Develop
Transfer

## Slide 3: DIS has been Involved in International Energy and Environmental Systems Analysis for more than 20 Years
CAPACITY BUILDING IS A MAJOR COMPONENT OF ANL’S INTERNATIONAL ENERGY AND ENVIRONMENTAL SYSTEMS STUDIES
DEVELOP energy systems analysis software (ENPEP, GTMax, APEX, new complex adaptive systems tools, etc.)
APPLY models to
  conduct country-specific studies for foreign governments and power companies
  consult lending agencies on specific energy project loans
TRANSFER software tools by
  conducting training programs in energy demand forecasting, energy and electric system analysis, analysis of environmental impacts (first training course in 1978)
  participating in technical cooperation projects to provide technical support to in-country institutions (World Bank, IDB, USDOE, USDOS, IAEA, etc.)

## Slide 4: DIS has an Integrated Approach to Energy, Economic, and Environmental Systems Analysis
IMPACTS
ANALYSIS
SUPPLY/
DEMAND
BALANCE
DECISION ANALYSIS
ENERGY
DEMAND
ANALYSIS
ECONOMIC
ANALYSIS
ENERGY
TECHNOLOGY
CHARACTERI-
ZATION
ENERGY
RESOURCE
EVALUATION
ITERATION

## Slide 5: DIS Has Developed a Variety of Tools for Use in Energy, Economic, and Environmental Systems Analysis
Economic Analysis
Energy Demand Analysis
Energy Resource Analysis
Energy Technology Characterization
Supply/ Demand Balance
Impact Evaluation
Decision Analysis
ADAP
GASMAP
DECADES
IMPACTS
RAINS TAF
AIRPACTS
MDA
DAM
STATS
AMIGA
MACRO
LIEF
MAED
DEMAND
BALANCE PACE
ELECTRIC SMN
ICARUS GTMAX
Notes: <date/time>
Over the years, DIS has developed and assembled a unique set tools to support our broad-based analytical approach.
Each model is complex and sophisticated stand-alone tools. DIS goes beyond this myopic viewpoint to analyses the complex interactions among different aspects of economic, energy, and environmental control systems.
These tools have become increasing complex as we learn more about system behavior and as issues and problems in the world evolve.

## Slide 6: One of DIS’s Major Software Products, the Energy and Power Evaluation Program (ENPEP), Consists of 10 Integrated Analysis Tools

## Slide 7: ENPEP is Designed to Analyze the Entire Energy System in an Integrated Framework
Reveal cross-sectoral effects; provide structure for consistent energy “planning” program
Integrated framework allows evaluation of feedback effects
Price of Coal/
Carbon Tax
Demand for Coal
Demand for Electricity
Price of Electricity
Atmospheric Emissions

## Slide 8: BALANCE Determines the Equilibrium Supply/Demand Balance of the Energy System
Supply
Demand
Equilibrium
INPUT
Energy system structure
Base year energy flows and prices
Energy demand growth projections
Technical and policy constraints
BALANCE
OUTPUT
Quantity
Price/Cost

## Slide 9: BALANCE Uses an Energy Network to Simulate Energy Markets
Transmission and Distribution of Oil Products, Coal, Electricity, and Other Fuels/Resources
Residential
Paper Industry
Other
Industry
Food Proc.
Industry
Agriculture
& Fishing
Transport
Commercial
Cement
Industry
Chemical
Industry
Ceramic
Industry
Textile
Industry
Electric Sector
Oil and Gas Supply Sector
Coal Sector Supply Sector
Renewables and Others Sector

## Slide 10: In the Model, a Network Implementation May Look as Follows:

## Slide 11: Each Sector is Modeled Using a Series of Nodes and Links - Design Differs Depending on Data Availability and Type of Issue Analyzed
CO2 - With Carbon Tax
Fuel Shares - No C Tax
Fuel Shares - With C Tax
CO2 - No Carbon Tax

## Slide 12: BALANCE Uses a Logit-Function to Estimate Future Market Shares of Competing Commodities
Increasing
price sensitivity

price sensitivity for
this decision process
MS:
market share
P:
price
PM:
Q:
quantity
premium multiplier
MS
1
=
Q
1
Q
1
+ Q
2
=
1
P
1
x PM
1

+
1
P
1
x PM
1

1
P
2
x PM
2

Decision
P1
Q1
P2
Q2
Qdemand
Notes: 15
15
Balance uses a non-linear equilibrium algorithm to determine the energy supply and demand balance.
One of the key node types in the development of a network is the decision node. This node type is used to determine the market share of competing commodities. BALANCE uses a logit function shown here to estimate demand for various energy options based on relative prices.
When two commodities have the same price, the price ratio equal 1.0 and it is assumed that each commodity will get an equal share of the market.
However, when the price of the first fuel is more expensive expensive than the second, it market share is less than 50 percent. A relatively lower price for the first fuel results in a market share greater than 50 percent.
By adjusting the price sensitivity parameter in the logit function the shape of the price response curve can be changed.
Market share calculations assume a perfect market. However, adjustments can be made to simulate energy policies and energy system constraints. A lag factor is used to account for delays in capital stock.
The result is a market based equilibrium with policy constraint that is solved using the Jacobi iterative method.

## Slide 13: DIS Developed the New GTMax Model to Analyze the Complex Marketing and Operational Issues in Today’s Deregulated Power Markets
GTMax: Generation and Transmission Maximization Model maximizes net revenues and ensures that market transactions and system operations are within physical and institutional limitations
Identifies utilities and assets that can successfully compete in deregulated markets
Formulates optimal spot market transactions and strategies with interconnected systems/countries
Determines the optimal path of contractual power flows
Identifies operational and network bottlenecks and the marginal value of relieving system obligations and constraints
Identifies stranded investments

## Slide 14: ENPEP is Used by Energy and Environmental Experts Worldwide to Analyze a Variety of Critical Issues
Electric system analysis
  expansion analysis, demand side management
  optimal hydro/thermal dispatch ($, environment)
  deregulation, independent power producers, power market studies, interconnection studies, etc.
Total energy system
  overall energy sector development strategies
  natural gas market analysis
  energy conservation+efficiency
Environmental analysis
  emissions projections for PM, SO2, NOX, etc.
  emissions reduction strategies for PM, SO2 and NOX
  emissions trading for SO2 and CO2 (cap and trade)
  GHG mitigation studies and Kyoto Mechanisms
  waste generation, land use, water pollution
Notes: <date/time>

## Slide 15: Current/Recent ENPEP Applications in South America
URUGUAY
(BALANCE, IMPACTS)
National energy analysis
Market penetration of natural gas
GHG mitigation analysis
FCCC Nat Com (submitted)
VENEZUELA
(WASP, BALANCE, IMPACTS)
National energy analysis
GHG mitigation analysis
COLOMBIA
(MAED, WASP, BALANCE, IMPACTS, VALORAGUA)
National energy analysis
Natural gas expansion
Electric system development
Air pollution (PM, SOX, NOX, GHG, etc.)
PM + SOX control cost analysis
PERU
(WASP, BALANCE, IMPACTS)
Load forecasting
Electric system expansion
National energy analysis
Air pollution analysis
GHG mitigation
BRAZIL
(WASP, BALANCE, VALORAGUA, IMPACTS)
State energy analysis
State electric system development
Air pollution analysis
Land use analysis
Decision analysis
Notes: <date/time>

## Slide 16: Current/Recent ENPEP Applications in Eastern Europe
Lithuania
(WASP, MAED)
Electric system analysis
Poland
(MAED, WASP, BALANCE, IMPACTS)
Deregulated power market analysis
National energy analysis
Air pollution analysis
GHG mitigation analysis
PM and SOX control cost analysis
Romania
(WASP, BALANCE, IMPACTS)
National energy analysis
Energy sector restructuring
Natural gas imports
Rehabilitation, IPPs
Removal of energy subsidies
Air & water pollution analysis
GHG mitigation analysis
FCCC NatCom (submitted)
Waste generation
Croatia+Balkans
(MAED, WASP, BALANCE,
IMPACTS)
National energy plan
Electric system expansion
Air pollution analysis
IPP+Interconnection study
Bulgaria
(WASP, BALANCE, IMPACTS)
National energy plan
Electric system development
GHG mitigation analysis
FCCC Nat Com submitted
Belarus
(WASP, BALANCE, IMPACTS)
Electric system expansion
National energy analysis
Air pollution analysis
Turkey
(WASP, ICARUS, BALANCE, IMPACTS, etc.)
National energy plan
Electric sector dispatch and expansion
Privatization, Environmental assessments
Hungary
(WASP, BALANCE, IMPACTS)
Electric sector expansion
National energy analysis
GHG mitigation analysis
IPP Bid Evaluation
Slovakia
(BALANCE, IMPACTS)
National energy analysis
GHG mitigation analysis
FCCC Nat Com (submitted)
Joint implementation
Notes: <date/time>

## Slide 17: Current/Recent ENPEP Applications in Asia
Kazakstan
(BALANCE, IMPACTS)
National energy plan
GHG mitigation analysis
Indonesia
(WASP, BALANCE, IMPACTS)
Electric system analysis
National energy plan
Air pollution analysis
Vietnam
(MAED, WASP, IMPACTS, BALANCE)
Electric system development
National energy plan
Air pollution analysis
Nepal
(WASP)
National energy plan
GHG mitigation analysis
Pakistan
(WASP)
Electric system development
Thailand
(BALANCE, IMPACTS)
National energy plan
GHG mitigation analysis
China
(BALANCE)
Regional energy plan
South Korea
(WASP)
Electric system development
GHG mitigation analysis
FCCC Nat Com (submitted)
Bangladesh
(WASP)
IPP Evaluation

## Slide 18: DIS Used Several ENPEP Modules to Evaluate Two Proposed Transmission Lines in the Restructured Balkan Power Markets
PC-VALOR AGUA
Detailed Hydro Data
Project Finance Model
Financial Viability
GTMax
Power Transactions, Market Clearing Prices, etc.
ELECTRIC
(WASP-III+)
System Configurations 2005 + 2010
Demand forecast, existing generating units, system expansion options, etc.
Hourly system loads, location of power plants, transmission capacities, etc.
Economic and financial data and assumptions, etc.
Water inflows, reservoir characteristics, thermal and hydro generating units, etc.

## Slide 19: DIS Used Several ENPEP Modules to Evaluate Two Proposed Transmission Lines in the Restructured Balkan Power Markets

## Slide 20: Model Results Show Clear Economic Benefits of Proposed Interconnections

## Slide 21: Bi-Directional Transfers are Projected to be Significantly Below Line Capacities

## Slide 22: ANL and Local Experts Used ENPEP to Analyze Natural Gas and Electricity Issues in Uruguay
Overall energy sector development strategy in light of increasing regional integration
Uruguay’s energy supply system is undergoing change (MERCOSUR, natural gas imports, potential increase in electricity connections with other countries, energy sector reform, etc.)
For a total of six scenarios, analyze fuel substitution trends due to gas imports and increased electricity interties, and project future market penetration of natural gas by sector
DIS collaborated with a team of local energy experts from the Presidential Planning Office (OPP), Ministry of Energy (MoE), National Energy Office (DNE), Electric Utility (UTE), Oil Refinery (ANCAP), and Gas Company
Project sponsored by The World Bank
Notes: 33
33

## Slide 23: Uruguay’s Projected Natural Gas Imports Are Highest in an Open Regional Electricity Market

## Slide 24: ANL Used ENPEP to Assist the Hungarian Power Companies in Evaluating IPP Bids
The Hungarian Power Companies (MVMRt) were recently restructured from a state-owned vertically integrated utility into a transmission company; generation is owned by private (domestic and foreign) companies; 6 regional private distribution companies
MVMRt determined additional power generation capacity is needed; MVMRt issued a tender in 1997 and received 80 initial responses
MVMRt contracted Argonne to develop a methodology for evaluating the IPP bids and to audit the evaluation process
MVMRt signed two long-term PPA contracts with operators of gas-fired combined cycle combustion turbines worth $1.3 billion
Announcement can be found at http://www.mvm.hu/angol/angkapac.html

## Slide 25: What Will the Future Bring?
Model development to meet changing environment, such as restructuring and deregulation of energy markets
  continue to adapt existing tools
  create new, cutting-edge tools using agent-based complex adaptive systems approach
Model applications
  expand domestic and international client base
  promote restructuring and deregulation expertise
  promote interdependency expertise
Model transfer
  new model licensing arrangements to make tools available to private, for-profit companies
  new model distribution channels