## Slide 1: Real Options and Valuation of Fixed Assets in the Energy Industry
Vincent Kaminski
Enron Corp. Research Group
London, February 22, 2000
© 1999 VK-9010292-<number>

## Slide 2: Evolution of Energy Markets in the OECD Countries
Accelerating deregulation of the energy markets, including retail markets
Development of markets in energy derivatives
  Forward and futures markets
  OTC options markets
Two parallel, sometimes conflicting trends
  Vertical disintegration of many energy companies
  Horizontal consolidation

## Slide 3: Traditional Approaches to Valuation of Fixed Assets
Traditional approach to valuation of energy-related fixed assets - Discounted Cash Flow
This approach was justified under the conditions of a regulated industry and /or low price volatility
Recent sales of power plants in the United States often commanded prices that cannot be justified if one uses traditional valuation techniques
One possible explanation: adjusting the valuations for real options embedded in the existing plants
  Expansion option
  Access to the transportation and transmission grid

## Slide 4: Real Options Applications at ENRON Corp.
Valuation of energy and telecommunications related assets
  gas-fired power plans
  pumped storage power plants
  underground natural gas storage facilities
  pipelines
Real options provide a link between investment decisions and future operational decisions
  flexibilities are created and rigidities are removed through forward looking investment decisions
  options created through investment decisions are exercised through active management decisions
An analysis tool that helps to create value for the shareholders

## Slide 5: Types of Underground Natural Gas Storage
Depleted natural gas and oil fields with sufficient porosity, permeability and retention characteristics
Aquifers
  geology of aquifers is similar to that of depleted production fields
  water-bearing sedimentary rock covered with impermeable cap rock
Salt caverns
  storage developed by injecting water into a salt formation and creating a cavern

## Slide 6: Depleted Fields as Storage Reservoirs
Depleted gas/oil and aquifer fields are characterized by a low turnover rates
Injection season typically lasts from March/April till October/ November
The reservoir is emptied during winter
During an occasional upward spike in prices during summer, the injections can be suspended and gas earmarked for injections can be diverted to the market
These reservoirs take primarily advantage of summer/winter spread
Injections withdrawals are typically hedged in the futures/forwards markets in order to lock-in seasonal spread
Optionality consists in the ability to time hedging decisions and to occasionally suspend injections or withdrawals

## Slide 7: Salt Dome Storage
High deliverability compared to other types of underground storage
A salt formation storage facility can be turned over several times during the heating season
During summer, salt dome storage is used to satisfy cooling load
Injection/withdrawal rates(as in the case of aquifers) depend on the amount of gas in storage
  high pressure of gas in storage slows down injections, accelerates withdrawals
  low pressure has the opposite effect
Storage for peaking operations used to satisfy swing demand

## Slide 8: Storage Optionality
Depleted oilfield/aquifer storage is a an option on a seasonal spread
Additional optionality related to
  the option to switch from injection to withdrawal mode (or vice versa) when justified by market conditions
  the option to adjust timing of hedges
  the option to deliver to multiple pipelines (depends on the location of the storage facility)
Optionality is limited by operational constraints
  rate of injections/withdrawals changes with the level of working gas in storage
  gas has to be injected into storage due to contractual obligations even when it’s unprofitable based on the seasonal spread

## Slide 9: Storage Optionality (2)
Salt dome storage is an option on short-term calendar spread
Gas is being injected when prices drop and withdrawn when prices spike
Quick turnover allows the storage operator to take advantage of price spikes (upward and downward)
Additional optionality related to location (multiple pipelines)
The operations of a salt dome storage may be affected by contractual obligations (supporting the operations of an associated pipeline)

## Slide 10: Storage Optionality (3)
Optimal gas storage facility operation
  When to put gas in, and when to take it out
    These are interacting, compound options:
      Putting gas in costs money but creates the option to sell gas later
      Taking gas out returns money and creates the option to store gas again later
      The value and optimal exercise policy of these options interact
    Option exercise price:
      Price of gas plus cost of storing or removing gas
    Option exercise constraints reduce the value of the option

## Slide 11: Storage Optionality
Gas Storage Facility
  Operating value is the sum of the value of operating options considered above
  Valuing these options over the investment horizon requires a long term model of gas prices at facility location
The value of an option depends often on who owns the asset

## Slide 12: Gas-Fired Power Plant
A gas-fired power plant can be looked at as a portfolio of spark spread options
A spread option is an option on the difference between two prices
In the case of a power plant, a spark spread option is defined as a difference between the price of electricity ($/MWH) and the natural gas price ($/MM BTU) multiplied by the so-called heat rate
The heat rate is a measure of thermal efficiency of a power plant
  the number of BTUs of natural gas required to produce one kWh of electricity
  typical heat rate for a modern plant is 7,000 - 10,000

## Slide 13: Gas-Fired Power Plant
The strike for the spark spread option is the variable O&M cost
A gas-fired power plant can be relatively quickly turned-on and turned-off
This feature allows the power plant to take advantage of short-term power price spikes
A word of caution: there are many operational constraints that have to be taken into considerations in valuation of a peaking plant

## Slide 14: Real Options in the Energy Business: Challenges
What is at stake?
Investments with long gestation period and with long economic lives
High level of capital commitments and lumpiness of investment projects
Major challenges:
  modeling of energy prices
  capturing correctly the texture of a project and avoiding oversimplification

## Slide 15: Modeling Energy Prices
Energy prices have split personality (Dragana Pilipovic)
In the long run, the dynamics of energy prices can be modeled using Geometric Brownian Motion or a Mean Reversion Process
Once we enter the delivery period, the behavior off the prices is subject to supply/demand shocks
  one has to combine a diffusion process with a jump process
Examples: price spikes in the power markets in the summer of 1998 and the summer of 1999

## Slide 16: Natural Gas Prices
Natural gas futures contract available on NYMEX with the delivery point at Henry Hub in Louisiana
Price at a different location is given by Nymex price and the so-called basis
Basis is an independently traded OTC commodity
Physical gas for next month delivery is transacted during the so-called bid-week (a few days at the end of the month, around NYMEX natural gas contract expiration date)
  the average of the bid-week prices is available as the so-called index, based on a phone survey of transactions and published by industry newsletters
Gas for the next day delivery is traded at the OTC markets
  transactions prices form many locations available as the so-called Gas Daily Prices

## Slide 17: Power Prices
Power prices in the US have been characterized recently by very high volatility (especially during the summer periods)
High volatility can be explained by a number of different factors
  high convexity of the supply stack for most markets
  limited transfer capability between major markets
  partial deregulation
  relative immaturity of the market
High price volatility increases the value of options embedded in the generation assets

## Slide 18: Supply and Demand in The Power Markets
Supply stack
Demand
Price
Volume

## Slide 19: SP15 On-Peak Price

## Slide 20: Modeling Price Dynamics
Correct valuation of energy assets hinges on a correct model of price dynamics
Valuation of reservoir storage requires modeling of the forward price curve
  forward price curve should be modeled as a unified object
  the model should capture the possibility of reshaping of the forward price curve to allow for the evolution of the winter/summer price spread
In all cases, it is important to capture short-term price spikes
Most price dynamics models used in practice combine mean (or trend) reversion with jumps
Main danger: non-stationary nature of price processes

## Slide 21: Correct Representation of Optionality
Main danger in applications of real options in the energy industry: assumption of a perfect, frictionless world
Options embedded in real assets are often reduced and neutralized through restrictions on their exercise dictated by technology and operational constraints
The constraints are often ignored in practical applications:
  they can be identified through discussions with engineers and plant managers
  it is often difficult to capture the constraints in a model