## Slide 1: Key Techniques to Accurately Estimate Volatility
Vincent Kaminski, Ronnie Chahal
Enron Corp.
Power ‘99
Houston, June 23, 1999

## Slide 2: Importance of Volatility
Critical input to option pricing models
  More accurate volatility forecasts increase the efficiency of hedging strategies
Used as a measure of risk in models used in
  Risk management (value-at-risk)
  Portfolio selection
  Margining

## Slide 3: Different Types of Volatility
Historical volatility: volatility estimated from historical prices
Implied volatility: volatility calculated from option prices observed in the market place
Volatility implied by a fundamental model

## Slide 4: Volatility: Estimation Challenges
Limited historical data
Seasonality
  Insufficient number of price observations to properly deseasonalize the data
Non-stationary time series
The presentation below enumerates and exemplifies the difficulties
No easy solutions

## Slide 5: Definition of Volatility
Volatility can be defined only in the context of a stochastic process used to describe the dynamics of prices
Standard assumption in the option pricing theory: Geometric Brownian Motion
Definition of volatility will change if a different stochastic process is assumed

## Slide 6: Geometric Brownian Motion
dP = Pdt + Pdz
  P - price
   - instantaneous drift
   - volatility
  t - time
  dz - Wiener’s variable (dz =  dt, 

## Slide 7: Estimation of Historical Volatility
Estimation of historical volatility
  Calculate price ratios: Pt / Pt-1
  Take natural logarithms of price ratios
  Calculate standard deviation of log price ratios (= logarithmic price returns)
  Annualize the standard deviation (multiply by the square root of 300 (250), 52, 12, respectively, for daily (Western U.S., Eastern U.S.), weekly and monthly data
Why use 300 or 250 for the daily data? Answer: it’s related to the number of trading days in a year

## Slide 8: Annualization Factor
M
T
W
T
F
M
4 Daily Returns
Weekend Return

## Slide 9: Annualization Factor
Alternative approaches to annualization
  Ignore the problem: close-to-close basis
  Calendar day basis
  Trading day basis
Trading day approach
  French and Roll (1986): weekend equal to 1.107 trading days (based on close-to-close variance comparison) for U.S. stocks
  Number of days in a year: 52*(4+ 1.107) = 266

## Slide 10: Annualization Factor
Close-to-close variability of returns over weekend in the stock market is lower because the flow of information regarding stocks slows down
Is this true of energy markets?
The answer: Yes, but to a much lower extent
The information regarding weather arrives at the same rate, irrespective of the day of the week

## Slide 11: Seasonality
How does seasonality affect the volatility estimates?
Assume multiplicative seasonality
  Pt = sPa
  Seasonality coefficient s in calculations of price ratios will cancel
The price ratio corresponding to a contract rollover date should be eliminated from the sample

## Slide 12: SP15 On-Peak Price
$

## Slide 13: 20-Day Historical Volatility
%

## Slide 14: Mean Reversion Process
Prices of commodities gravitate to the marginal cost of production
Mean reversion models borrowed from financial economics
  Ornstein - Uhlenbeck
  Brennan - Schwartz

## Slide 15: Ornstein-Uhlenbeck Process
dP = (Pa - P)dt + dz
   speed of mean reversion
   volatility
  Pa average price level
The parameters of the equation above can be estimated using a discrete version of the model above (an AR1 model)
  Pt = a + b Pt-1 + t

## Slide 16: Ornstein-Uhlenbeck Process
The coefficients of the original equation can be recovered from the estimated coefficients of the the discrete version
  Pa = -a/b
   =-log(1+b)
In this case,  is measured in monetary units, unlike standard volatility

## Slide 17: Ornstein-Uhlenbeck Process
Coefficient estimates (SP15 prices, on-peak)
      4/1/98 - 6/15/ 99 7/1/98 - 9/30/98
  Pa 29.9 46.4
   0.225 0.341
   7.39 13.9
Alternative formulation
  dP = (Pa - P)dt + Pdz

## Slide 18: Limitations of Mean Reversion Models
The speed of mean reversion may vary above and below the mean level
A realistic price process for electricity must capture the possibility of price gaps
The spikes may be asymmetric
One should rather speak about a “floor reverting process”
  Floor levels are characterized by seasonality

## Slide 19: Modeling Price Jumps
A realistic price process for electricity must capture the possibility of price gaps
Price jumps result from interaction of demand and supply in a market with virtually no storage
The spikes to the upside are more likely
One should rather speak about a “floor reverting process”
  Floor levels are characterized by seasonality

## Slide 20: Jump-Diffusion Model
Standard approach to modeling jumps: jump-diffusion models
Example: GBM
  dP = Pdt + Pdz + (J-1)Pdq
  dq =1 if a jump occurs, 0 otherwise
  J - the size of the jumps
  J is typically assumed to follow a lognormal distribution, log (J) ~ N(,2)

## Slide 21: Stochastic Volatility
Stochastic volatility models have been developed to capture empirically observable facts:
  Volatility tends to cluster: extreme observations tend to be followed by extreme observations
  Volatility in many markets varies with the price level and the general market direction

## Slide 22: GARCH MODEL
GARCH (Generalized Auto Regressive Heteroskedastic model)
Definition
  ln (Pt/Pt-1) = k + tt, t ~ N(0,1)
  2t+1 =  + 2t2t + 2t
  
The term k represents average level of returns, tt - the stochastic innovation to returns

## Slide 23: Model-Implied Volatility
Future spot prices can be predicted using a fundamental model, containing the following components
  Representation of future generation stack
  Load forecast and load variability
  Assumptions regarding future fuel prices and price volatility

## Slide 24: Model-Implied Volatility
A fundamental model can be used as a simulation tool to translate the assumptions regarding load and fuel price volatility into electricity price volatility
The difficulty: a realistic fundamental model takes a very long time to run
One has to use a more simplistic model and face the consequences

## Slide 25: Summary Statistics
On-peak prices, South of Path 15
6x16 wholesale peak hours definition
April 1, 1998 to June 15, 1999
Prices
  Mean $ 29.79 / MWh
  Standard Deviation $ 15.55 / MWh
Returns
  Mean (annualized 300) 26.6 %
  Standard Deviation (annualized 300) 509 %

## Slide 26: Stochastic Process Formulation
Parameters estimated using the RATS software
Maximum likelihood estimator
GBM: dP = µPdt + σPdz
Jump Diffusion: dP = µPdt + σPdz + P*dq*N(mean, variance)
  dq = 1 with probability p
  = 0 with probability (1-p)

## Slide 27: Conditional Heteroskedasticity Models
ARCH: σ2 t+1 =  + α σ2 t υ2t
GARCH: σ2 t+1 =  + α σ2 t υ2t + β σ2 t
EGARCH: σ2 t+1 = (σ2 t)δ exp( + α σ2 t υ2t + β (|σ2 t υ2t|))

## Slide 28: GBM
K 0.0009 (0.0026)
0.05 (0.06)
2 0.08618 0.1252
24.86 9.021
Log
Likelihood 267 41
Full Sample Summer Only

## Slide 29: Jump Diffusion
K (0.031) (0.2363)
(4.25) (0.75)
2 0.0063 0.3534
5.89 2.72
mean 0.0734 0.0762
1.97 0.50
variance 0.1773 0.3219
9.64 1.20
p 0.4429 0.2757
10.37 1.71
Log
Likelihood 355 51
Full Sample Summer Only

## Slide 30: ARCH GBM
K 0.0096 (0.0007) 0.75 (0.02)
 0.0522 0.1129
20.60 8.66
α 0.4431 0.0868 4.90 1.13
Log
Likelihood 300 42
Full Sample Summer Only

## Slide 31: ARCH Jump Diffusion
K (0.0068) (0.0385)
(0.97) (2.84)
 0.0066 0.0014
5.13 1.16
 0.4887 0.2178
5.29 1.82
mean (0.0269) 0.0581
(0.49) 0.79
variance 0.1825 0.1869
4.52 4.47
p 0.2434 0.5522
5.14 5.49
Log
Likelihood 371 54
Full Sample Summer Only

## Slide 32: GARCH GBM
K 0.0089 (0.0001)
0.90 (0.001)
 0.0026 0.1142
4.56 8.54
 0.1603 0.0885
5.93 1.12
β 0.8259 (0.056)
39.92 (0.00)
Log
Likelihood 330 41
Full Sample Summer Only

## Slide 33: GARCH Jump diffusion
K (0.0195) (0.0126)
(2.66)
 0.0054 0.0255
4.84
 0.4525 0.1466
4.69
β (0.0359) (0.0242)
(0.00)
mean 0.1465 0.0569
2.87
variance 0.2043 0.3108
4.35
p 0.2679 0.2676
5.87
Log
Likelihood 378 51
Full Sample Summer Only

## Slide 34: EGARCH Pure Diffusion
K (0.0122) (0.0151) (1.06) (0.32)
 (0.9878) (1.967)
(9.37) (3.68)
 (1.6009) (0.8341)
(6.94) (1.85)
β 1.6468 0.2953
7.49 0.63
 0.7027 0.0904
20.41 0.41
Log
Likelihood 345 43
Full Sample Summer Only