## Slide 1: ENERGY DERIVATIVES© Class 1 March 1, 2001
Vince Kaminski

## Slide 2: Natural Gas
Natural mixture of gaseous hydrocarbons found issuing from the ground or obtained from specially driven wells
Its chief component, methane, usually makes up from 80% to 95%,
  the balance is composed of varying amounts of ethane, propane, butane, and other hydrocarbon compounds.

## Slide 3: Units
  The Btu is a unit of measurement for energy. It represents the amount of heat that is necessary to raise the temperature of one pound of water by 1 degree, Fahrenheit.
  Mcf stands for one thousand cubic feet.
  Bcf - Billion Cubic Feet. Gas measurement approximately equal to one trillion (1,000,000,000,000) Btu’s.
  Quad. An abbreviation for a quadrillion (1,000,000,000,000,000). For natural gas, roughly equivalent to one trillion (1,000,000,000,000) cubic feet, or 1 Tcf.

## Slide 5: Natural Gas (2)
Petroleum products and natural gas come from ancient plants and animals that died and their bodies have decomposed
The remains were deposited along the shorelines of old rivers and covered with mud and silt
Compression by the weight of the sedimentary rock layers
Organic materials transform over time into petroleum products due to intense heat and pressure present in the rock formations
Oil an natural gas migrate through the pores in the sedimentary rock formations
Some oil and gas becomes trapped under layers of rock formed above the sedimentary rock
Another explanation: primordial gases that rise up from the mantle

## Slide 6: Natural Gas (3)
Associated gas: dissolved in oil or available along oil deposits
  Separated from oil at the casing heads of the well
Non-associated gas occurs in reservoirs separate from crude oil
  Dry gas
  ~75% of the US production
Gas condensate

## Slide 8: Natural Gas (4)
Natural gas is also defined as lean (dry) or rich (wet) depending on the content of heavy components
Other substances:
  water
  hydrogen sulfide
  CO2
  Nitrogen
  Helium

## Slide 9: Natural Gas Liquids
Natural gas liquids belong to the family of saturated hydrocarbons known as paraffins
  CnH2n+2
Ethane
Propane
Butane
Iso-butane
Natural gasoline

## Slide 10: Natural Gas Liquids (2)
Processing of natural gas liquids
  Extraction of NGLs
  Fractionation of the NGLs into separate components
Absorption and cryogenic expander process

## Slide 11: Natural Gas Processing
Dehydration to remove water
Removal of hydrogen sulfide
Removal of CO2
Over 600 natural gas processing plants on the US
70,000 miles of pipelines used for transportation of unfractionated NGLs

## Slide 12: Natural Gas Transportation
  The U.S. gas transmission system ~ 300,000 miles of piping. Steel pipes 20 to 42 inches in diameter.
  Natural gas is transmitted at higher pressures (from 200 to 1500 psi) to reduce the volume of the gas, and provide a pushing force to propel the gas through the pipe
  Compressor stations about every 100 miles along the pipeline. Reciprocating compressors are powered by a portion of the natural gas that flows through the pipeline.
  8,000 gas compressing stations along gas pipelines, with a combined output capability of over 20 million horsepower

## Slide 13: Types of Underground Natural Gas Storage
Depleted natural gas and oil fields with sufficient porosity, permeability and retention characteristics
Aquifers
  geology of aquifers is similar to that of depleted production fields
  water-bearing sedimentary rock covered with impermeable cap rock
Salt caverns
  storage developed by injecting water into a salt formation and creating a cavern

## Slide 14: Depleted Fields as Storage Reservoirs
Depleted gas/oil and aquifer fields are characterized by a low turnover rates
Injection season typically lasts from March/April till October/ November
The reservoir is emptied during winter
During an occasional upward spike in prices during summer, the injections can be suspended and gas earmarked for injections can be diverted to the market
These reservoirs take primarily advantage of summer/winter spread
Injections withdrawals are typically hedged in the futures/forwards markets in order to lock-in seasonal spread
Optionality consists in the ability to time hedging decisions and to occasionally suspend injections or withdrawals

## Slide 15: Salt Dome Storage
High deliverability compared to other types of underground storage
A salt formation storage facility can be turned over several times during the heating season
During summer, salt dome storage is used to satisfy cooling load
Injection/withdrawal rates(as in the case of aquifers) depend on the amount of gas in storage
  high pressure of gas in storage slows down injections, accelerates withdrawals
  low pressure has the opposite effect
Storage for peaking operations used to satisfy swing demand

## Slide 16
Natural Gas Storage Facilities

## Slide 17: Storage Optionality
Depleted oilfield/aquifer storage is a an option on a seasonal spread
Additional optionality related to
  the option to switch from injection to withdrawal mode (or vice versa) when justified by market conditions
  the option to adjust timing of hedges
  the option to deliver to multiple pipelines (depends on the location of the storage facility)
Optionality is limited by operational constraints
  rate of injections/withdrawals changes with the level of working gas in storage
  gas has to be injected into storage due to contractual obligations even when it’s unprofitable based on the seasonal spread

## Slide 18: Storage Optionality (2)
Salt dome storage is an option on short-term calendar spread
Gas is being injected when prices drop and withdrawn when prices spike
Quick turnover allows the storage operator to take advantage of price spikes (upward and downward)
Additional optionality related to location (multiple pipelines)
The operations of a salt dome storage may be affected by contractual obligations (supporting the operations of an associated pipeline)

## Slide 19: Storage Optionality (3)
Optimal gas storage facility operation
  When to put gas in, and when to take it out
    These are interacting, compound options:
      Putting gas in costs money but creates the option to sell gas later
      Taking gas out returns money and creates the option to store gas again later
      The value and optimal exercise policy of these options interact
    Option exercise price:
      Price of gas plus cost of storing or removing gas
    Option exercise constraints reduce the value of the option

## Slide 20: Storage Optionality
Gas Storage Facility
  Operating value is the sum of the value of operating options considered above
  Valuing these options over the investment horizon requires a long term model of gas prices at facility location
The value of an option depends often on who owns the asset

## Slide 21: Forward Contract
Sale of commodity or a financial instrument
  At a price agreed at inception of the contract
  For delivery at a later date
  Cash flow occurs in the future
A forward contract has no immediate cash consequences
Distinction between a long and short position

## Slide 22: Arbitrage and Forward Contract Valuation
Taking a forward short position is equivalent to:
  Buying commodity today, at current (i.e. spot) price,
  Funding and storing commodity until delivery date,
  Delivering to the long party
Similarly, the long party can sell at spot price,
  Invest proceeds
  Use proceeds to pay for delivery

## Slide 23: Arbitrage and Forward Contract Valuations (Continued)
In a completely efficient market
  FP[T] = SP* (1+(r+h))^T
  where:
    SP=spot price
    FP[T] = forward price (for delivery at time T)
    (r+h) = cost-of-carry,
      where:
        r=interest rate
        h=storage cost

## Slide 24: Convenience Yield
The holder of physical asset has advantage over the holder of the long forward position:
Can profit from intervening price shifts and commodity shortages
This advantage is expressed as a convenience yield

## Slide 25: Spot vs. Forward Arbitrage
Recap (using continuous compounding):
  FP[T] = SP* exp ((r+h-c)*T)
Arbitrage acts to counteract deviations from this relationship

## Slide 26: Arbitraging Spot/Forward Discrepancies (l)
Strategy when FP[T] exceeds [SP*exp((r+h)*T)]
  (assume c=0 for convenience, and consider a unit volume of commodity):
Borrow cash (amount: SP*exp(h*T))
Sell forward contract (to deliver commodity at T)
Use loan to buy and store commodity
Cost: SP*exp(h*T))

## Slide 27: Arbitraging Spot/Forward Discrepancies (lI)
At time T, deliver commodity, collect FP[T], and pay off loan and interest: SP * exp((r+h)*T)
Profit = Revenues - Cost
= FP[T] - SP* exp((r+h) * T)

## Slide 28: Arbitraging Spot/Forward Discrepancies (lIl)
Strategy when FP[T] less than [SP*exp((r+h)*T)] (only applies to commodity holders):
Sell commodity holdings at spot price, and invest proceeds (at rate r)
Sell storage space (at rate h per unit of time)
Buy forward contracts with delivery date of T

## Slide 29: Arbitraging Spot/Forward Discrepancies (lV)
At time T, use investment and storage proceeds (equaling SP*exp( (r+h)*T)) to pay for gas delivered under the forward contract
Profit = SP*exp((r+h)*T) - FP[T]
For non-zero convenience yield, use probabilistic arguments to obtain similar results

## Slide 30: Structural Forward/Spot Price Relationship
Several school of thought on whether commodity spot/forward relationship is structurally one of
Contango (with SP < FP) or
Backwardation (with SP > FP)
Historical data shows spot/forward price biases as sometimes positive, sometimes negative, and rarely zero
Obviously, as delivery data approaches, FP  SP

## Slide 31: Futures Contracts
As with financial futures, commodity futures contract is forward contract transacted on an exchange and marked-to-market on a daily basis
Different exchanges have different ways trading: pit trading with open outcry, electronic trading, etc.
Enron owns two seats on NYMEX

## Slide 32: Futures vs. Forwards
Futures are:
More liquid
More public, implying more transparent prices
Less subject to credit risk, due to margin requirements
Less flexible
Transaction of futures is not limited to physical holders and consumers of commodity

## Slide 33: How Forward Curve is Used
 =correlation coefficient of commodity price and interest rate
If ( =0), can assume future and forward prices are equal
If ( >0), then for a long future position:
Spot price increasesan immediate (marked-to-market) gain, which is invested at new, higher rate
Spot price decreasesan immediate loss,which is financed at a new, lower rate
If ( <0), then for a long future position:
Spot price increasesan immediate gain invested at lower rate,
Spot price decreasesan immediate loss financed at higher rates
Implies: If  >0, Futures price> Forward price
If  <0, Futures price< Forward price

## Slide 34: Exchange for Physicals (EFP)
Vast majority of futures are closed out prior to maturity
Futures contracts can be modified in cases where a future buyer and seller do hold contracts to maturity
  Parties may negotiate exchange for physicals, a bilateral delivery arrangement off exchange floor
EFP parties lose the credit support of exchange
EFPs require price adjustments for contract modifications
E.g., transportation costs to ADP (alternate delivery point)

## Slide 35: NYMEX NG Contract (1)
Trading Unit
  Futures: 10,000 million British thermal units (mmBtu). Options: One NYMEX Division natural gas futures contract.
Trading Hours
  Futures and Options: Open outcry trading is conducted from 9:30 A.M. - 3:10 P.M. After-hours trading in futures and options is conducted via the NYMEX ACCESS® electronic trading system from 7 P.M. to 9 A.M. on Sundays and 4 P.M. to 9 A.M., Mondays through Thursdays. All times are New York time.

## Slide 36: NYMEX NG Contract (2)
Trading Months
  Futures: 36 consecutive months commencing with the next calendar month (for example, on January 2, 2001, trading occurs in all months from February 2001 through January 2004), plus a long-dated contract, initially listed 36 months out.
  Options: 12 consecutive months, plus 15, 18, 21, 24, 27, 30, 33, and 36 months on a June-December cycle.
Price Quotation
  Futures and Options: Dollars and cents per mmBtu, for example, $5.035 per mmBtu.
Minimum Price Fluctuation
  Futures and Options: $0.001 (0.1 ¢) per mmBtu ($10 per contract).

## Slide 37: NYMEX NG Contract (3)
Maximum Daily Price Fluctuation
  Futures: $1.00 per mmBtu ($10,000 per contract) for all months. If any contract is traded, bid, or offered at the limit for five minutes, trading is halted for 15 minutes. When trading resumes, expanded limits are in place that allow the price to fluctuate by $2.00 in either direction of the previous day's setlement price. There are no price limits on any month during the last three days of trading in the spot month. Options: No price limits.
Last Trading Day
  Futures: Trading terminates three business days prior to the first calendar day of the delivery month. Options: Trading terminates at the close of business on the business day immediately preceding the expiration of the underlying futures contract.

## Slide 38: NYMEX NG Contract (4)
Exercise of Options
  By a clearing member to the Exchange clearinghouse not later than 5:30 P.M. or 45 minutes after the underlying futures settlement price is posted, whichever is later, on any day up to and including the options expiration.
Option Strike Prices
  Twenty strike prices in increments of $0.05 (5¢) per mmBtu above and below the at-the-money strike price in all months, plus an additional 20 strike prices in increments of $0.05 per mmBtu above the at-the-money price will be offered in the first three nearby months, and the next 10 strike prices in increments of $0.25 (25¢) per mmBtu above the highest and below the lowest existing strike prices in all months for a total of at least 81 strike prices in the first three nearby months and a total of at least 61 strike prices for four months and beyond. The at-the-money strike price is nearest to the previous day±s close of the underlying futures contract. Strike price boundaries are adjusted according to futures price movements.

## Slide 39: NYMEX NG Contract (5)
Delivery Location
  Sabine Pipe Line Co.±s Henry Hub in Louisiana. Seller is responsible for the movement of the gas through the Hub; the buyer, from the Hub. The Hub fee will be paid by seller.
Delivery Period
  Delivery shall take place no earlier than the first calendar day of the delivery month and shall be completed no later than the last calendar day of the delivery month. All deliveries shall be made at as uniform as possible an hourly and daily rate of flow over the course of the delivery month.

## Slide 40: NYMEX NG Contract (6)
Alternate Delivery Procedure (ADP)
  An alternate delivery procedure is available to buyers and sellers who have been matched by the Exchange subsequent to the termination of trading in the spot month contract. If buyer and seller agree to consummate delivery under terms different from those prescribed in the contract specifications, they may proceed on that basis after submitting a notice of their intention to the Exchange.
Exchange of Futures For, or in Connection with, Physicals (EFP)
  The commercial buyer or seller may exchange a futures position for a physical position of equal quantity by submitting a notice to the Exchange. EFPs may be used to either initiate or liquidate a futures position.
Quality Specifications
  Pipeline specifications in effect at time of delivery.

## Slide 41: NYMEX NG Contract (7)
Position Limits
  7,000 contracts for all months combined, but not to exceed 1,000 in the last three days of trading in the spot month or 5,000 in any one month.
Exchange of Futures For, Or In Connection With, Physicals (EFP)
The commercial buyer or seller may exchange a futures position for a physical position of equal quantity by submitting a notice to the Exchange. EFPs may be used to either initiate or liquidate a futures position.
Trading Symbols - Futures: NG Options: ON

## Slide 42: Swaps
Swap is an exchange of future cash flows of equal present values
Swap is linear instrument
Typically a swap involves exchange of payments based on a fixed price (i.e. predetermined, not necessarily constant) and a floating (changing and unknown at inception) price. Fixed for floating swap.
Basis swap: floating for floating swap
Commodity swaps are based on a notional volume of the underlying commodity

## Slide 43: Swap Valuation
Swap valuation means determination of the fixed price
Floating leg:  (Volumei x Floating_pricei)/(1+r)i
Fixed leg:  (Volumei x Fixed_pricei)/(1+r)i
Both legs must be equal at inception. This allows to calculate the fixed price, given the value of the floating leg.
The valuation of the floating leg is based on the current set of the forward prices
A swap is a portfolio of forward contracts

## Slide 44: Natural Gas Basis Swap
An active forward market for basis differentials
The fixed component of the basis swap is the basis differential
In the following example: The buyer pays L3D (NX3) minus $0.25 and receives the Index
Profit on trade:
  (Index - L3D) > -$0.25
Loss on trade:
  (Index - L3D) < -$0.25

## Slide 45: Hedging Fixed Price Sale
XYZ sold 10,000 MMBtu/day on EPNG Permian Basinn@ $1.75
Purchase of the same amount of natural gas at Index
XYZ buys 30 NG Nymex contracts at the current market price
What is the risk of this position?
Additional hedge: basis swap

## Slide 46: Swing Swap
Swing: transaction under an interruptible contract that is renegotiated every day in terms of volume and price
Swing swap: a fixed-for-floating swap that references the Gas Daily price
The buyer pays a fixed price and receives the daily index

## Slide 47: EFP
EFP - Exchange For Physicals
A transaction under which one party will give futures contracts to the other and receive physical gas
  Posted Price - the price at which the futures contracts are transferred from one account to another
  Differential - the difference between the futures contracts and the physical gas
  Delivery point
  Size
  Invoice Price = Posted Price + Differential. The price paid by the buyer of an EFP to the seller.

## Slide 48: EFP Example
Posted price: $2.00
Differential: -$0.30
Net Purchase Price: $0.30 - Futures Cost
The effective purchase price depends on the price at which the buyer closes he short future position

## Slide 49
Buyer
Seller
L3D - $0.25
Index
Generic Basis Swap

## Slide 50
Futures Exchange
XYZ Trading
Basis Swap
L3D - $0.35
Permian Index
Gas @ Permian
Gas @ Permian
Supply
Market
L3D
30
Futures
30
Futures
$2.05
Permian Index
$1.75
Hedging Fixed Price Sale at Alternate Delivery Location with Futures

## Slide 51
Market
Swing Swap
ABC
XYZ Production
Gas @ Permian
$2.00
$2.00
Daily Permian
Index
Swing Swap for the Part of the Month allows XYZ to
participate in intra-month price changes

## Slide 52
XYZ
Producer
Swing Swap
Daily Permian
Index
$2.00
$2.00
Gas @ Permian
End-user application of a swing swap

## Slide 53
Trader
Supplier
Swing Swap
Daily Permian
Index
$2.00
$1.95
Gas @ Permian
Hedging Swing Swap Sale by Buying Fixed -Price Physical Gas - Base Load Gas Purchased

## Slide 54
Daily Market
Swing Swap
ABC
Trader
Gas @ Permian
Gas @ Permian
$1.95
$2.00
Daily Permian
Index
Daily Permian Index
Hedging Swing Swap Sale by Buying Fixed -Price Physical Gas - Base Load Gas Purchased

## Slide 55
Seller
(Producer)
Buyer
Futures Exchanged with Seller’s Broker
Gas @ Permian
P - $0.30 = $1.70
P = $2.00
Futures Contracts
Buying EFP and Fixing Effective Purchase Price
Posted Price - $2.00
Differential: -$0.30

## Slide 56
Futures Exchange
Buyer
Seller
Futures Exchanged with Seller’s Broker
Gas @ Permian
P - $0.30 = $1.70
P = $2.00
Futures Contracts
Futures Contracts
$1.90
Buying EFP and Fixing Effective Purchase Price