SensorBox Hardware Engineering Notes
# Overview
Sensor Box project will create a sensor system without UI:
This document provides functional requirements, and outlines design, and implementation.
# Document Change Log
Revision	Notes
Version 1.2, March 2024	Hardware revision B issues → Revision C.

# Board Check-Out
## Revision C SPI4 check
SPI4 has BMP581 12MHz and ND120 166kHz.
LPSI_CLK_ROOT is 132MHz; divisors inadequate for ND120? Try min LPSI (max divisor=8)=> 66MHz.
ASI is occasionally returning junk bytes. Need to validate SPI bus timing!
SPI4 signal	Scope Probe
SCK	D0
MISO	D1
MOSI	D2
CS0 – ND120 ASI	D3

Initial capture from ND120 initialization:

## Clock: Actual period 12.5us, frequency 80kHz. Specification 6us (spec has period only). Select to first clock edge: Actual 15.5us, specification 100us. Bugs Now Fixed: -  clock is supposed to be normally 0, data captured on falling edge (wrong polarity) -  inadequate pause after CS (tSC=100usec required) -  clock half speed (reduced to try improve results, didn’t work). ND120 SPI required timing: Weirdness: - a pause is specified between bytes: tbc=100us: a pause of (100-8*6)=52us is required. Bug: FSL LPSPI setup uses too small a prescaler whilst attempting wonderful precision on clock speed.