Source: Emil Mikulic, "Benchmarking and turbo"[[I]].
Figure 1: differences between back-to-back reads of rdtscp - standard
[I] Emil Mikulic, "Benchmarking and turbo," https://unix4lyfe.org, 2017. [Online]. Available: https://unix4lyfe.org/benchmarking/turbo.html , retr. 2025-06-19
Note y-axis linear 60 .. 90, and the rare but there are result points outside of the constant lines.
Source: Emil Mikulic, ibid.
Figure 2: the same with optimizations, warmup, disable turbo.
Note y-axis logarithmic 10 .. ~200, also the range covered on the x-axis is quite different, see better speed, better constancy, however more outliers.
You can find the pro

gram he used in the link to the sources, it helped me to check rdtscp() more stable than rdtsc() on my system, and I achieved the following picture:
The several closely packed lines are due to the fact that on my system several - 7 to 9 - pairs of values are always generated with the same start value and mostly consecutive values for the difference, whether this is due to compiler optimizations, threading, several cores or something else I can only guess. I estimate the outliers similar to Emil Mikulic, just the dots in my graph a bigger.
Figure 3: time between back-to-back rdtscp() readouts on my system
Shortest and most dense back-to-back timer measurements I achieved with:
enabling turbo mode by "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo",
spinning one core to full speed by: "while :; do :; done" in one terminal window,
measuring rdtscp()s acc. a refining proposal by Michael Stumpfl:
// Check program to test reading of CPU internal tick counter, and evaluate
// in which system state fastest back-to-back readout with least scatter is
// possible.
// Compile with: "gcc -O3 -Wall -Werror -Wpedantic -o stumpfl_2 stumpfl_2.c",
// run with: "./stumpfl_2 > rdtscp.res",
// then evaluate average, max and number of diffs greater than double of
// average.
// On my system ( linux, Kali / Debian )
// "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo"
// to enable turbo mode, and
// "while :; do :; done" in one terminal to keep the system at high speed works
// best:
// average: ~29 ticks, max devia: ~54k ticks, count of values >58 ticks: 38.
// "sudo nice -19 taskset -c 3 ./stumpfl_2 > rdtscp.res" doesn't improve,
// Changelog:
// 2025-07-21: in linux "( void )TSC_AUX" can be omitted, provides less scatter,
// 2025-07-21: prefer print macros "PRI(d/u)xx" over "%d", "%l",
// 2025-07-21: prefer sharp defined types "(u)intxx_t" over "int" and "long",
#include <stdio.h> // reg. e.g. printf, fprintf, ...
#include <stdint.h> // reg. e.g. uint64_t,
#include <inttypes.h> // reg. e.g. PRIu64,
Source: Emil Mikulic, "Benchmarking and turbo"[[II]].
Figure 4: differences between back-to-back reads of rdtscp - standard
[II] Emil Mikulic, "Benchmarking and turbo," https://unix4lyfe.org, 2017. [Online]. Available: https://unix4lyfe.org/benchmarking/turbo.html , retr. 2025-06-19
Note y-axis linear 60 .. 90, and the rare but there are result points outside of the constant lines.
ed with:
enabling turbo mode by "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo",
spinning one core to full speed by: "while :; do :; done" in one terminal window,
measuring rdtscp()s acc. a refining proposal by Michael Stumpfl:
// Check program to test reading of CPU internal tick counter, and evaluate
// in which system state fastest back-to-back readout with least scatter is
// possible.
// Compile with: "gcc -O3 -Wall -Werror -Wpedantic -o stumpfl_2 stumpfl_2.c",
// run with: "./stumpfl_2 > rdtscp.res",
// then evaluate average, max and number of diffs greater than double of
// average.
// On my system ( linux, Kali / Debian )
// "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo"
// to enable turbo mode, and
// "while :; do :; done" in one terminal to keep the system at high speed works
// best:
// average: ~29 ticks, max devia: ~54k ticks, count of values >58 ticks: 38.
// "sudo nice -19 taskset -c 3 ./stumpfl_2 > rdtscp.res" doesn't improve,
// Changelog:
// 2025-07-21: in linux "( void )TSC_AUX" can be omitted, provides less scatter,
// 2025-07-21: prefer print macros "PRI(d/u)xx" over "%d", "%l",
// 2025-07-21: prefer sharp defined types "(u)intxx_t" over "int" and "long",
#include <stdio.h> // reg. e.g. printf, fprintf, ...
#include <stdint.h> // reg. e.g. uint64_t,
#include <inttypes.h> // reg. e.g. PRIu64,
Source: Emil Mikulic, "Benchmarking and turbo"[[III]].
Figure 5: differences between back-to-back reads of rdtscp - standard
[III] Emil Mikulic, "Benchmarking and turbo," https://unix4lyfe.org, 2017. [Online]. Available: https://unix4lyfe.org/benchmarking/turbo.html , retr. 2025-06-19
Note y-axis linear 60 .. 90, and the rare but there are result points outside of the constant lines.
Source: Emil Mikulic, ibid.
Figure 6: the same with optimizations, warmup, disable turbo.
Note y-axis logarithmic 10 .. ~200, also the range covered on the x-axis is quite different, see better speed, better constancy, however more outliers.
You can find the program he used in the link to the sources, it helped me to check rdtscp() more stable than rdtsc() on my system, and I achieved the following picture:
The several closely packed lines are due to the fact that on my system several - 7 to 9 - pairs of values are always generated with the same start value and mostly consecutive values for the difference, whether this is due to compiler optimizations, threading, several cores or something else I can only guess. I estimate the outliers similar to Emil Mikulic, just the dots in my graph a bigger.
Figure 7: time between back-to-back rdtscp() readouts on my system
Shortest and most dense back-to-back timer measurements I achieved with:
enabling turbo mode by "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo",
spinning one core to full speed by: "while :; do :; done" in one terminal window,
measuring rdtscp()s acc. a refining proposal by Michael Stumpfl:
// Check program to test reading of CPU internal tick counter, and evaluate
// in which system state fastest back-to-back readout with least scatter is
// possible.
// Compile with: "gcc -O3 -Wall -Werror -Wpedantic -o stumpfl_2 stumpfl_2.c",
// run with: "./stumpfl_2 > rdtscp.res",
// then evaluate average, max and number of diffs greater than double of
// average.
// On my system ( linux, Kali / Debian )
// "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo"
// to enable turbo mode, and
// "while :; do :; done" in one terminal to keep the system at high speed works
// best:
// average: ~29 ticks, max devia: ~54k ticks, count of values >58 ticks: 38.
// "sudo nice -19 taskset -c 3 ./stumpfl_2 > rdtscp.res" doesn't improve,
// Changelog:
// 2025-07-21: in linux "( void )TSC_AUX" can be omitted, provides less scatter,
// 2025-07-21: prefer print macros "PRI(d/u)xx" over "%d", "%l",
// 2025-07-21: prefer sharp defined types "(u)intxx_t" over "int" and "long",
#include <stdio.h> // reg. e.g. printf, fprintf, ...
#include <stdint.h> // reg. e.g. uint64_t,
#include <inttypes.h> // reg. e.g. PRIu64,
Source: Emil Mikulic, "Benchmarking and turbo"[[IV]].
Figure 8: differences between back-to-back reads of rdtscp - standard
[IV] Emil Mikulic, "Benchmarking and turbo," https://unix4lyfe.org, 2017. [Online]. Available: https://unix4lyfe.org/benchmarking/turbo.html , retr. 2025-06-19
Note y-axis linear 60 .. 90, and the rare but there are result points outside of the constant lines.
Source: Emil Mikulic, ibid.
Figure 9: the same with optimizations, warmup, disable turbo.
Note y-axis logarithmic 10 .. ~200, also the range covered on the x-axis is quite different, see better speed, better constancy, however more outliers.
You can find the program he used in the link to the sources, it helped me to check rdtscp() more stable than rdtsc() on my system, and I achieved the following picture:
The several closely packed lines are due to the fact that on my system several - 7 to 9 - pairs of values are always generated with the same start value and mostly consecutive values for the difference, whether this is due to compiler optimizations, threading, several cores or something else I can only guess. I estimate the outliers similar to Emil Mikulic, just the dots in my graph a bigger.
Figure 10: time between back-to-back rdtscp() readouts on my system
Shortest and most dense back-to-back timer measurements I achieved with:
enabling turbo mode by "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo",
spinning one core to full speed by: "while :; do :; done" in one terminal window,
measuring rdtscp()s acc. a refining proposal by Michael Stumpfl:
// Check program to test reading of CPU internal tick counter, and evaluate
// in which system state fastest back-to-back readout with least scatter is
// possible.
// Compile with: "gcc -O3 -Wall -Werror -Wpedantic -o stumpfl_2 stumpfl_2.c",
// run with: "./stumpfl_2 > rdtscp.res",
// then evaluate average, max and number of diffs greater than double of
// average.
// On my system ( linux, Kali / Debian )
// "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo"
// to enable turbo mode, and
// "while :; do :; done" in one terminal to keep the system at high speed works
// best:
// average: ~29 ticks, max devia: ~54k ticks, count of values >58 ticks: 38.
// "sudo nice -19 taskset -c 3 ./stumpfl_2 > rdtscp.res" doesn't improve,
// Changelog:
// 2025-07-21: in linux "( void )TSC_AUX" can be omitted, provides less scatter,
// 2025-07-21: prefer print macros "PRI(d/u)xx" over "%d", "%l",
// 2025-07-21: prefer sharp defined types "(u)intxx_t" over "int" and "long",
#include <stdio.h> // reg. e.g. printf, fprintf, ...
#include <stdint.h> // reg. e.g. uint64_t,
#include <inttypes.h>

        // reg. e.g. PRIu64,
Source: Emil Mikulic, "Benchmarking and turbo"[[V]].
Figure 11: differences between back-to-back reads of rdtscp - standard
[V] Emil Mikulic, "Benchmarking and turbo," https://unix4lyfe.org, 2017. [Online]. Available: https://unix4lyfe.org/benchmarking/turbo.html , retr. 2025-06-19
Note y-axis linear 60 .. 90, and the rare but there are result points outside of the constant lines.
Source: Emil Mikulic, ibid.
Figure 12: the same with optimizations, warmup, disable turbo.
Note y-axis logarithmic 10 .. ~200, also the range covered on the x-axis is quite different, see better speed, better constancy, however more outliers.
You can find the program he used in the link to the sources, it helped me to check rdtscp() more stable than rdtsc() on my system, and I achieved the following picture:
The several closely packed lines are due to the fact that on my system several - 7 to 9 - pairs of values are always generated with the same start value and mostly consecutive values for the difference, whether this is due to compiler optimizations, threading, several cores or something else I can only guess. I estimate the outliers similar to Emil Mikulic, just the dots in my graph a bigger.
Figure 13: time between back-to-back rdtscp() readouts on my system
Shortest and most dense back-to-back timer measurements I achieved with:
enabling turbo mode by "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo",
spinning one core to full speed by: "while :; do :; done" in one terminal window,
measuring rdtscp()s acc. a refining proposal by Michael Stumpfl:
// Check program to test reading of CPU internal tick counter, and evaluate
// in which system state fastest back-to-back readout with least scatter is
// possible.
// Compile with: "gcc -O3 -Wall -Werror -Wpedantic -o stumpfl_2 stumpfl_2.c",
// run with: "./stumpfl_2 > rdtscp.res",
// then evaluate average, max and number of diffs greater than double of
// average.
// On my system ( linux, Kali / Debian )
// "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo"
// to enable turbo mode, and
// "while :; do :; done" in one terminal to keep the system at high speed works
// best:
// average: ~29 ticks, max devia: ~54k ticks, count of values >58 ticks: 38.
// "sudo nice -19 taskset -c 3 ./stumpfl_2 > rdtscp.res" doesn't improve,
// Changelog:
// 2025-07-21: in linux "( void )TSC_AUX" can be omitted, provides less scatter,
// 2025-07-21: prefer print macros "PRI(d/u)xx" over "%d", "%l",
// 2025-07-21: prefer sharp defined types "(u)intxx_t" over "int" and "long",
#include <stdio.h> // reg. e.g. printf, fprintf, ...
#include <stdint.h> // reg. e.g. uint64_t,
#include <inttypes.h> // reg. e.g. PRIu64,
Source: Emil Mikulic, "Benchmarking and turbo"[[VI]].
Figure 14: differences between back-to-back reads of rdtscp - standard
[VI] Emil Mikulic, "Benchmarking and turbo," https://unix4lyfe.org, 2017. [Online]. Available: https://unix4lyfe.org/benchmarking/turbo.html , retr. 2025-06-19
Note y-axis linear 60 .. 90, and the rare but there are result points outside of the constant lines.
Source: Emil Mikulic, ibid.
Figure 15: the same with optimizations, warmup, disable turbo.
Note y-axis logarithmic 10 .. ~200, also the range covered on the x-axis is quite different, see better speed, better constancy, however more outliers.
You can lowing picture:
The several closely packed lines are due to the fact that on my system several - 7 to 9 - pairs of values are always generated with the same start value and mostly consecutive values for the difference, whether this is due to compiler optimizations, threading, several cores or something else I can only guess. I estimate the outliers similar to Emil Mikulic, just the dots in my graph a bigger.
Figure 16: time between back-to-back rdtscp() readouts on my system
Shortest and most dense back-to-back timer measurements I achieved with:
enabling turbo mode by "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo",
spinning one core to full speed by: "while :; do :; done" in one terminal window,
measuring rdtscp()s acc. a refining proposal by Michael Stumpfl:
// Check program to test reading of CPU internal tick counter, and evaluate
// in which system state fastest back-to-back readout with least scatter is
// possible.
// Compile with: "gcc -O3 -Wall -Werror -Wpedantic -o stumpfl_2 stumpfl_2.c",
// run with: "./stumpfl_2 > rdtscp.res",
// then evaluate average, max and number of diffs greater than double of
// average.
// On my system ( linux, Kali / Debian )
// "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo"
// to enable turbo mode, and
// "while :; do :; done" in one terminal to keep the system at high speed works
// best:
// average: ~29 ticks, max devia: ~54k ticks, count of values >58 ticks: 38.
// "sudo nice -19 taskset -c 3 ./stumpfl_2 > rdtscp.res" doesn't improve,
// Changelog:
// 2025
Source: Emil Mikulic, "Benchmarking and turbo"[[VII]].
Figure 17: differences between back-to-back reads of rdtscp - standard
[VII] Emil Mikulic, "Benchmarking and turbo," https://unix4lyfe.org, 2017. [Online]. Available: https://unix4lyfe.org/benchmarking/turbo.html , retr. 2025-06-19
Note y-axis linear 60 .. 90, and the rare but there are result points outside of the constant lines.
Source: Emil Mikulic, ibid.
Figure 18: the same with optimizations, warmup, disable turbo.
Note y-axis logarithmic 10 .. ~200, also the range covered on the x-axis is quite different, see better speed, better constancy, however more outliers.
You can find the program he used in the link to the sources, it helped me to check rdtscp() more stable than rdtsc() on my system, and I achieved the following picture:
The several closely packed lines are due to the fact that on my system several - 7 to 9 - pairs of values are always generated with the same start value and mostly consecutive values for the difference, whether this is due to compiler optimizations, threading, several cores or something else I can only guess. I estimate the outliers similar to Emil Mikulic, just the dots in my graph a bigger.
Figure 19: time between back-to-back rdtscp() readouts on my system
Shortest and most dense back-to-back timer measurements I achieved with:
enabling turbo mode by "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo",
spinning one core to full speed by: "while :; do :; done" in one terminal window,
measuring rdtscp()s acc. a refining proposal by Michael Stumpfl:
// Check program to test reading of CPU internal tick counter, and evaluate
// in which system state fastest back-to-back readout with least scatter is
// possible.
// Compile with: "gcc -O3 -Wall -Werror -Wpedantic -o stumpfl_2 stumpfl_2.c",
// run with: "./stumpfl_2 > rdtscp.res",
// then evaluate average, max and number of diffs greater than double of
// average.
// On my system ( linux, Kali / Debian )
// "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo"
// to enable turbo mode, and
// "while :; do :; done" in one terminal to keep the system at high speed works
// best:
// average: ~29 ticks, max devia: ~54k ticks, count of values >58 ticks: 38.
// "sudo nice -19 taskset -c 3 ./stumpfl_2 > rdtscp.res" doesn't improve,
// Changelog:
// 2025-07-21: in linux "( void )TSC_AUX" can be omitted, provides less scatter,
// 2025-07-21: prefer print macros "PRI(d/u)xx" over "%d", "%l",
// 2025-07-21: prefer sharp defined types "(u)intxx_t" over "int" and "long",
#include <stdio.h> // reg. e.g. printf, fprintf, ...
#include <stdint.h> // reg. e.g. uint64_t,
#include <inttypes.h> // reg. e.g. PRIu64,
Source: Emil Mikulic, "Benchmarking and turbo"[[VIII]].
Figure 20: differences between back-to-back reads of rdtscp - standard
[VIII] Emil Mikulic, "Benchmarking and turbo," https://unix4lyfe.org, 2017. [Online]. Available: https://unix4lyfe.org/benchmarking/turbo.html , retr. 2025-06-19
Note y-axis linear 60 .. 90, and the rare but there are result points outside of the constant lines.
Source: Emil Mikulic, ibid.
Figure 21: the same with optimizations, warmup, disable turbo.
Note y-axis logarithmic 10 .. ~200, also the range covered on the x-axis is quite different, see better speed, better constancy, however more outliers.
You can find the program he used in the link to the sources, it helped me to check rdtscp() more stable than rdtsc() on my system, and I achieved the following picture:
The several closely packed lines are due to the fact that on my system several - 7 to 9 - pairs of values are always generated with the same start value and mostly consecutive values for the difference, whether this is due to compiler optimizations, threading, several cores or something else I can only guess. I estimate the outliers similar to Emil Mikulic, just the dots in my graph a bigger.
Figure 22: time between back-to-back rdtscp() readouts on my system
Shortest and most dense back-to-back timer measurements I achieved with:
enabling turbo mode by "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo",
spinning one core to full speed by: "while :; do :; done" in one terminal window,
measuring rdtscp()s acc. a refining proposal by Michael Stumpfl:
// Check program to test reading of CPU internal tick counter, and evaluate
// in which system state fastest back-to-back readout with least scatter is
// possible.
// Compile with: "gcc -O3 -Wall -Werror -Wpedantic -o stumpfl_2 stumpfl_2.c",
// run with: "./stumpfl_2 > rdtscp.res",
// then evaluate average, max and number of diffs greater than double of
// average.
// On my system ( linux, Kali / Debian )
// "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo"
// to enable turbo mode, and
// "while :; do :; done" in one terminal to keep the system at high speed works
// best:
// average: ~29 ticks, max devia: ~54k ticks, count of values >58 ticks: 38.
// "sudo nice -19 taskset -c 3 ./stumpfl_2 > rdtscp.res" doesn't improve,
// Changelog:
// 2025-07-21: in linux "( void )TSC_AUX" can be omitted, provides less scatter,
// 2025-07-21: prefer print macros "PRI(d/u)xx" over "%d", "%l",
// 2025-07-21: prefer sharp defined types "(u)intxx_t" over "int" and "long", // reg. e.g. uint64_t,
#include <inttypes.h> // reg. e.g. PRIu64,
Source: Emil Mikulic, "Benchmarking and turbo"[[IX]].
Figure 23: differences between back-to-back reads of rdtscp - standard
[IX] Emil Mikulic, "Benchmarking and turbo," https://unix4lyfe.org, 2017. [Online]. Available: https://unix4lyfe.org/benchmarking/turbo.html , retr. 2025-06-19
Note y-axis linear 60 .. 90, and the rare but there are result points outside of the constant lines.
Source: Emil Mikulic, ibid.
Figure 24: the same with optimizations, warmup, disable turbo.
Note y-axis logarithmic 10 .. ~200, also the range covered on the x-axis is quite different, see better speed, better constancy, however more outliers.
You can find the program he used in the link to the sources, it helped me to check rdtscp() more stable than rdtsc() on my system, and I achieved the following picture:
The several closely packed lines are due to the fact that on my system several - 7 to 9 - pairs of values are always generated with the same start value and mostly consecutive values for the difference, whether this is due to compiler optimizations, threading, several cores or something else I can only guess. I estimate the outliers similar to Emil Mikulic, just the dots in my graph a bigger.
Figure 25: time between back-to-back rdtscp() readouts on my system
Shortest and most dense back-to-back timer measurements I achieved with:
enabling turbo mode by "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo",
spinning one core to full speed by: "while :; do :; done" in one terminal window,
measuring rdtscp()s acc. a refining proposal by Michael Stumpfl:
// Check program to test reading of CPU internal tick counter, and evaluate
// in which system state fastest back-to-back readout with least scatter is
// possible.
// Compile with: "gcc -O3 -Wall -Werror -Wpedantic -o stumpfl_2 stumpfl_2.c",
// run with: "./stumpfl_2 > rdtscp.res",
// then evaluate average, max and number of diffs greater than double of
// average.
// On my system ( linux, Kali / Debian )
// "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo"
// to enable turbo mode, and
// "while :; do :; done" in one terminal to keep the system at high speed works
// best:
// average: ~29 ticks, max devia: ~54k ticks, count of values >58 ticks: 38.
// "sudo nice -19 taskset -c 3 ./stumpfl_2 > rdtscp.res" doesn't improve,
// Changelog:
// 2025-07-21: in linux "( void )TSC_AUX" can be omitted, provides less scatter,
// 2025-07-21: prefer print macros "PRI(d/u)xx" over "%d", "%l",
// 2025-07-21: prefer sharp defined types "(u)intxx_t" over "int" and "long",
#include <stdio.h> // reg. e.g. printf, fprintf, ...
#include <stdint.h> // reg. e.g. uint64_t,
#include <inttypes.h> // reg. e.g. PRIu64,
Source: Emil Mikulic, "Benchmarking and turbo"[[X]].
Figure 26: differences between back-to-back reads of rdtscp - standard
[X] Emil Mikulic, "Benchmarking and turbo," https://unix4lyfe.org, 2017. [Online]. Available: https://unix4lyfe.org/benchmarking/turbo.html , retr. 2025-06-19
Note y-axis linear 60 .. 90, and the rare but there are result points outside of the constant lines.
Source: Emil Mikulic, ibid.
Figure 27: the same with optimizations, warmup, disable turbo.
Note y-axis logarithmic 10 .. ~200, also the range covered on the x-axis is quite different, see better speed, better constancy, however more outliers.
You can find the program he used in the link to the sources, it helped me to check rdtscp() more stable than rdtsc() on my system, and I achieved the following picture:
The several closely packed lines are due to the fact that on my system several - 7 to 9 - pairs of values are always generated with the same start value and mostly consecutive values for the difference, whether this is due to compiler optimizations, threading, several cores or something else I can only guess. I estimate the outliers similar to Emil Mikulic, just the dots in my graph a bigger.
Figure 28: time between back-to-back rdtscp() readouts on my system
Shortest and most dense back-to-back timer measurements I achieved with:
enabling turbo mode by "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo",
spinning one core to full speed by: "while :; do :; done" in one terminal window,
measuring rdtscp()s acc. a refining proposal by Michael Stumpfl:
// Check program to test reading of CPU internal tick counter, and evaluate
// in which system state fastest back-to-back readout with least scatter is
// possible.
// Compile with: "gcc -O3 -Wall -Werror -Wpedantic -o stumpfl_2 stumpfl_2.c",
// run with: "./stumpfl_2 > rdtscp.res",
// then evaluate average, max and number of diffs greater than double of
// average.
// On my system ( linux, Kali / Debian )
// "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo"
// to enable turbo mode, and
// "while :; do :; done" in one terminal to keep the system at high speed works
// best:
// average: ~29 ticks, max devia: ~54k ticks, count of values >58 ticks: 38.
// "sudo nice -19 taskset -c 3 ./stumpfl_2 > rdtscp.res" doesn't improve,
// Changelog:
// 2025-07-21: in linux "( void )TSC_AUX" can be omitted, provides less scatter,
// 2025-07-21: prefer print macros "PRI(d/u)xx" over "%d", "%l",
// 2025-07-21: prefer sharp defined types "(u)intxx_t" over "int" and "long",
#include <stdio.h> // reg. e.g. printf, fprintf, ...
#include <stdint.h> // reg. e.g. uint64_t,
#include <inttypes.h> // reg. e.g. PRIu64,
Source: Emil Mikulic, "Benchmarking and turbo"[[XI]].
Figure 29: differences between back-to-back reads of rdtscp - standard
[XI] Emil Mikulic, "Benchmarking and turbo," https://unix4lyfe.org, 2017. [Online]. Available: https://unix4lyfe.org/benchmarking/turbo.html , retr. 2025-06-19
Note y-axis linear 60 .. 90, and the rare but there are result points outside of the constant lines.
Source: Emil Mikulic, ibid.
Figure 30: the same with optimizations, warmup, disable turbo.
Note y-axis logarithmic 10 .. ~200, also the range covered on the x-axis is quite different, see better speed, better constancy, however more outliers.
You can find the program he used in the link to the sources, it helped me to check rdtscp() more stable than rdtsc() on my system, and I achieved the following picture:
The several closely packed lines are due to the fact that on my system several - 7 to 9 - pairs of values are always generated with the same start value and mostly consecutive values for the difference, whether this is due to compiler optimizations, threading, several cores or something else I can only guess. I estimate the outliers similar to Emil Mikulic, just the dots in my graph a bigger.
Figure 31: time between back-to-back rdtscp() readouts on my system
Shortest and most dense back-to-back timer measurements I achieved with:
enabling turbo mode by "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo",
spinning one core to full speed by: "while :; do :; done" in one terminal window,
measuring rdtscp()s acc. a refining proposal by Michael Stumpfl:
// Check program to test reading of CPU internal tick counter, and evaluate
// in which system state fastest back-to-back readout with least scatter is
// possible.
// Compile with: "gcc -O3 -Wall -Werror -Wpedantic -o stumpfl_2 stumpfl_2.c",
// run with: "./stumpfl_2 > rdtscp.res",
// then evaluate average, max and number of diffs greater than double of
// average.
// On my system ( linux, Kali / Debian )
// "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo"
// to enable turbo mode, and
// "while :; do :; done" in one terminal to keep the system at high speed works
// best:
// average: ~29 ticks, max devia: ~54k ticks, count of values >58 ticks: 38.
// "sudo nice -19 taskset -c 3 ./stumpfl_2 > rdtscp.res" doesn't improve,
// Changelog:
// 2025-07-21: in linux "( void )TSC_AUX" can be omitted, provides less scatter,
// 2025-07-21: prefer print macros "PRI(d/u)xx" over "%d", "%l",
// 2025-07-21: prefer sharp defined types "(u)intxx_t" over "int" and "long",
#include <stdio.h> // reg. e.g. printf, fprintf, ...
#include <stdint.h> // reg. e.g. uint64_t,
#include <inttypes.h> // reg. e.g. PRIu64,
Source: Emil Mikulic, "Benchmarking and turbo"[[XII]].
Figure 32: differences between back-to-back reads of rdtscp - standard
[XII] Emil Mikulic, "Benchmarking and turbo," https://unix4lyfe.org, 2017. [Online]. Available: https://unix4lyfe.org/benchmarking/turbo.html , retr. 2025-06-19
Note y-axis linear 60 .. 90, and the rare but there are result points outside of the constant lines.
Source: Emil Mikulic, ibid.
Figure 33: the same with optimizations, warmup, disable turbo.
Note y-axis logarithmic 10 .. ~200, also the range covered on the x-axis is quite different, see better speed, better constancy, however more outliers.
You can find the program he used in the link to the sources, it helped me to check rdtscp() more stable than rdtsc() on my system, and I achieved the following picture:
The several closely packed lines are due to the fact that on my system several - 7 to 9 - pairs of values are always generated with the same start value and mostly consecutive values for the difference, whether this is due to compiler optimizations, threading, several cores or something else I can only guess. I estimate the outliers similar to Emil Mikulic, just the dots in my graph a bigger.
Figure 34: time between back-to-back rdtscp() readouts on my system
Shortest and most dense back-to-back timer measurements I achieved with:
enabling turbo mode by "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo",
spinning one core to full speed by: "while :; do :; done" in one terminal window,
measuring rdtscp()s acc. a refining proposal by Michael Stumpfl:
// Check program to test reading of CPU internal tick counter, and evaluate
// in which system state fastest back-to-back readout with least scatter is
// possible.
// Compile with: "gcc -O3 -Wall -Werror -Wpedantic -o stumpfl_2 stumpfl_2.c",
// run with: "./stumpfl_2 > rdtscp.res",
// then evaluate average, max and number of diffs greater than double of
// average.
// On my system ( linux, Kali / Debian )
// "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo"
// to enable turbo mode, and
// "while :; do :; done" in one terminal to keep the system at high speed works
// best:
// average: ~29 ticks, max devia: ~54k ticks, count of values >58 ticks: 38.
// "sudo nice -19 taskset -c 3 ./stumpfl_2 > rdtscp.res" doesn't improve,
// Changelog:
// 2025-07-21: in linux "( void )TSC_AUX" can be omitted, provides less scatter,
// 2025-07-21: prefer print macros "PRI(d/u)xx" over "%d", "%l",
// 2025-07-21: prefer sharp defined types "(u)intxx_t" over "int" and "long",
#include <stdio.h> // reg. e.g. printf, fprintf, ...
#include <stdint.h> // reg. e.g. uint64_t,
#include <inttypes.h> // reg. e.g. PRIu64,

Source: Emil Mikulic, "Benchmarking and turbo"[[XIII]].
Figure 35: differences between back-to-back reads of rdtscp - standard
[XIII] Emil Mikulic, "Benchmarking and turbo," https://unix4lyfe.org, 2017. [Online]. Available: https://unix4lyfe.org/benchmarking/turbo.html , retr. 2025-06-19
Note y-axis linear 60 .. 90, and the rare but there are result points outside of the constant lines.
Source: Emil Mikulic, ibid.
Figure 36: the same with optimizations, warmup, disable turbo.
Note y-axis logarithmic 10 .. ~200, also the range covered on the x-axis is quite different, see better speed, better constancy, however more outliers.
You can find the program he used in the link to the sources, it helped me to check rdtscp() more stable than rdtsc() on my system, and I achieved the following picture:
The several closely packed lines are due to the fact that on my system several - 7 to 9 - pairs of values are always generated with the same start value and mostly consecutive values for the difference, whether this is due to compiler optimizations, threading, several cores or something else I can only guess. I estimate the outliers similar to Emil Mikulic, just the dots in my graph a bigger.
Figure 37: time between back-to-back rdtscp() readouts on my system
Shortest and most dense back-to-back timer measurements I achieved with:
enabling turbo mode by "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo",
spinning one core to full speed by: "while :; do :; done" in one terminal window,
measuring rdtscp()s acc. a refining proposal by Michael Stumpfl:
// Check program to test reading of CPU internal tick counter, and evaluate
// in which system state fastest back-to-back readout with least scatter is
// possible.
// Compile with: "gcc -O3 -Wall -Werror -Wpedantic -o stumpfl_2 stumpfl_2.c",
// run with: "./stumpfl_2 > rdtscp.res",
// then evaluate average, max and number of diffs greater than double of
// average.
// On my system ( linux, Kali / Debian )
// "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo"
// to enable turbo mode, and
// "while :; do :; done" in one terminal to keep the system at high speed works
// best:
// average: ~29 ticks, max devia: ~54k ticks, count of values >58 ticks: 38.
// "sudo nice -19 taskset -c 3 ./stumpfl_2 > rdtscp.res" doesn't improve,
// Changelog:
// 2025-07-21: in linux "( void )TSC_AUX" can be omitted, provides less scatter,
// 2025-07-21: prefer print macros "PRI(d/u)xx" over "%d", "%l",
// 2025-07-21: prefer sharp defined types "(u)intxx_t" over "int" and "long",
#include <stdio.h> // reg. e.g. printf, fprintf, ...
#include <stdint.h> // reg. e.g. uint64_t,
#include <inttypes.h> // reg. e.g. PRIu64,

Source: Emil Mikulic, "Benchmarking and turbo"[[XIV]].
Figure 38: differences between back-to-back reads of rdtscp - standard
[XIV] Emil Mikulic, "Benchmarking and turbo," https://unix4lyfe.org, 2017. [Online]. Available: https://unix4lyfe.org/benchmarking/turbo.html , retr. 2025-06-19
Note y-axis linear 60 .. 90, and the rare but there are result points outside of the constant lines.
Source: Emil Mikulic, ibid.
Note y-axis logarithmic 10 .. ~200, also the range covered on the x-axis is quite different, see better speed, better constancy, however more outliers.
You can find the program he used in the link to the sources, it helped me to check rdtscp() more stable than rdtsc() on my system, and I achieved the following picture:
The several closely packed lines are due to the fact that on my system several - 7 to 9 - pairs of values are always generated with the same start value and mostly consecutive values for the difference, whether this is due to compiler optimizations, threading, several cores or something else I can only guess. I estimate the outliers similar to Emil Mikulic, just the dots in my graph a bigger.
Figure 39: time between back-to-back rdtscp() readouts on my system
Shortest and most dense back-to-back timer measurements I achieved with:
enabling turbo mode by "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo",
spinning one core to full speed by: "while :; do :; done" in one terminal window,
measuring rdtscp()s acc. a refining proposal by Michael Stumpfl:
// Check program to test reading of CPU internal tick counter, and evaluate
// in which system state fastest back-to-back readout with least scatter is
// possible.
// Compile with: "gcc -O3 -Wall -Werror -Wpedantic -o stumpfl_2 stumpfl_2.c",
// run with: "./stumpfl_2 > rdtscp.res",
// then evaluate average, max and number of diffs greater than double of
// average.
// On my system ( linux, Kali / Debian )
// "echo 0 | sudo tee /sys/devices/system/cpu/intel_pstate/no_turbo"
// to enable turbo mode, and
// "while :; do :; done" in one terminal to keep the system at high speed works
// best:
// average: ~29 ticks, max devia: ~54k ticks, count of values >58 ticks: 38.
// "sudo nice -19 taskset -c 3 ./stumpfl_2 > rdtscp.res" doesn't improve,
// Changelog:
// 2025-07-21: in linux "( void )TSC_AUX" can be omitted, provides less scatter,
// 2025-07-21: prefer print macros "PRI(d/u)xx" over "%d", "%l",
// 2025-07-21: prefer sharp defined types "(u)intxx_t" over "int" and "long",
#include <stdio.h> // reg. e.g. printf, fprintf, ...
#include <stdint.h>
#include <stdint.h> // reg. e.g. uint64_t,
#include <inttypes.h> // reg. e.g. PRIu64,

#include <stdint.h> // reg. e.g. uint64_t,
#include <inttypes.h> // reg. e.g. PRIu64,