## Slide 1: Storage Management
Dr. Alexios Louridas

## Slide 2: Mass Storage Structure

## Slide 3: Mass Storage
Hard Disk Drives (HDDs)
Nonvolatile Memory Devices

## Slide 4: HDD Performance
Transfer Rate
Positioning or Random-Access Time
Head Crash
Effective Transfer Rates
The rate of data transfer from HDD to the computer bus.
Consist of 2 parts:
Seek time – time to locate cylinder
Rotational latency – time to locate the sector
When the head damages the magnetic sections.
Stated transfer rates are always higher than effective transfer rate from disk to OS.

## Slide 5: SSD and Nand
Die
Plane
Block
Page

## Slide 6: NVM Performance
Flash Translation Layer (FTL)
Erasure
Over Provisioning
Wear Levelling
For nonvolatile memory, a table that tracks currently valid blocks.
Erasure can happen on an entire block.
Space set aside for data writes that is not counted in the device free space. (20% of an SSD)
The effort to select all NAND cells over time as write targets to avoid premature media failure due to wearing out a subset of cells.

## Slide 7: Drives to OS
local I/O ports
motherboards
network

## Slide 8: HDD Scheduling

## Slide 9: Scheduling
HDD Scheduling
Disk-scheduling algorithms can improve the effective bandwidth of HDDs, the average response time, and the variance in response time
NVM Scheduling
Because there are no moving parts there is no significant performance increase with use of similar scheduling algorithms.
Scheduling Algorithms
Algorithms such as SCAN and C-SCAN are designed to make such improvements through strategies for disk-queue ordering. Performance of disk-scheduling algorithms can vary greatly on hard disks.
Scheduling Algorithms
FCFS strategy is used.

## Slide 10: Errors
Data storage and transmission are complex and frequently result in errors. Error detection attempts to spot such problems to alert the system for corrective action and to avoid error propagation. Error correction can detect and repair problems, depending on the amount of correction data available and the amount of data that was corrupted.

## Slide 11: Device and Swap-Space Management

## Slide 12: Device Management
Low-Level Formatting
Sectors created, NVM pages initialised and FTL created.
OS Storage Device preparation
Record its own data structures on devices.

## Slide 13: OS Preparing a storage device
Partitioning
Partition 1
Partition 2
Partition 3
Volume creation
Implicit
  File system placed
Explicit
  RAID
Logical Formatting
File System Creation
Bootable file System
Raw Disk Allocation

## Slide 14: Bad Sectors - Blocks
Sector Sparing
Typical Bad-Sector Management
Sector Slipping
NVM Devices
Device controller replaces a sector with a spare one. Usually in each cylinder there are a few spare sectors.
1. Read logical block X -> ECC find block X is bad -> Device controller replaces block with a spare Y -> Any reads or writes on X are redirected to Y.
Move all sectors of a block by one space.
Also suffer from bad pages. Its easier to deal with as they just become inactive. Device controller still needs to maintain a record of all bad pages.

## Slide 15: Storage Types
Host-attached
Storage Area Networks (SAN)
HDDs
SSDs
CD-DVD
Flash Drives
…
Network-Attached
Cloud

## Slide 16: RAID Structure Redundant Arrays of Independent Disks

## Slide 17: Large system and RAID
Failure
Secondary storage become redundant using RAID algorithms.
Raid Algorithms
These algorithms allow more than one drive to be used for a given operation and allow continued operation.
Drive Failures
Automatic recovery techniques.
RAID Organisation
Multiple levels, each level provides some combination of reliability and high transfer rates.

## Slide 18: RAID Levels

## Slide 19: Object Storage
Object storage is used for big data problems such as indexing the Internet and cloud photo storage. Objects are self-defining collections of data, addressed by object ID rather than file name. Typically it uses replication for data protection, computes based on the data on systems where a copy of the data exists, and is horizontally scalable for vast capacity and easy expansion

## Slide 20: Thank you
I big thank you to Bob Eager, software carpentry for sharing their bash resources and Abraham Silberschatz; Peter B. Galvin; Greg Gagne book on Operating Systems for the valuable help in creating the lecture materials (images, resources etc…)